## Slide 1: Lecture 14 ~ ENGT 1200 Introduction to Industrial & Systems Engineering
Cause & Effect Diagrams, Ishikawa or Fishbone Charts, Operational Definitions, & CI Project Management

## Slide 2: Cause and Effect Diagram
Developed by Dr. Kaoru Ishikawa in 1943
Sometimes referred to as “Ishikawa diagram or Fishbone Chart”
The Cause and Effect Diagram is a picture composed of lines and symbols designed to represent a meaningful relation ship between effect and causes.
Notes: Notes

## Slide 3: Cause and Effect Diagram
Customer
waits
Machine/
Equipment
People
Methods
Material
Environment
Person called is absent
not at desk
Person called out of office
Customer
Not giving section and/or receiving party
Starts leaving message
Lengthy Conversation
Complaining
Operator
Absent
Doesn't Know Company Jobs
Misunderstands Customer
Connects Wrong Party
Telephone Rush Hour
Lack of directories
Old Switchboard
No call forwarding
Relief Schedule
Lunch Hour Scheduling
Training
of Operators
of Receiving Party
of Customer
Notes: Notes

## Slide 4: CAUSE-AND-EFFECT DIAGRAM
The cause-and-effect diagram offers a systematic way to pinpoint the various factors that may be causing a problem.
It prompts people to ask. "Why is this occurring?" As the diagram is developed, more and more potential causes come to light.
  Some people call this tool the Ishikawa Chart after its originator Kaoru Ishikawa, or an Ishikawa Chart and some call it a “Fishbone Diagram" because it takes the shape of a fish as more causes are brainstormed.
Cause & Effect Diagram
Notes: Notes

## Slide 5: Cause-and-Effect Diagram
  The effect (problem) is the "head of the fish." Leading from this the "backbone" and connected to this are the "main bones," which represent major categories of causes.
  Commonly used categories include people, policies, materials, procedures, equipment, and environment.
  These categories are only suggestions; you may use any major category the team deems appropriate.
Cause & Effect Diagram
Categories
Causes
The Effect
Notes: Notes

## Slide 6: Cause & Effect Diagram
The Effect
Machine
Process
People
Materials
Why?
Why?
Why?
Why?
Why?
Why?
Why?
Why?
Major Classifications
Cause & Effect Diagramming is easily associated with:
  Affinity Diagrams
  Brainstorming
  Root cause Analysis
As you can see, the diagram does indeed have the shape of a fish. The effect is on the right, and the causes form the "bones: of the fish. Note the four main categories of causes, these can be edited.
Cause & Effect Diagram
Notes: Notes

## Slide 7: Cause & Effect Diagram
Developing The Cause & Effect Chart: Charts can be developed simply using a template board and post-it-notes or select tools form the “Toolbox” are very effective…
  Both the effect and the causes may be generated by a team using the Brainstorming Session Technique that generates the group thinking and organizations perceptions…
  These may be used directly to create the Cause & effect Chart or Affinity Diagraming may be an intermediate step used to organize the materials into the major categories for your Fish Bone…
  Using a Pareto Diagram with the generated data may also lead you to the predominate items that cause the originally specified and/or identified effect.
Cause & Effect Diagram
Notes: Notes

## Slide 8: Cause & Effect Diagram
Putting it to work:
Follow these three steps when creating a cause-and-effect diagram:
  Decide on the effect (problem) to be analyzed, being sure it’s specific, well understood and agreed to by everyone. Write it in a box on the right side of the flip chart or marking board; this is the "head of the fish.“
  Next, draw a horizontal line form the head across the paper with several "major bones" drawn on a slant. At the end of each, write one of the major categories that contribute to the effect.
  Brainstorm specific causes. Attach each specific cause to an appropriate major category. Whenever possible, break down the specific cause into sub causes by using the "why" technique.
  Keep asking, "Why is this occurring?“
  to get to the Root Cause!
Cause & Effect Diagram
Notes: Notes

## Slide 9: Cause & Effect Diagram
Here are some additional tips:
If in doubt about possible causes, check your ideas with data. Look for causes that appear repeatedly. This will have the added benefit of helping the team reach consensus.
In most cases, it's not so important where the specific cause is placed on the diagram. The important point is that it's identified.
The cause-and-effect diagram can be useful when displayed publicly and people are invited to contribute. Think of this as a large-scale brainstorming effort.
When creating the diagram, try to use as few words as possible. This will require team members to focus their ideas.
Cause & Effect Diagram
Notes: Notes

## Slide 10: Cause & Effect Diagram
Downloadable Chart Templates from Microsoft for owners of PowerPoint 2007 or 2010
Notes: Notes

## Slide 11: Statistical Process Control / 6 Sigma
SPC / 6 Sigma today is comprised of these heavily used Core Tools:
    Data Collection: Data Collection Tools…
    Box Plot
    Cause and Effect Diagrams (Fishbone Charts)
    Histograms
    Pareto Diagrams
    Process Flow Diagrams or Process Mapping
    Scatter Diagrams
    Stratification
    Run Charts and /or Control Charts Chapters will be covered in MECH 2270 Engineering Statistics
Notes: Notes

## Slide 12: Collection and Reliability of Data
Today data collection that is Operationally Defined by an Action Team and collected by trained experience associates who understand how consistency is related to reliability, which is usually considered most reliable.
Data that is displayed using statistical tools or descriptive geometry is best interpreted, in a consistent manner and understood…
Notes: Notes

## Slide 13: Operational Definitions
A operational definition is a clear, concise, and detailed definition of a measure in document form. All data, especially attribute data, which requires assessment or interpretation must be collected, clarified & defined in terms that are consistent and quantifiable.
Example: The item must be “Red” is unacceptable, how many reds are there?
A better definition would be: “The item must be “Fire Engine Red as compared to a specific sample color chip viewed in daylight or under simulated daylight lighting” Associates making this assessment must pass a color blindness test and a performance test”.
  A set of decision making criteria that assures an attribute conforms to requirements or a standard such as a work instruction.
  The basic “who, what, when and where” questions are addressed and documented.
Notes: Notes

## Slide 14: Operational Definition
The Operational Definition provides a tangible or observable explanation of the variable.
If the variable is not directly measurable, it identifies characteristics of the variable that can be directly measured.
In addition, whether or not the variable can be directly measured, the operational definition names the possible associated elements of the variable that can be measured. For example, self-esteem is a measure of how people feel about themselves we can not see it, It is not directly measurable.
An aspects of self-esteem that can be measured and recorded is looks you in the eye when talking, acts confidently, or ask questions, etc. As these are observable and linked to self-esteem.
Notes: Notes

## Slide 15: Operational Definition
The ability to discern between the acceptable and unacceptable
  Operational Definitions allow people to do their jobs better with less confusion
  Yields yes or no answers, do or don’t, etc. conclusions and can be perform consistently based upon requirements and decision criteria.
  Is essential or fundamental to all types of data, but especially for attributes

## Slide 16: Operational Definitions
Variable data should also be collected following Operational Definitions.
Example: What type of instrument should be used to collect data concerning the roundness of a ball bearing.
Typical questions addressed by an operational definition:
  Type of instrument
  Discrimination of the instrument
  Location or environmental requirements
  Training requirements
Notes: Notes

## Slide 17: Lack of Operational Definitions
Few conclusions can be reached from data collected without an operational definition, which explains criteria such as :
  What was collected & the operational definition used
  How it was collected, method, environment, instrument used, etc.
  When it was collected, time, date, frequency, etc.
  Who collected it & are they trained & qualified.
When Data Completeness, Data Integrity, & Data Consistency are analyzed, data based decisions will make since & are used by management…
Notes: Notes

## Slide 18: Lack of Operational Definitions
What was collected must be understood ~ example: sports record or data collected 50 years ago were records of amateurs who held jobs and competed without today's technology today it is the records of the pro we are comparing.
How it was collected, method, environment, instrument used, etc. ~ example: 50 years ago stop watches were used versus the “touch wall” technology in swimming events.
When it was collected, time, date, frequency, etc. ~ example: in 50 years history of Olympic Swimming amateurs were replaced with professionals who use super swim suits, in track it may be shoes. In any case a new operational definition including modern equipment, professional trainers, etc., changes the scores…
Notes: Notes

## Slide 19: Lack of Operational Definitions
Who collected it and are they qualified to collect it ~ example: people with prejudice or volunteers with no training, many doing their best under less that perfect conditions, interpreted time pieces and recorded the records on paper, which had to be transcribed into other language to be understood by all, a very time consuming process!
Today “people” develop and administer hands off timing / recording system that automatically time the events, in smaller increments 100th of a second versus 1 second, record the data in pc systems that are monitored for reliability and accuracy! The output of the data is in multiple languages and immediate!
Only like systems should be compared, but understanding system discrepancies allows for some analysis which may need be explained …
Notes: Notes

## Slide 20: Good Operational Definitions
Good operational definitions address the following:
  Characteristic of interest
  Measuring instrument, metrology issues, or criterion
  Method of test criterion
  Decision criterion
  Employee training in collecting and interpreting data criterion.
  Following a consistent criterion allows analysis of measurements to be compared; & any data collection or analysis process to be repeated, time after time, or improved if necessary…
Notes: Notes

## Slide 21: When are they used
Operational definitions are used when:
  Work instruction are required for the job, as in ISO, TS, etc. registration procedures.
  To define and accomplish performance based training needs, these usually address the Metrology Issues…
  For improvement teams to assure the reliability of data, develop benchmarks, and to assess current work practices against current documentation, in a consistent Manner…
  When data must be visible and questioned by those who view it!
Notes: Notes

## Slide 22: Do…
When Operational Definitions are used :
Identify data that was collected without an operational definition and establish its reliability?
Use operational definitions with every project when defining quality measures and data collection.
Define any new measures added during a project.
Correct current definitions if changes to procedures have been made due to a quality improvement, new technology, etc.
Re-train all concerned associates if needed.
Notes: Notes

## Slide 23
GUIDE FOR CREATING A
PROCESS IMPROVEMENT
PROJECT
Notes: Notes

## Slide 24: Your Use of This Course to Improve That Which is Undesirable
CI or Continuous Improvement is a major component of today's Quality Systems and a focus of the Industrial and System Engineers vocation.
To manage an Improvement Project you need to use every topic we have covered to date, and possibly more, in our Introduction to Industrial and Systems Engineering course!
To end our ENGT 1200 Class we will focus on creating a process improvement project and the need to use a team and your leadership skills!
Notes: Notes Slide Courtesy of Quality Management: Creating and Sustaining Organizational Effectiveness, 2e Donna C. S. Summers
Copyright ©2009 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved ~ In part…

## Slide 25: No project always goes according to plan, but well planned projects are less likely to go astray.
We emphasize that: Involving the affected people in gathering information enhances the thoroughness of the process and increases the likelihood of reaching a consensus.
Teams are the most effective change agents…
Notes: Notes Slide Courtesy of Quality Management: Creating and Sustaining Organizational Effectiveness, 2e Donna C. S. Summers
Copyright ©2009 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved ~ In part…

## Slide 26: Project Management
Characteristics of a Project
  Projects have a start and a finish
  Projects have a time frame for completion
  Projects are unique, one-time occurrences
  Projects involve a variety of people
  Projects have a limited set of resources
  Projects require the sequencing of activities and phases
Notes: Notes Slide Courtesy of Quality Management: Creating and Sustaining Organizational Effectiveness, 2e Donna C. S. Summers
Copyright ©2009 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved ~ In part…

## Slide 27: Project Management
Effective project managers:
  create challenging possibilities
  inspire a shared vision
  increase visibility
  empower people
  praise
Notes: Notes Slide Courtesy of Quality Management: Creating and Sustaining Organizational Effectiveness, 2e Donna C. S. Summers
Copyright ©2009 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved ~ In part…

## Slide 28: Project Management
Functional Manager
  Specialist within a functional area
  Analysis focus
  Analytic approach
Project Manager
  Generalist with a wide background of experience and knowledge
  Synthesis focus
  Systems Approach
  Facilitator
Notes: Notes Slide Courtesy of Quality Management: Creating and Sustaining Organizational Effectiveness, 2e Donna C. S. Summers
Copyright ©2009 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved ~ In part…

## Slide 29: Project Management
Effective project managers ask:
  What needs to be done?
  When must it be done?
  Where will the resources come from?
  What is the most effective way to implement the project…
Notes: Notes Slide Courtesy of Quality Management: Creating and Sustaining Organizational Effectiveness, 2e Donna C. S. Summers
Copyright ©2009 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved ~ In part…

## Slide 30: Continuous Improvement
Continuous Improvement or CI is a method to achieve superior results and addresses all aspects of the organization.
Most importantly it recognizes that the performance of the individual parts of the organization improve most efficiently when all the parts are aligned to business goals and a shared philosophy!
It also recognizes systems cannot improve unless all the people involved improve.
Notes: Notes

## Slide 31: Project Management
Characteristics of an Effective Project Manager:
  Credibility: your personal traits, track record
      What do you know?
      What have you Accomplished?
      How consistent are you?
      Do they trust you?
  Sensitivity
  Leadership
  Ability to handle stress
Notes: Notes Slide Courtesy of Quality Management: Creating and Sustaining Organizational Effectiveness, 2e Donna C. S. Summers
Copyright ©2009 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved ~ In part…

## Slide 32: Project Management
Project Selection
  Major Projects are selected based upon their ability to fulfill the mission, goals, or objectives established by an organization.
They must be aligned with the organizational vision and goals..
Notes: Notes Slide Courtesy of Quality Management: Creating and Sustaining Organizational Effectiveness, 2e Donna C. S. Summers
Copyright ©2009 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved ~ In part…

## Slide 33: Project Management
Project Proposals Contain:
  Technical Description
  Implementation Plan Overview
  Plan for Logistic Support and Administration
  Experience of Participants
Notes: Notes Slide Courtesy of Quality Management: Creating and Sustaining Organizational Effectiveness, 2e Donna C. S. Summers
Copyright ©2009 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved ~ In part…

## Slide 34: Figure 14-3 Project Proposal Guidelines
The Project Proposal described by the text can also be a guide for creating a CI Improvement Team.
As CI is recommended and used in TQM, Lean Manufacturing, ISO 9000 Organizations, etc. We will explain what it looks like…
Notes: Notes Slide Courtesy of Quality Management: Creating and Sustaining Organizational Effectiveness, 2e Donna C. S. Summers
Copyright ©2009 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved ~ In part…

## Slide 35: CI or Continuous Improvement
CI deals with deliberate, controlled, measured, organizational change.
CI uses scientific methods or the use of data to establish standard against which something can be measured or assessed “benchmarks”.
CI recognizes “That which can be measured, can be controlled”
Notes: Notes

## Slide 36: CI or Continuous Improvement
CI is conducted by action teams versus the individual effort to assure group thinking is analyzed, synergy is created and consensus is gained.
Gaps between our visions and performance reality are determined and an improvement hypothesis is devised and acted upon, most often using a process such as the PDCA Cycle!
Notes: Notes

## Slide 37: Why Continuous Improvement
Simply stated we and our environment will change whether we want to or not as time, and external events we cannot account for or control, will affect the performance and outcomes of our efforts…
Customer expectations change, new laws are passed, competition improves, the economy changes, etc.
Notes: Notes

## Slide 38: Why Continuous Improvement
Uncontrolled sporadic, irregular, and inconsistent change can result in less than world class performance…
Uncontrolled change does little to keep us current, relevant, secure, or employable!
Notes: Notes

## Slide 39: Why Continuous Improvement
Worst yet is that overall performance of the elements that need improvement are accepted as normal and become part of the culture if not addressed…
World Class Organization are those that strive to achieve superior results throughout the total organization, they all ask what can we do better and practice CI!
Notes: Notes

## Slide 40: Guide for Creating a Process Improvement Project Goals…
  Determining what is a process
  By definition a “Process” is: –“the logical organization of people, materials, equipment, and procedures into a series of activities that lead to the creation of a specified service or product" the output.
  Our output or goal is a Process Improvement and this guide will give you a general guideline in “Getting Started or How to Select Your Project”.
  Determining how to measure
  Initially we need measurements to justify the creation of an Improvement Team. Our goal is to demonstrate how the measures are taken from a background statement.
  This defines a problem, or a project mission statement, which defines the output to be improved ( cost, timeliness, effectiveness or customer satisfaction, etc. ).
Notes: Notes

## Slide 41: Getting Started: How to Select Your First Projects
First we answer “WHY DO WE NEED A PROCESS TO PICK A PROJECT?”
It has been recognized that business, government, and service, organizations, that follow established procedures for improvement tend to dominate the list of world class organizations!
These organizations are benchmarks for quality, success, effectiveness and satisfied employees/customers!
Notes: Notes

## Slide 42: Getting Started: How to Select Your First Projects
Best projects are selected by trained or experienced teams that use an established system and understand:
The importance and need to measure and use data to make decisions.
The relationship of consistency to reliability.
The influence of consensus to aid us in idea acceptance and implementation.
Consensus
Reliability
Data
Notes: Notes

## Slide 43
Getting Started: How to Select Your Project
1
Agree on criteria for project selection
2
Generate list of project ideas (Brain-storming, call for suggestions, etc.)
3
Clarify
4
List reduction (Apply a reality check)
5
Prioritize (Relate to organization's mission and priorities)
6
Select only the number of projects that you can support well.
NOTE: Define the team members role after selecting the project.
“Project Selection Criteria "Pitfalls"
There is often the urge to take on too much. Remember that every good project requires focus - focus requires a
fairly narrow definition of what the team is meant to accomplish. Therefore, don't:
¨ Tackle morale, communication or something equally as massive.
¨ Pick pet peeves.
¨ Pick preconceived solutions for the team to implement.
¨ Pick a process so small or trivial that it doesn't matter to anyone if
it's improved or not.
¨ Try to solve other people's problems. (It's surprising that they
don't fully appreciate your good intentions.)
¨ Tamper with your boss' policy decisions
¨ Select anything without considering the agency's vision and mission.
¨ Select something where you are the primary customer.
¨ Settle on anything without talking to an experienced team member
¨ Tamper with a collection bargaining issue. (Salaries, grievances, benefits)
Notes: Notes

## Slide 44
1
Agree on criteria for project selection
  The project should improve or add value through deliberate organizational changes, such as:
  Added processes
  Increases in efficiency
  lowering cost,
  Humanizing customer/ employee/student communication/services,
  Elimination of waste, or improving consistency, which is also improved reliability.
Notes: Notes

## Slide 45: Criteria
  The project goal is to gain immediate organizational acceptance by creating teams of stakeholders that use scientific methods to gather constructive ideas, develop both informed consensus and a improvement hypothesis.
  The key to immediate acceptance is asking those involved to define the problem, find and implement the solution…a major rational for teams!
Notes: Notes

## Slide 46: Criteria
  Our goal is to pick process or performance issues that warrant changing while avoiding those that are outside of a teams ability to change, such as a law, a union contract, organizational policy, etc. or those that are trivial and unworthy i.e. a pet peeve or where change accomplishes little or nothing.
Notes: Notes

## Slide 47
2
Generate list of project ideas (Brain-storming, call for suggestions, etc.)
Brainstorming is not a individual or managers tool!
It is intended to deal with a problem or topic, develop a documented list of stakeholders ideas of how to deal with it…
It is the combination of individual actions that comprise the output in an organization and this is the first step in getting control of it!
Notes: Notes

## Slide 48: Hidden Value of Brainstorming
Brainstorming is not just the collection of ideas, it has the value of putting the collective thinking of the team on the table, and making differences in thought visible!
We can then organize the collective view (using tools such as Affinity Diagraming or Cause & Effect Charts) and prioritize what the group believes to be most relevant ( Using Pareto Analysis or Team Tools like Weight Voting…
Notes: Notes

## Slide 49: 3 Clarify
Sometimes, we all say, or write text that makes perfect sense to us, but leaves out information that readers unfamiliar with the subject might find difficult to understand. Or worse yet interpret differently…
We must use words that everyone interprets the same, or explain the use of words with an the aid of Operational Definitions…
Notes: Notes

## Slide 50: Clarify
Make sure to make it clear what's happening and to what. Example, this clarification from an version of
North American Blizzard of 2006
    “As the system completed bombing, or rapidly deepening, mesoscale banding features impacted the entire I-95 Corridor.”
  This may be unclear as to what is rapidly deepening-or is it? To attempt to explain…
Notes: Notes

## Slide 51
National Weather Center SPC Mesoscale Analysis Page
4 - National | 1 - MCO | 2 - BFL | 3 - ABY | 5 - 11R | 6 - PHD | 7 - LCI
Mesoscale Meteorology is the study of weather systems smaller than synoptic scale systems but larger than microscale and storm-scale cumulus systems. Horizontal dimensions generally range from around 5 kilometers to several hundred kilometers. Examples of mesoscale weather systems are sea breezes, squall lines, and mesoscale convective complexes. Vertical velocity often equals or exceeds horizontal velocities in mesoscale meteorological systems due to non-hydrostatic processes such as buoyant acceleration of a rising thermal or acceleration through a narrow mountain pass.
These are explanations from the National Weather Bureau and Wikipedia a less than reliable resource!
They may provide insight on the subject, but as for me I need to look up several more words to understand it fully!
Notes: Notes explanations from the national weather bureau and Wikipedia a less than reliable resource!

## Slide 52: Clarify
As our project criteria is to improve a performance issue.
A Performance Issue can be both Flow Charted and Measured
Developing and agreeing on a current Flow Chart and the explanation of current measurements or lack of measurements will most assuredly clarify and answer where are we …
Notes: Note

## Slide 53: 4 List reduction (Apply a reality check)
Use the three-part "reality check" that covers:
Technical Issues
Strategic Issues
Empowerment Issues
Notes: Notes

## Slide 54
Technical Issues
  Does the project deal with a process?
  Does the process occur frequently enough so it can be reliably measured?
  Has the process recently been changed?
  Is the appropriate data available? Can the data be gathered without excessive effort?
  Is there a good probability of success? (Apply the "do-ability test." The team should avoid trying to take on too much.)
Notes: Notes

## Slide 55
Strategic Issues
  Is the project compatible with the values and vision of the organization?
  Does the project help the organization accomplish its mission?
  Does the project have a customer focus?
Notes: Notes

## Slide 56: Empowerment Issues
  Is the process something the department has control of, or do other departments/administrators own a piece of the project?
  Is the process a contract issue? (Salaries, grievances, benefits, etc.)
  Are any preconceived solutions being forced upon the team?
  Is the lack of a sponsor an issue!
Notes: Notes

## Slide 57: Empowerment Issues
Are we prepared to devote the time necessary to make a difference?
Is the administration willing to implement the improvement on a pilot basis, as long as the solution is within the guidelines and boundaries given to the team?
Assuming a successful pilot implementation, is the administration prepared to implement the change on a full-scale basis?
Commitments must be made & defined early on …
Notes: Notes

## Slide 58: 5 Prioritize (Relate to organization's mission and priorities)
Organizational Alignment is the route to developing consensus and consent.
It is a good business practice to align the proposals, projects, even budgets with the overall organization or the department mission, which should already be aligned.
We win and they win…
Notes: Notes Actually its is very hard to fix a problem or improve a process without accomplishing alignment. What's important here is the process of identifying and stating the alignment.

## Slide 59: 6 Select only the number of projects that you can support well.
Projects must have both a defined start and end date as team members have only so much time available!
Also the talent and skill levels of team members should be considered when deciding what can be supported…
Notes: Notes

## Slide 60: What can we Support
Time should be negotiated, discussed, and understood as a deadline must be established for completion of a project for multiple reasons.
  There are Organization Accreditation issues.
  There are Department Work issues.
  There are Personal Time issues.
Notes: Notes

## Slide 61: What can we Support
Talent and Skill levels of the team may or may not be appropriate at the time a project is chosen.
  If needed additional talent may be necessary and may need to be negotiated…
  Training for the team may be necessary and may need to be negotiated…
As a rule no organization can improve above the level the people have improved! People are a factor to be considered in any CI project…Ask why so many organizations cannot find the right applicants?
Notes: Notes

## Slide 62: Define the team members role after selecting the project.
Here we are establishing individual expectations and accountability. The team member must agree they have the time, skill, and desire to participate.
A Team that learns to develop informed consensus will also implement the developed improvement theory…
Notes: Notes

## Slide 63: Hidden value in Defining Talent & Skill Levels
This is a (Win-Win) Scenario as in today's economic reality the opportunity to keep an organizations expensive established workforce competitive is defined.
And the individual is offered the opportunity to stay current with employment needs that keep them truly employable in today's market…It is also collaboration at it’s best!
Notes: This usually adds to the individuals security overall and makes the establishment appreciate the worker more and treat them better!

## Slide 64: Project Selection Criteria "Pitfalls"
There is often the urge to take on too much.
Remember that every good project requires focus - focus requires a fairly narrow definition of what the team is meant to accomplish.
Therefore, don't:
Notes: Notes

## Slide 65: don’t:
Tackle morale, communication, or something equally as massive.
  Pick pet peeves.
  Pick preconceived solutions for the team to implement.
  Pick a process so small or trivial that it doesn't matter to anyone if it's improved or not.
  Try to solve other people's problems. (It's surprising that they don't fully appreciate your good intentions.)
Notes: Notes

## Slide 66: don’t:
  Tamper with your boss' policy decisions.
  Select anything without considering the company or organizations vision and mission.
  Select something where you are the primary customer, “think organization”.
  Settle on anything without talking to an experienced team member
  Tamper with a collection bargaining issue. (Salaries, grievances, benefits) other methods exist to deal with these issues.
Notes: Notes

## Slide 67: Tool Kit Application
Suggested Tools for Generating ideas and collecting information
Affinity Diagram Brainstorming
Check Sheet
Force Field Analysis
Interviews
Surveys
Take the opportunity to view The CSCC Tool Kit on the course menu and review these items. These are CI Action Team tools…
Notes: Notes

## Slide 68: Sources of Analysis
The goal is to pick an appropriate CI project, therefore from the highest to lowest point on the organization chart we would chose from:
  Organizational list of improvement tactics
  Known system or safety breakdowns
  System/Department quality issues
  Customer and organizational complaints that deal with performance issues
  Improvement suggestions from any source
Notes: Notes

## Slide 69: A Project Statement Justifies Forming the Action Team
An action team project statement consist of two steps:
  Describe the process that will be improved
  Give two or three measures by which the process will be measured
These two steps have key words, such as Improve, Process, and Measurement. And as the following examples imply that we wish to improve Performance
If we have a project statement we can review it to assure the team is on the same page…If we do not we need to create one.
Notes: Notes

## Slide 70: Project Statement Examples
Example 1
To streamline the process of gathering information from part-time new hires through payroll as measured by:
  Reduction of inconsistent processes
  Improved accuracy of data
  Reduction of duplicate efforts
Example 2
To improve the degree of certification process as measured by:
  Timeliness
  Accuracy
  Efficiency
  Decentralization
  Occasions for feedback
  Tracking measures
Notes: Notes

## Slide 71: Project Statement Examples
Example 4
To improve leadership development by clear communication of the process for enhancing, broadening, and advancing within the college as measured by:
  Clearly identified skills
  Experiences
  Knowledge and practice of values
Example 3
To improve and clarify the purchasing process as measured by:
  Converting requisitions to purchase orders in a timely manner (2 days)
  Notify Business Office within two days of receipt of items
  Amended purchasing procedures
Notes: Notes

## Slide 72: Project Statement Examples
Example 5
To improve the staff evaluation process for fulltime staff employees as measured by:
  The number of successfully completed (and received) evaluations
  The number of participants satisfied with the process
  The number of participants satisfied with the process
  The top two or three “types” of professional development programs recommended to continually meet the College’s Vision, Mission, Values, and Goals
The Project Statement Gives us insight to the measurements that need improving…
“The number of successfully completed (and received) evaluation”.
We just need to establish the "AS IS" statement - a statement that describes the current situation - specific and measurable.
Then compare it to the "DESIRED" statement - a statement that describes the future situation; it is in essence a goal to be reached. It is based on input from customers and is a reflection of their needs and expectations.
Notes: Notes: A team bring combined knowledge and experience, the appropriate support and synergy to the table. The team can develop a proposal , which includes consensus, that will assure a greater chance of implementation.

## Slide 73: When & Where Does Measurement Start?
For the Action Team, measurement begins at the very inception of the project. Data that identifies an opportunity for improvement or tells us that a process is not working well or is not meeting customer needs – is the first measuring point.
The seeds of measurement is in the “team charter” with observations that something is not working well. Also the project mission statement that identifies measures the team should consider…
Notes: Notes

## Slide 74: Figure 14-4 Project Plan Guidelines
Notes: Notes Slide Courtesy of Quality Management: Creating and Sustaining Organizational Effectiveness, 2e Donna C. S. Summers
Copyright ©2009 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved ~ In part…

## Slide 75: Figure 14-5 Checkpoints and Milestones
A plans work best when broken into task that are both sequenced in a logical order and measured at predetermined checkpoints.
This process can also be flowcharted
Notes: Notes Slide Courtesy of Quality Management: Creating and Sustaining Organizational Effectiveness, 2e Donna C. S. Summers
Copyright ©2009 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved ~ In part…

## Slide 76: Figure 14-6 (continued) Gantt Chart
The Gantt chart best shows the task and dates to be accomplished…by assigning names to the task it becomes a project management tool!
Notes: Notes Slide Courtesy of Quality Management: Creating and Sustaining Organizational Effectiveness, 2e Donna C. S. Summers
Copyright ©2009 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved ~ In part…

## Slide 77: Shared Philosophy
1) From the organizational point of view:
“Change is inevitable, but growth is optional ”
2) From the CI view point:
“If change is the issue we want to control it!”
Notes: Notes

## Slide 78: Shared Philosophy
Projects conducted by teams with a shared philosophy result in better improvement hypotheses and assured implementation!
Three that have worked for me are:
3) From the personal point of view:
“Like the caterpillar to be beautiful we must change”
Notes: Notes

## Slide 79
End of Lecture 14
Notes: Notes