## Slide 1: Lecture 4 ~ ENGT 1200 Introduction to Industrial & System Engineering
Lean, Kaizen, and the 8 Forms of
Muda Waste
Notes: Notes

## Slide 2: Lean Manufacturing
The book “The Machine that Changed the World” introduced us to the term “Lean Manufacturing.”
A term used to explain the system used in Japan that had made them a challenger to the American Mass production System.

## Slide 3: Some History
Before World War II Kiichiro Toyoda had studied and admired the Ford Motor Company mass production system. This system in fact was a major factor in the defeat of Japan in WWII.
Toyoda wanted to rebuild his broken business after the war, but the country was in ruins, broke and without resources.

## Slide 4: Lean Manufacturing
The book “The Machine that Changed the World” introduced us to the term “Lean Manufacturing.”
A term used to explain the system used in Japan that had made them a challenger to the American Mass production System.

## Slide 5: Some History
What he did was copy the Ford Production System used in WWII following guidelines devise by the “War Production Board” and from necessity reduced the waste in the system.
Reduction of waste was essential to Mr. Toyoda as his country could not afford to waste anything and had little resources.
This system became the “Just in Time” or Toyoda Manufacturing System.
Notes: Notes

## Slide 6: Just-in-Time (JIT)
Just-in-Time is a name given the Toyota Production System developed by Taiichi Ohno at Toyota after WWII (resumed work started by Kiichiro Toyoda before the war) and sometimes referred to as:
  Lean Manufacturing
  Focused Factory
  Demand Flow, Demand Flow Technology
  Pull System Manufacturing
Notes: Everything studied in total quality management or Lean Manufacturing is used in just-in-Time or lean manufacturing

## Slide 7: Just-in-Time (JIT)
Just-in-Time permits the production of only what is needed, when it is needed, and in the quantity that is needed.
  In this mode there is no warehouse, no waste, no resources needed for wasted activities.
  JIT is more related to manufacturing activities than warehousing or supplier activities.
  it is much more than having your suppliers deliver material right before/as you are ready for it
Notes: Common misconceptions of JIT manufacturing are the belief that it is a system that only allows suppliers to deliver good when the customer is ready to use them and that warehousing is pushed back to the supplier and becomes a suppliers activity.

## Slide 8: Why do it
To save dollars
Only produce what is needed, do not depend on marketing forecasts, which are difficult to do accurately
Save money within the plant by reducing on hand inventory, WIP, time spent shifting material, storage costs, etc.
Notes: Notes

## Slide 9: Why do it?
When comparing lean Manufacturing to Mass Production. The book “ The Machine That Changed The World” by James Womack, Daniel Jones and Daniel Roos, claimed that Lean Production vs. Mass production requires:
  ½ the human effort
  ½ the manufacturing space
  ½ the investment tools
  ½ the engineering hours
  ½ the development time for new products
All of theses are significant Cost, Time Issues & ISE Topics…
Notes: Notes

## Slide 10: What is it?
The Text “ The Machine That Changed The World” outlined the following principle of “Lean Production which included:
  Teamwork
  Communication
  Efficient use of resources and elimination of waste
  Continuous Improvement
Notes: Notes

## Slide 11: Mass Production Push System
Mass production is a push system that relies on marketing forecast. Materials are ordered and products are produced based upon best guess of a multitude of forecasters.
  Money is spent…
  Products are produced…
  Products are handled, warehoused, shipped and warehoused…
  Orders may be under or over stock on hand…
Notes: See page 238, figure 14-5

## Slide 12: Mass Production Push System
Production
Control
Production
Schedule
Market
Forecast
Material
Control
Orders
Suppliers
Warehousing
Warehousing
For Excess
Product
Distribution
System
Customer
Factory
Processes
P
U
S
H
Finished Product
Finished Product
Control of Process Output, Handling, WIP, Expediting Factory Processes, Materials, etc. Pushing Work Through Factory.
Materials/Parts
Notes: Notes

## Slide 13: What’s Wrong with Mass Production?
Inflexible: Machines are often run constantly just because they are expensive; changeover to different product lines is very time consuming
Wasteful: Always pumping out product under the assumption that a high volume is needed
To ‘save for a rainy day’ parts are overproduced and stored
Notes: Notes

## Slide 14: JIT Demand Pull System
JIT is a pull system where a production schedule does not originate in a forecast.
  The customer originates the production demand…
  The finish production line pulls the product through the factory…
  The factory pulls needed supplies from their suppliers, etc...
Notes: See page 239, figure 14-6

## Slide 15: Just-in-Time Demand Pull System
Suppliers
Distribution
System
Customer
Factory
Processes
Materials
KANBAN
Pull
KANBAN
Pull
Demand Pull (Order)
Demand Pull (Order)
Finished Product
Finished Product
P
U
L
L
Note: Customers
order is the
trigger, result is
felt all the way
to the material’s
suppliers
KANBAN
Orders
Notes: Notes

## Slide 16: Push versus Pull
Marketing tells the factory what to produce
Raw materials and parts are bought and pushed onto the floor and through the process
Finished goods are pushed to the stores, dealers, distributors
When an order is made, it goes to the final assembly process, where the finished goods are pulled out
Each preceding step in the process then pulls more WIP through
This pull goes all the way back to the suppliers
Notes: Notes

## Slide 17: JIT Eliminates the 7 Wastes…
Overproduction: storage and inventory of finished products
Waiting: downtime due to setup changes, equipment breakdown, material or part shortages
Transporting: moving materials or people
Processing: minimize the number of process steps, such as by reducing the number and kinds of fasteners
Notes: Notes

## Slide 18: JIT Eliminates the 7 Wastes
Unnecessary stock: raw materials or WIP in storage
Unnecessary motion: eliminate processes are actions which do not add value (like getting WIP from a storage area)
Producing defective goods: if defective goods are being produced, stop the process
Notes: Notes

## Slide 19: Internal (JIT) MUDA Relationships
Internal Supplier-Customer Relationships:
      Overproducing
      Waiting
      Transporting
      Processing itself
      Having unnecessary stock on hand
      Using unnecessary motion
      Producing defective goods
      Human Resource Potential
MUDA is a the Japanese word for waste. Originally the 7 waste, but the 8th has been added to address the waste of human capital

## Slide 20: 8 Classic Forms of Waste
Transportation (unnecessary conveyance)
Inventory
Motion
People Underutilization
Waiting (delays)
Over processing (doing extra steps)
Overproduction (doing work not requested)
Defects (includes rework/repair rime to correct mistakes)
Process improvement requires elimination of waste.
Remember TIM P WOOD
From the Lean-Six Sigma
Green Belt Certification
From the Lean-Six Sigma Green Belt Certification

## Slide 21: Benefits of JIT
Reduce inventory and WIP, which cost $
  costs of materials and goods
  labor costs for storage, handling, and protections of the materials and goods,
  cost of warehouses, real estate, capital equipment used in inventorying
  cost of spoilage due to damage, deterioration, corrosion, obsolescence, etc.
  taxes
Notes: Notes

## Slide 22: Benefits of JIT
Forces you to get a grip on your process - becomes a natural driver for continuous improvement
Reduces finished goods inventory - leaves you in a better position to react to changes in the marketplace
Reduces cycle time
Elimination of waste (the 8 wastes)
Notes: Notes

## Slide 23: Lean Tools and Techniques
Lean thinking generates process improvement by following five key steps:
  1. Study the process by directly observing the work activities, their connections and flow.
  2. Study the process to systematically eliminate wasteful activities, their connections and flow.
  3. Establish agreement among those affected by the process in terms of what the process needs to accomplish and how the process will accomplish it.
  4. Attack and solve problems using a systematic method, like the PDCA Cycle.
  5. Integrate the above approach throughout the organization

## Slide 24: Lean Tools and Techniques
Lean tools include:
  Kaizen
  Value stream process mapping
  5 S
  Kanban
  Error proofing
  Preventive and predictive maintenance
  Setup time reduction
  Reduced lot sizes
  Line-balancing
  Schedule leveling
  Standardized work
  Visual Management

## Slide 25: Kaizen
Kaizen is the name given by Japanese to the concept of continual incremental improvement.
  Kai means change
  Zen means good
Kaizen uses all the quality tools, philosophies and techniques we have discussed to date and more…
Trained Teams such as yourselves are empowered to evaluate and change the undesirable to a improved state…
Notes: Notes

## Slide 26: Kaizen Philosophy
If the kaizen philosophy is in place, all aspects of an organization should be improving all the time.
  People
  Processes
  Management Practices
  Products
Notes: Notes

## Slide 27: Kaizen Value System
The underlying value system of kaizen can be summarized as continual improvement of all things, at all levels, all the time, forever.
Notes: Notes

## Slide 28: Elements of Kaizen
Notes: Notes

## Slide 29: Kaizen Checklist
To promote Continual Improvement, consider the following factors everyday and ask the following Question: How can this be improved?
Personnel at all levels
Work Techniques
Work Methods
Time
Facilities
Equipment
Systems
Software
Tools
Materials
Plant Layout
Production Levels
Inventory
Paradigms (mind-sets)
Notes: Notes

## Slide 31: Kaizen and Problem Solving
The starting point for improvement is to recognize the need, which comes from recognition of a problem!
If no problem is recognized there is no recognition of the need for improvement!
Complacency is the arch-enemy of Kaizen
Notes: Notes

## Slide 32: The Kaizen Five-Step Plan
The Five-Step Plan is the Japanese approach to implementing Kaizen.
    Step 1: Straighten up
    Step 2: Put things in Order
Step 3: Clean up
    Step 4: Personal Cleanliness
    Step 5: Discipline
Notes: Notes

## Slide 33: Lean Tools and Techniques
The American version of the Five Step is the 5S Programs: we will discuss in Lecture 5. The Japanese words for the 5S are:
  Seiri Separate
  Seiton Arrangement
  Seiso Cleanliness
  Seiketsu Repeat seiri, seiton, and seiso at regular intervals
  Shitsuki Discipline

## Slide 34: Kaizen Example
Introduction to
Wabtec Quality and
Performance Systems
The following was presented at the RPI - Rail Progress Institute Quality Conference September 2000 and is offered as an example of Kaizen Program use…
Notes: Notes

## Slide 35: How do we utilize QPS to continuously provide the maximum enterprise value possible in all of our operating units?
Quality & Performance Systems
Notes: Notes

## Slide 36
QPS Toolbox
  Strategic Planning
  Priority Deployment
  Risk Reduction Management
  Statistical Engineering
  Benchmarking
  Value Stream Mapping
  Kaizen
  Materials Management
  Visual Controls
Quality & Performance Systems
Notes: Notes

## Slide 37: Quality & Performance Systems
Wabtec Performance System
WORLD CLASS MODEL
FEA FMEA DFMA Robust Design Tollgates
Employee Involvement
PDCA SMED TPM Kanban Statistical Engineering 6 Sigma Poka Yoke
Value Stream Standard Work 5S 5 WHY Visual Mgmt JIT Cellular Flow
CUSTOMER SATISFACTION
Enterprise Value
Priority
Deployment
Kaizen
Daily
Mgmt
Q
U
A
L
I
T
Y
D
E
L
I
V
E
R
Y
C
O
S
T
P
E
R
F
O
R
M
A
N
C
E
VOICE OF CUSTOMER
S
A
F
E
T
Y
Notes: Notes

## Slide 38: Continuous Improvement
Kaizen
Notes: Notes

## Slide 39: A System Totally Based On The Elimination of Waste
Kaizen
Notes: Notes

## Slide 40: Kaizen Wastes
Wastes of Manufacturing
Wastes are the elements of a process that do not add value for the customer, but increase costs. There are eight types of waste:
Waste of Inventory
Waste of Motion
Waste of Transportation
Waste of Over Production
Waste of Defects
Waste of Unused Processes
Waste of Unused Creativity
Waste of Waiting
Notes: Notes

## Slide 41: What is a Kaizen?
A Kaizen event is used to “make a leap” when other tools have hit an obstacle. A multi-functional team is formed and for a 3-5 day period, they focus on resolving a problem.
It is characterized by the following:
• A short burst of intense activity and effort (3 to 5 days only)
• Biased toward action over analysis
• Focused on improving the value stream and achieving flow
• Driven to resolving a specific problem or achieving a specific goal
• Focused on a specific area or process (either plant or office)
• Managed with daily reviews of progress
• Aimed at achieving specific improvements in a short time
• Managed to resolution
Notes: Notes

## Slide 42: Kaizen
Waste
Those elements of production that do not increase the value of a product,
but only increase cost.
• Focus on the things that can be done within the
event
• Think within the boundaries of the
QPS business process
• Single piece flow
• Minimum inventory
• Production paced to TAKT time
• Pull production vs. push production
• Low cost solutions, creativity before money
• Right sized resources
• Maximum waste elimination
Attack Items That Impact
• Process flow
• Material flow
• Information flow
Plan
Countermeasures
Identify
Waste
Notes: Notes

## Slide 43: Kaizen What is an Improvement Activity
A kaizen is driven to two imperatives: - Solving Problems
- Eliminating Waste (Muda)
During a kaizen, the team will:
Identify problems and areas of waste
Ask Why?, Why?, Why?, Why?, Why?
Figure out ways to fix the problem or eliminate the waste
Implement solutions
1. Take Apart
2. Think About
3. Make New
Kaizen
Notes: Notes

## Slide 44: Lean Tools and Techniques
Kaizen
  Guiding words
    Combine
    Simplify
    Eliminate
  Kaizen seeks to standardize work processes while eliminating waste.
  A major Kaizen Tool is the Why Technique to get to the Root Cause of a problem…

## Slide 45: Why Technique or Root Cause Analysis
"WHY" TECHNIQUE
Some of the tools for continuous improvement require number-crunching, graphing and analysis -- but not all of them. Perhaps one of the most powerful tools is also one of the most basic. It has less to do with number crunching and more to do with simple curiosity. We refer to that old standby question: "Why?“
By asking "why," you can peel back the layers to discover the root cause of a problem. This may require you to ask "why" more than once -- sometimes as many as five to six times. Keep probing to find why the symptom (or "effect") is occurring. You'll eventually come to the root cause.
The process is also called “Root Cause Analysis”
Notes: Notes

## Slide 46: Why Technique or Root Cause Analysis Example
1ST LAYER | WHY aren't supply orders filled in time? Because the supplies are not in stock. |  |  |  | 
 | 2nd LAYER | WHY aren't the supplies in stock? Because the supply shipment has not been received. |  |  | 
 |  | 3rd LAYER | WHY hasn't the supply shipment been received? Because the order was placed late. |  | 
 |  |  | 4TH LAYER | WHY was the order placed late? Because the order / request for supplies takes 3 weeks to get approved. | 
 |  |  |  | 5th LAYER THE ROOT CAUSE | WHY does the order / request for supplies take 3 weeks to get approved? Because it is in transit for 12 days, going from one approval authority to another (total approvals needed = 5).
PROBLEM: SUPPLY ORDERS AREN'T FILLED ON TIME
Notes: Notes

## Slide 47: Why Technique Example
Deal with that within our power & communicate without fear that which must be dealt with at a higher level!
Notes: Notes

## Slide 48: Why Technique Example
"WHY" TECHNIQUE + TREE DIAGRAM
Sometimes you may want to use the Why Technique in conjunction with a tree diagram. This will provide a little more structure to the Why Technique and help you identify various root causes.
Putting it to work:
Once you have identified a problem ask the question "Why did this problem occur?" (This is your first layer).
Then take the answer to that question and ask the question again. Continue to do this until you have uncovered the possible root causes of the problem. It may be necessary to ask "why" several times before you uncover all the root causes (see example on next page)
Notes: Notes

## Slide 49: Why Technique Example
WHY? | WHY? | WHY? | WHY?
 | Orders not received on time |  | 
Supply orders are not filled on time | Not enough staff | Person not on disability Two vacancies | 
 | Supplies Not in | Shipment not received | Supply shipments are late Didn't get order in on time Supply order was lost
 | Orders no complete | Order form is complicated Lack of training to fill out the form properly | 
WHY AREN'T SUPPLY ORDERS FILLED ON TIME
This shows the use of the Why Technique with the Tree Diagram.
Notes: Notes

## Slide 50: Why Technique Example
A “why technique” that combines some affinity diagramming structure and classification…
Notes: Notes

## Slide 51: Lean Tools and Techniques
Kanban (Pull Inventory Management)
  Kanban improves process management by focusing on visual control of the process.
  Kanban cards tell the worker what must be produced as well as what has been produced.
  Workers can not do more than the Kanban cards tell them to.

## Slide 52: Lean Tools and Techniques
Error Proofing (Poka-yoke): to be discussed in Lecture 5
  Error proofing has five principles:
    Elimination
    Replacement
    Facilitation
    Detection
    Mitigation
  Error proofing seeks to improve a worker’s ability to do their job by improving how they do their work.

## Slide 53: Lean Tools and Techniques
Preventive and Predictive Maintenance
  Preventive maintenance maintains the equipment in good condition so that unexpected downtime does not occur.
  Predictive maintenance schedules routine maintenance so that everyone knows and can plan for a machine or a piece of equipment being unavailable.

## Slide 54: Lean Tools and Techniques
Setup time Reduction
  Setup time is the time between the production of the last good part in one series of parts and the production of the first good part in the next series of parts.
  Setup time reduction efforts find ways to eliminate waste in setups thus speeding up the process of setup.

## Slide 55: Lean Tools and Techniques
Reduce Batch Sizes (Single Piece Flow)
  Reduced batch sizes allow each piece as it is created to flow from one operation to the next with no delays, storages, or work-in-process inventories.
  Reduced batch sizes increase inventory turn-overs and help show where process improvements can be made.
  Reduced batch sizes allow quality issues to be found quickly.

## Slide 56: Lean Tools and Techniques
Line Balancing
  Line balancing occurs when work is performed by each operator evenly over time with no peaks or valleys.
  Each worker or machine on the assembly line has work that fills the same amount of time, so no one or no machine is waiting for something to do or is having to rush to keep up.

## Slide 57: Lean Tools and Techniques
Takt time refers to how often a single part should be produced in order to meet customer demand.
  Available working time per day
  Takt time = -----------------------------------
  Customer demand rate per day

## Slide 58: Takt Time
Takt time can be defined as the maximum time allowed to produce a product in order to meet demand. It is derived from the German word taktzeit which translates to clock cycle. There is a logic therefore to setting the pace of production flow to this takt time.
Product flow is expected to fall within a pace that is less than or equal to the takt time. In a lean manufacturing environment, the pace time is set equal to the takt time.
Notes: Notes

## Slide 59: Takt Time is defined as:
Where:
Ta = Net Available Time to Work eg. [minutes of work / day]
Td = Total demand (Customer Demand) eg. [units produced / day]
T = TAKT Time eg. [minutes of work / unit produced]
Net available time is the amount of time available for work to be done. This excludes break times and any expected stoppage time (for example scheduled maintenance, Team Briefings etc.)
Notes: As an example, if you have a total of 8 hours in a shift (gross time) less 30 minutes lunch, 30 minutes for breaks (2 x 15 minutes), 10 minutes for a Team Brief and 10 minutes for basic Operator Maintenance checks, then; Net Available Time to Work = (8 hours x 60 minutes) - 30 - 30 - 10 - 10 = 400 minutes. If Customer Demand was, say, 400 units a day and you were running one shift, then your line would be required to spend a maximum of one minute to make a part in order to be able to keep up with Customer Demand.
In reality, people can never maintain 100% efficiency and there may also be stoppages for other reasons, so allowances will need to be made for these instances and thus you will set up your line to run at a proportionally faster rate to account for this.

## Slide 60: Lean Tools and Techniques
Schedule Leveling
  Establishing a schedule which allows the same amount to be produced daily with minimal fluctuations in demand.
  Level scheduling enables an organization to link the customer schedule with the pace of manufacturing.
    Requires the cooperation of the customer

## Slide 61
End of Lecture 4