## Slide 1
Lecture 6 ~ ENGT 1200 Introduction to Industrial & System Engineering
Standardization Tools: The Visual Factory, 5s, Poka-Yoke, Kanban, & Setup Time Reduction
Notes: Notes

## Slide 2
“I would argue that Lean Tools & Techniques require the knowledge of Descriptive Geometry & Descriptive Statistics to be both Efficient & Effective in the workplace.
You may master the engineering skills needed and be a top notch mathematician, but if you cannot communicate with Visual Descriptive Tools & apply Visual Application Tools, no one may ever know it!”
Notes: Notes

## Slide 3: The Light Year: A Measure of Distance
The distance that light travels in a year is so large that it is a useful unit of distance in astronomy:
Light Year: the distance that light travels (through a vacuum) in one year (9.46 x 10^17 cm). Since the inch is defined as 2.54 centimeters, the speed of light also has an exact value in non-metric units
The speed of light in mph (miles per hour) is 670,616,629 mph.
That’s 670,616,629 *24 = 16,094,799,096 miles per day
That’s 16,0947,99,096 x 365 = 5,874,601,670,040 miles per year = 1 light year
The nearest star (other than the Sun) is 4.3 light years away.
Our galaxy (the Milky Way) is about 100,000 light years in diameter.
The distance to the galaxy M87 in the Virgo cluster is 50 million light years.
The distance to most distant object seen in the universe is about 18 billion light years (18 x 10^9 light years).
Notes: Notes

## Slide 4: Infinity???
One American-French vigintrillion = 1,000,000,000,000,000,000,000,000, 000,000,000,000,000,000,000,000,000,000,000,000,000.0
One English-German vigintrillion =
1,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000,000.0
Notes: Notes

## Slide 5: The Foot
Determination of the mean length of a foot in a German town during the 15th century, after a woodcut which was published in the book Geometrei by Jakob Koelbel (Frankfurt, ca. 1575).
Evolution of Standards & Early Measurements
Notes: Notes

## Slide 6: The Foot & An Early Operational Definition
The verification of the foot as described in the 16th century by Jacob Koebel in his book Geometrei. Von künstlichem Feldmessen und absehen is:
Stand at the door of a church on a Sunday and bid 16 men to stop, tall ones and small ones, as they happen to pass out when the service is finished; then make them put their left feet one behind the other, and the length thus obtained shall be a right and lawful rood to measure and survey the land with, and the 16th part of it shall be the right and lawful foot.
Evolution of Standards & Early Measurements
Notes: Notes

## Slide 7: Standards
Example taken from a
weather page. Words we use and hear daily, but do we really quantify what they mean?
The Beaufort Wind Scale
Notes: The words do not necessarily correspond to the same wind speed or description when used in conversation by either party. Even the words used in the description may be hard to quantify?

## Slide 8
Evolution of Standards

## Slide 9: Standards
The QWERTY Keyboard 1872
Notes: The QWERTY keyboard used in typewriter and PC’s is a standard, but so is the Dvorak
The QWERTY keyboard, named for the first six letters in the second row, was developed by Christopher Latham Sholes in 1872. Sholes had developed the first popular American typewriter, but had ran into a problem with keys jamming. A problem that he and his engineers could not solve mechanically.
So Sholes rearranged the keyboard into the most inefficient, awkward, ergonomically incorrect, hardest to learn, inconvenient pattern he could devise, the QWERTY keyboard.
Arranged solely to slow the fastest typist so the machines would not jam.
52%
32%
16%

## Slide 10: The QWERTY keyboard used in the Typewriter and PC’s is a standard
The QWERTY keyboard, named for the first six letters in the second row, was developed by Christopher Latham Sholes in 1872. Sholes had developed the first popular American typewriter, but had ran into a problem with keys jamming. A problem that he and his engineers could not solve mechanically.
Sholes rearranged the keyboard into the most inefficient, awkward, ergonomically incorrect, hardest to learn, inconvenient pattern he could devise, the QWERTY keyboard.
Arranged solely to slow the fastest typist so the machines would not jam.
Evolution of Standards
Notes: Notes

## Slide 11: The Dvorak Keyboard
After the introduction of the electric typewriter, which solved the mechanical typewriter problem of keys jamming, only one successful attempt at rearranging the keyboard has had any impact on the evolution of the typewriter design.
August Dvorak and William L. Dealey devised the optimal keyboard pattern designed to allow 70% of all typing task to be performed without lifting the fingers up or down from the home row.
Evolution of Standards
Notes: notes

## Slide 12: Standards
The Dvorak Keyboard 1936
Notes: After the introduction of the electric typewriter, which solved the mechanical typewriter problem of keys jamming, only one successful attempt at rearranging the keyboard has had any impact on the evolution of the typewriter design.
August Dvorak and William L. Dealey devised the optimal keyboard pattern designed to allow 70% of all typing task to be performed without lifting the fingers up or down from the home row.
The design increased typing accuracy 50% increased speed by 15 to 20% and decreased average training time to one third compared to the QWERTY.
Yet the people were use to the QWERTY and resisted the change. Why? Invest in new equipment? Why retrain all those typist?
Today we use PC based word processing using a PC keyboard based upon the QWERTY. Designed by Sholes over 100 years ago to correct a problem that has not existed for over 70 years.
22%
70%
8%

## Slide 13: The Dvorak Keyboard
The design increased typing accuracy 50% increased speed by 15 to 20% and decreased average training time to one third compared to the QWERTY.
Yet the people that used the QWERTY resisted the change. Why? Invest in new equipment? Why retrain all those typist?
Today we use PC based word processing using a PC keyboard based upon the QWERTY. Designed by Sholes over 100 years ago to correct a problem that has not existed for over 70 years.
Evolution of Standards
Notes: Notes

## Slide 14: Establishment of Standards
Industrialization mandated a better system with world wide acceptance for assembly lines and interchangeable parts to work.
The National Bureau of Standards was established by Congress in 1901 as the central measurement laboratory of the Federal Government.
The institute is the focal point in the United States for assuring the ultimate application of physical and engineering science to the development of technology in industry and commerce.
Notes:     INSTRUCTORS NOTES: National Institute of Standards and Technology (NIST), Is comprised of the National Measurement Laboratory, the National Engineering Laboratory, the Institute for Materials Science and Engineering, and the Institute for Computer Sciences and Technology. The NIST promotes the use of precision technology by conducting research and providing centralized services in four broad program areas: basic measurements and standards, materials measurements and standards, technological measurements and standards, and transfer of technical information.
    The NIST provides facilities necessary for a complete and consistent system of basic physical and chemical measurements and standards in the United States, and it furnishes essential services leading to accurate and uniform measurements throughout the scientific community, industry, and commerce. In 1972, for example, agency scientists developed a helium-neon gas-laser technique that for the first time gave the precise measurement of the speed of light as 299,792.45 km/sec (186,282.396 mi/sec).
    The NIST also cooperates with public and private organizations to develop technological standards and test methodologies by conducting research on the properties of materials that are needed by industry, commerce, educational institutions, and government. This research leads to improved methods of standardizing measurements and collecting data.

## Slide 15: System Flow Charts
Elements of Lean Manufacturing & Reliability
Notes: Notes

## Slide 16: Lean Tools and Techniques
Visual Management is all around us today! When driving my car gauges tell me the tank is full and warn me to fill up with a little light, I stay between white lines that indicate my lane on the freeway and yellow line tell me not to pass.
My GPS alerts me to lane changes miles ahead of time and if going to the airport international signs tell all regardless of language barriers all that’s needed to park and navigate to restrooms, baggage check-ins and boarding procedures.

## Slide 17: Lean Tools and Techniques
Visual Management
  Visual management reduces training & work time.
  Visual management keeps us from getting lost
  Visual management transcends language barriers.
  Visual management reduces ergonomic issues & makes us safer.
  Visual management enables someone looking at a job or a work space to know in at a glance that something has been misplaced or mismanaged.
  Visual management encourages a place for everything, everything to have its place & eliminating unneeded item.

## Slide 18: Make it Visual
To make it visual we must learn to communicate with things we see:
Example:
We clean the workplace and put up a sign that said “Keep it Clean”…it got dirty over time!
We cleaned the workplace, Used a 5s Tool and , took a picture of it clean and put it under the Keep it Clean sign, we then wrote on the sign this is what clean looks like…it stayed clean!
Notes: Notes

## Slide 19: Photo Examples
Visual Examples develops the expectation of clean!
Before

## Slide 20: The American Standard Kaizen or the 5S's
The author Hiroyuki Hirano was born in 1946 and graduated from Senshu University’s School of Economics in 1970 He joined a large software company to work in the consulting division.
There he laid the conceptual groundwork for Japans first full fledged production management system.
His personal interpretations of the JIT or Just-in-Time philosophy revolutionized the Toyoda Manufacturing System
His philosophy which emphasized the elimination of waste resulted in what we call Lean Manufacturing today!
The whole idea of 5-S is to organize and clean up your workspaces in order to improve safety, efficiency, and effectiveness as well as to eliminate waste and frustration in your daily work…
Notes: Notes

## Slide 21: 5S’s Origin
The 5S's originate from 5 Japanese words that have been translated into English.
As with most interpretations variations will exist due to usage…
Japanese Term | English Comparable
Seiri | Sort
Seiton | Set In Order
Seiso | Shine
Seiketsu | Standardize
Shitsuke | Sustain
Notes: Notes

## Slide 22: The 5S's - an English "translation“
Sort: Clearing the work area
Set in Order: Designating locations
Shine: Cleanliness & workplace appearance
Standardize: Everyone doing things the same way
Sustain: Ingraining the 5S's into the culture
Notes: Notes

## Slide 23: 5s Step 1
1st Step ~ Sort Clearing the area means organizing the workplace so that it is a more effective, more efficient place to work.
During this process items not needed are eliminated.
    Define what is needed.
    Define what is NOT needed.
    Disposition the items is determined, keep, move to new location, trash, sell, etc.
    Take action: Sort out (move out) what is not needed and move in what is needed (and is not there now).
Notes: Notes

## Slide 24: 5s Step 2
Step 2 ~ Set in Order or designating locations is about organization and orderliness.
It means that there is a place for everything and everything must be in its place.
  Creating 5s designated locations enables employees to exert visual control over everything needed in the work area.
  At a glance, employees are able to see if things are in-place or out-of-place and if more materials, supplies, or tools need to be ordered.
Notes: Notes

## Slide 25: 5s Step 3
Step 3 ~ The Shine phase is more than making the work area spic and span.
There are three aspects of shine: getting the workplace clean, maintaining its appearance, and using preventive measures to keep it clean.
  Continued housekeeping is one way to keep the work area, tools, and equipment clean, but cost money.
  Root cause analysis, mistake-proofing, and the use of preventive measures are important to keep the workplace clean and orderly & save money.
Notes: Notes

## Slide 26: 5s Step 4
Step 4 ~ Standardize, the fourth of the 5S's, involves putting the systems in place to ensure that everyone does things the same way.
The methodology for Sorting needs to be standardized
The approach to Set in Order needs to be standardized, and Shine especially needs to be standardized.
In order to standardize roles and responsibilities must be clear and consistently applied.
Notes: Notes

## Slide 27: 5s Step 5
Step 5 ~ Sustain is perhaps the most difficult phase of the 5S's.
Sustaining the 5S effort takes a lot of work. It takes commitment and involvement by everyone to keep the effort going and to prevent the organization from just sliding back into the old ways of doing things.
  Sustaining requires keeping everyone involved, continually reinforcing what and why the 5S's are important.
  Audits can serve as on-going checks on 5S activities.
Notes: Notes

## Slide 28: The 5S's lead to Improved Processes and Ultimately:
Reduced set-up times
Reduced cycle times
Increased floor space
Lowers safety incident/accident rate
Has less wasted labor
Improved equipment reliability
Notes: Notes

## Slide 29
Graphic Source http://www.tpfeurope.com/cms/view/44
5s & The Seven Waste
The Seven Waste
Over Production
Unnecessary Stock
Inefficient Transportation
Unnecessary Motion
Waiting Time
Rejects & defects
Inappropriate Processing
The use of the 5s to attack the Seven Waste is the basis of todays Lean Manufacturing and tomorrows Flexible Manufacturing Systems
Notes: Source http://www.tpfeurope.com/cms/view/44 in part.

## Slide 30: The 3P - Production Preparation Process
Used by Toyoda and brought to The Ford Motor Company by W. Edwards Deming The 3P or Production Preparation Process is a powerful and transformative cutting-edge marketing and engineering tools, and it is typically only used by organizations that have experience implementing other lean methods.
Kaizen and other lean methods deal with a production process & seek to make improvements,
The 3P or Production Preparation Process focuses on eliminating waste through product and process design, which results in products that are less complex, easier to manufacture & easier to use and maintain..
A lean tool to design customer satisfaction into the product!
Notes: Notes

## Slide 31: Shigeo Shingo & Poka Yoke
Shigeo Shingo was one of the industrial engineers at Toyoda who has been credited with creating and formalizing (ZQC), Zero Quality Control, an methodology of quality management that relies on the use of Poka-Yoke devices.
Poka-yoke (pronounced POH-kah YOH-kay) is Japanese for mistake-proofing. These devices are used to eliminate mistakes caused by human error such as plugging in an electrical cord backwards with the ground wire hot and the hot wire used as a ground.
Today electrical devices are designed to only assemble in the correct orientation, even batteries will only fit one way!
Notes: Notes

## Slide 32: Poka-Yoke Examples
For some file cabinets, opening one drawer locks all the rest, a poke-Yoke solution for reducing the chance of the file cabinet tipping and causing injury to a user.
This file cabinet has a sign to warn user that they may be harmed by opening too many drawers…wonder where that instruction manual is?
Notes: Notes

## Slide 33: Poka-Yoke Examples
Automobile controls have a mistake-proofing device to insure that the key, which cannot be inserted upside down, is in the on position before allowing the driver to shift out of park, this also requires a foot on the brake.
The keys also cannot be removed until the car is in park.
Lights warn us if we leave a door open and monitor systems such as Temperature, low gas, lights on, bright Lights, seat belts etc.
Notes: Notes

## Slide 34: Poka-Yoke Examples
Fueling area of car has three fuel system mistake-proofing devices:
filling pipe insert keeps larger, leaded-fuel or diesel fuel nozzle from being inserted and prevents damage to the engine and exhaust systems.
gas cap tether does not allow the motorist to drive off without the cap.
gas cap is fitted with ratchet to signal proper tightness and prevent over-tightening.
Sensor to stop grandkids from opening sliding door on van when the gas cap door is open and causing damage.
Notes: Notes

## Slide 35: Poka-Yoke Examples
Electronic door locks can have three mistake-proofing devices:
insures that no door is left unlocked.
doors automatically lock when the car exceeds 18 miles an hour.
lock won't operate when door is open and the engine is running to keep from locking key in the car.
Antilock Braking Systems (ABS) compensate for drivers who stomp on the conventional brake and lose control of the vehicle. What used to be a driving error is now the proper braking procedure.
ABS Brake Pump & Valves
Notes: Notes

## Slide 36: Honda engineers develop "pre-collision" safety technology to support drivers' efforts to prevent collisions before they occur.
Honda introduced the world's first Collision Mitigation Braking System (CMBS) utilizing millimeter wave radar technology to help detect the possibility of a collision.
Visual and audio warnings and an automatic tug of the seat belt alert the driver to take action. If a collision cannot be avoided, and even if no prior alerts have been given, front seat belts are automatically retracted and braking force is automatically applied to reduce the vehicle's speed to help mitigate the effects of the collision.
The system made its American debut on the 2006 Acura RL, and is now featured on other Acura models, as well as the Honda FCX Clarity.
Notes: Notes

## Slide 37: Poka-Yoke Examples
New lawn mowers are required to have a safety bar on the handle that must be pulled back in order to start the engine. If you let go of the safety bar, the mower blade stops in 3 seconds or less. This is an adaptation of the "dead man switch" from railroad locomotives.
Circuit breakers prevent electrical overloads and the risk of a fires. When the load becomes too great, the circuit is broken.
Notes: Notes

## Slide 38: Poke-Yoke Examples
This bathroom sink has a mistake-proofing device. It is the little hole near the top of the sink that helps prevent overflows.
This microwave oven stops operating when the door is opened, which prevents injuries.
Notes: Notes

## Slide 39: Poka-Yoke Examples
Car washes & parking garages have low clearance. To avoid damage to vans & cars, that will not fit, they use a go/no-go gauge at the entrance, a swinging bar.
Hitting the swinging sign or pipe will not damage the vehicle as much as driving into a concrete beam.
This brings up the question “How tall is this thing I'm driving”???
Notes: Notes

## Slide 40: Poka-Yoke Examples
Today sinks, toilets & urinals are fitted with sensors.
These sensors are poka-yoke devices that insure that the water is turned off in the sink and that the urinal is flushed.
Notes: Notes

## Slide 41: Poka-Yoke Examples
The bathyscaph Triete is a deep water submarine used to explore the very lowest parts of the ocean.
It is electrically powered. Once at the bottom, if the batteries or electrical system fail the sub by design returns to the surface…
The designers made this outcome occur by holding the ballast in place with electromagnets. When power is lost, the ballast drops off automatically and the sub starts its ascent.
Notes: Notes

## Slide 42: Automatic Motion Sensor Switch
A Poka-Yoke device that prevents accident by turning on the lights if your hands are full and turns off lights if forgotten!
Motion Sensor controlled lights are also a deterrent to unwanted visitors that do not like lighted areas…
Notes: Notes

## Slide 43: Garage Door Openers
Garage door openers cause injury and property damage everyday
Poka-Yoke devices like the Genie Safe-T-Beam Replacement Kit helps prevent injury and property damage. When objects pass through its infrared beam, the garage door automatically stops closing and reverses.
The system provides safety, security & peace of mind.
Notes: Notes

## Slide 44: Poka-Yoke in Manufacturing & Other Organizations
Simple items such as a switch with a pin that sticks up through a drilled hole that would stop a conveyor belt if the pin was not drilled….
The bracelet put on patients in a hospital their insistence on you giving information to confirm the proper medication is going into the correct patient…
And even the safety caps on pill bottle to protect the young in a household.
Notes: Notes

## Slide 45: What’s New in Poke Yoke Devices
What new poke Yoke devices are you aware of today?

## Slide 46: The Kanban
When Taiichi Ohno, considered the father of the Toyoda Manufacturing System, introduced the concept of control from the output level of a factory he also introduced the “Kanban”, a Japanese word meaning card, to trigger activity.
  When a succeeding process uses the output from a preceding process it issues a kanban or card to the preceding process to produce another…
Today it is more than just the issuing of cards. It is a bin, spot, a conveyor belt with a predetermined capacity, or a loading mechanism…
Notes: Notes

## Slide 47: Kanban Management Tool
Kanban (Pull Inventory Management)
  Kanban improves process management by focusing on visual control of the process.
  Kanban devises, slots, spaces, etc. tell the worker what must be produced as well as what has been produced.
  Workers can not do more than the Kanban device allow them to do.
Notes: Notes

## Slide 48: Kanban Locations
A kanban is a signal to trigger replenishment of inventory.
The kanban signals it is time to pull inventory from storage & to start the next production run.
A kanban space includes full boxes, peg boards with a specific number of openings or slots, and containers for predetermined quantities.
Signs above the kanban areas that note the item and maximum quantities that should be stored in the space control WIP
Notes: Notes

## Slide 49: Follow the 6 Kanban Rules…
Never send defective parts to a downstream process
The downstream process can only take what is needed when it is needed
The upstream process can only make as many parts as will be requested by the downstream process at a given time
Smooth the process: so that there is little waiting around for a new Kanban request, use takt time…
Notes: Notes

## Slide 50: Follow the 6 Kanban Rules
Follow the rules while fine tuning.
  this is the only way you can see where adjustments need to be made
Stabilize and Rationalize the process
  establish uniform methods
  reduce confusing and unreasonable steps
Notes: Notes

## Slide 51: Kanban ~ Visibility/Visual Control
By not storing WIP and by organizing the floor by product processing steps, problems are easier to see
Post information where everyone in the work cell can see it, such as:
  anticipated units for the day
  number of units so far
  SPC data being tracked
  problems experienced, and their frequency
Notes: Notes

## Slide 52: SETUP TIME REDUCTION
Companies, such as Honda in Marysville uses Just-In-Time (JIT) manufacturing which involves the frequent delivery of small lots of material. To supply small lots suppliers must practice Setup Time Reduction a technologies that enable JIT replenishments while raising productivity, lowering inventory, slashing lead time, and improving quality.
Reviewing the slide from our first chapter 12 lecture the waste of storage space, material handling, and cost of large inventories, etc. are eliminated because of the development of Setup Time Reduction Processes
Notes: Notes

## Slide 53: What is Lean: setup reduction?
Lean: setup reduction is the process of reducing changeover time (i.e., from the last good piece of the previous run to the first good piece of the next run).
Since setup activities add no marketable form, fit, or function to the product, they are by definition non-value adding.
By reducing setup time, more setups can be completed each day.
Notes: Notes

## Slide 54: What are the benefits of Lean: setup reduction?
Implementation of Lean: setup reduction will help
reduce batch size, leading to increased frequency of production for each model.
reduce lead time, resulting in improved delivery.
improve documentation of setup processes, leading to improved quality.
decrease inventory and costs, while increasing capacity.
Notes: Notes

## Slide 55: Establishment of Standards
The US standard railroad gauge (distance between the rails) is 4 feet 8.5 inches. Why was this gauge used?
Because that’s the gauge used in England and our railroads were built by English expatriates. Why did the British build use that gauge?
Because the first railroads were built by the same people who built the pre-railroad tramways and that’s the gauge they used. So! why did they use that gauge?
Notes: Notes

## Slide 56: Establishment of Standards
Because the people who built tramways used the same jigs and tools that they used to build wagons, which used that wheel spacing. OK Then! why did wagons use that spacing?
Because that’s the spacing of old rutted roads. OK! So who built these rutted roads?
The first long distance roads were built by Imperial Rome for their legions. The roads have been used ever since. The ruts which everyone else had to match
or brake axles and wheels were made by Roman War Chariots.
Notes: Notes

## Slide 57: Establishment of Standards
Roman armies who used chariots and quickly found the need to standardize the distance between wheels and made all their chariots alike. A “military spec” we still follow
which was based upon their power source or two horses.
The United States Standard Railroad Gauge of 4 Feet, 8.5 Inches is based upon the Roman Military Spec. derived from the width of the back-end of two war horses.
Notes: Notes

## Slide 58: Setup Time Reduction Process
Notes: Notes

## Slide 59: Total Time
During any CNC machine’s usage, there are really only three activities. The machines is down (for either maintenance, or lack of production), is in setup or is running production.
Setup Time & maintenance time is the total time the machine is down between production runs.
Cycle Time is the time it takes to complete a Production Run divided by the number of good work pieces produced.
Notes: Notes

## Slide 60: Setup Time Reduction Process
The setup process is the key function in the total process as it affects all the other time factors
First allows for orderly, consistent, time saving setups that do not unnecessarily overly burden operators. Rushing, disorientation, and fatigue can cause errors
It frees up more time to address takt time, and for preventive maintenance, both of which affect quality.
It ultimately reduces cost & increases quality which aids in sales or more orders.
Notes: Notes

## Slide 61
Much is Directly Related to Setup:
Tearing down the old setup
Putting old tooling away
Cleaning the machine
Making the new setup
Cutting tool tasks
  Assemble, measure, and enter offsets
  Assign program zero
  Measure position and enter fixture offsets
Load program
Verify program
Optimize program
Notes: Notes

## Slide 62
And some non-productive setup activities:
Time spent gathering needed items
Personal time
Time spent waiting:
  Looking for lost items
  For inspection
  For tool crib attendant
  For fork lift operator
These are all normal items found during a setup reduction program!
Notes: Notes

## Slide 63
But maybe some non-productive activities that can be eliminated or done prior to a setup:
Time spent gathering needed items
  Hand tools
  Cutting tools
  Fixtures
  Gauges
  Material
  Paperwork
  Storage containers
Tool carts used to store only the setup tool needed can be laid out in an orderly fashion to be most efficient & Designated Setup Carts used to store the last setup for future use and another Designated Setup Cart for the new part number or next setup.
The old setup can be inspected to replace worn items and immediately stored for reuse.
Notes: Notes

## Slide 64: Setup Cost Savings
Down Time Reduction and Production Time Increases will pay for any cost occurred developing carts, storage containers, etc. use to organize tools & setup materials.
Notes: Notes

## Slide 65: End of Lecture 6
Notes: Notes