## Slide 1
ENGT 1200 Version
Notes: Notes

## Slide 2: WELCOME to the CSCC~AQIP TOOLKIT FOR CONTINUOUS IMPROVEMENT
  Inside are detailed descriptions of all the tools you need to generate ideas, collect information, analyze and display data, reach consensus, and plan actions.
It's a small book in PowerPoint format, but it can make a big difference in what you accomplish each and every day.
These tools, by the way, represent the very best practices. They're routinely used in all world-class organizations and those trying to become world –class because they work. And they're easy to use! The next time you're working to generate ideas, try brainstorming. If you're analyzing a process, create a flow chart. When you're trying to pinpoint a root cause, use a Pareto chart or the “WHY Technique”. You'll be amazed by the power of these simple tools!
Best of all, you can use these tools starting now. If you're in a formal process-improvement team or an informal work group, you'll have all sorts of opportunities. If you participate in meetings, the tools will help you reach new levels of meeting effectiveness. You can even use them on your own. If you want the best result, then use the best practices.
Please keep your track of your ToolKit for Quality, and make it a routine reference source. You'll find that great things really do come in small packages!
Q
Notes: Notes

## Slide 3: Tools & Hyperlinks
 | Generating ideas and collecting info Affinity Diagram Brainstorming Check Sheet | Force Field Analysis Interviews Sampling Surveys
 | Analyzing and displaying data Attribute Charts Cause-and -Effect diagram Control Chart Control Chart Interpretation Flow Chart Histograms | Matrix Diagram Pareto Chart Relationship Diagrams Run Chart Systematic Diagrams Variable Charts “Why” Technique
 | Reaching consensus Balance Sheet List Reduction | Criteria Rating Form Nominal Group Technique Weighted Voting
 | Planning actions Flow Chart Gantt Chart | Pert Chart Operational Definition PDCA/DMAIC
Notes: Notes

## Slide 4: The CSCC AQIP Quality Process
There are several Quality Improvement or CI approaches promoted today! Don’t let the word “Quality” through you off as it is used in the sense of performance improvement as is CI!
We will use a hybrid of the oldest PDSA and one of the newest the Six Sigma DMAIC

## Slide 5: PDSA
The “PDSA” or Plan, Do Study, Act Cycle was originally developed by Walter Shewhart, but was made prominent by W. Edwards Deming.
Today there are variations of the PDSA and comprehensive programs such as the Six Sigma Program to consider.
Notes: Notes

## Slide 6: PDSA Cycle
Plan
Do
Act
Study
Define the System
Assess Current Situation
Analyze Causes Develop Improvement Theory
Try Out Improvement Theory
Study the Results
Standardize Improvements
Plan Continuous Improvement
The output of system improvement is your completed improvement project which is best accomplished by explaining the PDCA Cycle as we use it in the QUAL 150 ~ Quality Transformation Class.
Seven steps are used to explain & complete the cycle
Notes: The PDSA Cycle has been explained many different ways by many different Guru’s. It has been repackage several times and is essential technique in all current quality systems…
The DMAIC Methodology
Improvement teams use the DMAIC methodology to root out and eliminate the causes of defects:
  D Define a problem or improvement opportunity.
  M Measure process performance.
  A Analyze the process to determine the root causes of
  poor performance; determine whether the process can
  be improved or should be redesigned.
  I Improve the process by attacking root causes.
  C Control the improved process to hold the gains.

## Slide 7: Predictive Six-Sigma
Define
Measure
Analyze
Improve
Control
Replicate
Predictive 6-Sigma is the DMAIC process with
the “Define” stage being the identification of
CC’s, SC’s and Process HIC’s.
Continuous Improvement through Variability
Reduction.
Definition of Quality Procedures and requirements
to control all “significant” sources of variation.
SPC and Control Charting. Quality Index
supported by a Stable and In-Control Process.
6-Sigma (DMAIC)
Notes: The comparison of our CI process to the DMAIC or Six sigma process

## Slide 8: System Improvement Comparison
Plan
Do
Act
Study
Define the System
Assess Current Situation
Analyze Causes Develop Improvement Theory
Try Out Improvement Theory
Study the Results
Standardize Improvements
Plan Continuous Improvement
Define
Measure
Analyze
Improve
Control
Replicate
Six Sigma & PDSA Compared
Notes: All organizations face challenges, posed by customers, competition, and investors, to stay in business. These usually are described as high cost of production, scrap, rework, safety, efficiency, lack of profits, strategic focus customer satisfaction, etc.
Total Quality Transformation is a step-by-step process for improving work systems, which includes the team skills training needed to accomplish each step or function, and the opportunity to practice these skills, by completing a project.
In addition the team is taught the need to be aligned with the organizations vision, mission statement, strategic objective, or a current tactic to achieve and objective.

## Slide 9: The Toolkit
The Toolkit is arraigned in alphabetical order with no prominence given to any particular tool!
  The tool are classified as: Generating ideas and collecting Info, Analyzing and displaying data, Reaching consensus, and Planning Actions.
Just like the Sears Craftsman “The Toolkit” is full of tool, some of which are used constantly and some less frequently. Some are not used because of the specific work we do, or maybe our knowledge of the tools use!
Notes: Notes

## Slide 10: The Toolkit
Teams are usually formed of system expert who lack total knowledge of the following team & statistical tools. This is not a problem as we will discuss. The ENGT 1200 team should have at a minimum one statistical techniques mentor or CSCC should provide one.
In Fact learning the various tools is one of the personal improvements offered by participating in the Action Team, “it is also a resume issue”!
Notes: Notes

## Slide 11: Affinity Diagrams
If you ever find yourself wrestling with too much information, unable to organize it in an effective way, the affinity diagram is for you. This powerful tool pulls together an enormous volume of ideas, leaving you with well-sorted groups that give the information clear meaning.
Putting it to work:
  Begin by writing the issue to be considered. Keep it neutral and concise, and write it on a flip chart so all can see. For example: "What do our customers want from us?" Another example: "What implementation issues do we need to address as a steering committee?" Discussion and editing will likely be necessary as the team works to decide on the exact phrasing. Make sure there is consensus support for the final version.
  Spend the next 15 or so minutes brainstorming ideas in response to the phrase. Have one person record the statements on a flip chart - while a second person uses a thick marker to write each statement on a separate note card or Post-It-Note. (Post-It-Notes work best, especially for displaying the finished product on a wall or flip chart. However, make sure they're big enough?) These responses should be concise (no more than seven words), yet they should be thorough and understandable.
Affinity Diagrams
Notes: Notes

## Slide 12: Affinity Diagrams
  Consider the issue. "What do our customers want from us?" Vague responses include "quality" and "service". A richer response would be: "Answer call-in questions within five minutes." Another brief; yet to-the-point response: "Receive all the necessary info by mail.“
  Continue generating responses while following all the guidelines of brainstorming. All ideas are accepted without criticism and without editing by the recorder. The more ideas, the better.
  After all the ideas have been put forward, take the cards (or Post-It Notes) and spread them out on a large table. At this point, there's no need to organize them. In fact, it's better if they are mixed up in a completely random fashion.
  See exhibit A.
Affinity Diagrams
Notes: Notes

## Slide 13: Affinity Diagrams
  Now it's time to sort. Have the team members locate and place side-by-side two cards that are connected in some way - perhaps they deal with the same subtopic, or they touch on activities done by the same group of people, or they have something else in common.
  This matching process continues, with people building groups of related cards, until the random bunch of ideas has been transformed into 5 - 10 groupings. If one card seems completely unrelated to all the other cards, no problem, simply let it stand alone as its own grouping. See exhibit B. (For an interesting twist to this step, have tem members do their sorting in silence. If one person wants to move a card from one grouping to another, let it happen. Consensus will eventually emerge.)
Affinity Diagrams
Notes: Notes

## Slide 14: Affinity Diagrams
  Now that the cards have been sorted, look through each grouping for the one card that conveys the main idea of that grouping and ties all the various ideas together. This become the "header" card and is placed at the top, while the other cards are positioned vertically beneath it. If a grouping doesn’t seem to include an all-encompassing header card, create one and put it at the top. See exhibit C.
  Do one last sort. Looking at the header cards, move the groupings so that related ones are next to each other on the table. If you're working with cards, tape them in sorted order on a flip-chart sheet (or, more likely, on several!) If you've opted for Post-It-Notes, all you need to do is press them on. Finish up by drawing a box around the related groupings, and create a "super header" for each of these. You now have a detailed analysis of the issue. It's clearly presented and ready to share.
Affinity Diagrams
Notes: Notes

## Slide 15: Affinity Diagram Example
Exhibit A
Exhibit B
Exhibit C
Exhibit D
Affinity Diagrams
Notes: Notes

## Slide 16: Affinity Diagrams
Downloadable Chart Template from Microsoft owners of PowerPoint 2007
Affinity Diagrams
Menu
Notes: Notes

## Slide 17: Attribute Control Charts
For a quick example my choice was an internet site source: http://www.itl.nist.gov/ (Data Plot Reference Manual)
Government Sources are public domain and a reliable source that can be used for a good foundation at no cost…
These are supplemented with Microsoft Excel and Minitab examples as using these tools are more efficient, save time, and cost. This also fits with our philosophy of team learning!
As CSCC AQIP teams make future presentation I would suggest using CSCC team examples and case studies!
Four principle type of charts are the np-chart, the p-chart, the c-chart, and the u-chart
Attribute Control Charts
Notes: Notes

## Slide 18: Attribute Control Charts
The same data used to create a histogram is used, but the data must be plotted in the order it is collected over time… The control chart is used when we need system stability and wish to see how the frequency of measures, such as is recorded in a histogram, occur over time, the pattern of the data, how well the process is centered and analysis of the control we have over the process.
Attribute Control Charts are run charts with statistically calculated upper and lower control limits and the calculated center line of the process added to the chart.
Attribute Control Charts
Notes: Notes

## Slide 19: Selecting Type of Attribute Data Charts
Notes: Notes

## Slide 20: Attribute Data Table
Attribute Control Charts
Notes: Notes

## Slide 21: NP Control Chart
NP Control Charts for Non Conforming Attributes
Putting it to work:
The np-chart shows how a system, measured by the number of items addressed in a constant subgroup size, change over time.
The characteristic of interest is always a pass/fail, good/bad, or yes/no answer. For example the number of students who pass/fail quizzes or have acceptable/non-acceptable homework on a weekly basis using a constant subgroup size such as a department average population…
Control charts assess stability over time and can be used to monitor improvement! They minimize mistakes of over control and under control and identify whether common cause variation or special cause variation exist, which will indicate the proper improvement to make!
Attribute Control Charts
NP Control Chart
Notes: Notes

## Slide 22: NP Control Chart
When it is Used?
Use a np chart when you can answer yes to all these questions:
  Do you need system stability?
  Is the data the number of nonconforming items in a subgroup?
  Are all subgroups the same?
  Are there only two outcomes, good/bad, pass/fail. Etc.
  Has the characteristic being charted been “Operationally Defined” prior to the data collection?
  Is the time order of the preserves?
Order is important as analysis and chart interpretation rules will not apply!
Attribute Control Charts
NP Control Chart
Notes: Notes

## Slide 23: NP Control Chart
Notes: Source: http://www.itl.nist.gov/

## Slide 24: NP Control Chart
Attribute Control Charts
Notes: Source: http://www.itl.nist.gov/

## Slide 25: NP Control Chart
Attribute Control Charts
Notes: Source: http://www.itl.nist.gov/

## Slide 26: NP Control Chart
Teams are encouraged to use tools to reduce time, calculation errors, and to standardize the descriptive geometry or chart format. My choice is Microsoft Excel or Minitab.
I would not limit any team to these choice, but offer the following examples!
Note: This is an older version, but CSCC has current versions of this software
Attribute Control Charts

## Slide 27: NP Control Chart
Microsoft Excel & Minitab Example
First collect and record your data in MS Excel
( Histograms and Various Charts can be analyzed using Excel)…
For the attribute chart we copy and paste the data into Minitab for your np chart example!
Attribute Control Charts
Notes: Notes

## Slide 28: NP Control Chart
Paste the data into Minitab then chose “Stats” on the menu bar
Attribute Control Charts
Notes: Notes

## Slide 29: NP Control Chart
After picking Stats, choose control charts, then np
Attribute Control Charts
Notes: Notes

## Slide 30
Choose C1 where we pasted our data and select, then enter the subgroup size as shown, then pick OK. Remember for the np chart the subgroup must be constant.
subgroup size
Notes: Notes

## Slide 31: NP Control Chart
This chart shows a non normal distribution with two points on the lower control limit and 1 point out of control. This would warrant a process improvement teams time to analyze causes.
This chart shows the Trend, the calculated average, and the upper & lower control limits
Notes: Notes

## Slide 32: P Control Chart
P Control Charts for Non Conforming Attributes
Putting it to work:
The p-chart shows how a system, measured by the proportion of nonconforming items addressed in a constant or variable subgroup size, change over time.
The characteristic of interest is always a pass/fail, good/bad, or yes/no answer. For example the number of students who pass/fail quizzes or have acceptable/non-acceptable homework on a weekly basis .
Control charts assess stability over time and can be used to monitor improvement! They minimize mistakes of over control and under control and identify whether common cause variation or special cause variation exist, which will indicate the proper improvement to make!
Attribute Control Charts
P Control Chart
Notes: Notes

## Slide 33: P Control Chart
When it is Used?
Use a p chart when you can answer yes to all these questions:
  Do you need system stability?
  Is the data counts that can be converted to proportion?
  Are there only two outcomes, good/bad, pass/fail. Etc.
  Has the characteristic being charted been “Operationally Defined” prior to the data collection?
  Is the time order of the preserves?
Order is important as analysis and chart interpretation rules will not apply!
Attribute Control Charts
P Control Chart
Notes: Notes

## Slide 34
Attribute Control Charts
P Control Chart

## Slide 35
Notes: Source: http://www.itl.nist.gov/

## Slide 36: P Control Chart
Attribute Control Charts
Notes: Source: http://www.itl.nist.gov/

## Slide 37: C Control Chart
C Control Charts for Nonconformities
Putting it to work:
The c-chart monitors a system measured by number of nonconformities per subgroup of nonconforming items.
The c charts is used where the characteristic being counted can theoretically occur an infinite number of times.
Nonconformities are defects or occurrences found in sampled subgroups.
Errors on test, quizzes, forms, computer programs or screens, number of absence, tardy, etc. are examples of nonconformities. Missing or unwanted items are also counted as nonconformities.
Control charts assess stability over time and can be used to monitor improvement! They minimize mistakes of over control and under control and identify whether common cause variation or special cause variation exist, which will indicate the proper improvement to make!
Notes: Notes

## Slide 38: C Control Chart
When it is Used?
Use a C chart when you can answer yes to all these questions:
  Do you need system stability?
  Does the data represent the number of nonconformities per subgroup?
  Is the subgroup size the same for all subgroups, if not consider using a u chart.
  Has nonconformities been “Operationally Defined” prior to the data collection?
  Is the time order of the preserves?
Order is important as analysis and chart interpretation rules will not apply!
Attribute Control Charts
C Control Chart
Notes: Notes

## Slide 39: C Chart
Attribute Control Charts

## Slide 40
Attribute Control Charts
C Control Chart

## Slide 41: C Chart
Attribute Control Charts

## Slide 42
Data was input a Microsoft Excel spreadsheet.
This data was copied to paste in a version of Minitab to calculate and display a C Chart
Attribute Control Charts
C Control Chart
Notes: Notes

## Slide 43: C Chart
The data was pasted from MS Excel into Minitab ver. 12
Attribute Control Charts
Notes: Notes

## Slide 44
To calculate the C Chart choose Stats, then Control Charts, then C…
Attribute Control Charts
C Control Chart

## Slide 45
Variable: Choose C8 Totals, then Select then OK
Attribute Control Charts
C Chart
Notes: Notes

## Slide 46: C Chart
The chart will display the trend , the calculated average, and the upper and lower control limits
Attribute Control Charts
Notes: Notes

## Slide 47: U Control Chart
U Control Charts for Non Conformities
Putting it to work:
The U-chart is an attribute control chart which shows how a system, measured by number of nonconformities unit produced will change over time..
Nonconformities are that which is missing or that which is present on a item and should not be. Errors in quizzes, forms, number of late deadlines, tardiness, etc The subgroup size can be constant or change over time
Control charts assess stability over time and can be used to monitor improvement! They minimize mistakes of over control and under control and identify whether common cause variation or special cause variation exist, which will indicate the proper improvement to make!
Attribute Control Charts
U Control Chart
Notes: Notes

## Slide 48: U Control Chart
When it is Used?
Use a U chart when you can answer yes to all these questions:
  Do you need system stability?
  Does the data represent the number of nonconformities per subgroup?
  Has the possible nonconformities being charted been “Operationally Defined” prior to the data collection?
  Is the time order of the preserves?
Order is important as analysis and chart interpretation rules will not apply!
Attribute Control Charts
U Chart
Notes: Notes

## Slide 49
Notes: Source: http://www.itl.nist.gov/

## Slide 50
Notes: Source: http://www.itl.nist.gov/

## Slide 51: U Chart
Attribute Control Charts
Notes: Source: http://www.itl.nist.gov/ (Dataplot Reference Manual)

## Slide 52: BALANCE SHEET
Balance sheets allow a group to identify and review the pros and cons of various options. Like the other tools for reaching consensus, balance sheets won't make decisions. They will, however, organize the information and facilitate discussion among group members.
Putting it to work:
Using a flip chart or marking board, set up a large grid consisting of two columns and a row for each of the options being discussed.
Label the columns + and - (or "pros" and "cons"). The team then "fills in" each cell of the grid, brainstorming and reaching consensus on positive and negative aspects for each option.
Balance Sheet
Notes: Notes

## Slide 53: BALANCE SHEET EXAMPLE
The balance sheet shown here was used to identify the pros and cons of three methods of brainstorming.
METHOD | PROS | CONS
Free Wheeling | Very spontaneous Trends to be creative Easy to build on other' ideas. | Strong individuals may dominate the session. Confusion sets in; ideas may be lost when too many talk at once.
Round Robin | Difficult for one individual to dominate. Discussion tends to be more focused. Everyone is encouraged to take part. Easy to build on others' ideas. | Difficult to wait one's turn. Some loss of energy. Reluctance to pass.
Slip Method | Anonymity allows sensitive topics to Surface. Can be used with very large group. Not necessary to speak out. | Not possible to build on others ideas. Some ideas may not be legible/understandable. Slow
Balance Sheet
Notes: Notes

## Slide 54: BRAINSTORMING
Brainstorming is a powerful way to generate input.
Working in a team setting, people express their ideas the moment they think of them. Brainstorming is an informal process in which:
  No one evaluates the ideas as they're announced.
  Wild ideas are encouraged.
  People build on the ideas of others.
  Everyone strives for quantity. The more ideas, the better!
Putting it to work:
The team leader (or facilitator) presents the topic for which ideas are sought.
  The wording should encourage specific, tangible ideas -- not abstract or vague thoughts.
  Make sure everyone in the team understands the topic that's the focus of the brainstorming as well as the process to be followed.
Brainstorming
Notes: Notes

## Slide 55: BRAINSTORMING
There are three methods of brainstorming.
The most familiar is freewheeling, in which:
Group members call out their ideas spontaneously.
The scribe records the ideas as they are suggested.
In round-robin brainstorming:
The leader or scribe asks each member, in turn, for an idea.
Members may pass on any round.
The session continues until all members have passed during the round.
Ideas are recorded as in freewheeling brainstorming.
The slip method differs markedly from the other two approaches:
The leader asks members to write down their ideas on small slips of paper or index cards
The ideas are then collected and organized. See Affinity Diagramming
Brainstorming
Notes: Notes

## Slide 56: CAUSE-AND-EFFECT DIAGRAM
The cause-and-effect diagram offers a systematic way to pinpoint the various factors that may be causing a problem. It prompts people to ask. "Why is this occurring?" As the diagram is developed, more and more potential causes come to light.
  Some people call this tool the Ishikawa Chart after its originator Kaoru Ishikawa and some call it a "fishbone diagram" because it takes the shape of a fish as more causes are brainstormed.
  The effect (problem) is the "head of the fish." Leading from this the "backbone" and connected to this are the "main bones," which represent major categories of causes. Commonly used categories include people, policies, procedures, equipment, materials and environment. These categories are only suggestions; you may use any major category the team deems appropriate.
Cause & Effect Diagram
Notes: Notes

## Slide 57: Cause & Effect Diagram
The Effect
Machine
Process
People
Materials
Why?
Why?
Why?
Why?
Why?
Why?
Why?
Why?
Major Classifications
Cause & Effect Diagramming is easily associated with:
  Affinity Diagrams
  Brainstorming
  Root cause Analysis
As you can see, the diagram does indeed have the shape of a fish. The effect is on the right, and the causes form the "bones: of the fish. Note the four main categories of causes, these can be edited.
Cause & Effect Diagram
Notes: Notes

## Slide 58: Cause & Effect Diagram
Putting it to work:
Follow these three steps when creating a cause-and-effect diagram:
  Decide on the effect (problem) to be analyzed, being sure it’s specific, well understood and agreed to by everyone. Write it in a box on the right side of the flip chart or marking board; this is the "head of the fish.“
  Next, draw a horizontal line form the head across the paper with several "major bones" drawn on a slant. At the end of each, write one of the major categories that contribute to the effect.
  Brainstorm specific causes. Attach each specific cause to an appropriate major category. Whenever possible, break down the specific cause into sub causes by using the "why" technique. Keep asking, "Why is this occurring?“
Cause & Effect Diagram
Notes: Notes

## Slide 59: Cause & Effect Diagram
Here are some additional tips:
If in doubt about possible causes, check your ideas with data. Look for causes that appear repeatedly. This will have the added benefit of helping the team reach consensus.
In most cases, it's not so important where the specific cause is placed on the diagram. The important point is that it's identified.
The cause-and-effect diagram can be useful when displayed publicly and people are invited to contribute. Think of this as a large-scale brainstorming effort.
When creating the diagram, try to use as few words as possible. This will require team members to focus their ideas.
Cause & Effect Diagram
Notes: Notes

## Slide 60: Cause & Effect Diagram
Downloadable Chart Templates from Microsoft owners of PowerPoint 2007
Notes: Notes

## Slide 61: Control Chart Charting
If you choose to use paper charting you must collect the data, choose the proper format and plot your data.
Once you have plotted your data, you will need to calculate the average, the upper control limit (UCL) and the lower control limit (LCL) of the data and place them on the chart. The LCL and UCL are figured by determining three standard deviations from the average.
The data & formulas for each of these calculations are on the following pages, with examples, but most people could simply use a calculator or Software such as Excel or MiniTab...
Generic Chart Construction
Control Charts Interpretation
Notes: Notes

## Slide 62: Control Chart
Putting it to work:
Before you can create a control chart you need to collect data, paper is ok, but the very accessible Microsoft Excel spread sheet is the better choice as Excel has analysis & descriptive geometry capability and the ability to export data to other analysis software such as Minitab…
You need at least 20 to 30 data points on your run chart to make a control chart that is statically valid. The more points used the better!
We will focus on attribute charts for non conforming or non conformities, specifically:
Non Conforming includes np charts and p charts
Non Conformities include c charts and u charts
Generic Chart Construction
Control Charts Interpretation
Notes: Notes

## Slide 63: Generic Chart Construction
Generic Chart Construction
Control Charts Interpretation
Paper charting required recording the data and plotting the data
A place for data
A place for the scale
A place for the Plotted Data
Notes: Notes

## Slide 64: Generic Chart Construction
Data is collected
Average & Range is calculated
Points are Plotted
Upper & Lower Control limits are Calculated
Notes: Notes

## Slide 65: Control Chart Interpretation
The construction of the various control charts is but one topic needed as only the knowledge of the “Central Limit Theorem” and basic chart interpretation allow us to appreciate the full power of the control chart as an analysis & control tool. A basic understanding of this subject matter have been added to this toolbox.
A Control Chart Primer
Interpreting Control Charts
Notes: Notes: The presence of a team member with a statistical techniques background and experience is highly recommended. One goal of every Action Team is to increase & expand this knowledge, experience and the use of scientific decision making!!

## Slide 66: Chart Interpretation Topics
Collection and Reliability of Data
Variability of Data
Shape of Data
Central Limit Theorem
Generic Chart Construction
Trends & Chart Rules
Normal Data & Capability Analysis
Capability Analysis
Interpreting Control Charts
Notes: Notes

## Slide 67: Collection and Reliability of Data
Today data collection that is Operationally Defined by an Action Team and collected by trained experience associates who understand how consistency is related to reliability is usually considered most reliable.
Data that is displayed using statistical tools or descriptive geometry is best interpreted, in a consistent manner and understood…
Collection and Reliability of Data
Interpreting Control Charts
Notes: Notes

## Slide 68: Variability of Data
All things in nature or man made exhibit variation. No two trees, snow flacks, people or products are the same.
In 1920 Dr. Walter Shewhart of Bell Labs observed that variation followed a normal pattern, that of the bell shaped curve.
Identifying, and measuring variation is a key to CI projects.
Interpreting Control Charts
Variability of Data
Notes: Notes: A side note that may be of interest to those in academia is that most all of the quality Guru,s came out of the electronic industry’s or have electrical engineering backgrounds. This is primary the fact that quality initiatives and technical or more complicated items require greater reliability.

## Slide 69: Shape of Data
NORMAL Distribution
Skewed Distribution
Bimodal Distribution
Skewed RIGHT
Skewed LEFT
Data Distribution Examples
Control Charts Interpretation
Variability of Data
Notes: Notes

## Slide 70: Analyzes of the Shape of Data
Analyzing the shape of the data which can be discerned by creating a run chart helps to determine frequency of data collection. It also allow for control point and data collection point analysis…
Control Charts Interpretation
Shape of Data
Notes: Notes

## Slide 71: Central Limit Theorem
This allows us to rely on SAMPLE DATA to make DECISIONS?
Population Data
Distributions of
Samples of the
Population
Definition:
  The distribution of Means of independent samples from any distribution with finite Mean and Variance, will converge to the Normal distribution as the sample size goes to infinity.
  BASICALLY – The averages of groupings of samples from a Normal OR Non-Normal population will move toward a Normal distribution as more data is collected and analyzed.
Control Charts Interpretation
Notes: notes

## Slide 72: Attribute Control Chart
A control chart, also called an attribute control chart, is simply a run chart with statistically derived upper and lower control limits added. These limits are the calculation of the normal variation in the system. The control chart tells a team how the system is operating. It helps determine if the system is stable or out of control. This is done by gathering the data over time on a run chart, then calculating the process average and upper and lower controls limits.
The purpose of a control chart is:
  To find out a system's capacity so that normal variations are not misinterpreted as significant, thus causing tampering with results.
  To identify “special causes” of variation (those that fall outside of the control limits) so they can be eliminated.
  To know when changes have actually improved the system and are not merely common cause variation.
Notes: Notes

## Slide 73: Trends & Chart Rules
Charting reveals the shape of data over time or the trends. These trends show normality or non-normality and gives us control over a process.
It is important to understand and to view as out of control system need be controlled to establish consistency and only consistent normal data can be assessed for capability or reliability!
Interpreting Control Charts
Trends & Chart Rules
Notes: Notes

## Slide 74: Variation Should Be Random
It is very important to remember that:
Process Variation is expected to be RANDOM.
If it is NOT, then you need to start looking for signals in
your process to help you understand what is going on.
(exceptions are for known patterns such as tool wear)
The process must become random or its output can NOT
be predicted and any Cpk Index Is meaningless.
Interpreting Control Charts
UCL
LCL
Trends & Chart Rules
Notes: As we have shown, it is very important to remember that: Process Variation is expected to be RANDOM
If it’s NOT, then you need to start looking for signals in your process to help you understand what is going on.
Note that there are examples of Non-Random events such as tool wear in a manufacturing process. In this case, the affect of the non-random event (tool ware) needs to be removed from our process monitoring or our method of control needs to be modified. This is done using a modified control chart, or endpoint control, discussed later.

## Slide 75: Control Charts Interpretation
  What we expect to see in a chart is a normal distribution such as this near perfect histogram, which rarely exist.
If the order of points are plotted as collected we will see the actual shape of the process over time. We would expect to see 68.26% of the data in the green zone. and 95.46 of the data in the yellow and green zones.
Interpreting Control Charts
Trends & Chart Rules
Notes: Notes

## Slide 76: Types of “Out-of-Control”
Points OUTSIDE the Control Limits
UCL
LCL
UCL
LCL
Run of 7 Points UP or DOWN
Cause
Action
Prevention
Cause
Action
Prevention
Cause
Action
Prevention
Cause
Action
Prevention
Interpreting Control Charts
Trends & Chart Rules
Notes: Here we will talk about Types of Out-of-Control:
  Points On or Outside of the Control Limits
  A Run of 7 Consecutive Points Up or Down
Notice that for the Run of 7 Consecutive Points can go in either direction
NOTE: In general, these conditions are describing what you would look for on an X-Bar & R, X-Bar & S. The rules for an X & MR (IMR) are slightly different.
Notes

## Slide 77: Types of “Out-of-Control”
7 Points Above / 7 Points Below
UCL
LCL
UCL
LCL
Cyclical Patterns
Cause
Action
Prevention
Cause
Action
Prevention
Interpreting Control Charts
Trends & Chart Rules
Notes: In addition:
  7 Consecutive Points Above/Below the Center Line
  Cyclical Patterns
Cyclical Patterns can indicate that your process is being affected by things like Tool Wear, improper maintenance of equipment, external factors like temperature or humidity, etc.
Notes

## Slide 78: Types of “Out-of-Control”
As you can see, some of these conditions
are more difficult to notice, and are easier
caught if using a computer.
Points TOO Close to the Mean
UCL
LCL
Possibly something has changed with this process over time,
OR the Control Limits were calculated incorrectly,
OR this data has been fabricated.
2 out of 3 points more than 2s from the Center Line (Same Side)
UCL
LCL
3s
2s
1s
Center Line
-1s
-2s
-3s
Interpreting Control Charts
Trends & Chart Rules
Notes: Two more items to keep in mind are:
  Points TOO Close to the Center Line (X-Double Bar)
  2 out of 3 points more than 2s from the Center Line (Same Side)
If points are all too close to the Mean Center Line (e.g. all between +1s and –1s ), either your process has changed from the original calculation of the UCL and LCL, you calculated the UCL and LCL incorrectly, or someone is manufacturing the data without taking proper measurements.
2 out of 3 points more than 2s away from the Center Line indicates that for a short period of time we had a shift in the process.
If normally distributed, 6 out of every 10 parts will be produced between the mean of the process and +/- 1 standard deviation. If 2 out of 3 points are more than 2 sigma from nominal, that’s 66% of all production. This would indicate that the mean of the process has shifted and is now somewhere around 2 sigma from nominal. The process needs retargeted.
Notes

## Slide 79: Types of “Out-of-Control”
4 out of 5 points more than 1s from the Center Line (Same Side)
8 out of 9 points in a row more than 1s from Center Line (Either Side)
UCL
LCL
3s
2s
1s
Center Line
-1s
-2s
-3s
UCL
LCL
3s
2s
1s
Center Line
-1s
-2s
-3s
As you can see, some of these conditions
are more difficult to notice, and are easier
caught if using a computer.
Interpreting Control Charts
Trends & Chart Rules
Notes: Further indications of possible instability include:
  4 out of 5 points more than 1s from the Center Line (Same Side) This also indicates a shift in the mean of the process.
  8 out of 9 points in a row more than 1s from the Center Line (Either Side)
As the note above implies, some of these conditions are difficult to pick out when looking at a chart. These are usually best found if you are using a computer.
But again, a computer is NOT a requirement of control charting. Hand charting can be effective on a known stable process. Using a computer initially to flag all non-random events for a period of time after launch is suggested, then moving to hand charting has less risk.
Notes

## Slide 80: Other Signals
Points OUTSIDE the Control Limits
UCL
LCL
Cause
Action
Prevention
Cause
Action
Prevention
Points OUTSIDE the Control Limits signal: Instability
They are indicative of presence of Special Causes of Variation
Distribution associated with Instability
Interpreting Control Charts
Trends & Chart Rules
Notes: For a capable process out-of-control points should happen 0.27% of the time in the entire population of production. Therefore, the odds are very low that you would see this in your sampling. Due to the low probability of seeing this in your sampling, when an out-of-control point is seen it’s usually due to “special cause” variation that can be managed or eliminated, The identification and elimination of “special cause is one of the purposes of control charting.

## Slide 81: Other Signals
Gradual Level Changes
UCL
LCL
These types of chart signal: Shift in Level
They are Characterized by an apparent increase in variation, or on Control charts
a run that is consistently in one direction
Often indicates new procedures, effects of old/new material component mixtures.
Distribution associated with Gradual Shift in Level
Expected Spread
Interpreting Control Charts
Trends & Chart Rules
Notes: Here, we aren’t Out-of-Control with respect to 7 points in a row going in any one direction… but, there IS a gradual level change going on. As the chart at the bottom shows, the distribution is much wider than a normal distribution (bell shaped discussed later) and you are probably building product that does NOT meet the customer expectation.
This can signal a failure to control targeting, a general failure to follow procedures, or a lack of proper procedures.
It can also indicate the presence of a Special Cause such as Tool Wear trending or the effects of temperature.
Notes

## Slide 82: Other Signals
Trends
UCL
LCL
These types of chart signal: Trends
They are Characterized by gradual unidirectional changes in level
Indicative of tool wear, deterioration, etc.
Distribution of samples associated with Trends
Interpreting Control Charts
Trends & Chart Rules
Notes: This example shows a very obvious trend upward. Again, NOT the traditional Out-of-Control condition of 7 points in a row, but a distinctive process movement.
Notes

## Slide 83: Other Signals
Level Shift (Sudden)
These types of chart signal: Level Shift (Sudden)
They are Characterized by an obvious change in the average, X.
Often reflects change in motivation, operator’s ability, equipment, material, etc.
Separately
Jointly
UCL
LCL
Interpreting Control Charts
Trends & Chart Rules
Notes: This sudden level shift is many times easy to figure out much sooner than is displayed here. Look for a new operator, a new machine, new material, lot to lot variation such as a change in material hardness, tool setup failure, gage failure, etc. to determine what may have caused it.
Of course, we would expect that the reaction took place at the first occurrence of the out-of-control point, not after 7 events.
Notes

## Slide 84: Other Signals
Mimicking
These types of chart signal: Mimicking
Characterized by the tendency of one chart to follow another.
Indicative of two sets of data from same examples.
(expected for multiple spindles with common nominal targeting)
UCL
LCL
Variable A
Variable B
Interpreting Control Charts
Trends & Chart Rules
Notes: In these two process, there is a mimicking pattern shown. When one point on Variable A goes up, the same point on Variable B goes up. When one point on Variable B goes down, the same point on Variable A goes down.
This can mean that your process is being affected the same way by either a common ingredient, a common tool/machine, or something environmental like Humidity, Temperature, etc.
This is not necessarily a bad thing if you are running 2 spindles on the same transfer machine with common targeting. In that case, this would be desirable and would indicate the individual spindles do not contribute any Special Cause variation.
Notes

## Slide 85
  An alternate type of pattern that can occur is a trend such as six or more points steadily increasing or decreasing with no reversals. Neither pattern would be expected to happen based on random chance. Such a significant change calls for some research and analysis - and possible action. Plotting the data gives you a picture of the trend.
Control Charts Interpretation
Trends & Chart Rules
Trends & Chart Rules
Notes: Notes

## Slide 86: Normality Check - Histogram
“Normal” Histogram
  The tallest bars should be in the center with the bars getting smaller as they move away from the center
  (e.g. it should resemble a Bell Shaped Curve).
Normality
Interpreting Control Charts
Notes: For a “Normal” Histogram, the tallest bars should be in the center with the bars getting smaller as they move away from the center. (a bell shape)

## Slide 87: Normality Check - Tools
Some Tools to be used:
  Histogram
    Displays the shape of the data.
  Normal Probability Plot
    This is a scatter diagram which plots the data points
    against what they would be if Normally distributed.
  P-Value (from Minitab)
    Anderson-Darling Normality Test
    If p < 0.05, the data may NOT be Normally Distributed.
Normality
Interpreting Control Charts
Notes: Some tools used to assess Normality include:
  Histogram (already discussed)
  Normal Probability Plot
  P-Value (from Minitab)
    – Anderson-Darling Normality Test

## Slide 88: Normality Check - Rules
Rules* used in determining Normality:
  Start with a minimum of 30 data points (randomly selected from a significant production run)
  In general, two tests (e.g. Histogram, and a Normal Probability Plot, should indicate the data is Normally distributed. (If not, use a larger set of data).
  If a larger set is used to determine Normality and it is Normal, use the same set to do further calculations (e.g. Control Limits, Capability).
  (X-Bar & R Chart ONLY) If the data is Normal, the data may be used to calculate Cp/Cpk. (Normality is not required to use this Control Chart to understand and improve the process. It is only necessary to calculate a valid Cp/Cpk index).
  (Individuals Chart ONLY) If the data is Normal (100 pt. min.), the data can be used to calculate UCL and LCL on an Individuals & Moving Range chart and the data may be used to calculate Cp/Cpk.
  (Normality is required to calculate UCL/LCL on an X & MR Chart, NOT just for the Capability calculations).
Normality
Interpreting Control Charts
Notes: Further Rules used in the process of checking for Normality include:
  Start with a minimum of 30 data points (randomly selected out of a larger population).
  Two tests must indicate the data is Normally distributed. (If not, use a larger set of data).
  If the data is set is Normally distributed, the same set can be used for further calculations (Control Limits, Capability).
  X-Bar & R Chart ONLY - If the data is Normal, the data may be used to calculate capability (Cp/Cpk), (Normality is not required to use Control Charts to understand, adjust and improve the process).
  X & MR or Individuals Chart ONLY - If the data is Normal, you may chart the data on an X & MR chart with UCL and LCL and the data may be used to calculate capability (Cp/Cpk). Remember that you need to be very selective on when an X & MR chart is used. Use it when the characteristics being studied are Homogeneous, or virtually identical part to part, or measurement to measurement, such as Coolant Concentration.
  (For X & MR, Normality IS required to chart the data, calculate limits, and calculate capability).

## Slide 89: Normality Check
NORMAL Distribution
WHEN DO WE NEED TO CHECK for Normality:
  Before calculating control limits for an Individuals & Moving Range chart.
  Before calculating any capability as control & stability must be established before calculating Cp or Cpk
Note: A quick normality check is calculating the median, the mode, and the average. If the data is normal the calculation will be the same or close to…
A Histogram will show the shape of data & Minitab will also check data normality!
Normality
Interpreting Control Charts
Notes: Notes

## Slide 90: Create Normal Probability Plot
Normality ~ Minitab Example
p-Value (must be greater than 0.05)
1. Enter Data
2. Stat, then Basic Statistics, Then Normality Test
3. Enter Data Column # C1in Variable
4. Click Ok
Notes: To perform a “Normality Test” and to create a Normality Plot in Minitab, the steps are shown above.
Enter or copy your data to Minitab
Then use the pull down menu: Stat/Basic Statistics/Normality Test
Step 1: Enter your data as shown in Column C1 (top down to allow sorting if necessary).
Select C1 as the Variable
If you are testing the Individuals data, this would be your Individual Measurements
If you are testing the Subgroup data, this would be your Subgroup sample data. First four individual readings within a sub-group entered in one column in lines 1-4, each additional sub-group would be similarly entered (stacked in one column)
Step 2: Click on the Anderson-Darling button, then OK (supply a title if desired)
The p-Value (from Minitab) from the Anderson-Darling Normality Test will appear in the lower right corner of the graph. If the p-Value < 0.05, the Data may NOT be a Normal Distribution. P-values of greater than 0.05 are considered normal and Ppk & Cpk calculations are valid without data transformation.

## Slide 91: Normal Data & Capability Analysis
Normal data takes the shape of the bell shaped curve and is plus & minus 3 standard deviations or 6 wide
Short Term Capability is the specification divided by the process width now described as 6
Notes: Notes

## Slide 92: Capability
When using Capability Analysis to assess a current situation, it is important to ask questions:
  First ask whether the data was tested for normality.
  Understand whether a system or machine capability is used.
  Or was a process capability used to establish capability.
  The team should also analyze the metrology system or methods used to collect the data used for statistical analysis.
  This can best be done by verifying an acceptable operational definition existed and was followed by certified or trained associates.

## Slide 93: Capability as Seen on a Histogram
CONE No. L68149
FREQUENCY
40
35
30
25
20
15
10
5
0
-.0020 -.0017 -.0014 -.0011 -.0008 -.0005 -.0002 .0001 .0004 .0007 .0010 .0013 .0016 .0019
Cell Number
LCL
UCL
Center of Spec.
By putting the specification limits on the chart we can see the distribution is not centered, but all the data is within the specifications. This Histogram is skewed to the left indicating it is not exactly normal and a normality test should be conducted…
Notes: Notes

## Slide 94: Long Term Capability Analysis
LSL
USL
Long Term Capability analysis is the comparison of the process to the specifications and the location of the process within the specifications over time for this calculation we use CPk
 3 Sigma
See comparison of CP & CPK on following slide. CPK uses the X-Bar (average) or X-Double Bar (the Average of X-Bars) in the calculation to assess capability over time!
Interpreting Control Charts
Process Capability
Notes: Long Term Capability analysis is only done with a process that is in statistical control or stable.

## Slide 95: Formulas for Capability Indices
USL = UPPER SPECIFICATION LIMIT LSL = LOWER SPECIFICATION LIMIT
UCL = UPPER STATISTICAL CONTROL LIMIT LCL = LOWER STATISTICAL CONTROL LIMIT
= GRAND AVERAGE or AVERAGE of X-Bars
= ESTIMATED STANDARD DEVIATION FOR INDIVIDUAL MEASUREMENTS
= ACTUAL STANDARD DEVIATION FOR INDIVIDUAL MEASUREMENTS
= ACTUAL STANDARD DEVIATION FOR SUBGROUP AVERAGES
whichever
is smaller
whichever
is smaller
whichever
is smaller
Where:
or
or
or
Notes: CP and PC assume a centered process
Cpk and CR adjust for a lack of centering
CP and Cpk use an estimated standard deviation
PC and CR use an actual standard deviation

## Slide 96: Process Capability
Capable Process (virtually all output is centered & within the specifications)
Lower
Specification
Limit
(LSL)
Upper
Specification
Limit
(USL)
Size
Size
Size
Size
(LSL)
(USL)
(LSL)
(USL)
(LSL)
(USL)
Non-Capable Process (output is produced beyond one/both specs.)
Interpreting Control Charts
Process Capability
Notes: Notes

## Slide 97: Example Calculation CP
Interpreting Control Charts
Process Capability
Notes: Notes

## Slide 98: Example Calculation CPK
Interpreting Control Charts
Process Capability
Notes: Notes

## Slide 99: Example Calculation of CR
Interpreting Control Charts
Process Capability
Notes: Notes

## Slide 100: Evaluation of CR
CR TOTAL LIMITS EOT % Tolerance Defects per
No.  Consumed Million (DPM)
     
     
     
     
     
     
     
     
     
     
     
      
     
     
     
     
     
     
     
     
     
Interpreting Control Charts
Process Capability
Notes: NOTE: CR is based on the actual standard deviation.
  A CR of 1.00 uses +/- 3 standard deviations and produces 2700
defects per million
  A CR of 1.33 uses +/- 4 standard deviations and produces 63
  defects per million

## Slide 101: Capability Ratios Tolerance Consumption
CAPACITY RATIO TOLERANCE
CONSUMPTION
4.00 25%
3.00 33%
2.00 50%
1.75 57%
1.50 67%
1.33 75%
1.00 100%
0.75 133%
0.50 200%
0.25 400%
Interpreting Control Charts
Notes: Notes

## Slide 102: Check Sheet
Check sheets make it easy to compile and analyze data. They're used to determine how often an event occurs over a designated period of time. Information is usually collected for events as they happen.
Less frequently, check sheets are used to record events that already have occurred. Although check sheets are intended mainly to track (not analyze) data, they often help to indicate why a problem may be occurring.
  All sorts of data can be tracked using check sheets:
  Number of times something happens.
  Length of time it takes to get something done.
  Cost of a certain operation over a period of time.
  Frequency of occurrence -- by unit, program, level, work area, etc.
  Impact of an action over a period of time.
Check Sheet
Notes: Notes

## Slide 103: Check Sheet
Putting it to work:
There are two questions that must be answered when setting up a check sheet:
  What do you want to know?
  What is the most reliable way to collect the data?
Information on a check sheet is usually collected in categories: by work unit code, branch, date, shift, sub process, and so on.
When creating a check sheet, make sure categories are logical and easily understood.
This is important not only for the people who will be interpreting the gathered data, but also for those who use the check sheet to collect the data.
They should not have to make difficult judgments about when and where to enter a check mark on the form..
Check Sheet
Notes: Notes

## Slide 104: Check Sheet Example
Below is a check sheet prepared by a telephone coverage team. Their objective is to tackle the number of callers who had to wait "on hold" when calling a help line.
 | MON | TUE | WED | THU | FRI
8 a.m. to noon | 12 | 4 | 3 | 9 | 2
Noon to 5 p.m. | 10 | 2 | 1 | 4 | 1
TOTALS | 22 | 6 | 4 | 13 | 3
Number of callers "on hold" when calling the help line:
Number of callers "on hold" when calling the help line using an MS Excel generated graph:
Check Sheet
Notes: Notes

## Slide 105: Criteria Rating Form
If you've ever made a major purchase, such as a car or a house, you've probably used a criteria form. Well, maybe you didn't create the actual form, but you most likely went through the exercise in your mind. When buying a vehicle, for example, nearly everyone considers such criteria as cost, mileage, trunk space and safety record.
If you listed these on a sheet of paper and rated (say, on a scale of 1 to 5) the three options you were considering on each of the factor, you'd be constructing a criteria rating form. Adding the scores for each vehicle give you a relative rating of the vehicles under consideration. (See important note on the next page regarding adding
up the numbers of each option). Here's how it would look:
 | OPTIONS |  | 
CRITERIA | VAN | SPORTS CAR | MOTORCYCLE
Trunk Space | 5 | 1 | 1
Mileage | 3 | 4 | 5
Cost | 3 | 3 | 4
Safety Record | 5 | 3 | 2
TOTAL | 16 | 11 | 12
Rating Scale:
5 = Very Good
4 = Good
3 - Fair
2 - Bad
1 - Very Bad
Criteria Rating Form
Notes: Notes

## Slide 106: Criteria Rating Form
Weight: Criteria can be treated equally, or they can be weighted relative to each other.
In the example at the top of the next page, weights have been added to each criteria. They indicate that the vehicle's safety record is three times as important as its cost and gas mileage. And trunk space is twice as important as cost and mileage.
Each scale rating is then multiplied by its respective weight…
  Many times Safety, Laws, and Regulations must be given weight over other issues, even if the customer does not seem to care, Example seat belts, safety glasses, steel toed shoes, motorcycle helmets, etc.
  Customer satisfaction criterion changes as factors such as gas prices changes, etc.
  Thing that are taken for granted are only counted if not included.
Criteria Rating Form
Notes: Notes

## Slide 107: Criteria Rating Form
Follow these steps when creating a criteria rating form:
Decide what factors or criteria are to be considered. Normally, three to six criteria will be sufficient. However, it's up to the team to define the criteria and decide the optimal number. Having too many criteria will seriously complicate the exercise -- without adding much value.
Reach agreement on their definitions.
Agree on the scale to be used ( 1 - 3, 1 - 5, or something else) to rate the options. Determine what (if any) weights should be assigned.
NOTE: Some people prefer not to total the numbers for each option. This way, they guard against the risk that the criteria rating form will become just another mechanism for win-or-lose voting. This tool is not the decision-maker.
 | OPTIONS |  | 
CRITERIA | VAN | SPORTS CAR | MOTORCYCLE
Trunk Space | 5 | 1 | 1
Mileage | 3 | 4 | 5
Cost | 3 | 3 | 4
Safety Record | 5 | 3 | 2
TOTAL | 16 | 11 | 12
Criteria Rating Form
Notes: Notes

## Slide 108: Flow Charts
A flow chart is a picture or graphical representation of a process (sequence of events, steps, activities, or task) which transform inputs into outputs in a system.
  Flow charts are drawn with standard symbols which represent different types of activities or task.
  Many software programs are available to develop flow charts but, Microsoft Word & PowerPoint have most of the capability needed by the beginning Action Teams.
Flow Chart
Notes: Flow charts are also used for training, used as an operating tool, and are extremely useful in ISO documentation to explain processes. Teams use them to benchmark and as an improvement tools.

## Slide 109: Types of Flow Charts
Organization Charts
Total Productive Maintenance
Business Process
Dataflow
Audit
Process
Process Mapping
Schematic
Network
Office
Quality
Quality – ISO
Telecommunication
Din
Types of Flow Chart Palettes include:
Flow Chart
Notes: Notes

## Slide 110: Flow Charting
Many different symbol set are used in flow charting…
Notes: Notes

## Slide 111: Example of Flow Chart
Start
Have
we done
enough
work
is it
a good time
to break?
Take A Break
Continue
Working
Yes
Yes
No
No
Flow Chart
Notes: Notes

## Slide 112: System Flow Charts
Elements of Reliability
Notes: Notes

## Slide 113: Process Flow Charts
Process flow charts are used to show how a manufacturing process is laid out or functions.
How a PC program functions.
Or how a system such as an ordering or shipping system may operate, etc..
Flow Chart
Menu
Notes: Notes

## Slide 114: Force Field Analysis
Force field analysis identifies two sets of forces: those that help you close the gap between where you are now and where you want to be (driving forces), and those that hinder you (restraining forces).
Putting it to work:
  Begin by drawing a horizontal line through the middle of a flip chart. This line represents the current level. For clarity, it's best to write down exactly what "current level" we're talking about - as shown in the example on the right. Also, label the top of the chart "restraining forces" ~ these are keeping the level from moving higher. Label the bottom "driving forces ~ these are pushing up the level.
Notes: Notes

## Slide 115: Force Field Analysis
  Start with the top half of the sheet. Brainstorm all the different restraining forces that are holding or pushing down the current level. Write all ideas above the horizontal line. Next ~ use brainstorming to identify all the positive driving forces. Write these below the line to show that they're pushing up the current level. As a last step, you may be able to combine related items; other items may need additional explanation or clarification.
  Evaluate each factor as assess its relative impact. Use this information to develop specific actions for reducing or eliminating the restraining forces (top half) and increasing or adding to the driving forces (bottom half).
  Use force field analysis to analyze the current level of CI implementation in your department (or division, site, work unit, etc.)
Notes: Notes

## Slide 116: Force Field Analysis
All meetings seen as waste of time
No clear purpose for meetings
People can't get away from their "real work"
Insufficient meeting space
All meetings No one trained in meeting management
Not enough equipment
Restraining Forces
Management support
Training on how to conduct effective meetings
Clear understanding of meeting objectives
Availability of meeting facilitators
People are frustrated with current meeting effectiveness
Adequate meeting facilities
Effectiveness
Of Meetings
Driving Forces
EXAMPLE: To improve the effectiveness of meetings, we'd want to increase the driving forces - or add new ones - while decreasing or eliminating the restraining forces shown above the horizontal line.
Forced Field Analysis
Notes: Notes

## Slide 117: Gantt Chart
The Gantt chart helps to organize an individual or a team's plan for implementing its proposed solution. It documents what is to be accomplished, by whom and when. The chart also allows a group to document the assumptions underlying their plan. For example, if it's based on installation of equipment by May 15, that assumption can be noted. The group can develop contingency plans in case the deadline slips.
Putting it to work:
What occurs before the chart itself is created is crucial to the effectiveness of this tool. Here are the steps:
  Brainstorm all the tasks that need to be carried out as part of implementation.
  Assign responsibility for each task to a team member and/or to people outside the team.
  Decide how long each task will take, when it can be started and when it's to be completed.
  Enter this information on the chart, sequencing and overlapping the various steps as appropriate.
  Document the assumptions on which the plan is based and the contingency plans to implement if those assumptions are not valid.
Gantt Chart
Notes: Notes

## Slide 118: Gantt Chart Example
The Gantt chart below shows part of one team's test implementation. Notice the sheer volume of information you can easily absorb simply by looking at this chart. Consider its value as a tracking tool once implementation is under way.
Gantt Chart
Notes: Notes

## Slide 119
To make a Gantt Chart in Excel first enter the data, leave the A1 cell blank to remind Excel to use the 1st row as series labels
Select the first three columns and open the chart wizard.
Chose the horizontal bar charts and the stacked bar chart. Chose next…

## Slide 120
Label the axis and chose next, your chart will appear as shown.
Notes: Notes

## Slide 121
Double click on the start series to eliminate them. The Format Data Series will appear and in the pattern tab, you will chose none for border and none for area, then click OK.

## Slide 122
We get a chart, but not the one we wish to show the team, we need to change some parameters…

## Slide 123
Double click on the category axis, then check the categories in reverse order box and the value (Y) axis crosses at maximum category, then OK

## Slide 124
Then double click on the date axis and change the number in the minimum box, I chose 39810…

## Slide 125: Gantt Chart Example
This is the result, a Gantt Chart made with Excel
And remember if we put names or initials with the task, we have accountability!

## Slide 126: Gantt Chart Example
A Gantt Chart Example created using Microsoft Project (MSP)
Note (1) the critical path is in red, (2) the slack is the black lines connected to non-critical activities, (3) when using MSP, you must use the task ID when labeling predecessor activities, and (4) since Saturday and Sunday are not work days (as described above) some bars on the Gantt chart are longer if they cut through a weekend.
THE GANTT & PERT are tools used in Microsoft Project Management
Gantt Chart
Menu
Notes: Notes

## Slide 127: Histogram
A histogram is a specialized type of bar chart that shows the distribution of measurement data. It is a snapshot of a data set. A histogram shows the frequency of occurrence and basic information about the data set, such as central tendency (mean, median, and mode). It reveals the amount of variation occurring in the system.
A team uses the histogram to assess the current situation and to study results. The histogram's shape and statistical information help the team know how to improve the system.
Putting it to work:
  Follow these steps when creating a histogram:
  Organize your data set with a frequency distribution table (or check sheet). Data can be individual points or grouped.
  Draw vertical and horizontal axes on graph paper.
  Mark data values along the horizontal axis, from the smallest to the largest; label the axis to indicate what is being displayed and the unit of measurement (such as pounds, minutes, etc.)
  Label the vertical axis and mark values. (This axis is usually labeled "frequency." Or the label can be more specific as in the example on the following page.)
  Using the information in the frequency distribution table, construct vertical bars for each of the values, with height corresponding to frequency.
Notes: Notes

## Slide 128: Histogram - Green Cup O.D.
CONE No. L68149
FREQUENCY
40
35
30
25
20
15
10
5
0
-.0020 -.0017 -.0014 -.0011 -.0008 -.0005 -.0002 .0001 .0004 .0007 .0010 .0013 .0016 .0019
Cell Number
It is easy to see that the greatest frequency bar is the -.0005 measurement and the distribution heavier to the left.
Notes: Notes

## Slide 129: Histogram - Green Cup O.D.
CONE No. L68149
FREQUENCY
40
35
30
25
20
15
10
5
0
-.0020 -.0017 -.0014 -.0011 -.0008 -.0005 -.0002 .0001 .0004 .0007 .0010 .0013 .0016 .0019
Cell Number
LCL
UCL
Center of Spec.
By putting the specification limits on the chart we can see the distribution is not centered, but all the data is within the specifications.
Notes: Notes

## Slide 130: Histogram
Study the shape of the histogram. A normal "bell curve" shape indicates normal variation in the system and a stable, predictable process. Any other shapes in the data are clues to look further for causes of the variance. Calculate mean, median and mode to further analyze the data.
Histograms from several common shapes. A bell-shaped picture is usually a normal distribution and indicates a generally stable system. Any of these other shapes would indicate some special cause of variation and invites further inquiry.
Notes: Notes

## Slide 131: Interviews
The interview is a structured technique for collecting information from individuals or groups, including (perhaps most importantly?) your internal and external customers.
If you have access to the people who have the information you need, interviewing either in person or on the telephone can be a very efficient means of data collection. It's often the best way to learn about your customer's needs and expectations.
Putting it to work:
  Tackle the interview just as a reporter would:
  Before the interview, develop a list of questions. Ideally, this should be done in a group setting. Write down a "clean" version of the question list and take it to the interview.
Interviews
Notes: Notes

## Slide 132: Interviews
Be sure to include follow-up questions to get at the information you really need.
When you conduct the interview, take notes of the responses. Remember to keep listening while you write.
If possible, bring along a note taker who can do the writing -- allowing you to zero in on asking the questions and listening. Also consider bringing a tape recorder.
Stick with the list of questions, but don't get too locked in.
Verify your understanding of the interviewee's responses. Restate what you're hearing and ask whether your interpretation is accurate. (You are seeking information and testing understanding.)
If you're collecting sensitive information, ensure the confidentiality of the responses. Do not use respondents' names, identifiable quotes or other "identifier" information.
Interviews
Notes: Notes

## Slide 133: List Reduction
This tool helps in processing the output of a brainstorming session. The objective is to clarify the items so that all team members understand them and then reduce the items to a manageable number.
Putting it to work: Before the list of items (potential problem areas or solutions) can be shortened, everyone in the group must have a clear understanding of each item.
  The first activity, therefore, is for the leader or facilitator to review the items, asking if anyone needs clarification.
  If so, the suggesting member should be asked to explain in brief what he or she meant by the comment. The discussion shouldn't go beyond simple clarification at this point.
List Reduction
Notes: Notes

## Slide 134: List Reduction
The team then identifies some "filters" - criteria that should be satisfied for an item to remain in consideration. Some filters selecting problems are:
  Does this problem lend itself to being solved by a team?
  Is the problem within our control or influence?
  Is it worth solving?
  Some filters for selecting solutions are:
  Is it likely to solve the problem?
  Is it feasible?
  Can we afford it?
Keeping the agreed upon criteria in mind, group members vote on each item: "yes" if it satisfies the criteria, "no" if it doesn't.
A simple majority (one-half the number of the group, plus one) keeps an item on the list, fewer votes mean the item is bracketed [ ].
List Reduction
Notes: Notes

## Slide 135: Matrix Diagram
A matrix diagram is used to organize various items by showing relationships between the items and the strength of those relationships. It is often used as a tool to allocate tasks or as a way to chart the products or services you provide and your customer expectations of those products or services.
Although there are various ways to configure a matrix diagram, only two, the L-Shaped Matrix and the T-Shaped Matrix, will be mapped out in this book. Both are easy to use and will show relationship between these two items and the strength of that relationship.
Putting it to work:
In the L-Shaped Matrix two groups of interrelated items are charted. One group of items will be input down the first column of the chart and the other across the bottom row of the chart. You also need to decide on the "key" or the symbols that will be used to evaluate the strength of each relationship. Once these tasks have been completed, each intersection needs to be evaluated to see if there is any relationship between the two items and, if there is a relationship, what is the strength (See Example A)
Notes: Notes

## Slide 136: Matrix Diagram
To construct a T-Shaped Matrix you will need to list two groups of items down the first column, one after the other with one row left open between each group. In the row left open between the two sets of items input the third set of items. From this point on, complete the T-Shaped Matrix just like the L-Shaped Matrix discussed earlier.
The T-Shaped Matrix creates an additional leg to the chart and allows for the analysis of three relationships within one chart. While you can still only compare two relationships at a time, the T-Shaped Matrix also lets you infer a third set of relationships. (See Example B).
Notes: Notes

## Slide 137: Nominal Group Technique
The Nominal Group Technique (NGT) is a structured method for working toward consensus. Its strength is that it gives everyone in the team an equal voice in sharing ideas.
Putting it to work:
  NGT unfolds in two phases. In Phase 1, Idea Generation, the team follows these steps:
  Write a statement that describes an established goal, problem, or other subject. Put it on a flip chart or marking board, making sure all participants are focused on the topic and understand it.
  Each participant, working individually, proceeds to list as many ideas as they can in response to the statement.
  Each person in the team can share the ideas, one by one in round-robin fashion. A recorder writes each idea on a flip chart, in full view of everyone. With this format, there's no discussion about the pros, cons or intent of any idea. If a participant's ideas are exhausted, he or she can pass. The round robin continues until all ideas have been recorded. (Do not number the items until later in the process.)
Notes: Notes

## Slide 138: Nominal Group Technique
  If confidentiality is an issue, the written ideas can be passed on to a recorder -who would then write them on the flip chart. This way, there's no way to link specific ideas to specific people.
  To facilitate the next phase of NGT, it's suggested that the recorder leave space between items and that no more than five or six be on a sheet
Phase 2, Priority Setting, is when the group indicates its preferences. Here's how it happens:
  Go over the list and ask for clarifications. Fine-tune the wording as needed.
  Number each of the items starting at the top. Give the same number to items that are similar in content and meaning.
  For lists of 20 or fewer items, give each participant five 3 x 4 Post-It notes. Ask each person to pick the five items that she or he feels are the highest priority.
Notes: Notes

## Slide 139: Nominal Group Technique
  (For lists of 20 to 30 items, you may want to use seven Post-It notes; for lists of 30 or more you may want to use nine.) Instruct participants to write the number of each of their chosen items on the upper right-hand corner of a Post-It not. Also have them put a word or phrase in the middle of the note to describe the item. Remember, each item is on a separate note.
  When the participants are finished, they place their Post-It notes in front of themselves for ranking. Before giving a ranking, each participant should consider what makes this a priority item -- such as cost, value added, and importance and so on.
  Participants are asked to choose the highest priority item form the ones they have selected and to give it the highest number. If each participant has five Post-It notes, this number would be five. The number is written in the lower center of the note and circled. Participants are next asked to select the lowest priority item from the remaining items and to assign it a value of one. Then, of the remaining items, the participants select the highest-priority item and give it a four. This process continues until the other remaining items have been ranked.
Notes: Notes

## Slide 140: Nominal Group Technique
  When participants have finished their rankings, they place each of the Post-It notes on the flip chart --directly next to the corresponding item as written on the flip chart during Phase 1.
  For each numbered item on the flip chart, add the rankings on the Post-It notes and record the total. Then count the number of Post-It notes for each item and record the total.
  The results show the team's ranking of all the items. The item with the largest number of points is deemed to be most important or significant to the team. (Knowing how many Post-It notes was received for a given item can prove useful in the event there's a tie in the rankings.)
  Before finalizing, the team should discuss the results to be sure there were no misunderstandings. Create a table showing (in descending order) the item number, a brief statement of each item, the number of votes it received and the number of participants voting for the item.
Notes: Notes

## Slide 141: Operational Definitions
A operational definition is a clear, concise, and detailed definition of a measure in document form. All data, especially attribute data, which requires assessment or interpretation must be collected, clarified & defined in terms that are consistent and quantifiable.
Example: The item must be “Red” is unacceptable, how many reds are there?
A better definition would be: “The item must be “Fire Engine Red as compared to a specific sample color chip viewed in daylight or under simulated daylight lighting” Associates making this assessment must pass a color blindness test and a performance test”.
  A set of decision making criteria that assures an attribute conforms to requirements or a standard such as a work instruction.
  The basic “who, what, when and where” questions are addressed and documented.
Notes: Notes

## Slide 142: Operational Definition
The Operational Definition provides a tangible or observable explanation of the variable. If the variable is not directly measurable, it identifies characteristics of the variable that can be directly measured. In addition, whether or not the variable can be directly measured, the operational definition names the possible associated elements of the variable that can be measured. For example, self-esteem is a measure of how people feel about themselves we can not see it, It is not directly measurable. An aspects of self-esteem that can be measured and recorded is looks you in the eye when talking, acts confidently, or ask questions, etc. As these are observable and linked to self-esteem.
Notes: Notes

## Slide 143: Operational Definition
The ability to discern between the acceptable and unacceptable
  Operational Definitions allow people to do their jobs better with less confusion
  Yields yes or no answers, do or don’t, etc. conclusions and can be perform consistently based upon requirements and decision criteria.
  Is essential or fundamental to all types of data, but especially for attributes

## Slide 144: Operational Definitions
Variable data should also be collected following operational definitions.
Example: What type of instrument should be used to collect data concerning the roundness of a ball bearing.
Typical questions addressed by an operational definition:
  Type of instrument
  Discrimination of the instrument
  Location or environmental requirements
  Training requirements
Notes: Notes

## Slide 145: Lack of Operational Definitions
Few conclusions can be reached from data collected without an operational definition, which explains criteria such as :
  what was collected
  How it was collected, method, environment, instrument used, etc.
  when it was collected, time, date, frequency, etc.
  who collected it and are they qualified to collect it
Without addressing these issues most data, data based conclusions don’t make since or are ignored by management.
Notes: Notes

## Slide 146: Lack of Operational Definitions
What was collected must be understood ~ example: sports record or data collected 50 years ago were records of amateurs who held jobs and competed without today's technology today it is the records of the pro we are comparing.
How it was collected, method, environment, instrument used, etc. ~ example: 50 years ago stop watches were used versus the “touch wall” technology in swimming events.
When it was collected, time, date, frequency, etc. ~ example: in 50 years history of Olympic Swimming amateurs were replaced with professionals who use super swim suits, in track it may be shoes. In any case a new operational definition including modern equipment, professional trainers, etc., changes the scores…
Notes: Notes

## Slide 147: Lack of Operational Definitions
Who collected it and are they qualified to collect it ~ example: people with prejudice or volunteers with no training, many doing their best under less that perfect conditions, interpreted time pieces and recorded the records on paper, which had to be transcribed into other language to be understood by all, a very time consuming process!
Today “people” develop and administer hands off timing / recording system that automatically time the events, in smaller increments 100th of a second versus 1 second, record the data in pc systems that are monitored for reliability and accuracy! The output of the data is in multiple languages and immediate!
Only like systems should be compared, but understanding system discrepancies allows for some analysis which may need be explained …
Notes: Notes

## Slide 148: Good Operational Definitions
Good operational definitions address the following:
  Characteristic of interest
  Measuring instrument or criterion
  Method of test criterion
  Decision criterion
  Personnel training in collecting and interpreting data criterion.
Notes: Notes

## Slide 149: When are they used
Operational definitions are used when:
  Work instruction are required for the job, as in ISO registration procedures.
  To define and accomplish performance based training needs
  For improvement teams to assure the reliability of data, develop benchmarks, and to assess current work practices against current documentation…
  When data must be visible and questioned by those who view it!
Notes: Notes

## Slide 150: Do…
When Operational Definitions are used :
Identify data that was collected without an operational definition and establish its reliability?
Use operational definitions with every project when defining quality measures and data collection.
Define any new measures added during a project.
Correct current definitions if changes to procedures have been made due to a quality improvement, new technology, etc.
Re-train all concerned associates if needed.
Menu
Notes: Notes

## Slide 151: Pareto Analysis
The Pareto Chart is a form of vertical bar graph that helps to reveal problems by the frequency of their occurrence in a process. As a graphic display, the Pareto Chart draws attention to and enlists cooperation in making improvements. It helps a team set priorities.
It's effective because it graphically demonstrates how seemingly small matters can cause big problems, taller bars represent more significant problems and the shorter bars represent less significant problems. The name of the chart derives from the Pareto principle: 80% of the trouble comes from 20% of the problems.
Pareto diagrams are sometimes shown with a "cumulative line." This represents the percentage sum of the vertical bars, as if they were stacked on each other going from left to right.
Pareto Chart
Notes: Notes

## Slide 152: Pareto Chart
Putting it to work:
Follow these steps when creating a Pareto Chart.
  Select problems to be compared by brainstorming, examining data or other means.
  Select the unit of measurement that appropriately quantifies the problems to be assessed.
  Determine how much time to allow for collection data.
  Draw horizontal and vertical axes on graph paper. On the left-hand vertical axis, label the measurement values in equal increments.
  Order the bars, going from left to right in order of decreasing frequency, or cost, or defects - or whatever is measured on the vertical axis.
  On the horizontal axis, order and label the bars by category, going form left to right in order of decreasing frequency or cost.
  “Other” used to collect misc. or insignificant data is always placed at the end.
Pareto Chart
Notes: Notes

## Slide 153: Pareto Analysis
  To include a cumulative line, label a percentage scale on the right-hand vertical axis, making sure the two axes are drawn to scale.
  Plot the percentage line showing the cumulative total with the addition of each category.
  All categories totaled should reach 100%
Number | Category | Freq. | Percent. | Cumulative Percent.
1 | Loose Trim | 57 | 39.6 | 39.6
2 | Folding Problem | 27 | 18.8 | 58.3
3 | Wobble | 15 | 10.4 | 68.8
4 | Scratched Paint | 15 | 10.4 | 79.2
5 | Color Match | 12 | 8.3 | 87.5
6 | Scratched Top | 12 | 8.3 | 95.8
7 | Other | 6 | 4.2 | 100.0
Pareto Chart
Notes: Notes

## Slide 154: Pareto Chart Example
Compare the frequency or cost (or other measure) of each category relative to all the others.
Example:
The cumulative percentage scale, when used, must match with the dollar or frequency scale. In this case 100% matches the total of 139
By looking at the Pareto Chart shown below, it becomes obvious why application processing is being delayed. Much of the problem would be solved by eliminating the one cause that's most responsible for the problem.
Pareto Chart
Notes: Notes

## Slide 155: Pert Chart
A PERT Chart (Program Evaluation and Review Technique Chart) is a tool used for planning action and is designed to manage time.
PERT Charts show the "critical path" or the minimum elapsed time that is required to complete a project.
Putting it to work:
  Before drawing the actual PERT Chart, you need to identify all the activities in your process or plan. Then put the activities in the order that they must occur. Also, determine if there are any activities that can be completed at the same time. Number each of the activities in the order that they occur, giving the same number to activities that can be completed simultaneously.
  You are now ready to draw the diagram. Place each number in a circle. Connect each of the circled numbers with an arrow. Above each arrow write the activity and below each arrow write the estimated time to complete each activity. Depending on the project, time can be minutes, hours, days or months.
  Once the chart is complete you can see the critical path of your project and the minimum amount of time that will be necessary to complete the project.
Notes: Notes

## Slide 156: PERT charts
This PERT chart follows the “Activity on Arrow” style.
  The tasks are shown by arrows. Task name are shown by letters, in this case.
  The circles are called nodes. The nodes indicate the start or end of tasks.
  Task durations are the shown by the numbers.

## Slide 157: PERT charts
To Calculate the “Critical Path”:
The top route is 1+0.9+2.1+3+1.5=8.5
The middle route is 1+0.9+2.1+2.1+1.5=7.6
The bottom route is 1+1.3+4.2+1.5=8
The top route is the Critical Path as it is the longest.

## Slide 158: Pert Chart
Example:
The PERT Chart below is mapping out the critical path for printing and distributing a new form
1
2
3
4
6
7
5
5
Receive final form to print
Fill out printing request
Send form to printer
Proof Form
Form delivered
Send Form out
Develop mailing list
Prepare Envelopes
1 day
5 day
2 days
2 days
1 day
3 days
3 days
5 days
1 day
3
Notes: Notes

## Slide 159: PERT Chart Lag & Lead Time
Lag Time the minimum amount of time that must pass between the finish of one activity and the start of its successor's).
  For example, if task A is laying a house’s concrete slab, and dependent task B is putting up the house walls, there would need to be some lag time between the end of task A and the start of task B to let the concrete set.
Lag time is shown in a PERT chart as an arrow with a duration but no task assigned to it.
Lead time Occurs when a task should theoretically wait for its predecessor to finish, but can actually start a little early. The time that the tasks overlap is lead time.
  E.g. when replacing computers in a computer lab, you could actually start bringing in the new computers while the old ones were being packed up and moved out.

## Slide 160: Pert Chart
An example of a critical path calculation using Microsoft Project.
The Critical path is shown in red as it is the longest path…
Notes: Notes

## Slide 161: Relationship Diagram
Some questions must be examined to see if relationships exist and are best understood if displayed properly using a descriptive geometry tool, such as a Venn Chart or a relationship diagram
  A Venn Diagram is a graphic arranger that is made up of two or more overlap circles.
  In mathematics, Venn diagrams are used to visualize the relationship between two or more sets of data.
  Venn diagrams can also be used to match up the characteristics of various items, like groups or individual people, text books, or actions, etc.
Relationship Diagram
Notes: Notes.

## Slide 162: Relationship Diagram
13 Clubs in
a deck of
52 Cards
4 Jacks in
a deck of
52 cards
Question: If we asked the question in a card game “What is the Probability of drawing a Jack or a Club?” we could show it mathematically or with a Venn chart. Which is quicker to digest?
Mathematically the probability of drawing a Club or a Jack: P(C or J) = P(C) +P(J) – P(Jack of Clubs) 13/52 + 4/52 – 1/52 = 16/52 = .307 OR…
Jacks 4/52
Clubs 13/52
1 card can be a Both a Jack & a Club, the Jack of Clubs
1 of 52 cards in the deck
13 Clubs and 4 Jacks would indicate that there are 17 chances, but one of the cards is both a Jack and a club so we only have 16/52 or .307 percent probability
Notes: Notes. I surmise this depends on you background, the mathematician would go one way and the other s would prefer the latter.

## Slide 163: CSCC Relationship Diagram Example
Notes: Notes

## Slide 164: Relationship Diagram
Downloadable Chart Templates from Microsoft owners of PowerPoint 2007
Relationship Diagram
When things get complex the diagram is worth 1000 words…
Notes: Notes.

## Slide 165: Run Chart
The Run Chart is used when we simply wish to see how the frequency of measures, such as is recorded in a histogram, occur over time.
If this data is needed to analyze control of the process several methods are used depending on the source, that is whether we have variable measurements or using attributes, (pass/fail, good/bad, etc.) Simply calculating the control limits transforms the run chart into a control chart.
Notes: Notes

## Slide 166: Run Chart
A run chart displays trends within observation points over a specified time period. It can be used to monitor a process to see whether or not the long-range average is changing.
  Run charts are easy to construct and use. Points are plotted on the graph in the order in which they become available. It is common to graph the results of a process such as delays, errors, rework and so on as they vary overtime.
  A danger in using a run chart is the tendency to see every variation in data as being important. The run chart, like other charting techniques, should be used to focus attention on truly vital changes in the process.
  For example, when monitoring any process, it is expected that we should find an equal number of points falling above and below the average. When six or more points "run" on one side of the average, it indicates a statistically unusual event.
  Such changes should always be investigated. If the shift is favorable, it should be made a permanent part of the system. If it is unfavorable, it should be eliminated.
Notes: Notes

## Slide 167: Run Chart
Putting it to work:
At its most basic; the run chart is nothing more than a single line showing a single measurement over time. Here are several key points:
Notes: Notes

## Slide 168: Run Charts
The run chart is a line graph of data plotted over time.
  The plotted data can be variable (measurements) or attribute (counts) data.
  The purpose of the run chart is to look at a systems behavior over time.
  Trends or patterns can be easily seen and analyzed.
  Can be used as a baseline.
  By adding control limits it becomes a control chart, which tells you if the process is in or out of control.
Notes: Notes

## Slide 169: Run Charts
Run Charts are easily made using Microsoft Excel & Chart Wizard.
Notes: Notes

## Slide 170: Run Charts
By adding upper and lower control limits the chart shows a process that is not in control or predictable
Notes: Notes

## Slide 171: Sampling
Sampling may be:
  A survey of a select population of people
  A taste test for a batch of beer, ice-cream, etc.
  A color match from a batch of paint
  A hardness test of a lot of steel products
  A lot size for a control chart
Sampling
Sampling is that part of statistical practice concerned with the selection of individual observations intended to yield some knowledge about a population of concern, mainly for the purposes of statistical deduction.
Sample measurements of one or more properties (length, location, etc.) are used to describe the population it came from
Notes: Notes

## Slide 172: Sampling
Sampling is the tool that guides the quantitative study of a system.
Sampling is used to reduce cost
Sampling is used to improve statistical accuracy
Sample frequency depends on:
  The process shape
  How fast a process changes
Sampling
Notes: Notes

## Slide 173: Sampling
Because sampling is a mental process of deciding how much data to collect and how often to gather it, it is difficult to picture.
Using a “Data Gathering Form” gives us a starting Place.
What Data | How | How Much | How Often | Where | Method | Who
Sampling
Notes: Notes

## Slide 174: Sampling Steps
The following steps assures that the system to be improved has been described, a flow chart has been developed, and the data to be gathered has been determined and operationally defined.
  Determine the question you are asking of the data
  Determine the frequency (how often) of the sampling
  Determine the actual frequency times
  Select the subgroup (sample size) for variable or attribute data.
Sampling
Notes: Notes

## Slide 175: Determine the question you are asking of the data…
The following data will be used to answer different questions?
Sampling
Notes: Notes

## Slide 176: How the students compare weekly?
Sampling
Notes: Notes

## Slide 177: Is there any difference weekly
Sampling
Notes: Notes

## Slide 178: Is there a difference between students?
Sampling
Notes: Notes

## Slide 179: Scatter Diagram
A scatter plot reveals relationships or association between two variables. Two variables with a strong relationship will follow closely to a straight line. Plots with little or no association will be scattered or loosely follow some pattern.
Note in the plot above how a straight line comfortably fits through the data; hence a linear relationship exists. The scatter about the line is quite small, so there is a strong linear relationship. The slope of the line is positive
(small values of X correspond to small values of Y; large values of X correspond to large values of Y), so there is a positive co-relation (that is, a positive correlation) between X and Y.
Positive Correlation
Scatter Diagram
Notes: Notes Source in part to nist.gov

## Slide 180: Scatter Diagram
This sample plot reveals a linear relationship between the two variables indicating that a linear regression model might be appropriate.
Note in the plot above how for a given value of X (say X = 0.5), the corresponding values of Y range all over the place from Y = -2 to Y = +2. The same is true for other values of X. This lack of predictability in determining Y from a given value of X, and the associated amorphous, non-structured appearance of the scatter plot leads to the summary conclusion: no relationship.
Scatter Diagram

## Slide 181: Negative Correlation Between X & Y
Note in the plot above how a straight line comfortably fits through the data; hence there is a linear relationship. The scatter about the line is quite small, so there is a strong linear relationship.
The slope of the line is negative (small values of X correspond to large values of Y; large values of X correspond to small values of Y), so there is a negative co-relation (that is, a negative correlation) between X and Y.
Negative Correlation
Scatter Diagram

## Slide 182: Exponential Relationship.
Note that a simple straight line is grossly inadequate in describing the relationship between X and Y.
A quadratic model would prove lacking, especially for large values of X. In this example, the large values of X correspond to nearly constant values of Y, and so a non-linear function beyond the quadratic is needed. Among the many other non-linear functions available, one of the simpler ones is the exponential model
for some A, B, and C. In this case, an exponential function would, in fact, fit well, and so one is led to the summary conclusion of an exponential relationship.
Scatter Diagram

## Slide 183: MS Excel Scatter Diagram Example
1.) Enter the data with
the independent or controllable data in the first column
2.) Open the Chart Wizard and pick the XY Scatter Diagram
3.) After making your choice choose next
Notes: Notes

## Slide 184: MS Excel Scatter Diagram Example
The Source Data Box will appear, then highlighting the data will fill in the data range and create the chart.

## Slide 185: Scatter Diagram
Clicking on the data points allow you to add a trend line
Clicking on the scale allow you to edit the scale
Clicking on titles allows you to edit titles
Notes: Notes

## Slide 186: Stratification
Stratification deals with the separating data from mixed source that has been combined to show the total output of a system.
  Unfortunately the fix or improvement of the system may be a particular process, shift, or training/experience issue, etc.
Stratifying the data into units, such as the parts of the system flow cart, machines that produce parts or even work shifts may reveal where to concentrate our efforts

## Slide 187
Days
Evenings
Days Only

## Slide 188
By stratifying the data we get a clear picture of which shift has the bigger problem
Notes: Notes

## Slide 189: SURVEY
Surveying is much like interviewing - but on paper. Instead of responding to interviewers, people answer items on a questionnaire.
The major advantage is that you can get a great deal of information from a lot of people very economically. The downside is that people may interpret the questions somewhat differently than intended. Their answers may be ambiguous as well, and there's no opportunity to test understanding.
Putting it to work:
Follow these simple steps to ensure a successful survey:
  Identify the information you need.
  Decide who has this information in its most reliable form.
  Plan how you will use the information when you have it in hand.
  Develop a series of questions that will enable respondents to provide the information accurately and unambiguously.
  Keep the questionnaire short, simple and clear.
  Try out the questions with several people to uncover any unclear questions. Conduct several "test surveys" to work out the bugs.
  Questionnaires can be "closed" with a limited number of responses from which to choose
  Example: How long have you worked in your present job? Circle one:
Less than 1 yr. 1 - 3 years more than 3 years
Notes: Notes

## Slide 190: Beginning Steps in Developing an Attitude Instrument
Review literature in the domain which you wish to measure (i.e., "computer attitudes")
Develop a list of categories (subscales) that you wish to sample from the domain. The domain may be "Computer Attitudes" and the categories may be "ease of use of computers" and "usefulness in education".
Write 8 to 10 items/statements (operational definitions) for each category (i.e., "Computers will help students learn material faster."). Avoid common survey pitfalls when writing your statements.
Give the items to at least 5 experts for classification (Content Validity). The panel of experts will attempt to match the operational definitions with their appropriate categories within the domain.
Develop an instrument with the successfully classified items. Use a Likert scale to design your instrument. You may wish to rewrite some of the items that were not successfully classified.
Field test the instrument (6 to 10 people per item on the instrument) with the populations for which the instrument is being developed.
Run a factor analysis (exploratory) on the field test responses. More advanced students may wish to do a confirmatory factory analysis.
Name each factor (category) based on the items which loaded on it (>.40)
Review whether each item conceptually belongs with its factor (subscale) and remove those which do not.
Run Cronbach's Alpha Reliability for each factor/category (subscale) to investigate internal consistency reliability.
Modify and retest the instrument if necessary (alpha<.70).
Notes: Source: Del Siegle, Ph.D. Neag School of Education - University of Connecticut del.siegle@uconn.edu www.delsiegle.com

## Slide 191: Likert Scale
AGREEMENT
The following choices may help you when you design an attitude instrument.
The Red Face sets are the most popular.
Notes: Source: Del Siegle, Ph.D. Neag School of Education - University of Connecticut del.siegle@uconn.edu www.delsiegle.com

## Slide 192: Likert Scale
FREQUENCY
Very Frequently Frequently Occasionally Rarely Very Rarely Never | Always Very Frequently Occasionally Rarely Very Rarely Never | Always Usually About Half the Time Seldom Never | Almost Always To a Considerable Degree Occasionally Seldom
A Great Deal Much Somewhat Little Never | Often Sometimes Seldom Never | Always Very Often Sometimes Rarely Never | 
Notes: Source: Del Siegle, Ph.D. Neag School of Education - University of Connecticut del.siegle@uconn.edu www.delsiegle.com

## Slide 193: Likert Scale
IMPORTANCE
Very Good Good Barely Acceptable Poor Very Poor | Extremely Poor Below Average Average Above Average Excellent | Good Fair Poor
QUALITY
Notes: Notes

## Slide 194: Likert Scale
LIKELIHOOD
Notes: Source: Del Siegle, Ph.D. Neag School of Education - University of Connecticut del.siegle@uconn.edu www.delsiegle.com

## Slide 195: Example:
Converting a Likert Scale survey into a Quantifiable Data Source.
As it is we can get a view of what the student thought of the sample questions, but how would you quantify it as is?
An example of a simple technique: First let’s assign numbers giving 5, the heaviest weight to Always and (0) to never…
  Always = (5)
  Very Frequently = (4) Occasionally = (3)
  Rarely Very = (2)
  Rarely = (1)
  Never = (0)
The top score is 5 and we have 9 lines or a total of 45 points for a perfect score
Looking down the form we see instead of Xs 2, 4, 2, 3, 4, 4, 5, 4, and 5
which equals 33 We then calculate the acceptance measurement 33/45=.7333 or 73%
Notes: Notes

## Slide 196: Systematic Diagrams
A systematic (or tree diagram) is a graphic representation of the different levels of actions (or means) used to accomplish a broad goal.
  The purpose of making a systematic diagram is to generate the most specific level of action items that can be implemented to accomplish a broader goal.
  Implementation of these action items sets off a “domino effect” that leads to the accomplishment of the main goal
Systematic Diagrams
Notes: Notes

## Slide 197: Systematic Diagrams
An improvement team uses a systematic diagram to generate action items to test an improvement theory, standardize an improvement, or plan for continuous improvement It is used when:
  A broad task or goal becomes the focus of the team’s work
  The action plan to accomplish the goal or task is likely to be complex
Systematic Diagrams
Notes: Notes

## Slide 198: Systematic Diagrams – Step1
How is it Made:
1. Record the Problem or Goal Statement.
The problem or goal statement can come from several different sources. I can be a root cause determined in a relationship diagram, a category identified in an affinity diagram, or and original issue.
Record the problem or goal statement to the for left of side of an area such as a flip chart.
“Develop a complete curriculum and support it”
Systematic Diagrams
Notes: Notes

## Slide 199: Systematic Diagrams – Step 2
2. Generate the first level of items.
Through team discussion, generate the first level of items for the diagram. It is helpful to ask the question “What needs to happen to achieve this goal or solve a problem”
  Keep the first level broad and avoid jumping to action items.
Systematic Diagrams
Notes: It is important to progress through the levels logically, the first level of items is the “means”
Source QUAL 150 lectures & text from PQ Systems

## Slide 200: Systematic Diagrams – Step 3
3. Complete the systematic diagram under each major path.
For each first level item identified continue to ask the question “What needs to happen to achieve this goal or solve a problem”
  Continue asking the question for each level until you reach specific action items to the right…
Systematic Diagrams
Notes: Notes
Source QUAL 150 lectures & text from PQ Systems

## Slide 201: Systematic Diagrams – Step 4
4. Study the systematic diagram
The diagram is only effective if the implementation of action items will accomplish the next level of items, and so on until the goal is achieved.
Starting from the right and ask “will this set of items achieve the next highest level”?
Systematic Diagrams
Notes: Why, What, Who, When and Where?
Asking “Why” brings us to Root Cause.
Asking “What” develops action items to accomplish goals and solve problems.
Asking “Who assesses resources and assigns responsibility.
Asking “When” develops a time frame or plan.
Asking “Where” localizes or set criteria for implementation of an action item.
Source QUAL 150 lectures & text from PQ Systems

## Slide 202: Systematic or Tree Diagram
Downloadable Chart Template from Microsoft owners of PowerPoint 2007
Notes: Notes

## Slide 203: Open Survey Example
Or the survey questions can be "open" Example:
How do you use the information combined in the monthly progress report?
COMBINED PETTY CASH/LOCAL TRAVEL QUESTIONNAIRE Please take a minute to answer the following questions, then leave the survey on the table in the back of the room before you leave. It there's an area of concern that has not been covered, please let us know. Thanks for your time and valued input! |  | 
1. Do you like the concept of combining Petty Cash and Local Travel on one form? | YES | NO
2. Do you feel you would have occasion to use both sections of the combined form for one transaction? | YES | NO
3. Do you like the uniform handling and signature area? | YES | NO
4. Do you like the uniform size of the combined form? | YES | NO
5. Do you feel there is an advantage with this uniform size combination for filing purposes. | YES | NO
6. Do you like the idea of a total mileage concept vs. listing separate trips for Local Travel. | YES | NO
How much time do you feel this new form will save you on a monthly basis?______ *___ *Indicate minute or hours. |  | 
COMMENTS: |  | 

## Slide 204: Variable Control Charts
The X-Bar & R Chart
When the process is variable measurements comparable and traceable to a standard, such as the Metric System or English Inch, etc. and the data will be used to control a process we would use the X-Bar & R when subgroups are less than 10 or the X-Bar & S Chart when subgroups are 10 or more.
Notes: Notes

## Slide 205: Variable Chart
In Variable Control Charting two charts are need to show the true nature of a process that is the centering of the process and it’s width.
  With the X-Bar & R chart the X-Bar or  charts the center of the process or subgroup averages. X-bars are used to assess long term capability.
  The R charts the width of the process and the  represents the average of the of the R’s. R-Bars are used to calculate standard deviation.
  Six standard deviations divided into specifications = Short Term Capability
Notes: Notes

## Slide 206: Variable Control Chart Data
Subgroup | X1 | X2 | X3 | X4 | X-bar | UCL-X-ar | X-D-bar | LCL-X-bar | R | UCL-R | R-bar | LCL-R
1 | 6.35 | 6.4 | 6.32 | 6.37 | 6.36 | 6.47376 | 6.4099 | 6.34604 | 0.08 | 0.1999 | 0.0876 | 0
2 | 6.46 | 6.37 | 6.36 | 6.41 | 6.4 | 6.47376 | 6.4099 | 6.34604 | 0.1 | 0.1999 | 0.0876 | 0
3 | 6.34 | 6.4 | 6.34 | 6.36 | 6.36 | 6.47376 | 6.4099 | 6.34604 | 0.06 | 0.1999 | 0.0876 | 0
4 | 6.69 | 6.64 | 6.68 | 6.59 | 6.65 | 6.47376 | 6.4099 | 6.34604 | 0.1 | 0.1999 | 0.0876 | 0
5 | 6.38 | 6.34 | 6.44 | 6.4 | 6.39 | 6.47376 | 6.4099 | 6.34604 | 0.1 | 0.1999 | 0.0876 | 0
6 | 6.42 | 6.41 | 6.43 | 6.34 | 6.4 | 6.47376 | 6.4099 | 6.34604 | 0.09 | 0.1999 | 0.0876 | 0
7 | 6.44 | 6.41 | 6.41 | 6.46 | 6.43 | 6.47376 | 6.4099 | 6.34604 | 0.05 | 0.1999 | 0.0876 | 0
8 | 6.33 | 6.41 | 6.38 | 6.36 | 6.37 | 6.47376 | 6.4099 | 6.34604 | 0.08 | 0.1999 | 0.0876 | 0
9 | 6.48 | 6.44 | 6.47 | 6.45 | 6.46 | 6.47376 | 6.4099 | 6.34604 | 0.04 | 0.1999 | 0.0876 | 0
10 | 6.47 | 6.43 | 6.36 | 6.42 | 6.42 | 6.47376 | 6.4099 | 6.34604 | 0.11 | 0.1999 | 0.0876 | 0
11 | 6.38 | 6.41 | 6.39 | 6.38 | 6.39 | 6.47376 | 6.4099 | 6.34604 | 0.03 | 0.1999 | 0.0876 | 0
12 | 6.37 | 6.37 | 6.41 | 6.37 | 6.38 | 6.47376 | 6.4099 | 6.34604 | 0.04 | 0.1999 | 0.0876 | 0
13 | 6.4 | 6.38 | 6.47 | 6.35 | 6.4 | 6.47376 | 6.4099 | 6.34604 | 0.12 | 0.1999 | 0.0876 | 0
14 | 6.38 | 6.39 | 6.45 | 6.42 | 6.41 | 6.47376 | 6.4099 | 6.34604 | 0.07 | 0.1999 | 0.0876 | 0
15 | 6.5 | 6.42 | 6.43 | 6.45 | 6.45 | 6.47376 | 6.4099 | 6.34604 | 0.08 | 0.1999 | 0.0876 | 0
16 | 6.33 | 6.35 | 6.29 | 6.39 | 6.34 | 6.47376 | 6.4099 | 6.34604 | 0.1 | 0.1999 | 0.0876 | 0
17 | 6.41 | 6.4 | 6.29 | 6.34 | 6.36 | 6.47376 | 6.4099 | 6.34604 | 0.12 | 0.1999 | 0.0876 | 0
18 | 6.38 | 6.44 | 6.28 | 6.58 | 6.42 | 6.47376 | 6.4099 | 6.34604 | 0.3 | 0.1999 | 0.0876 | 0
19 | 6.35 | 6.41 | 6.37 | 6.38 | 6.3775 | 6.47376 | 6.4099 | 6.34604 | 0.06 | 0.1999 | 0.0876 | 0
20 | 6.56 | 6.55 | 6.45 | 6.48 | 6.51 | 6.47376 | 6.4099 | 6.34604 | 0.11 | 0.1999 | 0.0876 | 0
21 | 6.38 | 6.4 | 6.45 | 6.37 | 6.4 | 6.47376 | 6.4099 | 6.34604 | 0.08 | 0.1999 | 0.0876 | 0
22 | 6.39 | 6.42 | 6.35 | 6.4 | 6.39 | 6.47376 | 6.4099 | 6.34604 | 0.07 | 0.1999 | 0.0876 | 0
23 | 6.42 | 6.39 | 6.39 | 6.36 | 6.39 | 6.47376 | 6.4099 | 6.34604 | 0.06 | 0.1999 | 0.0876 | 0
24 | 6.43 | 6.36 | 6.35 | 6.38 | 6.38 | 6.47376 | 6.4099 | 6.34604 | 0.08 | 0.1999 | 0.0876 | 0
25 | 6.39 | 6.38 | 6.43 | 6.44 | 6.41 | 6.47376 | 6.4099 | 6.34604 | 0.06 | 0.1999 | 0.0876 | 0
Notes: Notes

## Slide 207: Plotted Data & Calculated Control Limits & Process Center
X-double Bar = 160.25 = 6.41
25
LCLx-bar = 6.41 - .729 * .0876 = 6.35
UCLx-bar = 6.41 + .729 * .0876 = 6.47
X-Bar Chart Trial Limits
Notes: Notes

## Slide 208: Plotted R or Range Chart, Calculated Average & Trial Control Limits
LCL R-bar = 0 *.0876 = 0
UCL R-bar = 2.282 * .0876 = .20mm
Notes: Notes

## Slide 209: Eliminating Assignable Cause Data from Average or X-Bar Chart
Notes: Notes

## Slide 210: Eliminating Assignable Cause Data from R or Range Chart
Notes: Notes

## Slide 211: Weighted Voting
This tool enables teams to quantify the various positions and preferences of team members. It differs from criteria rating forms in two ways: first, no decision factors or criteria are used; second, individual member's votes are recorded, there is no discussion or effort to reach agreement on a single number.
Using a flip chart, set up a grid as shown on the right, with the options listed horizontally and team members listed vertically. Give each person a number of votes to distribute in accordance with their preferences. As a rule of thumb, the number of votes should be about 1/2 times the number of options.
Team Members | Option 1 | Option 2 | Option 3
Totals |  |  | 
Members then decide how to distribute their votes among the options to indicate their relative preferences. Keep in mind these few guidelines:
Encourage people to spread their votes to represent their relative feelings about the options, rather than lump all their votes on a single favorite.
Notes: Notes

## Slide 212: Weighted Voting
Have members decide how they will distribute their votes (preferably jotted down on paper) before any votes are recorded on the chart.
  Ask members to show their votes for each option all at once by raising the number of fingers that represent their vote.
  Ask for and record votes by option, not by person. That is, call for the votes for the first option, the second and so on. Record all the votes so the team can see where agreements and disagreements occur.
  Weighted voting does not make decisions. It merely provides information about where individual members stand and how strongly. This information makes it easier to bring opposing viewpoints to the surface. This must be done if consensus is to be achieved.
Notes: Notes

## Slide 213: Weighted Voting
NOTE: Some people prefer not to total the numbers for each option.
This way, they guard against the risk that weighted voting will become just another mechanism for a win-or-lose outcome.
This tool, like the criteria rating form, is not the decision-maker. The team is the decision-maker.
Regardless of whether you total the numbers, the most important thing is that you use weighted voting as a vehicle for moving more closely to consensus.
Team Members | Option 1 | Option 2 | Option 3 | Option 4
Jim | 2 | 1 | 2 | 1
Clara | 1 | 0 | 1 | 4
Susan | 3 | 1 | 1 | 1
Justin | 4 | 1 | 1 | 0
Mark | 2 | 1 | 1 | 2
Frank | 1 | 1 | 3 | 2
TOTAL | 3 | 5 | 9 | 10
A team can readily see that option 3 and 4 outweigh the other options, but a cost, risk analysis, safety issues, or even alignment issues may be decision breakers…
Notes: Notes

## Slide 214: Why Technique or Root Cause Analysis
"WHY" TECHNIQUE
Some of the tools for continuous improvement require number-crunching, graphing and analysis -- but not all of them. Perhaps one of the most powerful tools is also one of the most basic. It has less to do with number crunching and more to do with simple curiosity. We refer to that old standby question: "Why?“
By asking "why," you can peel back the layers to discover the root cause of a problem. This may require you to ask "why" more than once -- sometimes as many as five to six times. Keep probing to find why the symptom (or "effect") is occurring. You'll eventually come to the root cause.
The process is also called “Root Cause Analysis”
Notes: Notes

## Slide 215: Why Technique or Root Cause Analysis Example
1ST LAYER | WHY aren't supply orders filled in time? Because the supplies are not in stock. |  |  |  | 
 | 2nd LAYER | WHY aren't the supplies in stock? Because the supply shipment has not been received. |  |  | 
 |  | 3rd LAYER | WHY hasn't the supply shipment been received? Because the order was placed late. |  | 
 |  |  | 4TH LAYER | WHY was the order placed late? Because the order / request for supplies takes 3 weeks to get approved. | 
 |  |  |  | 5th LAYER THE ROOT CAUSE | WHY does the order / request for supplies take 3 weeks to get approved? Because it is in transit for 12 days, going from one approval authority to another (total approvals needed = 5).
PROBLEM: SUPPLY ORDERS AREN'T FILLED ON TIME
Notes: Notes

## Slide 216: Why Technique Example
"WHY" TECHNIQUE + TREE DIAGRAM
Sometimes you may want to use the Why Technique in conjunction with a tree diagram. This will provide a little more structure to the Why Technique and help you identify various root causes.
Putting it to work:
Once you have identified a problem ask the question "Why did this problem occur?" (This is your first layer).
Then take the answer to that question and ask the question again. Continue to do this until you have uncovered the possible root causes of the problem. It may be necessary to ask "why" several times before you uncover all the root causes (see example on next page)
Notes: Notes

## Slide 217: Why Technique Example
WHY? | WHY? | WHY? | WHY?
 | Orders not received on time |  | 
Supply orders are not filled on time | Not enough staff | Person not on disability Two vacancies | 
 | Supplies Not in | Shipment not received | Supply shipments are late Didn't get order in on time Supply order was lost
 | Orders no complete | Order form is complicated Lack of training to fill out the form properly | 
WHY AREN'T SUPPLY ORDERS FILLED ON TIME
This shows the use of the Why Technique with the Tree Diagram.
Notes: Notes

## Slide 218: Why Technique Example
Deal with that within our power & communicate without fear that which must be dealt with at a higher level!
Notes: Notes

## Slide 219: Why Technique Example
A “why technique” that combines some affinity diagramming structure and classification…
Notes: Notes