## Slide 1: Lecture 2 ENGT 1200 Introduction to Industrial & System Engineering
“History of the Lean Machine” Selecting & Sequencing
Notes: Notes

## Slide 2: Lecture Objectives
Define the history of the mass manufacturing system.
Define the Ford Model T a car made for manufacture!
Define the Ford Model T a car that was user friendly!
Define the achievement of interchangeable parts and its relationship to metrology, value, & reliability!
Define the achievement of the interchangeable worker and its relationship to value & reliability!
Define the history of the Toyota/lean manufacturing system.
Describe the key figures in developing the Toyota Manufacturing System.
Define tools essential to the system.
Notes: Notes

## Slide 3
Notes: Notes

## Slide 4: Metrology, Value, & Reliability
Metrology, Value, & Reliability are the foundation of all the world class quality systems such as Lean Manufacturing, Six Sigma, ISO/QS/TS Registration Programs, etc.
The book “The Machine That Changed The World” is the story of Lean Manufacturing and a history of the development of the Automobile which starts with the history of mass production…
Notes: Notes

## Slide 5: The Rise of Mass Production
The beginning
In 1894, the Honorable Evelyn Henry Ellis a wealthy member of English Parliament went to Paris to buy a car.
  There were no English dealerships nor manufactures.
  There were no French dealerships nor manufactures of cars as we know then today
Notes: Notes

## Slide 6: Mass Production
Ellis went to the Paris machine tool company of Panhard et Levassor and commissioned an automobile. P&L is little known today, but:
  P&L was the worlds leading car company in 1894
  In 1887 Emile Levassor met Gottlieb Daimler known today as the founder of Mercedes-Benz
  Levassor negotiated a license to manufacture Daimlers new “high-speed” gasoline engine…
Notes: Notes

## Slide 7: Mass Production
By the early 1890s P&L was producing several hundred cars a year, but no two were alike…
Different contractors made the parts using different gauges/measuring processes…
Heat treating warped the parts…
Panhard- Levassor (1890-1895)
When the parts arrived at arrived at P&L they could only be described as close or approximate and needed to be “Fitted” to work…
Notes: Notes

## Slide 8: Mass Production
Fitted is described as “hand fileing” in the 1890s, that is taking first two parts to be fitted, finding the part that was too big, as you can not add stock with a file, and using the hand file to make it fit…
Then the third part needed to be fit to the first two, then the fourth to the first three, and the fifth to the first four…
Emile Levassor’s
First Car
The sequential fitting produced what we call to day “Dimensional Creep” and resulted in significant production variation car to car…
Notes: Notes

## Slide 9: Mass Production
Henry Ford and the Quadricycle, 1896.
The story of mass production did not begin with Henry Ford, but he should be credited with its perfection and success… Ford manufacturing beginning with the original Model A in 1903 and the quest for mass production also began
1908 Model T
Ford was very much an assembler and bought engines and chassis from the Dodge brothers until 1931, his early focus was the perfection of interchangeable parts, assembly lines, tools that could cut hardened metals and interchangeable workers

## Slide 10: Skilled Fitters vs. the Assembler
Prior to 1908 the skilled fitters average task cycle took 514 minutes or 8.46 hours to assemble a car and each worker would assemble a large part of the car before repeating the task cycle. After 1908 it was reduced to 2.3 minutes.
The Model T made its debut in 1908 with a purchase price of $825.00. Over ten thousand were sold in its first year, establishing a new record.
Four years later the price dropped to $575.00 and sales soared. By 1914, Ford could claim a 48% share of the automobile market.
Most of this due to interchangeable Parts, which
allowed the moving assembly line to be introduced.

## Slide 11: Skilled Fitters vs. the Assembler
By 1913 with the introduction of the moving assembly line which cost less than $3,500.00 to install.
The assembler did not need to move and the average cycle time was reduced to 1.9 minutes.
the movement of the line enforced the cycle time!
It reduced human effort.
Reduced the inventory of parts waiting to be assembled.
Other examples of production improvement were in 1913 it took 594 minutes to produce an engine, but only 226 in 1914. In 1913 an Axle took 150 minutes and only 26.5 in 1914.
Notes: Notes

## Slide 12: Skilled Fitters vs. the Assembler
Savings due to interchangeable parts, time to assemble and work in progress constantly reduced the cost of the car…
Notes: Notes

## Slide 13: Mass Production
By 1915 Ford had perfected the interchangeable worker at the newly built Highland Park Plant where 7000 workers newly hired at the Detroit facility came directly from or were right off the boat and new to the United States.
A survey revealed that more than 50 languages were spoken in plant, but workers need only accomplish the task at their work station on the moving assembly line…It took years to train the skilled worker, but only 5 minutes to show the assemble how to do their job!
The more skilled worker was removed from production and concentrated on the production and maintenance of fixtures and tools…

## Slide 14: 1913 Assembly Line
Here the chassis and body are assembled at the end of the 1913 line.
Notes: Notes

## Slide 15: The Model T
The Model T was Henry Ford’s twentieth design over a five year period that began with the original Model A. With the Model T Ford achieved two objectives
  He had designed a car for manufacture
  He had designed a car that was user friendly
These two point are the basis for his success and far outweigh the prominence given to the assembly line…
Notes: Notes

## Slide 16: Myths
No one really knows if Henry Ford said that “you can have Model T Fords "in any color, so long as it's Black”?
This was only true after 1913, as earlier cars were available in green, red, blue and grey. In fact, in the first year, Model T Fords were not available in black at all!
The switch to all black cars in 1913 was due to Ford's ongoing obsession with cost and price reduction, a value issue, and was not, as is generally believed, to reduce drying time or increase production.

## Slide 17: Design for Manufacture
The design for manufacture was achieved through Henry Fords obsession with using standard gauging systems and measurements to achieve interchangeable parts.
  He insisted on working to a gauge
  He worked to reduce needed parts
  He realized the payoff on simplicity of parts and the savings to be realized in assembly
This was the groundwork for “Reliability Engineering” and reduced the cost of an automobile significantly a Value Engineering issue…
Notes: Notes

## Slide 18: Design for Use
The friendly use of the Model T was by design and he achieved an unprecedented ease of operation and maintenance for the day.
  He assumed his buyer would be a farmer with modest tools and mechanical skill…
  He wrote the Model T’s owners manual in a question-and-answer form. In sixty four pages he explained how owners could use simple tools to solve any of the 140 problems likely to crop up with the car…
Notes: Notes

## Slide 19: Customer Focus
Identifying the customer and the environment the product would be use in this book was a great seller or the product.
As there were no paved roads in most towns or any in the country the Model T was indeed the first SUV.
The distance to a dealer or repair shop was an issue to be solved.
The vehicle was to be used as a replace a horse and as a tool…
Notes: Notes

## Slide 20: Sample Page Example
“Fords competitors were amazed at the designed-in reparability”
Notes: Notes

## Slide 21: Design For Use
For example, owners could remove cylinder-head carbon, which cased knocking and power loss, from chamber roofs and piston crowns by removing by fifteen cap screws that held the cylinder head and use a putty knife as a scraper.
Unlike any other manufacturer, if a part needed replacement the owner could buy a spare at a Ford dealer and simply screw or bolt it on. With Ford Model T parts there was no fitting needed.
Design for use achieved a second innovation “Value Engineering.” These principals allowed for the Ford mass production system to work.
Notes: Notes

## Slide 22: Many Accessories Became Available…
Notes: Notes

## Slide 23: The Affect on Businesses!
The start of second source parts was mainly because of the success and the volume of the Model T.
Everyone realized that making it more useful, more reliable, or easier to operate would result in a profit and more jobs…
Mass Production had started…
Mass Production was the dominate manufacturing system in the world until 1950 when Toyoda Manufacturing System was introduced.
Notes: Notes

## Slide 24: The Term Lean
Lean in the manufacturing environment also refers to the Toyota Production system established by the Toyota Corporation, originally the Toyoda Automatic Loom Works.
• Sakichi Toyoda, born in 1867, invents the wooden Toyoda handloom in 1890 Sakichi Toyoda was the inventor of automatic looms who founded the Toyota Group.
• He invented a loom in 1902 that would stop automatically if any of the threads snapped. His invention opened the way for automated loom works where a single operator could handle dozens of looms.
Notes: Notes

## Slide 25: Toyoda History & Lean
Within the organization, four prominent gentlemen are credited with developing the system:
Sakichi Toyoda, who founded the Toyoda Group in 1902;
Kiichiro Toyoda, son of Sakichi Toyoda, who headed the automobile manufacturing operation between 1936 and 1950;
Eiji Toyoda, Managing Director between 1950 and 1981 and Chairman between 1981 and 1994; and
Taiichi Ohno, the Father of the Kanban System.
1936 AA Sedan
1930 Kiichiro Toyoda experiments with gasoline engines.
1933 Automobile Department is established in Toyoda Automatic Loom Works, Ltd.
Notes: Notes

## Slide 26: 1937 Toyoda Become Toyota
The family name Toyoda means “abundant rice fields” in Japanese.
A contest to make a distinction between the two family businesses, but many believe to be a publicity stunt was conducted, and the name “Toyota” was the winner…
The name Toyota has no meaning in Japanese and only takes 8 strokes to write which is considered lucky, versus the ten stokes needed to write Toyoda!
The last and perhaps most significant motivation why "Toyota" was preferred was because Japanese people feel that it has a clearer sound than "Toyoda".

## Slide 27: Japan 1945
Effects of conventional bombing campaign on major Japan cities.
Imagine a country the size of California that looked like New Orleans after Katrina…
Notes: Notes

## Slide 28: Toyoda Post WWII History & Lean
Eiji Toyoda, a nephew of Sakichi Toyoda, joined the Toyoda Automatic Loom Works family business after graduating from the University of Tokyo in 1936.
In 1950, Eiji was named Managing Director of the Toyoda Automotive Works when the Japanese government forced Kiichiro Toyoda into reorganizing the Toyoda Group.
The forced reorganization separated the family businesses and resulted in the resignation of Kiichiro and his entire staff.
Koromo Plant (currently Honsha Plant) starts operations. "Just-in-time" system launches on a full-scale basis.
Notes: Notes

## Slide 29: Toyoda Post WWII History & Lean
The history of Kiichiro Toyoda contribution to Toyoda was considered a failure but warrants a closer look…
In 1930 the Japanese Government urged the company to build trucks for the war effort & hindered their efforts to develop or produce a car.
The War itself put the company at risk and they were scheduled to be targeted by B29s when the war ended narrowly escaping destruction.
Post war Japan was in chaos with new laws, new freedoms and changes in the workforce for the employees…
In thirteen years of effort by 1950 they had produced a total of 2,685 cars, Ford was producing 7000 a day!
Notes: Notes

## Slide 30: Toyota Production System
Post World War II, Most of Japan & Toyota were almost bankrupt.
Factories, power systems, communication systems, were mostly destroyed.
Manpower was limited as a result of the WWII casualties.
Between 1945 &1950 Japan under military occupational rule endured turbulent times…
In the spring of 1950 Eiji Toyoda spent 3 months at the Ford Rouge Plant in Detroit. His Uncle Kiirhiro had visited in 1929. The Japanese greatly admire the Mass Production System accredited to Ford & believed it was a major reason for the loss of WWII

## Slide 31: Toyota Production System
Post war demand was low and minimising the cost per unit through economies of scale was inappropriate. This led to the development of demand-led pull systems.
The Japanese could not afford the expensive mass production facilities of the type used in the USA so they instead focused on reducing waste and low cost automation.
Likewise, Toyota could not afford to maintain high inventory levels.
Under Eiji Toyoda leadership and his collaboration with Taiichi Ohno and Shigeo Shingo the world was about to change.
Notes: Notes

## Slide 32: 1955
In 1955 the competitive edge held by the United States had all but ran its course as most of the world were using the mass manufacturing system devised by Henry Ford.
The exception was Japan, which was a champion of the system, but could not make it work
Eiji Toyoda, unlike most Japanese, realized mass manufacturing would not work in Japan and must devise way to use resources better.
without the elimination of waste and the essential conservation of recourses a system would not work...
Two of the best engineers in Japan working in this endeavor were Toyota employees

## Slide 33
Taiichi Ohno
(1912 ~ 1990)
Shigeo Shingo
1909 ~ 1990
Founders of the Toyota Production System (TPS)

## Slide 34: Taiichi Ohno
The man who did the most to structure the Toyota Production System as an integrated framework was Taiichi Ohno.
In the late 1940s, Ohno was in charge of a machining shop.
He experimented with various ways of setting up the equipment to produce needed items in a timely manner.
But he got a whole new perspective on just-in-time production when he visited the United States in 1956.
Notes: Notes

## Slide 35: Taiichi Ohno
Ohno went to the United States to visit automobile plants, but his most important U.S. discovery was the supermarket. Japan did not have many self-service stores yet, and Ohno was impressed. He marveled at the way customers chose exactly what they wanted and in the quantities that they wanted. Ohno admired the way the supermarkets supplied merchandise in a simple, efficient, and timely manner.
In later years, Ohno often described his production system in terms of the American supermarket
Notes: Notes

## Slide 36: Taiichi Ohno
Using the super market format Ohno devised the
Pull System, which driven by the needs of the following lines.
It contrasted with conventional push systems, which were driven by the output of preceding lines.
Ohno developed a number of tools for operating his production format in a systematic framework.
The best known of those tools is the kanban system, which provides for conveying information in and between processes on instruction cards.
Notes: Notes

## Slide 37: Taiichi Ohno
Western methods to supply the needed stamped part to build a car and save time on changeovers was to simply buy more presses and dedicate them to a specific part…
Ohno knowing the capital was not available to match this solution.
Using a few presses he devised a plan to stamp a whole car
His idea was to develop simple die-change techniques and change dies frequently
Starting in the late 1940s by the late 1950s he had reduce change-over from a day to 3 minutes.
Change-over specialist were eliminated and accomplished by the operator.
Notes: Notes

## Slide 38: Shigeo Shingo
Poka-yoke (pronounced POH-kah YOH-kay) is Japanese for mistake-proofing.
These devices are used either to prevent mistakes that result in defects, or to cheaply inspect each item that is produced to determine whether it is acceptable or defective.
Shigeo Shingo was one of the industrial engineers at Toyota who has been credited with creating Zero Quality Control (ZQC), an approach to quality management that relies heavily on the use of poka-yoke devices.

## Slide 39: Poke Yoke Examples
Gas pumps are equipped with hose couplings that break-away and quickly shut-off the flow of gasoline.
Garage door openers have two safety features that prevent toys, people, or pets from being crushed by a closing door:
a contact safety reverse feature, which opens the door if it hits a person or object, and
an infrared beam across the doorway that causes the door to reverse automatically if a person or pet who passes through the beam.

## Slide 40: Toyota Production System
Toyoda, Ohno, & Shingo along with Deming, Juran, Etc.; working continuously changed the manufacturing system, the workforce, the supply chain, and the service system to develop the Toyota Production system. The text does a good job:
Telling how we developed the systems we have today…
Defining the problems the “Big Three” face to change their systems…
Describing the Benchmarks and the Gaps to be eliminated…
Notes: Notes

## Slide 41: Just-in-Time Manufacturing
Toyota had fully worked out the principles of Lean Production by 1960 and most of Japans auto firms followed their lead.
In 1960 Japan had around 6% share of the worlds motor vehicle production.
By 1980 they had almost 30% of the worlds vehicle production
The text outlines circa 30 years of history laced with events and circumstances that took them a different path and why Toyota developed into todays benchmark for manufacturing!
1957 Toyota USA Established

## Slide 42: JIT Just-in-Time Manufacturing
“In the broad sense, an approach to achieving excellence in a manufacturing company based upon the continuing elimination of waste (waste being considered as those things which do not add value to the product). In the narrow sense, JIT refers to the movement of material at the necessary time. The implication is that each operation is closely synchronised with subsequent ones to make that possible”
APICS Dictionary 1987.
JIT became part of Lean Manufacturing after the publication of James Womack’s
The Machine that Changed the World in 1991

## Slide 43: An American Paradigm
Ford and the Toyoda’s forged empires in the days when paradigms were explained by “its always been that way”. They were big thinkers not afraid to explore new frontiers…
The following is the story of a young navel officer that changed the world. Perhaps you’ve not heard of him?

## Slide 44: The Spanish American War 1898
As a young naval artillery
officer William Sowden Sims changed the world through a process we now call reengineering

## Slide 45
In the late 1800’s the process of reengineering was alive and well. After 100 years and the invention of the buzz word the obstacles in getting an organization to recognize the
need for reengineering have changed little.
Case in point - During the Spanish American War the U.S. Navy fired 9,500 shells Only 121 of these shells, or 1.3 percent, hit anything.

## Slide 46
After firing at a target one mile away for 25 Minutes two hits were registered, neither of which were considered fatal.
This in fact was considered state of the art gunnery, or “World Class Performance” of the day in 1898.
In a display of its prevailing leadership in naval gunnery the U.S. Navy held an exhibition target practice to benchmark it’s performance.

## Slide 47
By 1902 the U.S. navy could hit a similar target every time it fired; half the shells could hit a square 50 inches on each side.
What caused this remarkable change in so short of a time was not new technology, but a young naval officer, William Sowden Sims.
It could be said that Sims changed the world through a process we now call “Reengineering”

## Slide 48
Sims discovered a simple way to dramatically improve the gun aim which would compensate for height and timing of the ships roll without adding cost.
First adjustment of the gear ratio so that gunners
could follow the target easily throughout the ships
roll
Second moving the gun sight from the gun barrel
to a location removing the gunner from the smoke
and recoil of the gun and giving them the ability
to follow a target during the act of firing.

## Slide 49
Originally his ideas were ignored by the then navigator controlled U.S. Navy.
The reasons for rejection included:
If it could be done a navigator would have though of it.
If it could be done someone would already be doing it.
If it is done how would it impact the current structure
of the Navy?
In other words the people in control would lose control.

## Slide 50: Today
“Today empowerment as used in the Lean Manufacturing Systems to eliminate the waste of manpower and enhance Continuous Improvement Processes is a recognized philosophy/tool that uses the synergy of teams to maximize efficiency”
                William Hughes

## Slide 51: GAME THEORY
Game Theory: the analysis of a situation involving conflicting interests (as in business or military strategy) in terms of gains and losses among opposing players.
Merriam-Webster
Sometimes we need a little help in deciding to get into the game! Lets use math to decide and have a little fun!

## Slide 52
PROBLEM STATEMENT
1. PLAY A GAME 100 TIMES
2. DRAW A SINGLE DIGIT RANDOM NUMBER
3. RULES: IF 0,1,2,3,4,5, THEN LOSE $1.00
IF 6 OR 7 THEN LOSE $5.00
IF 8 OR 9 THEN WIN $10.00
Notes: Game Theory is an actual course of study
It assigns both probability and costs to courses of action

## Slide 53
PROBLEM SOLUTION
1. IF 0,1,2,3,4,5 THEN LOSE PERCENT = 60
2. IF 6 OR 7 THEN LOSE PERCENT = 20
3. IF 8 OR 9 THEN WIN PERCENT = 20
4. THEREFORE:
EXPECTED VALUE = .60(-1.00) + .20(-5.00) + .20(10.00)
EXPECTED VALUE = (-.60 -1.00 +2.00)
EXPECTED VALUE = $0.40
$0.40 x 100 PLAYS = $40.00
Notes: The answer can be determined mathematically
On the average a player should win $0.40 per play
If the game is played 100 times, $40.00 should be won

## Slide 54: Funny Math!
A Farmer who had 3 sons died…In his will he stated that his first born son should get 1/2 the horses, The second son 1/3 the horses, and the third son, who was not a good worker 1/9 the horses.
The lawyers problem was the farmer had 17 horses. How did he divide the herd?

## Slide 55
Graphical Solution to Decision Making
Cabinet Shop Revenue Optimization
A furniture company only produced tables and hutches, but needs to maximize production to achieve maximum revenue!
Notes: The solution of this problem is NOT intuitive!

## Slide 56
Graphical Solution to Decision Making
Cabinet Shop Revenue Optimization

## Slide 57
Graphical Solution to Decision Making
Cabinet Shop Revenue Optimization

## Slide 58
Graphical Solution to Decision Making
Cabinet Shop Revenue Optimization

## Slide 59
Graphical Solution to Decision Making
Cabinet Shop Revenue Optimization

## Slide 60
Graphical Solution to Decision Making
Cabinet Shop Revenue Optimization
Notes: Notice that combined revenue first increases and then decreases.
The maximum point of 48,000 is at 300 hutches and 400 tables.

## Slide 61: End of The History of the Lean Machine and Sequencing and Selection.
Notes: Notes