## Slide 1: Lecture 13 ~ ENGT 1200 Introduction to Industrial and Systems Engineering
Pareto Diagrams, Bar Charts, & Scatter Diagrams

## Slide 2: Bar Chart
A Bar Chart differs from a Frequency Chart and is made up of columns plotted on a graph, used to display:
The X Axis as categorical variables
The Y Axis as a scale representing the size of the individual column variables.
Example: This chart pictures the per capita income for Four States
Per Capita by State

## Slide 3: Histogram
Both Bar Charts and Histograms can be made using the Bar Chart Wizards. The difference in the charts are:
The Histogram columns represent quantitative variables.
The x axis column labels can be a range of variables or a single variable
The y axis represents size of the individual columns defined on the x axis.

## Slide 4: The Difference Between Bar Charts & Histograms
The difference is with bar Charts each column represents a group defined by a category variable; and with Histograms, each column represents a group that is a quantitative variable.
Another distinction is that skewness of a Bar Chart is not considered as it is categorical, not quantifiable.

## Slide 5: Frequency vs. Cumulative Frequency
In a data set, the Cumulative Frequency for a value x is the total number of scores that are less than or equal to x. The examples below illustrate the difference:
Both charts show scores for a test administered to 300 students
The Frequency Chart shows number of students in groups that could represent A, B, C, & D, grades and failure grades.
The Cumulative Frequency Chart shows that 30 student receive a score of 50 and 60 students received at most 60, 120 received at most 70, etc.
Test Score for 300 Students

## Slide 6: Pareto Analysis
The Pareto Chart is a form of vertical bar graph that helps to reveal various topics/problems by the frequency of their occurrence in a process. As a graphic display, the Pareto Chart draws attention to and enlists cooperation in making improvements.
It helps a team set priorities.
It's effective because it graphically demonstrates how seemingly small matters can cause big problems, taller bars represent more significant problems and the shorter bars represent less significant problems.
The name of the chart derives from the Pareto principle derived by J. M. Juran: 80% of the trouble comes from 20% of the problems.
Pareto diagrams are sometimes shown with a "cumulative line." This represents the percentage sum of the vertical bars, as if they were stacked on each other going from left to right.
Pareto Chart
Notes: Notes

## Slide 7: Pareto Chart
Putting it to work:
Follow these steps when creating a Pareto Chart.
  Select problems to be compared by brainstorming, examining data or other means.
  Select the unit of measurement that appropriately quantifies the problems to be assessed.
  Determine how much time to allow for collection data.
  Draw horizontal and vertical axes on graph paper. On the left-hand vertical axis, label the measurement values in equal increments.
  Order the bars, going from left to right in order of decreasing frequency, or cost, or defects - or whatever is measured on the vertical axis.
  On the horizontal axis, order and label the bars by category, going form left to right in order of decreasing frequency or cost.
  “Other” used to collect misc. or insignificant data is always placed at the end.
Pareto Chart
Notes: Notes

## Slide 8: Pareto Analysis
  To include a cumulative line, label a percentage scale on the right-hand vertical axis, making sure the two axes are drawn to scale.
  Plot the percentage line showing the cumulative total with the addition of each category.
  All categories totaled should reach 100%
Number | Category | Freq. | Percent. | Cumulative Percent.
1 | Loose Trim | 57 | 39.6 | 39.6
2 | Folding Problem | 27 | 18.8 | 58.3
3 | Wobble | 15 | 10.4 | 68.8
4 | Scratched Paint | 15 | 10.4 | 79.2
5 | Color Match | 12 | 8.3 | 87.5
6 | Scratched Top | 12 | 8.3 | 95.8
7 | Other | 6 | 4.2 | 100.0
Pareto Chart
Notes: Notes

## Slide 9: Pareto Chart Example
Compare the frequency or cost (or other measure) of each category relative to all the others.
Example:
The cumulative percentage scale, when used, must match with the dollar or frequency scale. In this case 100% matches the total of 139
By looking at the Pareto Chart shown below, it becomes obvious why application processing is being delayed. Much of the problem would be solved by eliminating the one cause that's most responsible for the problem.
Pareto Chart
Notes: Notes

## Slide 10: Figure 13-7 Pareto Chart of Problems Related to the Instrument Panel
Figures 13-7 & 13-8 from the text shows that the same data can show different problems by changing the Y Axis 13-7 shows frequency of occurrence and the next slide 13-3 shows Cost.
Notes: Notes

## Slide 11: Figure 13-8 Costs of Instrument Panel Problems
Notes: Notes

## Slide 12: Figure 13-10 Glove Box
Pareto Data may originate in a Brainstorming session or from a Check Sheet, but to display it and decide which elements to focus on to maximize our improvement, the Pareto is the tool of choice…
Notes: Notes

## Slide 13: Figure 13-11 Pareto Chart of Problems Related to the Glove Box Latch
It is clear that fixing Broken & Misadjusted will solve most of the problems found. Then Binds is next…
Notes: Notes

## Slide 14: Pareto diagrams
  Developed by Alfredo Pareto (1848-1923)
  Recognized for it’s universal application to many fields by Dr. Joseph Juran
The Pareto diagram is used to identify the most important problems.
Usually 80 percent of the total results from 20 percent of the items.
Notes: Notes

## Slide 15: Pareto Chart of Problems Related an Instrument Panel
The Pareto Chart is used to prioritize or show that which happens most frequently. We can choose that which happens most to fix first…
Notes: Notes

## Slide 16: Minitab Pareto Chart Example 3
Open Minitab then choose the “File Tab”
Choose the Minitab “EXC-QC File” then “Open”

## Slide 17: EXH-QC File Data
Imagine you work for a company that manufactures dolls. Lately, you have notice that an increasing no of dolls are being rejected at final inspection due to scratches, peels, and smidges in the paint. You want to see if a relationship exist between the type and number of flaws and the work shift producing the dolls.
The data for this exercise is in columns C16-7 “Flaws” &C18-T “Period”
Notes: Notes

## Slide 18: Stratified Pareto Chart Example
In the Stat Tab we choose “Quality Tools” the “Pareto Chart”. We pick “Chart defects data in:” then type Flaws in the first dialog box & Period in the second as shown, then click OK
Notes: notes

## Slide 19: Stratified Analysis the Data
We get a chart with the shifts & weekends stratified for our analysis.
The data reveals the Night Shift is producing more flaws overall.
Most of which are due to scratches and peels.
Focus on the night shift for the greatest improvement results!
The shift and largest problem is very visual for the first round of improvement…
Notes: Notes

## Slide 20: Stratification
Stratification is a technique used in combination with other data analysis tools.
When data from a variety of sources or categories, Example various shifts have been lumped together, the meaning of the data can be impossible to see.
This technique separates the data so that patterns can be seen.
Notes: Source http://asq.org/learn-about-quality/data-collection-analysis-tools/overview/stratification.html

## Slide 21: Making Pareto Diagrams with Microsoft Excel 2010
Since doing Pareto Diagrams in Excel 2010 is a bit complicated, here is a summary of what to do:
Sort the data and create the cumulative percentage values as described in the 2007 video or this PowerPoint Presentation
Make a column graph using both the frequency and cumulative % (you will get 2 sets of columns).
Right click on the cumulative % columns (note, if they are too short to grab, temporarily reduce the max value on the y-axis scale - right click on the y-axis, choose Format Axis, and under Axis Options click 'fixed' and enter a value)
Choose Series Options and select Plot Series on Secondary Axis - (once this is done, you can change the max value on the primary y axis back to 'automatic')
Right click on the cumulative % columns again
Choose Change Data Series Chart Type and select Line with Markers

## Slide 22: Open the “table 2-12” file

## Slide 23: Sort Data
1. Highlight & 2. choose the Sort Tool to Sort the Data, 3. choose Sort by Frequency and 4. Largest to Smallest…
1
2
3
4

## Slide 24: Macros
Going back to our data we have a % for each item, but we need a Cumulative Percent. We make a new column and our first item is equal to C2.

## Slide 25: Copy Macro
If we grab the little box at the bottom right hand corner and pull down to D11 Excel copies the formula in D3 and results in a calculated Cumulative Percent up to 100%
1
2

## Slide 26: Highlight Data & Make Chart
1. Choose the Insert Tab then…2. We Highlight the Cause & Frequency Data. Then we only want the Cumulative Percent, so we 3. Hold Down the Control Key and Highlight Cumulative Percent as shown
Then 4. we choose a Column and pick a 2D Clustered Column…
1
2
3
4

## Slide 27
We get a chart, but need to change the Cumulative %, which is hard to see, to a line

## Slide 28
We need to 1 right click on the Cumulative % and choose Format Data Series, 2 Then Change the Primary Axis to 3 Secondary Axis
1
2
3

## Slide 29
The results is a messy bar chart…

## Slide 30
We still don’t have what we want so we Change to the 1 Insert Tab 2 left click on a Data Bar, 3 Choose Scatter, the Scatter with Straight Lines and Markers..
1
2
3

## Slide 31
And we get a Pareto Chart that needs both Labeled and Formatted

## Slide 32
Expanding the Chart and opening the Chart Tools allows us to see that the Percent Scale can be reduce to 100% and the Chart Titled & Major Axis can be labeled to

## Slide 33
1
2
In Chart Tools Layout Tab, we 1. Choose Chart Title and place a title at the top, the 2. choose Axis Titles and format the primary axis as shown….Now we only need to change the percent column to 100% as we have learned making a histogram…

## Slide 34: Changing Percent Scale
2
1. Left Click on the Percent Data and choose Format Axis…2. Change the Maximum to 1.0 and close…
1

## Slide 35
1
2
1. Choosing the Move Chart in Chart Tools Design and 2. Titling the sheet we get…

## Slide 36
We have a Pareto Chart, the title tab at the bottom and a file that can be saved…

## Slide 37: What is a Scatter Diagram?
A graph showing the pairs of plotted values of two factors, one that is believed to be Independent or Controlled Factor, such as speed of a car and is plotted on the X axis.
The other believed to be the Dependent Factor, such as gas mileage is plotted on the Y axis.

## Slide 38: What does it look like?
Besterfield, D.H., QUALITY CONTROL 6/E, ©2000. Electronically reproduced by permission of Pearson Education, Inc., Upper Saddle River, New Jersey.
This plot shows a negative relationship as when the car speed is increased the gas mileage decreases

## Slide 39: When is it used?
When you want to test whether the performance of one factor is related to the performance of another?
Are the two factors
  a quality characteristic (system performance measure) and a factor you suspect affects it, OR
  two related quality characteristics, OR
  two factors suspected of relating to the same quality characteristic
  In the end it only shows if a relationship exist!

## Slide 40: Scatter Diagram Interpretation
When interpreting a scatter diagram, you are looking to see if there is a correlation or relationship between the two factors.

## Slide 41: WARNING!
A correlation Does Not mean that there is a cause and effect and one will change the other!
For example, if you found a positive correlation between income level and heart disease, would you conclude that having money causes heart disease?
No! You would then dig further to see what behaviors people with more money engage in which causes their heart disease. Look for the Relationship…

## Slide 42: Scatter Diagram
A scatter plot reveals relationships or association between two variables. Two variables with a strong relationship will follow closely to a straight line. Plots with little or no association will be scattered or loosely follow some pattern.
Note in the example plot how a straight line comfortably fits through the data; hence a linear relationship exists. The scatter about the line is quite small, so there is a strong linear relationship. The slope of the line is positive
(small values of X correspond to small values of Y; large values of X correspond to large values of Y), so there is a positive co-relation (that is, a positive correlation) between X and Y.
Positive Correlation
Notes: Notes Source in part to nist.gov

## Slide 43: Scatter Diagram
This sample plot reveals a linear relationship between the two variables indicating that a linear regression model might be appropriate.
Note in the plot above how for a given value of X (say X = 0.5), the corresponding values of Y range all over the place from Y = -2 to Y = +2. The same is true for other values of X. This lack of predictability in determining Y from a given value of X, and the associated amorphous, non-structured appearance of the scatter plot leads to the summary conclusion: no relationship.

## Slide 44: Negative Correlation Between X & Y
Note in the plot above how a straight line comfortably fits through the data; hence there is a linear relationship. The scatter about the line is quite small, so there is a strong linear relationship.
The slope of the line is negative (small values of X correspond to large values of Y; large values of X correspond to small values of Y), so there is a negative co-relation (that is, a negative correlation) between X and Y.
Negative Correlation

## Slide 45: Types of relationships you may find:
(d) Negative Correlation May Exist
(e) Correlation by Stratification
(f) Curvilinear Relationship
Besterfield, D.H., QUALITY CONTROL 6/E, ©2000. Electronically reproduced by permission of Pearson Education, Inc., Upper Saddle River, New Jersey.

## Slide 46: Positive and Negative Correlation
Positive Correlation: The correlation in the same direction is called positive correlation. If one variable increase other is also increase and one variable decrease other is also decrease. For example, the length of an iron bar will increase as the temperature increases.
Negative Correlation: The correlation in opposite direction is called negative correlation, if one variable is increase other is decrease and vice versa, for example, the volume of gas will decrease as the pressure increase or the demand of a particular commodity is increase as price of such commodity is decrease.
No Correlation or Zero Correlation: If there is no relationship between the two variables such that the value of one variable change and the other variable remain constant is called no or zero correlation.
Source http://www.emathzone.com/

## Slide 47: Exponential Relationship.
Note that a simple straight line is grossly inadequate in describing the relationship between X and Y.
A quadratic model would prove lacking, especially for large values of X. In this example, the large values of X correspond to nearly constant values of Y, and so a non-linear function beyond the quadratic is needed. Among the many other non-linear functions available, one of the simpler ones is the exponential model
for some A, B, and C. In this case, an exponential function would, in fact, fit well, and so one is led to the summary conclusion of an exponential relationship.

## Slide 48: How is it made?
Draw and label the horizontal and vertical axes
Scale each axis the, the independent factor on the X axis and the dependent on the Y axis
Plot the points
Interpret the scatter diagram

## Slide 49: Graph the data
After you have created your axes, plot each data pair as a single point - find the value of the first datum in the pair on the x-axis, find the value of the second datum on the y-axis and plot the point at the location where these two values meet
Because the data is collected & recorded, pairs, it is important to keep the pairs together and in order (don’t mix them up or sort them)

## Slide 50: Microsoft Excel
A scatter graph may be created by hand on graph paper, or you can use Excel
If using Excel remember to put your XY data in columns just like you say it!
X in the first column and Y in the second column…

## Slide 51: MS Excel Scatter Diagram Example
1.) Enter the data with
the independent or controllable data in the first column, this will be the X axis and the dependent data in the second column is the Y axis
2.) Open the Chart Wizard and pick the XY Scatter Diagram
3.) After making your choice choose next
Notes: Notes

## Slide 52: MS Excel Scatter Diagram Example
The Source Data Box will appear, then highlighting the data will fill in the data range and create the chart.

## Slide 53: Scatter Diagram
Clicking on the data points allow you to add a trend line
Clicking on the scale allow you to edit the scale
Clicking on titles allows you to edit titles
Notes: Notes

## Slide 54
End of Lecture 13 ~ Introduction to Industrial & Systems Engineering