## Slide 1: Lecture 12 ~ ENGT 1200 Introduction to Industrial & Systems Engineering
Problem Solving Tools: Check Sheets, Histograms, Box Plots

## Slide 2: Check Sheet
Check sheets make it easy to compile and analyze data. They're used to determine how often an event occurs over a designated period of time. Information is usually collected for events as they happen.
Less frequently, check sheets are used to record events that already have occurred. Although check sheets are intended mainly to track (not analyze) data, they often help to indicate why a problem may be occurring.
  All sorts of data can be tracked using check sheets:
  Number of times something happens.
  Length of time it takes to get something done.
  Cost of a certain operation over a period of time.
  Frequency of occurrence -- by unit, program, level, work area, etc.
  Impact of an action over a period of time.
Notes: Notes

## Slide 3: Check Sheet
Putting it to work:
There are two questions that must be answered when setting up a check sheet:
  What do you want to know?
  What is the most reliable way to collect the data?
Information on a check sheet is usually collected in categories: by work unit code, branch, date, shift, sub process, and so on.
When creating a check sheet, make sure categories are logical and easily understood.
This is important not only for the people who will be interpreting the gathered data, but also for those who use the check sheet to collect the data.
They should not have to make difficult judgments about when and where to enter a check mark on the form..
Notes: Notes

## Slide 4: Check Sheet Example
Below is a check sheet prepared by a telephone coverage team. Their objective is to tackle the number of callers who had to wait "on hold" when calling a help line.
 | MON | TUE | WED | THU | FRI
8 a.m. to noon | 12 | 4 | 3 | 9 | 2
Noon to 5 p.m. | 10 | 2 | 1 | 4 | 1
TOTALS | 22 | 6 | 4 | 13 | 3
Number of callers "on hold" when calling the help line:
Number of callers "on hold" when calling the help line using an MS Excel generated graph:
Notes: Notes

## Slide 5: Check Sheet Troubleshooting
A manufacture of oven doors had a problem with dents and scratches so the made a drawing of a door and asked inspectors to put an S in the location found on the drawing for every scratch seen and a D at any dent location seen…
S
S
S
S
S
S
S
S
S
S
D
D
D
S
D
At the end of a short period the observed many S’s in the same location and concluded they had a process problem… They observed D’s in random locations and concluded this was a handling problem
They Check Sheet told them where to look!
Notes: Notes

## Slide 6: Figure 13-42 Check Sheet
This Check Sheet Example is a candidate for a Pareto Chart which will show that the Material not ordered and the Materials late are the biggest problems shown and where fixing them will give the greatest improvement results
Notes: Notes

## Slide 7
Green O.D. Size Histogram
CONE L68149
This histogram for the outside dimensions of a tapered bearing cone is tolerance in four decimal places along the x axis.
We can readily see the process width and the frequency of where the data falls…
Notes: Notes

## Slide 8
Green O.D. Size Histogram
CONE L68149
Cell Number
Notes: Notes

## Slide 9: Histogram
A Histogram is a specialized type of bar chart that shows the distribution of measurement data. It is a snapshot of a data set.
A Histogram shows the frequency of occurrence and basic information about the data set, such as central tendency (mean, median, and mode). It reveals the amount of variation occurring in the system.
Key words that tell you when a Histogram is the Chart of Choice are:
  Need to know the Frequency…
  Need to See the Shape of Data.
  Need to see how data is dispersed.
  Need to see if a change has occurred in data.
Notes: Notes

## Slide 10: Histogram
A team uses the histogram to assess the current situation and to study results. The histogram's shape and statistical information help the team know how to improve the system.
Putting it to work:
  Follow these steps when creating a histogram:
  Organize your data set with a frequency distribution table (or check sheet). Data can be individual points or grouped.
  Draw vertical and horizontal axes on graph paper.
  Mark data values along the horizontal axis, from the smallest to the largest; label the axis to indicate what is being displayed and the unit of measurement (such as pounds, minutes, etc.)
  Label the vertical axis and mark values. (This axis is usually labeled "frequency." Or the label can be more specific as in the example on the following page.)
  Using the information in the frequency distribution table, construct vertical bars for each of the values, with height corresponding to frequency.
Notes: Notes

## Slide 11: Histogram - Green Cup O.D.
CONE No. L68149
FREQUENCY
40
35
30
25
20
15
10
5
0
-.0020 -.0017 -.0014 -.0011 -.0008 -.0005 -.0002 .0001 .0004 .0007 .0010 .0013 .0016 .0019
Cell Number
In this Example it is easy to see that the greatest Frequency Bar is the -.0005 measurement and the Shape of the Distribution heavier to the left.
Notes: Notes

## Slide 12: Histogram - Green Cup O.D.
CONE No. L68149
FREQUENCY
40
35
30
25
20
15
10
5
0
-.0020 -.0017 -.0014 -.0011 -.0008 -.0005 -.0002 .0001 .0004 .0007 .0010 .0013 .0016 .0019
Cell Number
LCL
UCL
Center of Spec.
Later when we Lecture on Capability in Engineering Statistics we will see that by putting the specification limits on the chart we can see the distribution is not centered, but all the data is within the specifications.
Notes: Notes

## Slide 13: Creating a Histogram
If creating a paper chart versus using Microsoft Excel, which is used in the MECH 2270 Course, and is an industry standard!
The first question usually asked is how many bars should I use and the answer will depend more on the text you use then any mathematical solution? The Juran Handbook suggest in table 23.8 “Number of cells in frequency distribution”:
Number of observations | Recommended number of cells
20-50 | 6
51-100 | 7
101-200 | 8
201-500 | 9
501-1000 | 10
Over 1000 | 11 to 20
What’s most important here is consistency so that comparing Histograms over time is not biased by inconsistent visual differences by switching number of cells.
Describe how do it in a Operational Definition or Work Instruction…

## Slide 14: Figure 13-16 Histogram Cell Description
In cell terminology, Each cell is like a bucket and the cell boundary describes what fits in that bucket…Changing the number of bars will affect the bucket size, midpoints, etc. affecting the shape of the histogram.

## Slide 15: Figure 13-15 Tally Sheet for Thickness of Clutch Plate
The example given in the text gives a picture that rotated counter clock wise would look like a histogram, but this method is really time consuming and there is a better way…
Notes: Notes

## Slide 16: Figure 13-17 Clutch Plate Thickness Histogram
The last cell contains all measurements between 0.06306 & 0.06335
The Cell midpoint is 0.0632

## Slide 17: Determining Width of Class Interval
Taking a page from our MECH 2700 Applied Statistics text and how we do it…
We have a data base of fish lengths in mm we with to display as a Histogram.
First we need to sort the data fro smallest to largest and find it measures from 292mm to 457mm
The Range of this data is 457-292=165mm
165 bars is way to many bars but 5, 6 or 7 bars will give us a good Histogram to display our data…
Choosing 6 bars we divide 165/6=27.5
Rounding up we get 28.
Starting with 292 & adding 28 we create our intervals…
Max Range
Min Range

## Slide 18: Determining Width of Class Interval
Note: As you are creating buckets or bars to hold your data you could start with 290, but we will use the 292…
Starting with 292 & adding 28 we create our intervals until we pass 457 and we get…
292 - 319
320 - 347
348 - 375
376 - 403
404 - 431
432 - 459
460
Then we create our by subtracting 1 from the next number or 320 as our lengths are in whole numbers. If we had 1 decimal we would use 319.9 or 2 decimals 319.99, etc.
292 to 319
320 to 347
348 to 375
376 to 403
404 to 431
432 to 459
Buckets

## Slide 19: Determining Width of Class Interval
292 - 319
320 - 347
348 - 375
376 - 403
404 - 431
432 - 459
460
Min Value | Max Value | Midpoint
292 | 319 | 305.5
320 | 347 | 333.5
348 | 375 | 361.5
376 | 403 | 389.5
404 | 431 | 417.5
432 | 459 | 445.5
Chart: Female Fish Histogram
| 292 | 320 | 348 | 376 | 404 | 432 | 460 | More
Frequency | 1 | 1 | 6 | 18 | 12 | 2 | 2 | 0
I used Excel to calculate the Midpoints. We can draw our histogram using graph paper or use Excel, which is today’s preferred method, to create our Histogram.

## Slide 20: Histogram
Study the shape of the histogram. A normal "bell curve" shape indicates normal variation in the system and a stable, predictable process. Any other shapes in the data are clues to look further for causes of the variance. Calculate mean, median and mode to further analyze the data.
Histograms from several common shapes. A bell-shaped picture is usually a normal distribution and indicates a generally stable system. Any of these other shapes would indicate some special cause of variation and invites further inquiry.
Notes: Notes

## Slide 21: Shape of Data
NORMAL Distribution
Skewed Distribution
Bimodal Distribution
Skewed RIGHT
Skewed LEFT
Data Distribution Examples
Control Charts Interpretation
Variability of Data
Notes: Notes

## Slide 22: Normality Check - Histogram
“Normal” Histogram
  The tallest bars should be in the center with the bars getting smaller as they move away from the center
  (e.g. it should resemble a Bell Shaped Curve).
  We will revisit this when discussing Capability
Normality
Interpreting Control Charts
Notes: For a “Normal” Histogram, the tallest bars should be in the center with the bars getting smaller as they move away from the center. (a bell shape)

## Slide 23: Normality Check
NORMAL Distribution
WHEN DO WE NEED TO CHECK for Normality:
  Before calculating control limits for an Individuals & Moving Range chart.
  Before calculating any capability as control & stability must be established before calculating Cp or Cpk
Note: A quick normality check is calculating the median, the mode, and the average. If the data is normal the calculation will be the same or close to…
A Histogram will show the shape of data & Minitab will also check data normality!
Normality
Interpreting Control Charts
Notes: Notes

## Slide 24: Figure 13-19 Skewness
As the Histogram shows us the Shape of data, the Frequency of data points, and data Location in respect to a specification.
We can use this information to assess the Reliability of the data and the Capability of the process.
Understanding these shapes will aid you in understanding the Capability Lecture and Statistics in General
Notes: Notes

## Slide 25: Figure 13-21 Bimodal Distribution
Notes: Notes

## Slide 26: Figure 13-20 Leptokurtic and Platykurtic
Notes: Notes

## Slide 27: Figure 13-18 Shape, Location, and Spread
Notes: Notes

## Slide 28
The shapes of Histograms tell us if data is near normal, exponential, skewed, etc. we explored this to great length in Unit 18 core tools
Notes: Notes

## Slide 29: Histogram Terminology
Mean - The average of all the values.
Standard Error - The “Standard Error” (SE) indicates how close the sample mean is from the ‘true’ population mean. The standard error is calculated by dividing the standard deviation of the population (or the sample) by the square root of the total number of observations. The SE can be used to roughly define a range of certainty for the mean.
Median - a statistic which measures the center of a set of data by finding that value which divides the data in half.
Mode. a statistic defined as the most frequently occurring data value. It is sometimes used as an alternative to the mean or median as a measure of central tendency.
Microsoft Excel generated “Descriptive Statistic”
Notes: Notes

## Slide 30: Histogram Terminology
Standard Deviation - An expression of how widely spread the values are around the mean.
Standard Variance - The variance is roughly the arithmetic average of the squared distance from the mean. The variance is roughly the arithmetic average of the squared distance from the mean. Squaring the distance from the mean has the effect of giving greater weight to values that are further from the mean. For example, a point 2 units from the mean adds 4 to the above sum while a point 10 units from the mean adds 100 to the sum.
Class Width - The x-axis distance between the left and right edges of each bar in the histogram.
Number of Classes - The number of bars (including zero height bars) in the histograms.
Microsoft Excel generated “Descriptive Statistic”
Notes: Notes

## Slide 31: Histogram Terminology
Kurtosis - Is a measure of how pointy the distribution is.
The standard normal curve has a kurtosis of zero. The Matterhorn, has negative kurtosis, while a flatter curve would have positive kurtosis. Positive kurtosis is usually more of a problem for quality control, since, with "big" tails, the process may well be wider than the spec limits.
Skewness - Is the histogram symmetrical? Skewness is zero.
If the left hand tail is longer, Skewness will be negative.
If the right hand tail is longer, Skewness will be positive.
Where Skewness exists, process capability indices are suspect.
For process improvement, it is prudent to look at the long tail of your distribution; that is usually where quality problems lie.
Microsoft Excel generated “Descriptive Statistic”
Notes: Notes

## Slide 32: Histogram Terminology
Range – In the descriptive statistics, the range is the length of the smallest interval which contains all the data. It is calculated by subtracting the smallest observation (ample Minimum) from the greatest (sample Maximum) and provides an indication of statistical dispersion.
It is measured in the same units as the data.
Since it only depends on two of the observations, it is a poor and weak or crude measure of dispersion except when the sample size is large.
For a population, the range is greater than or equal to twice the standard deviation, with equality only for the coin toss (Bernoulli distribution with p = ½).
Minimum - The smallest value.
Maximum - The biggest value.
Sum – Sum of the numbers in a data set.
Largest – largest number in a data set.
Smallest – Smallest number in a data set.
Microsoft Excel generated “Descriptive Statistic”
Notes: Notes

## Slide 33: Histograms
A histogram is a specific type of bar chart. Individual data points are grouped together in classes, to show how frequently data in each class occur in a data set. High bars indicate more points in a class, and low bars indicate less points.
The strength of a histogram is that it provides an easy-to-read picture of the location and variation in a data set. There are, however, two weaknesses of histograms that you should bear in mind:
The first is that histograms can be manipulated to show different pictures. If too few or too many bars are used, the histogram can be misleading. This is an area that demands some judgment, and perhaps some experimentation, based on the analyst's experience.
Histograms can also obscure the time differences among data sets. For example, example the differences in 3 shifts, or discrepancies in the amount of data generated or quality of data generated.
It is a essential to continually review the histograms and control charts for consecutive process runs over an extended time to gain useful knowledge about a process
Notes: Notes

## Slide 34: Histograms
Interval 144.705
Interval 4.048
Interval, bin or bucket that holds from 346.78 to 491.48
Same data, but different number of intervals or “Bins” The question is always how many to use, the problem is interpreting the results of not consistent!
Source http://www.shodor.org/interactivate/activities/Histogram/ In part
Notes: Source http://www.shodor.org/interactivate/activities/Histogram/ In part

## Slide 35: Histograms
14.167
Interval 22.263
Interval 14.167
Notice gaps in data
Notes: Source http://www.shodor.org/interactivate/activities/Histogram/ In part

## Slide 36: Histograms
Interval 7.59
Interval 31.37
The gaps disappear and a clearer picture of a continuous process is shown with the larger Bins.
Data Points | Number of Cells or Bins
20 to 50 | 6
51 to 100 | 7
101 to 200 | 8
201 to 500 | 9
501 to 1000 | 10
Over 1000 | 11 to 20
Recommended Cells or Bins From Page 563 Juran’s Quality Handbook
Notes: Source http://www.shodor.org/interactivate/activities/Histogram/ In part

## Slide 37: Histograms
Interval Circa 29
Interval Circa 32
Notice the difference between the bars with just a small variance in Intervals. Just enough to change the shape of the distribution…
Difference in Y axis scale gives slightly different visual results
Notes: Source http://www.shodor.org/interactivate/activities/Histogram/ In part

## Slide 38: Minitab Histogram
Minitab made the chart and determined that 15 bins was appropriate, which did not match the Chart on page 563 Juran’s handbook.
This somewhat points out the importance of the Operational Definition
Notes: Notes

## Slide 39
GREEN OD SIZE
CONE L68149
SPC REVIEW
My experience is to let the process & gage discrimination dictate the number of bars, then be consistent by recording it in the Operational Definition, Work Instruction, & Training program
Notes: Notes

## Slide 40: Capability As Seen On A Histogram
CONE No. L68149
FREQUENCY
40
35
30
25
20
15
10
5
0
-.0020 -.0017 -.0014 -.0011 -.0008 -.0005 -.0002 .0001 .0004 .0007 .0010 .0013 .0016 .0019
Cell Number
LCL
UCL
Center of Spec.
By putting the specification limits on the chart we can see the distribution is not centered, but all the data is within the specifications.
This Histogram is skewed to the left indicating it is not exactly normal and a normality test should be conducted…
Notes: Notes

## Slide 41: Histogram Patterns
Histogram Pattern | Symptom | Possible problem
 | Low With gaps | Bar range too narrow (check horizontal scale) or too few measurements (check vertical scale).
 | High with few bars | Bar range too wide (check horizontal scale) or too few measurements (check vertical scale).
 | Right Skewed (Left Skewed is the reverse of the diagram) | Natural distribution (more variation in one direction) - often found item count or time distributions.
 | Exponential | Distribution is not bell shaped (extreme skewed or truncated data) could be tail of a bell curve.
 | Dual peaked (bimodal) | Measurement is of two process (very common i.e., data from two time periods or process change in mid stream
Notes: Notes

## Slide 42: Histogram Patterns
Histogram Pattern | Symptom | Possible problem
 | Isolated-peaked | Two processes being measured (definitely separated isolated peaks)
 | Combed (or cog-toothed) | Faulty measurement, rounding error or version of plateau distribution
 | Plateau | Combination of multiple bell shaped curve. Extreme version of bimodal distribution or faulty process
 | Edge peaked | Modified data often cause by shifting out of spec limit data back into spec. limits
 | Truncated | Incomplete reported data or after inspection has rejected out of spec product.
Notes: Notes

## Slide 43: Minitab Boxplot Tutorial
Boxplots , like Histograms, provide a graphic summary of the pattern of variation in a set of data. It is especially useful when working with small data sets & when comparing many different distributions. (Juran page 393)
Notes: Minitab Version 15

## Slide 44: Minitab Boxplot Tutorial
The output of the Boxplot is a graphic , 5 number summary of variation in a data set, summarized as shown below. The Boxplot is used to show the variation in a data set or compare variation among groups…(Juran page 549-550)
Notes: Minitab Version 15

## Slide 45: Minitab Boxplot Tutorial
Notes: Minitab Version 15

## Slide 46: Minitab Boxplot Tutorial
Notes: Minitab Version 15

## Slide 47: Minitab Boxplot
We use Boxplots (called box & whisker plots) to assess & compare sample distributions.
This figure illustrates the components of a default Boxplot
Notes: Minitab Version 15

## Slide 48: Minitab 15 Box Plot
You want to assess the durability of four experimental carpet products. Samples of the carpet products are placed in four homes and you measure the durability after 60 days. Create a boxplot with median labels and color-coded boxes to examine the distribution of durability for each carpet product.
Notes: Minitab Version 15

## Slide 49: Minitab Boxplot with Whiskers
Notes: Minitab Version 15

## Slide 50: Interpreting the results
Carpets 1 & 3 have similar median durability's (13.52 & 12.895, respectively).
Carpet 3 also exhibits the least variability, with an interquartile range of only 2.8925 Median durability for Carpet 2 is only 8.625.
This distribution & that of Carpet 1 are positively skewed, with an interquartile range of about 5-6 respectively.
Median durability is highest for Carpet 4 (19.75). However, this product also demonstrates the greatest variety, with an interquartile range of 9.855. in addition, the distribution is negatively skewed, at least one durability measurement of about 10.
Notes: Minitab Version 15

## Slide 51
Minitab 15 SAT Score Run Chart
Notes: Notes

## Slide 52
Minitab 15 SAT Score Dotplot
Notes: Notes

## Slide 53: Stratification
Stratification is a technique used in combination with other data analysis tools.
When data from a variety of sources or categories, Example various shifts have been lumped together, the meaning of the data can be impossible to see.
This technique separates the data so that patterns can be seen.
Notes: Source http://asq.org/learn-about-quality/data-collection-analysis-tools/overview/stratification.html

## Slide 54: Stratification
Stratification is a technique used in combination with other data analysis tools.
When data from a variety of sources or categories have been lumped together, the meaning of the data can be impossible to see.
This technique separates the data so that patterns can be seen.
Notes: Source http://asq.org/learn-about-quality/data-collection-analysis-tools/overview/stratification.html

## Slide 55: Stratification
When to Use Stratification
Before collecting data.
When data come from several sources or conditions, such as shifts, days of the week, suppliers or population groups.
When data analysis may require separating different sources or conditions.
Notes: Source http://asq.org/learn-about-quality/data-collection-analysis-tools/overview/stratification.html

## Slide 56: Stratification
Stratification Procedure:
First ~ Before collecting data, consider which information about the sources of the data might have an effect on the results.
Set up the data collection so that you collect that information as well.
Notes: Source http://asq.org/learn-about-quality/data-collection-analysis-tools/overview/stratification.html

## Slide 57: Stratification
Stratification Procedure:
Second ~ When plotting or graphing the collected data on a scatter diagram, control chart, histogram or other analysis tool, use different marks or colors to distinguish data from various sources.
Data that are distinguished in this way are said to be “stratified.”
Notes: Source http://asq.org/learn-about-quality/data-collection-analysis-tools/overview/stratification.html

## Slide 58: Stratification
Stratification Procedure:
Third ~ Analyze the subsets of stratified data separately.
For example, on a scatter diagram where data are stratified into data from source 1 and data from source 2, draw quadrants, count points and determine the critical value only for the data from source 1…
then only for the data from source 2.
Notes: Source http://asq.org/learn-about-quality/data-collection-analysis-tools/overview/stratification.html

## Slide 59: Stratification
Stratification Example
The ZZ-400 manufacturing team drew a scatter diagram to test whether product purity and iron contamination were related, but the plot did not demonstrate a relationship. Then a team member realized that the data came from three different reactors. The team member redrew the diagram, using a different symbol for each reactor’s data:
Notes: Source http://asq.org/learn-about-quality/data-collection-analysis-tools/overview/stratification.html

## Slide 60: Stratification
Now patterns can be seen. The data from reactor 2 and reactor 3 are circled. Even without doing any calculations, it is clear that for those two reactors, purity decreases as iron increases. However, the data from reactor 1, the solid dots that are not circled, do not show that relationship. Something is different about reactor 1.
Notes: Source http://asq.org/learn-about-quality/data-collection-analysis-tools/overview/stratification.html

## Slide 61
Template available at:
http://asq.org/learn-about-quality/data-collection-analysis-tools/overview/stratification.html
Notes: Source http://asq.org/learn-about-quality/data-collection-analysis-tools/overview/stratification.html

## Slide 62: Stratification
Stratification Considerations
Here are examples of different sources that might require data to be stratified:
  Equipment
  Shifts
  Departments
  Materials
  Suppliers
  Day of the week
  Time of day
  Products
Survey data usually benefit from stratification.
Always consider before collecting data whether stratification might be needed during analysis. Plan to collect stratification information. After the data are collected it might be too late. On your graph or chart, include a legend that identifies the marks or colors used.
Excerpted from Nancy R. Tague’s The Quality Toolbox,
Second Edition, ASQ Quality Press, 2004, pages 485-487.
Notes: Excerpted from Nancy R. Tague’s The Quality Toolbox, Second Edition, ASQ Quality Press, 2004, pages 485-487.

## Slide 63: End of Lecture 12 Introduction to Industrial & Systems Engineering