## Slide 1
Value Stream Mapping &
Function Analysis
Lecture 5 ~ ENGT 1200
Introduction to Industrial Systems Engineering
Notes: Notes

## Slide 2: Lecture 5 Objectives
More on Value Stream Mapping and the tie to Function Analysis
Describe Value Analysis.
Define Value Analysis Systematic Application Techniques.
Define Value Analysis Philosophy, to include: The need to lower cost
Define Unnecessary Cost
Define Esteem value
Define the Exchange Value
Define the Use value
Define Function & Utility
Describe The Value Analysis Job Plan
Notes: Notes

## Slide 3: Lean Tools and Techniques
Value Stream Process Mapping
  Value streams are the actions required to create a product or service from raw material until it reaches the customer.
    A value stream may include both value and non-value added activities.
  Value stream process maps seek to capture the activities taking place while people do the work they do.
  Value stream process maps will show where improvements can be made to eliminate non-value added activities.

## Slide 4
Microsoft Visio Value Stream Map Example
These waste measurements become topics for an Improvement Project

## Slide 5: Value Stream Mapping Definitions
Value Stream Mapping (VSM)
A special type of flow chart that use, measurements and symbols known as “the language of lean”
  They illustrate, measure, and improve the performance elements of a flow chart.
  They are indicators of undesirable areas in need of improvement of inventory and information flow.

## Slide 6: Value Stream Mapping Purpose
To provide optimal value to the customer through a complete value process with minimal waste in:
Design from concept to delivery to the customer.
Build from the order to the delivery to the customer.
Warranty ( through life cycle of service).

## Slide 7: Why Do It?
Kaizen events or a Continuous Improvement Project is not enough.
  These are limited events…
  Value Stream Mapping & Analysis strengthen the gains by providing vision and tactics that connect all improvement activities
It is a tool that allows you to visualize waste and eliminate it!

## Slide 8: Value is What The Customer is Buying!
Defined by the customer as a capability provided:
Of the highest value.
At the right time and place.
At an appropriate price

## Slide 10: What is Value that Flows
Viewing value from the perspective of the customer ask how you current products, services, and processes dissatisfy your customers expectations such as:
Price
Quality
Reliability
Delivery
Response to changing requests

## Slide 11: What Flows?
“Items” flow through a value stream
In Administration internal customer needs are items.
In Design & Development the design and specs are items.
In Manufacturing parts, assemblies, and materials are items.
In Service external customers needs are items.

## Slide 19: Microsoft Visio Example
Visio Support Example

## Slide 20: Visio Example
A Microsoft Visio example from Microsoft Support gives us the visual of flow with the measurements to establish a baseline benchmark.
Undesirable measures can be addressed using tool we have already learned and many more yet to be explained

## Slide 21: Visio Example
Applying Muda, setup time reduction, line balancing, takt-time, 5s tools, statistical techniques or any quality tools yet to be discussed will reduce steps improve reliability, lower cost, mistake proof the process or system used!

## Slide 22: What is Value Analysis?
Value Analysis is a systematic, creative approach to ensure that the essential functions of a product, process, procedure, or service are provided at a minimum total cost consistent with the required performance, reliability, quality, and maintainability.
Notes: Notes

## Slide 23: Value Analysis is the systematic application of recognized techniques that:
Identify the functions of a product or service
Establish a value for those functions
Endeavor to provide those functions, reliably, at the lowest total cost.
Notes: Notes

## Slide 24: For Example: What is the function of a Light Bulb…
If we picked to signal from the list, how many things could you think of rapidly...Can you describe a value for the items pictures?

## Slide 25: Lowest Cost & Enhanced Function
Today LED lights have lowered the cost of power requirements, maintenance, etc.
Additions to crosswalk signals include countdown timers and audible signals to aid vision impaired persons.
How does the new technology affect safety, reliability, etc.

## Slide 26: The Value Analysis Philosophy
For better total performance, we need to:
Have a positive approach concerning the need and ability to lower cost
Emphasize teamwork for interdisciplinary idea stimulation
Stress the need to do a better job in the areas of cost and total value.
Notes: Notes

## Slide 27: Unnecessary Costs
Value Analysis is a technique for identifying and removing unnecessary costs.
    What are unnecessary costs?
Notes: Notes

## Slide 28: Unnecessary Costs
These are costs that do not contribute to the accomplishment of the required junctions. They can be removed without impairing the essential performance, quality, reliability, maintainability, sale-ability, etc.
Some of the more common reasons for unnecessary costs are:
Lack of information (cost, usage) or inaccurate information, before decisions are made
Lack of ideas or alternatives
Expediency or temporary circumstances –shortage of time
Honest but wrong beliefs, mental blocks in certain areas
Habits and attitudes of persons or organizations
Policies, procedures, and traditions of organizations, companies, or industries
Lack of value measurement
Impact of technological advances
Insufficient‑or excessive ‑standardization or N.I.H.* factor. (*Not Invented Here.)
Notes: Notes

## Slide 29: Lets Discuss the Function of a Jack
If I sent you to a store to get a Jack you may need some information to assure you will get what I sent you for…
So to clarify the task I want the floor jack, now what do you need to know?

## Slide 30: Aristotle!
Value. The so‑called "soft science" of economics brought with it a sustained debate about "values. " This philosophic debate seemed to be going strong in 350 B.C. when Aristotle classified kinds of values as:
          a. Aesthetic
          b. Ethical
          c. Moral
          d. Political
          e. Social
          f. Spiritual
          g. Economic.
Notes: Notes

## Slide 31: Correa M. Walsh (Author)
In 1926 Correa M. Walsh directed his complete attention to economic values and identified these into four categories:
          Esteem
          Exchange (Market)
          Cost
          Use.
Notes: Notes

## Slide 32: Esteem value
is appreciation for the customer's desire and willingness to buy services. Since our corporate growth and health are dependent upon this economic value, a portion of our time will be spent in increasing the merit and decreasing the cost for the esteem held by all our customers for our products or service.
Notes: Notes

## Slide 33: The exchange (market) value
is the actual measure by which our customers appraise the influence of our competitors and agree to our price. In an appraisal of the market value, the selling organization compares the features, performance, and service of competitor's products as a basis for pricing the services he offers to the customer.
Notes: Notes

## Slide 34: Cost value
usually comes to mind in relation to cost
reduction efforts. Value analysis has a pattern
of historic success in cost reduction, where firm disciplines of cost visibility became the means to see causal relationships which permitted elimination of unnecessary costs. Our design decisions affect the marketplace and our total dollar sales volume. Value analysis uses projected costs as a basis of designing for profit.
Notes: Notes

## Slide 35: Use value
is a concept, which can be applied to a design before the design takes form. Use value is frequently projected on the basis of an insight from comparisons and observations. However, it can also be an orderly calculation of the minimum cost to achieve a specific level of physical performance.
Therefore: Value is a measure of the relationship of utility, or function, to cost as seen by the user (or customer)
Notes: Notes

## Slide 36: Function & Utility
Function is the natural or characteristic action performed by a product or service.
This includes the basic considerations of the actions that make a product or service work or sell, which stress the use and esteem parts of economic value.
Utility is a measurement of the degree to which an objective is obtained.
Notes: Notes

## Slide 37: VE uses a questioning approach
Value Engineering uses a questioning approach ‑based on 6 questions:
1. What is the item, project, or service?
2. What does it do? (Define the function)
3.What is the value of the function? (In dollars)
4. What does the item, project, or service cost?
5. What else will perform the function?
6. What will this new approach cost?
Notes: Notes

## Slide 38: The Value Analysis job Plan
The job Plan is divided into five phases:
          Information
          Creation
          Evaluation
          Investigation
          Recommendation
The key to an effective Value Analysis program is the organized and systematic application of the Value Analysis job Plan and the contributing techniques.
Notes: Notes

## Slide 39: Purpose of the VA job Plan
The purpose of the VA job Plan is to provide a guide in the form of:
Discrete, sequential steps for the conduct of the analysis
To ensure an organized, systematic, and logical approach.
Notes: Notes

## Slide 40: Information Phase
The‑functions of this‑phase are:
            Gather data
            Organize data
            Analyze data.
This phase answers four of the questions of the VA questioning approach:
What is it?
What does it do?
What is the value of the function?
What does it cost?
Notes: Notes

## Slide 41
The elements are:
The selection of the item to be analyzed
The determination of the kinds of information needed and the sources of that formation
The systematic inquiry into all aspects of the item and the collection of all relevant information in order to:
  Define the item and establish its boundaries
  Determine the cost of the present item
  Determine the constraints on the item.
Information organization and analysis to disclose meaningful relationships, including:
  Cost Analysis (of existing part, method, etc.)
  Function Analysis: The identification, definition, classification, and evaluation of functions.
  Analysis of technical and other requirements:
The analysis of requirements relative to performance, reliability, service life, maintainability, development and production schedules; also marketing, and so‑called intangibles.
Notes: Notes

## Slide 42: Creation Phase
The function of this phase is to generate ideas:
This is the most important phase in the VA job Plan. The Information Phase was just a foundation for this phase. Creative thinking, or creative problem solving, certainly is not peculiar to value engineering. However, a key element in the success of VA has been the emphasis placed on the exploitation of each individual's latent, creative potential.
There are numerous "ideation" techniques, of which "brainstorming" is probably the best known. You are encouraged to use any of these techniques, singly or in combination, as you see fit.
This phase answers the VA question, "What else will perform the function?”
Notes: Notes

## Slide 43: Evaluation Phase
The function of this phase is: Evaluate ideas.
The objective of this phase of the VA job Plan is the selection, from the ideas conceived during the preceding phase, of the optimum solution to the problem.
In order to ensure the best selection, each idea must be critically evaluated, not only on the basis of potential savings, but also in terms of its effects on performance, schedule, contractual requirements, etc.
Notes: Notes

## Slide 44: Evaluation Phase
The following considerations must be used when making the evaluations:
Economic benefits (will it approach the "function value")
Technical feasibility
Schedule
Technical acceptability
Economic analysis.
Notes: Notes

## Slide 45: Investigation Phase
The function of this Phase is: Develop alternatives.
This phase determines how the ideas that were evaluated in the previous phase need to be modified or refined to perform all the essential functions and technical requirements. This becomes a more detailed analysis of the factors used for the preliminary evaluation and selection of ideas.
The assistance of many specialists and vendors or suppliers is necessary as the intent is to confirm and document the practicality, delivery schedule, and cost of the new idea.
This phase answers or re-answers the VA questions:
  What else will perform the function?
  What will it cost?
Notes: Notes

## Slide 46: Recommendation Phase
The functions of this‑phase are: Present Proposals and Motivate Positive Action.
The successful completion of the Evaluation and Investigation Phases should culminate in selection of the best of the alternatives that have been developed.
The next step is to propose this solution to those having authority to implement it or to those in a position to continue the study and make future recommendations. Therefore, it will be necessary to submit a written report covering the project activities, findings, and proposals.
Notes: Notes

## Slide 47: The functions of this report are to:
Provide the company with a record of what has been done, ideas generated, problem areas investigated, contacts made, etc., which serves as a point of departure if further investigation and action are needed.
Provide a uniform, organized format to follow when recording project analysis work and proposals. (Note, this is an automatic or required process if ISO 9000, QS 9000, or TS 16949 Registered)
Provide top management an insight into projects being studied, and provide middle management with information spotlighting cost saving opportunities in areas under their own jurisdiction.
Notes: Notes

## Slide 48: Function Analysis
Function analysis is the process of (1) identifying, (2) defining, in accordance with the established VA precepts, and (3) assessing the value of the functions of a product, service, or production factor. Function analysis is the very essence of good VA. Without it, you don't have VA; you have something else, probably more-or-less conventional cost reduction. There are four steps to Function Analysis. They are:
Identification of functions and Technical requirements
Definition of functions in terms of a verb and a noun
Classification of functions as basic or secondary
Evaluation of functions and technical requirements
Notes: Notes

## Slide 49: Function Analysis
Functional Approach Versus Conventional Approach
The difference can best be illustrated by how questions are asked.
Conventional Approach: How can this part be made for less? Software: How else can we do this task?
Functional Approach: What is the function? In what manner can the function be accomplished?
Notes: Notes

## Slide 50: Ten Fundamental Tenets of Value Analysis
1. The key to increasing profits and improving our competitive position is better satisfaction of customer needs. Customer needs can generally be defined in terms of (a) accomplishing required functions, (b) satisfying quality, reliability, maintainability, safety, service life, and other requirements, (c) meeting schedules, and (d) minimizing costs.
2. Providing the customer with a product or service which represents maximum value requires consideration of total cost to the customer. Consequently, selling price alone does not indicate whether or not the customer is receiving maximum value. Operating costs, service life, maintainability, and many other factors influence the total cost to the customer.
Notes: Notes

## Slide 51: Ten Fundamental Tenets of Value Analysis
3. There shall be no degradation of quality, reliability, or other characteristics essential to performance requirements, but quality or performance characteristic's that exceed what is necessary to perform functions represent waste and should be challenged. This is an inviolable rule of VA (Note: without Reliability Engineering measurements, or data, this cannot be accomplished)
4. The two keys to achieving maximum value are:
  Identification and elimination of non­essential functions and technical requirements.
  Assurance that essential functions and technical requirements are accomplished at the lowest total cost to the customer.
Notes: Notes

## Slide 52: Ten Fundamental Tenets of Value Analysis
5. Costs, which do not contribute to the accomplishment of required functions, are "unnecessary costs" and should be eliminated.
6. Most products and services contain unnecessary costs, which are "built in" by a wide variety of factors; most of these factors are traceable to the imperfections of human behavior.
7. "Cost visibility" is a prerequisite to cost reduction or avoidance. To be eliminated, costs must be visible to those whose decisions affect cost. "Cost visibility" requires that costs be identified, measured, and communicated to everyone in the organization making such decisions.
Notes: Notes

## Slide 53: Ten Fundamental Tenets of Value Analysis
8. Poor value is more often caused by lack of ideas than by lack of technology. It is for this reason that VA places so much emphasis on creative thinking, overcoming roadblocks, and changing habits and attitudes.
9. The major cause of poor value in products and services is insufficient information at the point (and time) of decision-making. Therefore, the achievement of better value requires that more and better information be provided to personnel making decisions, which affect value. The recognition of this fact explains the emphasis in Value Analysis on information techniques and the utilization of resources.
Notes: Notes

## Slide 54: Ten Fundamental Tenets of Value Analysis
10. Value Analysis is, and must always remain, an advisory function. It does not arrogate any of the responsibilities or authority of other organizational functions. Its job is to help others do their jobs better.
These are the fundamentals of Value Analysis. The knowledge of these concepts and techniques provides only the theory for lower costs, better value, and higher profits. It is their application that results in substantial cost avoidance, cost reduction, and product improvement. Learn these fundamentals, apply them, and improve your skill in identifying and removing unnecessary costs.
In so doing you will strengthen the security of both YOURSELF and YOU’RE COMPANY.
Notes: Notes

## Slide 55
Quality Assurance
Concurrent Engineering
Value Analysis
Value Assurance
Value Management
Cost Engineering
Cost Analysis
Functional Analysis
Value Engineering…
TERMS WHICH ARE USED TO MEAN VALUE ENGINEERING
Notes: Notes

## Slide 56
Value
Engineering
Examples
Notes: Notes

## Slide 57
Examples from www.nab.usace.army.mil See Corresponding Handouts

## Slide 63
Examples from http://www.dot.state.oh.us/Divisions/ConstructionMgt/Pages/ValueEngineering.aspx
See Corresponding Handouts

## Slide 64: End of Lecture 5