## Slide 1
ACADs (08-006) Covered
Keywords
Line source, disk source, 6CEN
Description
Supporting Material
3.3.1.10 | 4.12.2 |  |  |  |  |  | 
Notes: <number>

## Slide 2: Exposure Rate Calculations
In order to get an idea of what the exposure rate is from a gamma emitting radionuclide one needs certain information
  Activity
  Energy
  Efficiency
Do all gammas that are emitted from the source come in your direction?

## Slide 3: Dose
In order to determine the dose given to a space at a certain distance one needs to determine two things
  Total number of gamma rays coming off of the source
  Total surface area of a sphere of radius of that distance
  Does one need the area of the object that is irradiated?

## Slide 4: Activity to dose
Gamma flux
D= 3.7 x 1010 C E
4π r2
Top is total number of photons
Bottom is total surface area of sphere with radius r
Units are G/sec/cm 2
Convert to dose using chart that relates gamma energy to conversion factor
Notes: <number>
The number of gammas passing through an area per unit time will determine the exposure

## Slide 5: Activity to Dose
Main parameters that determine dose from source is g/d and energy of gamma
If one were to use nuclide specific information for each radionuclide and perform the calculations
The only unknown would then be the activity of the source
Can simplify equation

## Slide 6: Short formula
Pre calculated conversion factors for activity to exposure rate conversion. (mR/hr calculated at 1 foot)
Cs-137 Multiply # of mCi X 3.4
Ir-192 Multiply # of mCi X 6
Ra-226 Multiply # of mCi X 8.8
Co-60 Multiply # of mCi X 14.5
Am-241 Multiply # of mCi X 0.15
Notes: <number>
Easy short formula for converting activity in mcis to an exposure rate in mR/hr

## Slide 7: Dose Rate
Can calculate dose rate from any gamma emitting radionuclide if you have
  Activity
  Gamma ray emission rate
  Energy of gamma ray

## Slide 8: Dose Rate
D = 6CEN
D= exposure rate at 1 foot in R/hr
C= number of Ci
E= energy of emitted gamma ray in MeV
N= number of gammas per disintegration
Good for any gamma emitting radionuclide
Notes: <number>
Generic exposure rate formula. Can use the number of curies , the energy of the emitted gamma ray and the percent emission to determine the exposure rate at one meter

## Slide 9: Dose Rate
Co-60
Cs-137
Am-241

## Slide 10: Distance
For unshielded point sources exposure is inversely proportional to the square of the distance
I = Io (r0/r1) 2 or I1 r21= I0 r20
  I = intensity at point 2,
  Io = intensity at point 1,
  r0 = first distance
  r1 = final distance
Notes: <number>
Inverse square law

## Slide 11: Distance Example
Io = 100 mR/hr at 1 ft
What is the reading at 10 ft?
I = 100 (1/10) 2
I = 1 mR/hr
Can be used to calculated closer to or farther away from source
Notes: <number>

## Slide 12: Distance
In order to be considered an point source the distance from the source that is being measured has to be greater than 3-4 times the longest dimension of the source.
Closer than this the source is considered a line source. 1/r
Other important shapes are disc or plane source
Notes: <number>
There are different formulas for line and disc sources

## Slide 13: Distance
For line sources exposure is inversely proportional to the distance
I = Io (1/r)
Io = 100 at 1 ft
What is the reading at 10 feet?
I = 10 at 10 ft
Notes: <number>

## Slide 14: Line source
Line sources are more complicated because one needs to take into account not only how far away you are but also where you are in respect to the end of the source
This would represent a contaminated pipeline or a leak along a wall or floor
Г= activity to dose conversion factor
A= activity in mCis
Distances need to be in cm

## Slide 15: Line Source
ER= ГA (tan-1 ((a+b)/h)- tan-1(b/h)
ah
b may be negative
source
a
b
h

## Slide 16: Line source
Source is Co-60 and is 3 Ci
Length of source 6 feet
Г for Co-60 is 14.5 R/h/Ci
You are 10 feet from the source but you are directly on front of one end of the source
What is your exposure rate?

## Slide 17: Disc or planer sources
Disc sources are still more complicated from line sources because you need to worry about a 3rd dimension
This would be an example of
  a contaminated floor due to spill
  A field that has surface contamination
If your area is not a circle one can approximate by using the radius that is ½ the length of a square

## Slide 18: Disc source
Another dimension is added
DR= ГA ln (a2-b2+h2+(a2-b2+h2)2+4b2h2)/2h2
a
B is 0 if b<a
a
b
h

## Slide 19: Disc source
You had a spill
I-131 is all over the floor
  Г for I-131 is .22 R/hr/Ci at 1 meter
  It has been estimated there is 5 Ci present
Your waist is 1 m from the floor and you are in the center of the room
What is your dose?

## Slide 20: Questions