## Slide 1
ACADs (08-006) Covered
Keywords
Transuranic, radioactive waste, radwaste, waste regulations.
Description
Supporting Material
3.3.1.6 | 3.3.2.4.4 | 3.3.5.6.6 | 3.3.5.6.7 | 4.9.6 | 4.16.6.6 | 4.16.6.7 | 
Radioactive Management and Disposal NUCP 2311
contributions from :
  John Poston (Texas A&M University)
  Ashley Bernardi (Purdue University)
  And www.wipp.ws
Notes: <number>

## Slide 2: Transuranics
What is a Transuranic?
Part of the actinide series.
Elements with atomic numbers >92
Many radionuclides have long half-lives.
Many radionuclides are alpha-emitters.
<number>
Notes: <number>

## Slide 3: Definition of TRU Waste
“Radwaste that is not classified as HLW but contains an activity of more than 100 nCi/g from alph-emitting TRU isotopes with half-lives greater than 20 years.”
- Radioactive Waste Management, Saling & Fentiman, p. 193
<number>
Definition varies internationally and with time.
Activity can range from 0.3 to 1000 nCi/g of waste.
Notes: <number>

## Slide 4: Practices Use to Treat and Immobilize Transuranic Wastes
<number>
Notes: <number>

## Slide 5: Practices Use to Treat and Immobilize Transuranic Wastes
<number>
X
Notes: <number>

## Slide 6: Transuranic Waste (prior to 1970)
TRU waste was not managed separately from LLW.
TRU and LLW waste were combined into a single waste form.
Disposed of in shallow burial trenches.
<number>
Notes: <number>

## Slide 7: Transuranic Waste (after 1970)
US adopted retrievable storage approach.
Storage in metal drums or boxes.
Either above- or below-grade, soil-covered storage pads.
Some storage in buildings.
TRU waste is managed at 20-21sites in the DOE complex.
There are 12 sites at which the TRU waste from weapons production is managed.
Most TRU waste is located at only 6 sites.
<number>
Notes: <number>

## Slide 8: Transuranic Waste Storage and Disposal Sites (Resulting from Nuclear Weapons Production)
<number>
Notes: <number>

## Slide 9: Transuranic Waste Storage and Disposal Sites (Resulting from Nuclear Weapons Production)
<number>
Notes: <number>

## Slide 10: Transuranic Waste
Further categorized by the external dose rate.
Contact-handled TRU waste – dose rates less than 200 mrem/h (CHTRU).
Remote-handled TRU waste – dose rates exceeding 200 mrem/h (RHTRU).
<number>
Notes: <number>

## Slide 11: Transuranic Waste
Typical CHTRU contains the long-lived actinides which are alpha-emitters, e.g., Pu-239, -239, -240, -241, Am-241 and Cm-244.
Typical RHTRU contains fission products, activation products and their resulting daughter radionuclides, e.g., Sr-90, Y-90, Cs-137, Ba-137, Co-60, Eu-152, -154, -155.
        Why are these TRU ????
<number>
Notes: <number>

## Slide 12: Transuranic Waste
May also contain hazardous substances subject to regulation under the Resource Conservation and Recovery Act (RCRA) – called “mixed TRU waste.”
May contain materials subject to the Toxic Substances Control Act such as polychlorinated biphenyls (PCBs) – called “PCB-TRU waste.”
<number>
Notes: <number>

## Slide 13: Sources of TRU Wastes
Fuel reprocessing.
Waste immobilization facilities.
Fuel fabrication of recycle Pu.
Weapons material production.
Decommissioning of nuclear facilities.
<number>
Notes: <number>

## Slide 14: Transuranic Waste Radioactivity Categorized by Half-Life (Stored Waste Only)
<number>
Notes: <number>

## Slide 15: Estimates of Pu-239 Content
About 88 kg of Pu-239 is assumed to be in the buried TRU waste.
About 2,600 kg of Pu-239 is assumed to be in the stored TRU waste.
Activity of stored Pu-239 is estimated to be 160,000 curies.
<number>
Notes: <number>

## Slide 16: WIPP – Deep Geologic Disposal
<number>
Notes: <number>

## Slide 17: What is WIPP?
First geological repository for permanent disposal of transuranic radioactive wastes and transuranic mixed wastes.
Department of Energy Facility.
Plant opened March 26,1999.
<number>
From: http://www.wipp.energy.gov/index.htm
Notes: <number>

## Slide 18: What does WIPP do?
Deep disposal site for defense-generated transuranic waste from across the nation.
WIPP can store a max of 6.2 million cubic feet of transuranic waste.
Currently, WIPP has 2.32 million cubic feet of waste.
In next 35 years 3.7 million cubic feet if waste will be generated.
<number>
Notes: <number>

## Slide 19: Types of Transuranic Waste
Contact-handled transuranic waste (CHTRU)
  97% of the volume currently at WIPP.
  Packed in 55-gallon metal drums or boxes.
  Primarily emits alpha particles.
Remote-handled transuranic waste (RHTRU)
  Emits more radiation than CHTRU.
  Handled and transported in shielded casks.
  Primarily emits gamma radiation.
<number>
Notes: <number>

## Slide 20: Why Salt?
Deposits are geologically stable.
Presence shows absence of free-flowing water.
Salt is easy to “mine.”
Formations will eventually fill in mined areas and seal radioactive waste from the environment.
Rock salt heals its own fractures because of plastic quality.
<number>
Notes: <number>

## Slide 21: Waste Isolation Pilot Project
Authorized by Congress in 1979
Located in southeast New Mexico
Site is a salt bed about 2000 feet thick
Serves as an underground laboratory
Site for permanent isolation or TRU wastes
<number>
Notes: <number>

## Slide 22: WIPP Timeline
1955 Atomic Energy Commission (AEC) asked National Academy of Sciences (NAS) to study permanent disposal methods for radioactive wastes from nuclear weapons produced in the US.
1957 NAS study suggested that AEC bury TRU or high level waste in geologic formations (ie salt beds or salt domes).
1972 Original location in Lyons, Kansas was withdrawn due to “drilling concerns.”
Mid 1970’s The WIPP site near Carlsbad, New Mexico was selected.
1979 Congress authorized and funded the construction of WIPP.
1981 The first exploratory shaft was drilled.
1983 The go-ahead was given for full construction.
1991 US Department of Energy assumed control of WIPP.
1992 The “WIPP Land Withdrawal Act” passed in congress.
1999 WIPP received first shipment of TRU waste.
<number>
Notes: <number>

## Slide 23: Who is in charge WIPP?
In 1993, the Carlsbad Area Office (CAO) was created by the DOE to head transuranic program.
  Program includes waste-generating sites and national labs
Westinghouse is the WIPP programs managing and operating contractor.
Sandia National Laboratories is the programs lead technical contractor.
<number>
Notes: <number>

## Slide 24: WIPP Facility Features
For the first 5 years, used as a laboratory (i.e., the pilot phase).
All waste will be retrievable during this time.
Operations will be limited to handling fixed amounts of CHTRU and RHTRU.
Nominal operating life of 25 years
Accommodate >14,000 m3/y of CHTRU
Accommodate >280 m3/y of RHTRU
Design capacity – 1.78 x 105 m3 of CHTRU
Design capacity – 5100 m3 of RHTRU
<number>
Notes: <number>

## Slide 25: WIPP Facility Features
Requires several shafts.
Requires the construction of a number of rooms.
Each room is 13 ft. high, 33 ft. wide, and 300 ft. long.
Support is provided by 100 ft. thick columns.
Emplaced waste will be back-filled with salt.
<number>
Notes: <number>

## Slide 26: Where is WIPP?
Chihuahuan Desert, New Mexico
<number>
From: http://www.wipp.energy.gov/index.htm
Notes: <number>

## Slide 27: Waste Isolation Pilot Plant
Notes: <number>

## Slide 28
Transuranic Waste Repository at Carlsbad, NM

## Slide 29
<number>
Notes: <number>

## Slide 30: Typical TRU Container
Most waste stored in 55-gallon drums.
Waste is “bagged” in polyethylene.
Barrel has polyethylene liner.
Waste stored in stacks inside and outside.
<number>
Notes: <number>

## Slide 31: Typical TRU Container
Effort underway to recover drums from storage.
Assumed that 1% of the drums will have “failed”.
Industrial and radiological safety challenge.
<number>
Notes: <number>

## Slide 32: Specialized Routes to WIPP
<number>
From: http://www.nsc.org/ehc/wipp/transp.htm#tran_routes
Notes: <number>
Taken from: http://www.wipp.energy.gov/

## Slide 33
<number>
A truck carries three TRUPACT-II containers to the WIPP site pictured in the distance. This is the method by which transuranic waste is shipped to the WIPP. Waste shipments to the WIPP began on March 26, 1999.
Notes: <number>

## Slide 34: Waste Acceptance Criteria
Container properties
Radiological properties
Physical properties
Chemical properties
Gas generation properties
Data package contents (documentation)
- See DOE/WIPP-069 (1999) for details.
<number>
Notes: <number>

## Slide 35: Waste to WIPP
All waste shipped to WIPP must be characterized before shipment.
Constituents of the waste provide a huge challenge.
A number of methods under development.
No single method acceptable for all waste packages.
<number>
Notes: <number>

## Slide 36: TRUPACT-II Waste Container
(Contact Handled)
<number>
From: http://www.wipp.energy.gov/fctshts/TRUwastecontainers.pdf
Notes: <number>

## Slide 37: Half PACT Waste Container
(
<number>
From: http://www.wipp.energy.gov/fctshts/TRUwastecontainers.pdf
Notes: <number>

## Slide 38: RH-72B Waste Container
<number>
From: http://www.wipp.energy.gov/fctshts/TRUwastecontainers.pdf
Notes: <number>

## Slide 39: RHTRU Waste at WIPP
WIPP cannot accept RHTRU with a surface dose rate in excess of 1000 rems per hour.
WIPP cannot accept more than 5 percent by volume of RHTRU with a surface dose rate in excess of 100 rems per hour.
WIPP cannot accept more than 5.1 million curies of RHTRU.
No more than 7,079 cubic meters of RHTRU can be emplaced in WIPP.
<number>
Notes: <number>

## Slide 40
<number>
Miners at the WIPP use a Marietta Drum Miner to cut passages and rooms 2,150 feet underground in ancient, stable salt deposits.
Notes: <number>

## Slide 41
<number>
An underground scaling machine, referred to in the mining industry as the "Fletcher Scaler, " removes loose rock from walls and ceilings in the WIPP underground, assuring safe working conditions.
Notes: <number>

## Slide 42
<number>
A service vehicle travels a pathway 2150 feet (almost a half mile) underground in rock salt. All 7.1 miles of tunnels that make up the WIPP underground are mined with the same precision that is exhibited in this photo.
Notes: <number>

## Slide 43
<number>
The underground facilities include maintenance shops, such as this one, where vehicles and machinery are repaired.
Notes: <number>

## Slide 44: Step by Step (CH-TRU)
Waste arrives by tractor trailer in TRUPACT-II or HalfPACT
Security inspection, radiological survey and shipping document review
Forklift transports package into waste handling building
Radiological surveys still done to ensure does not have internal leaks
The containers are then removed from TRUPACT-II or HalfPACT
  Two seven-packs (55-gallon steel drums)
  Two standard waste boxes
  One ten drum over pack
Forklift moves containers to conveyance loading car in airtight handling shaft
Waste descends 2,150 feet into WIPP repository
Underground machinery moves waste to disposal room
Bags of Magnesium Oxide are placed on top and around the waste container for backfill and to control the solubility of radionuclide's
<number>
Notes: <number>

## Slide 45
<number>
Upon arrival at the WIPP, the truck is inspected and TRUPACT-II shipping containers are tested to ensure that no radioactive material exists on the outer surface.
Notes: <number>

## Slide 46
<number>
After radiological inspection, TRUPACT-II shipping containers are moved inside the waste handling building for unloading.
Notes: <number>

## Slide 47
<number>
Forklifts move the TRUPACT-II shipping containers to the waste handling bays.
Notes: <number>

## Slide 48
<number>
Waste handlers perform a "swipe test" prior to unloading 55-gallon transuranic waste drums from a TRUPACT-II. These tests are conducted before waste is unloaded to detect the presence of radioactive contaminants.
Notes: <number>

## Slide 49
<number>
The 55-gallon waste drums are removed from the TRUPACT-II's using overhead cranes.
Notes: <number>

## Slide 50
<number>
After unloading the TRUPACT-II, seven-packs of transuranic waste are transferred by forklift from the docks to the waste hoist.
Notes: <number>

## Slide 51
<number>
Drums are removed from the transporter by forklift to be placed in disposal rooms, 2150 feet underground.
Notes: <number>

## Slide 52
<number>
Drums of transuranic waste are stacked in a disposal room where salt will eventually move in and permanently encapsulate the containers.
Notes: <number>

## Slide 53: Recertification
The disposal facility must reapply every five years to required by the WIPP Land Withdrawal Act.
The CRA was submitted to EPA on March 26, 2004.
  Exactly five years after the first waste was received at WIPP.
March 29, 2006: EPA officially recertified.
CRA is due to EPA by March 26, 2009.
CRA:Compliance Recertification Application.
<number>
Notes: <number>

## Slide 54: Recent WIPP Facts
8,400 shipments received since opening in 1999
10 million transportation miles for WIPP material
<number>
** Updated as of April 4, 2006 Taken from: http://www.wipp.energy.gov/TeamWorks/index.htm
Notes: <number>

## Slide 55: WIPP Information
In June 2000 the Carlsbad Office of the US Department of Energy and Institute for Nuclear Particle Astronomy and Cosmology sponsored a workshop to encourage the research world to use their underground facility.
  Neutrino research
  Setup to make the first measurement of electron neutrino
WIPP serves as a test bed for future geological repositories for other permanent disposal programs in repository performance and transparency.
  Transparency-technologies and processes that provide information to outside parties for assessments of materials control
<number>
Notes: <number>

## Slide 56: Questions