## Slide 1
ACADs (08-006) Covered
Keywords
Types of air samplers, air sample locations, particulates, noble gases, radon, flow rate, concentration, DAC, dose calculation, ALI.
Description
Supporting Material
Air Sampling
3.2.4.1 | 3.2.4.5.2 | 3.2.4.5.3 | 3.3.7.6.2
3.3.9.6 | 3.3.10.5 | 3.3.10.6 | 3.3.14.7.4
3.3.14.7.5 | 3.3.16.3 | 3.3.16.4 | 

## Slide 2: Purpose -Type
Purpose of air sampling
  Comply with regulation
  Monitor for worker safety
  Confirm models
  Estimate dose to public
Types
  Personnel
  Area
  Chemical
  Particulate
  Gasses

## Slide 3: Air sampling
Material can be in the air in two forms
  Particulate
  Gasses
Particulate material can be separated from the air by means of filters
Gasses since they blend in with the other gas ions in the air, they are more complicated to separate out

## Slide 4: Sample Locations
Air samplers are expensive so usually the minimum amount of samples will be taken
The location of the samples should be
  Facility boundary
  Residence with highest predicted concentration
  In the closest town
  At background locations which are usually upwind from facility or source.

## Slide 5: Particulate Air sampling instruments
BZ samplers
Area samplers
Low volume
High volume

## Slide 6: BZ Pumps
Small pumps that sample the breathing zone of worker
Worn by workers
Battery operated, light weight
Usually set at 1.2 l/min
Can be used to see if respiratory protection is needed

## Slide 7: Area Monitors
Set off the side and collects air from general work area.
Can be used to determine work airborne concentrations or off site concentrations
Usually need AC to operate
Fairly portable

## Slide 8: Sampling
Radionuclides are usually in particulate form
Usually in very low concentrations
Typical method is to use filters to catch particles
  Usually a glass fiber filter
Draw large volume through filter to get enough so one can count
Store filter paper in paper envelope

## Slide 9: Sample counting
In areas high in radon, the sample is usually counted twice to see if Rn is a factor.
once several hours after collection and a second time 10-20 hours after collection
If there is a significant difference one may have to wait longer to get an accurate reading because of thoron daughters in the sample
One must take into account background count rate of the filter when calculating activity

## Slide 10: Concentrations
Collect sample
Get flow rate off of instrument
  Start/stop rates will be different
Get start and stop times
Calculate total time
Calculate total volume of air

## Slide 11: Flow rates
As mentioned the flow rates will be different from start to finish of the sampling times
  This is caused by the loading of the filter
One usually takes the average of the start and stop time flow rates
This is usually acceptable unless there is a known cause that would make the flow rate change in a nonlinear fashion
  Dust storm, pump failure, etc

## Slide 12: Concentrations
Count sample on some sort of detector, usually a alpha counter
Calculate total activity(uCi)
Divide total activity by total volume of air
Get results in uCi/ml of air
Compare to DACs to see if some action is needed.

## Slide 13: Dose calculation
From the air concentration one can calculate the dose given to a person breathing this air all year long
The DAC-Derived Air Concentration- is the concentration of material in the air that if breathed for 2000 working hours would result in the inhalation of 1 ALI
ALI- Annual Limit of Intake- is the amount of activity if in the body would lead to a dose of 5 rem over the course of a year

## Slide 14: Calculation
Take the concentration of the air sample in uCi/ml and multiply by the amount of air breathed per minute (20000 ml/min) times 60 min in an hour times 2000 (approximate number of hours in a working year) to get total activity potentially breathed in by this person
Total activity = # uCi/ml X 2 E 4 ml/ min X 60 min/hr X 2000 hr

## Slide 15: ALI
Compare the total activity calculated from the air sample to the ALI listed in the chart
The ratio of those numbers is the same ratio as 5 rem is to your dose due to that radionuclide
Say you have

## Slide 16: Example
Say you have a results of 2.5 E -10uCi/ml of Am-241 found in the air
Take this result and multiply by all your factors
2.5 E -10 uCi/ml X 2 E 4 ml/min X 60 min/hr X 2000 hr = 0.6 uCi
ALI = 6 E-3 uCi
So .6/6E-3 = X/5 rem
X = 500 rem

## Slide 17: Calculations from start
Have air monitor starts at 12 noon on Monday and finishes 12 noon on Friday
Start flow rate is 40l/min end in 32l/min
  What is total volume of air
Put filter on detector and it reads
100 cnt in one min
  Eff is .05
  What is the activity in uCi
  What is concentration

## Slide 18: cont
Say your radionuclide of interest is U-238
Get ALI
Take concentration from last slide
  Find total inhaled activity
  Compare to ALI
  Total inhaled activity/ALI= dose/5rem
Determine total dose to person

## Slide 19: Particulates
Some large particulates can be collected but using open Petri dishes or other large flat collection pans
Some have a sticky coating to prevent material from being blown off
Can be used to determine particle distribution around a source of particulate radiation.

## Slide 20: Sample protection
Samplers are usually out in the environment but this leaves them open to mercy of the weather
They can be enclosed in a protective housing
  Cannot interfere with sampling
Ideas on protective enclosures!

## Slide 21: GASSES
Gases are hard to capture on filter paper with any reliable efficiency they need to be either
  Adsorbed
  Absorbed
Most are collected using activated charcoal

## Slide 22: Gasses in Air
I-131
Ar-41
Kr -85-89-91-92
Xe-133-135-137-138-139
Radon
H-3

## Slide 23: Iodine
Collected on activated charcoal
Radioactive Iodine (mostly I-131) is significant dose to public
Can be sampled by
  Particulate filter
  Cd-I canister- elemental
  Iodophenol canister- HOI
  AgZeolite canister- organic I
Only Elemental I can get into food chain
Water is big factor in efficiency of I collection
I-131 sampling should be done weekly

## Slide 24: Noble gasses
Can be collected on charcoal but very inefficient
Direct measurement by in stack scint monitors set up with SCA
Can count the daughter products
Large volumes of air can be cooled to a point where only noble gasses are left an they are then counted
Most have short half lives

## Slide 25: Radon
Noble gas
Very dense
densest mononuclear gas
9.73 Kg/m3 (O-1.43 Kg/m3)
Rn 222, 221, 220, and 219 are in nature
222 is most prevalent
Emanation rate is dependant on the concentration of Ra, type of soil, soil moisture and rain
Outdoor concentration are higher
  In the morning
  Dec-Jan

## Slide 26: Radon
Rn is usually 3-10 time higher concentrations inside as outside
Higher in basements that in rest of house
Usually emanates from the ground at .5 pCi/m3 and the Ra concentration is for the soil at 1 pCi/g
Working level(WL) equal to 1.3 E5 Mev of energy emitted by radon daughters equal to about 100 pCi of Rn

## Slide 27: Radon remediation
EPA says need to do something about Rn if concentration gets above 4 pCi/l
Some states have mandatory Rn sampling for homes
Remediation
  Active soil depressurization
  Mechanical ventilation
  Above slab air pressure differential barrier

## Slide 28: Radon Map

## Slide 29
Radon and the Uranium Decay Series
Uranium-238
4.5E9 y
Radium-226
1600 y
Radon-222
3.825 days
Lead-214
27 min (RaB)
Polonium-218
3.1 min (RaA)
Polonium-214
163.7 msec (RaC’)
Bismuth-214
19.9 min (RaC)
Lead-210
22.3 y (RaD)
Notes: Uranium eventually decays into Ra-226 then into Rn-222 and then to Po-218. But the interesting phase change happens in this process. Ra is a solid but Rn is a gas and Po is a solid again. So one of the properties of Rn that makes it so mobile is that it is a gas and can migrate through the soil and get released to either the atmosphere or into a enclosed structure (basement or house). The accumulation in Rn in enclosed spaces may become a problem.

## Slide 30
1. Cracks in Solid Floors
2. Construction Joints
3. Cracks in Walls
4. Gaps in Floors
5. Gaps around Pipes
6. Cavities in Walls
7. The Water Supply
3.
4.
1.
2.
7.
6.
5.
How Does Radon Get in the Home?
Notes: Rn can enter your house in many ways. But it depends on if your house is in an area that is prone to Rn and has an space in which Rn can accumulate many buildings that have a earth floor basement or other on enclosed area can accumulate Rn.

## Slide 31: Radon
Two methods
  Count for Rn directly
  Count for daughters
Charcoal canisters have been used in the past to count radon and daughters
  Gas gets into charcoal and decays
    Count canister in a gamma spect system
  But is weighed to the last 8-10 hours of collection time
Eperm Radelec system
  Collects Rn and then daughters decay in chamber causing a voltage drop in teflon disc
  Calculates radon concentration

## Slide 32: Rn canister

## Slide 33: EPerms

## Slide 34: Track Etch
Thick emulsion (similar to film badge material) can be used to detector Radon gas
It is set out where the gas is and over time the Rn in the air will decay emitting alpha particles
the alpha particle will leave a imprint on the emulsion
When the emulsion is process the tracks will be easy to see and count
The number of tracks it related to the number of alpha particles which is then related to the amount of Rn gas in the air

## Slide 35: Track Etch

## Slide 36: Tritium
Tritium is collected usually as HTO
  higher probability of dose to the public
Drawn into a container that has silica gel in it
Flow rate times time equals total volume of air collected into the container
Sample is then analyzed by liquid scintillation
Concentration of pCi/ml can be calculated
Water samples can be counted directly by putting sample into liquid scintillation vials

## Slide 37: Questions