## Slide 1
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 6.1
Attacking Connected/automated vehicles: V2V and V2I communication
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 2: What is Vehicle-to-Vehicle (V2V) communication?
V2V communication is primarily designed for communication of safety and traffic warnings (e.g. accidents, roadside hazards)
The method of communicating with roadside devices is Vehicle-to-Infrastructure (V2I) communication
<number>

## Slide 3: Vehicle-to-Vehicle (V2V)
<number>

## Slide 4: How does V2V work?
<number>
Intelligent Transportation System (ITS) - a dynamic mesh network between vehicles and roadside devices is the driving force behind the function of V2V
This mesh connects various nodes, whether they be vehicles or roadside devices, in a network and relays information between them
ITS can be used for traffic management, systems, traveler information systems, vehicle control systems, public transportation systems, rural transportation systems, and commercial vehicle operations systems

## Slide 5: ITS in Developing Countries (Video)
<number>
ITS in Developing Countries (Video)

## Slide 6: The Premise of V2V
<number>
In February 2014, the US Department of Transportation announced a desire to implement a mandate which would require V2V-based communication be implemented in all new light vehicles
V2V is the first automotive protocol that considers cybersecurity threats at the design stage as opposed to after the fact
V2V implementation details and interoperation between countries is still in development; therefore, many processes and security measured are still undecided and undetermined, but who knows what the future will hold?

## Slide 7: Methods of V2V Communication
<number>
In V2V communication, vehicles and devices interact in one of three ways:
  Cellular Networks
  Dedicated Short-Range Communication (DSRC)
  Hybrid Method (combination of Cellular & DSRC)

## Slide 8: Methods of V2V Communication (2)
<number>

## Slide 9: Cellular Networks with V2V Communication
<number>
Does not require roadside scanners
Existing cellular networks already have a security system in place; therefore, V2V communication can rely on the existing security methods already in place
  This security is at the wireless level (GSM), not the protocol level
  If a device is using IP traffic, then standard IP security, such as encryption still needs to be applied

## Slide 10: Cellular Networks with V2V Communication (2)
<number>

## Slide 11
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 6.2
Attacking Connected/automated vehicles: IEEE 1609 & Wireless Access in Vehicular Environments (WAVE)
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 12: DSRC with V2V Communication
<number>
Dedicated Short-Range Communication (DSRC)
Requires installation of specialized equipment in modern vehicles and new roadside equipment
Designed specifically for V2V communication so security measures can be implemented prior to the widespread adoption
More reliable than cellular communication with lower latency

## Slide 13: More on DSRC
<number>
It is a one- or two-way short-range wireless communication system that is specifically build for vehicle communications between vehicles and roadside devices, or vehicle to vehicle
Typically operates in the 5.85 to 5.925 GHz band that is specially reserved for V2V and V2I
The transmit power used by DSRC device dictates the range
  Roadside equipment can transmit at higher-power ranges, often up to a 1,000 meter specification
  Vehicles can broadcast only at a power level providing up to 300 meter ranges

## Slide 14: DSRC Wireless Protocols
<number>
DSRC is based on wireless 802.11p and 1609.x protocols
For example, DSRC and Wi-Fi based protocols, such as Wireless Access for Vehicle Environments (WAVE), use IEEE 1609.3 specification, other the WAVE short-message protocol (WSMP)
  These messages are single packets, with no more than 1500 bytes and typically are less than 500 bytes
  You can easily decode WAVE packets with network sniffers such as Wireshark, meaning you can easily sniff network traffic!

## Slide 15: WAVE Packet Architecture
<number>

## Slide 16: DSRC Data Rates
<number>
Data rates with DSRC are totally dependent on the number of users concurrently accessing the local system
A single user would typically see data rates of 6-612 Mbps, whereas users who are in a high-traffic area (such as a busy interstate during rush hour) would see 100-500 Kbps.
A typical DSRC system can handle almost 100 users in high-traffic conditions, but if the vehicles are traveling only 60 km/h (~ 37 mph), the DSRC system could only support around 32 users

## Slide 17: DSRC Band Channels
<number>
We know DSRC uses the 5.9 GHZ band exclusively; however, how many channels does it have?
Answer: it varies between countries!
The US system is designed to support 7 channels, with one channel dedicated as a control channel reserved for sending short, high-priority management packets.

## Slide 18: DSRC Band Channels (2)
<number>
The European design supports 3 channels with no control channels
The reasoning behind this disparity is the fact that each country has different drivers for the technology
Europe is more market driven, whereas the US is more security/safety-driven
The protocols are interoperable, but the types of messages supported and sent will differ greatly

## Slide 19: DSRC Channels in the US
<number>

## Slide 20: Features and Uses of DSRC
<number>
Most European DSRC systems use DSRC for:
Car sharing
Connections to points of interest
Diagnostics and maintenance
Driving profiles for insurance purposes
Electronic toll notification
Fleet management
Parking information

## Slide 21: Roadside DSRC Systems
<number>
These are systems used to pass standardized messages and updates to vehicles with information such as traffic data and hazard info, or road works warnings
The European Telecommunications STandards Institute (ETSI) has designed two formats for continuous traffic data, both utilizing 802.11p:
  Cooperative Awareness Message (CAM)
  Decentralized Environmental Notification Message (DENM)

## Slide 22: CAM for DSRC
<number>
CAMs are typically broadcast periodically through the Vehicle-to-Everything (V2X) network
  ETSI defines the packet size of a CAM message as 800 bytes, and its reporting rate is 2 Hz
CAMs are still in preliminary stages, but should we encounter them in the future, they may be slightly different. What is reported here is what we could expect.

## Slide 23: Station Characteristics in a CAM Packet
<number>
The station characteristics in the CAM packet may consist of any of the following:
Mobile ITS station
Physical relevant ITS station
Private ITS station
Profile parameters
Reference position

## Slide 24: Station Characteristics in a CAM Packet
<number>

## Slide 25: Vehicle Common Parameters in CAM Packet
<number>
Acceleration
Acceleration confidence
Acceleration controllability
Confidence ellipse
Crash status (optional)
Curvature
Curvature change (optional)
Dangerous goods (optional)
Distance-to-stop line (optional)
Door open (optional)
Exterior lights
Heading confidence

## Slide 26: Vehicle Common Parameters in CAM Packet (2)
<number>
Occupancy (optional)
Station length
Station-length confidence (optional)
Station width
Station-width confidence (optional)
Turn advice (optional)
Vehicle speed
Vehicle-speed confidence
Vehicle type
Yaw rate
Yaw rate confidence

## Slide 27: DENMs for DSRC
<number>
DENMs are event-driven messages, whereas CAMS are periodically sent so that they’re regularly updated.
DENMs are triggered by safety and road hazard warnings

## Slide 28: DENMs for DSRC (2)
<number>

## Slide 29: DENM Packet Architecture
<number>

## Slide 30: DENMs for DSRC
<number>
DENMs may be sent for the following cases:
Collision risks (determined by roadside devices)
Entering hazardous locations
Hard braking
High wind levels
Poor visibility
Precipitation
Road adhesion
Road work
SIgnal violations
Traffic jams
Vehicles involved in an accident
Wrong-way driving

## Slide 31: WAVE Short-Messaging Protocol (WSMP)
<number>
WSMP is used in both service and control channels
It uses IPv6 for service channels only
  IPv6 is configured by WAVE management entity (WME) and also handles channel assignments and monitors service announcements
  WME is unique to WAVE, and handles the overhead and maintenance of protocol
Control channels are used for service announcements and short messages from safety applications

## Slide 32: WAVE Short-Messaging Protocol (WSMP)
<number>
WSMP is used in both service and control channels
It uses IPv6 for service channels only
  IPv6 is configured by WAVE management entity (WME) and also handles channel assignments and monitors service announcements
  WME is unique to WAVE, and handles the overhead and maintenance of protocol
Control channels are used for service announcements and short messages from safety applications

## Slide 33: WSRC Message Architecture
<number>

## Slide 34: WAVE Service Announcement (WSA)
<number>
The actual announcement of a service comes from a WSA packet.
The type of application provided by a roadside device, or hosted by a vehicle, is defined by the provider service identifier (PSID)

## Slide 35: WAVE Service Announcement (WSA)
<number>

## Slide 36: Tracking Vehicles with DSRC
<number>
You can actually attack other vehicles utilizing DSRC communication via vehicle tracking
If attackers can create their own DSRC receiver by buying a DSRC-capable device or using a software-defined radio (SDR), they could receive information about vehicles within the receiver’s range and use the information to track a vehicle. Some pertinent information that may be useful to an attacker is:
  Length
  Body width
  Body height
  Bumper height
All of that info should be relatively accurate down to a fraction of an inch since it is set by the manufacturer

## Slide 37
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 6.3
Attacking Connected/automated vehicles: Attacking Wireless Systems
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 38: Attacking Wireless Systems with SDR
What is an SDR?
An SDR is a Software-Defined Radio, which usually has an RF front-end with an FPGA or programmable System-on-Chip (SoC) to perform digital functions
They range in cost anywhere from $20 -$2000
The most influencing factor on cost is the sample rate, which is the number of samples of audio carried per second.
The larger the sample rate, the more bandwidth that can be simultaneously watched - but also, the greater the cost
<number>

## Slide 39: What is an SDR?
<number>

## Slide 40: What is signal modulation?
Signal modulation is the way you represent binary data using a wireless signal.
This comes into play when you need to be able to tell the difference between a digital 1 and a digital 0.
There are two common types of digital signal modulation: amplitude-shift keying (ASK) and frequency-shift keying (FSK)
<number>

## Slide 41: Amplitude-Shift Keying (ASK)
When ASK modulation is used, the bits are designated by the amplitude of the signal.
They are transmitted in carrier waves, which is the amplitude of the carrier.
When there is no wave, the carrier wave is the signal’s resting state.
When the carrier line is high for a specific duration, registering as a wave, it is a binary 1.
<number>

## Slide 42: Amplitude-Shift Keying (ASK) (2)
When the carrier line is at a resting state for a shorter duration, it is a binary 0.
ASK modulation is also known as On-Off Keying (OOK), and typically uses a start-and-stop-bit.
Start-and-stop bits are common ways to separate when a message starts and where it stops.
<number>

## Slide 43: Frequency-Shift Keying (FSK)
FSK always has a carrier signal, but that signal is instead measured by how quickly it changes - its frequency.
In FSK, a high-frequency signal is a 0, and a low-frequency signal is a 1.
When the carrier waves are close, that’s a 1; when they’re spaced far apart, that’s a 0.
<number>

## Slide 44: Frequency-Shift Keying (FSK) Graph
<number>

## Slide 45: TPMS Hacking (Video)
<number>

## Slide 46: What is TPMS?
The TPMS is a device which sits inside the tire of a car and sends data on tire-pressure readings, wheel rotation, temperature, and also warnings about certain conditions, such as low sensors batteries, to the ECU.
The data is displayed via gauges, digital displays, or warning lights.
In fall of 2000, the US enacted the Transportation Recall Enhancement, Accountability and Documentation (TREAD) Act, which required all new vehicles to have a TPMS system installed.
<number>

## Slide 47: What is TPMS?
<number>

## Slide 48: TPMS Signals
The TPMS device sits inside the wheel and transmits wirelessly into the wheel well, which allows its signals to be partially shielded by the body of the vehicle to prevent too much leakage.
Most TPMS systems use a radio to communicate with the ECU.
The signal frequency varies between devices, but it typically runs at 315 MHz or 433 MHz UFF, and uses either ASK or FSK modulation.
Some TPMS systems use Bluetooth, which has its own pros and cons:
  Bluetooth has a greater default range!
  Bluetooth protocol can also enable secure communication.
<number>

## Slide 49: TPMS Signals
<number>

## Slide 50: Eavesdropping with a Radio Receiver
TPMS systems have very weak signals, and as such, don’t leak data too far from the vehicle. To overcome this, you will need to add a low-noise amplifier (LNA) to your radio receiver to increase sniffing range.
  This will allow you to capture a TPMS signal from the side of the road or from a vehicle traveling alongside the target.
TPMS sensors transmit only every 60-90 seconds, and sensors usually aren’t required to send data until the vehicle is traveling at 25 mph or higher. However, many sensors transmit even when the car is idle, and some transmit even when the car is off.
<number>

## Slide 51: Eavesdropping with a Radio Receiver (2)
The best way to know how your target TPMS sensor works is to listen for packets with the vehicle completely off.
You will need to decode the signal - there is a free tool made by Jared Boone, and can be found at (https://github.com/jboone/gr-tpms/)
<number>

## Slide 52: TPMS Packets
<number>

## Slide 53: TPMS Packets
The SensorID is a 28- or 32-bit number unique to each sensor and registered with the ECU.
If your goal is to only fingerprint a target for tracking or triggering an event, then the SensorID field is probably the only part of the packet you’ll want.
The Pressure and Temperature fields contain readings from the TPMS device.
The Flags field can contain extra metadata, such as warnings about a low battery.
When determining packet encoding, check whether Manchester encoding was used. Manchester encoding is commonly used in near-field devices, like TPMS systems.
<number>

## Slide 54: Activating a Signal
TPMS sensors typically transmit around once per minute; rather than wait 60 seconds for a packet, an attacker can send a 125 kHz activation signal to the TPMS device with an SDR.
The interception of the response needs to be timed carefully since there is a delay between when the activation signal is sent and when the response is transmitted.
The activation signal is designed primarily for TPMS test equipment, so getting it working for a moving vehicle might be difficult. This will be easier if the target vehicle sends packets when it’s stationary or off.
TPMS sensors don’t use input validation, so the ECU will check to make sure it recognizes only the SignalID.
<number>

## Slide 55: Event Triggering
Besides simply tracking a vehicle, TPMS can also be used to trigger an event, such as opening a garage door or something malicious such as dealing with explosives.
Since you have four (4) tires, the attacker would have reasonable assurance that they have the correct vehicle if they receive a signal for each tire.
Using all four tires would allow you to create a basic, but accurate sensor fingerprint for a target vehicle.
<number>

## Slide 56: Sending Forged Packets
Once you have access to the TPMS signal, you can actually send your own forged packets by setting up the GNU Radio as a transmitter instead of a receiver.
By forging packets, you can spoof dangerous PSI and temperature readings and also cause other engine lights to trigger.
<number>

## Slide 57: Sending Forged Packets
It’s possible to drain a vehicle’s battery by flooding the sensor with activation requests as well.
NOTE: Shutting down the ECU while a vehicle is traveling at a high speed could be extremely dangerous, so be sure to take necessary precaution when playing with TPMS!
<number>

## Slide 58: Key Fob Basics
In 1982, radio-frequency identification (RFID) was first introduced into remote keyless entry systems via the Renault Fuego. Earlier systems used infrared light sources.
Today’s systems use a key fob to send an RFID signal to a vehicle to remotely unlock doors or even start a vehicle.
The key fob uses a transponder operating at 125 kHz to communicate with an immobilizer in the vehicle, preventing the vehicle from starting unless it receives the correct code or token.
<number>

## Slide 59: Key Fob Basics (2)
<number>

## Slide 60: Key Fob Hacks
There are multiple ways to hack key fob systems, including:
  Jamming the key fob signal
  Pulling response codes from memory
  Brute-forcing a key code
  Forward-Prediction Attacks
  Dictionary Attacks
  Dumping the Transponder Memory
  Reversing the CAN Bus
  Key Programmers and Transponder Duplication Machines
<number>

## Slide 61: Jamming the Key Fob Signal
You can jam the key fob signal by passing garbage data within the RFID receiver’s passband, which is the area the receiver is listening to for a valid signal.
The width of the passband window includes some extra space where you can add noise to prevent the receiver from changing the rolling code, while still allowing the attacker to view the correct key sequence.
<number>

## Slide 62: Jamming the Key Fob Signal
<number>

## Slide 63: Jamming the Key Fob Signal (2)
While holding onto the valid unlock request in memory, the attacker waits for another request to be sent, and records that request too.
The attacker can replay the first valid packet to the vehicle, which causes the car to unlock or lock (depending on signal sent by key fob).
When the car owner leaves the vehicle, the attacker has the last valid key stored and can replay it to either open the vehicle doors, or even start the vehicle.
<number>

## Slide 64: Jamming Key Fob Signal: Samy Kamkar at DEFCON 23 Demonstration (Video)
<number>

## Slide 65: Pulling Response Codes from Memory
It’s possible to find the response code still in immobilizer’s memory, even a few minutes after the key fob has stopped sending signals.
This provides a window of opportunity to start the car, not by capturing signals live from a key fob, but rather by pulling the signal from the immobilizer’s memory.
If an area of memory can be identified to contain this info, then the attacker needs to either quickly get access to the vehicle, or have a device on the vehicle that can respond to record this info.
<number>

## Slide 66: Pulling Response Codes from Memory (2)
<number>

## Slide 67: Brute-Forcing a Key Code
Some response codes can be accessed by brute force, though the feasibility of a brute-force attack depends on key code length and algorithm.
In order for a brute-force attack to succeed, the attacker needs to build custom software to brute-force the key using an SDR, a custom hardware component, or a combination of the two.
<number>

## Slide 68: Brute-Forcing a Key Code - Samy Kamkar Demonstration (Video)
<number>

## Slide 69: Forward-Prediction Attacks
If an attacker is able to observe challenge-response exchanges occurring when the key fob sends a signal to the vehicle, and the vehicles transponder responds, the attacker can perform a forward-prediction attack.
In this attack, the attacker observes multiple challenges, and from these, predicts what the next challenge request will be.
If the transponder’s psuedo-random number generator (PRNG) is weak, the attack may succeed.
<number>

## Slide 70: Dictionary Attacks
If an attacker can record numerous valid challenge-response exchanges between the key fob and transponder, they can store them in a dictionary and then use the collected key pairs to repeatedly request challenges from the transponder until one challenge matches a response in the dictionary.
This attack is possible only when the keyless entry system doesn’ts use sender verification to make sure responses are valid.
The attack would also need to be able to continuously request authentication from transponder.
<number>

## Slide 71: Dictionary Attacks (2)
To perform the dictionary attack, the attacker would need to build a system to trigger the key fob request and record the exchange with an SDR.
An Arduino wired to the button press of the researcher’s valid key fob could also suffice.
Assuming the authentication takes place over CAN, it is also possible to grab the key fob ID over ultra-high frequency and attempt to gather the key stream by replaying and recording the communication over the CAN bus.
<number>

## Slide 72: Key Fob Attack: Getting into a Tesla Model S (Video)
<number>

## Slide 73: Attacking a PKES System
Passive Keyless Entry and Start (PKES) systems are very similar to traditional transponder immobilizer systems, except that the key fob can remain in the owner’s pocket and no button needs to be pressed.
When a PKES system is implemented, antennae in the vehicle read RFID signals from the key fob when it’s in range.
PKES key fobs use a low-frequency (LF) RFID chip and an ultra-high-frequency (UHF) signal to unlock or start the vehicle.
<number>

## Slide 74: Attacking a PKES System
<number>

## Slide 75: PKES Systems
The vehicle ignores UHF signals from the key fob if the LF RFID isn’t seen (meaning the key isn’t nearby).
The RFID on the key fob receives a crypto challenge from the vehicle, and the microcontroller on the key fob solves this challenge and responds over the UHF signal.
<number>

## Slide 76: PKES Systems (2)
Some vehicles use RFID sensors inside the vehicle to triangulate the location of the key fob to ensure the key fob is inside the vehicle.
If the battery dies in a PKES key fob, there’s typically a hidden physical key in the fob that will unlock the door, though the immobilizer will still use the RFID to verify the key is present before starting the vehicle.
<number>

## Slide 77: PKES Attack (Video)
<number>

## Slide 78: Relay Attacks in PKES Systems
<number>
In a relay attack, an attacker places a device next to the car and another next to the owner or holder of the key fob (target).
The device relays the signals between the target’s key fob and the vehicle, enabling the attacker to start the car.

## Slide 79: Relay Attacks in PKES Systems
<number>
The relay tunnel can be set up to communicate over any channel that’s fast and has a larger range than the normal key fob.
Packets would go from the target’s key fob into the device to be transmitted over cellular and replayed by the laptop.

## Slide 80: Amplified Relay Attacks in PKES Systems
<number>
An amplified relay attack uses the same basic principles as a relay attack but with only a single amplifier.
The attacker stands by the target vehicle and amplifies the signal, and if the target is nearby with the key fob, the vehicle will unlock.
This is an unsophisticated attack that simply increases the range of vehicle’s sensors.

## Slide 81: Immobilizer Cryptography
<number>
Immobilizer systems are usually created using a combination of cheap components; as such, manufacturers need to be creative with things like cryptography. Cryptography introduces numerous weaknesses into the systems…
Some immobilizer vendors make the common mistake of creating their own crypto and hiding it behind some trade secret clause that’s designed to protect it instead of validating it with public structiny.
This method is known as security through obscurity

## Slide 82: Immobilizer Cryptography (2)
<number>
The immobilizer-key exchange uses a challenge-response system and PRNGs. The PRNG is equally important as the crypto algorithm, as a poor PRNG can lead to predictable results regardless of how good your crypto algorithm is.

## Slide 83: Immobilizer Cryptography (3)
<number>
The typical key exchange implementation follows this general sequence:
  The immobilizer sends a challenge to the key using a PRNG.
  The key encrypts the challenge using a PRNG and returns it to the immobilizer.
  The immobilizer sends a second random number challenge.
  The key encrypts both challenges and returns them to the immobilizer.

## Slide 84: Different Cryptographic Systems
<number>
EM Micro Megamos
EM4237
Hitag 1
Hitag 2
Hitag AES
DST-40
DST-80
Keeloq
Open Source Immobilizer Protocol Stack

## Slide 85: EM Micro Megamos
<number>
Introduced: 1997
Manufacturer: Volkswagen/Thales
Key Length: 96 bits
Algorithm: Proprietary
Vehicles: Porsche, Audi, Bentley, Lamborghini
Crack Status: Broken, but attack methods have been censored by lawsuit

## Slide 86: EM Micro Megamos
<number>

## Slide 87: EM4237
<number>
Introduced: 2006
Manufacturer: EM Microelectronic
Key Length: 128 bits
Algorithm: Proprietary
Vehicles: Unknown
Crack Status: No known published cracks

## Slide 88: Hitag 1
<number>
Introduced: Unknown
Manufacturer: Philips/NXP
Key Length: 32 bits
Algorithm: Proprietary
Vehicles: Unknown
Crack Status: Broken

## Slide 89: Hitag 2
<number>
Introduced: 1997
Manufacturer: Philips/NXP
Key Length: 48 bits
Algorithm: Proprietary
Vehicles: Audi, Bentley, BMW, Chrysler, Land Rover, Mercedes, Porsche, Saab, Volkswagen, and more
Crack Status: Broken

## Slide 90: Hitag AES
<number>
Introduced: 2007
Manufacturer: Philips/NXP
Key Length: 128 bits
Algorithm: AES
Vehicles: Audi, Bentley, BMW, Porsche
Crack Status: No known published cracks

## Slide 91: DST-40
<number>
Introduced: 2000
Manufacturer: Texas Instruments
Key Length: 40 bits
Algorithm: Proprietary (unbalanced Feistel cipher)
Vehicles: Ford, Lincoln, Mercury, Nissan, Toyota
Crack Status: Broken

## Slide 92: DST-80
<number>
Introduced: 2008
Manufacturer: Texas Instruments
Key Length: 80 bits
Algorithm: Proprietary (unbalanced Feistel cipher)
Crack Status: No known published cracks

## Slide 93: Keeloq
<number>
Introduced: Mid-1980s
Manufacturer: Nanoteq
Key Length: 64 bits
Algorithm: Proprietary (NLFSR)
Vehicles: Chrysler, Daewoo, Fiat, General Motors, Honda, Jaguar, Toyota, Volkswagen, Volvo
Crack Status: Broken

## Slide 94: Keeloq (2)
<number>

## Slide 95: Open Source Immobilizer Protocol Stack
<number>
Introduced: 2011
Manufacturer: Atmel
Key Length: 128 bits
Algorithm: AES
Crack Status: No known published cracks

## Slide 96: Physical Attacks on Immobilizer System
<number>
There are three different classifications of physical attacks on the immobilizer system:
  Attacking Immobilizer Chips
  Brute-Forcing Keypad Entry
  Hotwiring

## Slide 97: Attacking Immobilizer Chips
<number>
It’s actually possible to completely remove the immobilizer chip (typically from the vehicle’s ECU) and still operate a vehicle.
In order to physically remove immobilizer-based security, you can purchase or build an immobilizer bypass chip and then solder it where the original immobilizer chip was to keep the rest of the ECU happy.
  These chips, referred to immo emulators, typically cost $20-$30.

## Slide 98: Attacking Immobilizer Chips
<number>

## Slide 99: Brute-Forcing Keypad Entry
<number>
The method for brute-forcing a keypad lock on a vehicle was discovered by Peter Boothe, available at (http://www.nostarch.com/carhacking/)
If the vehicle has keypad under the door handle with buttons labeled “1/2, 3/4, 5/6, 7/8, 9/0”, you can enter a long key sequence in about 20 minutes. (Found on pp. 228-230 of textbook).
This works because the key codes roll into one another; the vehicle doesn’t know where one code ends and the other starts.

## Slide 100: Hotwiring
<number>
This has been obsolete since the mid-1990s, but it’s still seen in movies today.]
To hotwire a susceptible car, you would remove the steering wheel to expose the ignition cylinder and typically three bundles of wires.
Using the car’s manual or simply by tracing wires, you’d locate the ignition-battery bundle and starter wire.
Next, you’d strip the battery and ignition wires and twist them together.
Then, you’d “spark” the bundle with the starter wire and start the car. Once the car starts, you’d remove the starter wire.

## Slide 101: Hotwiring (2)
<number>

## Slide 102: Security Concerns with V2V Communication
<number>
Aside from DSRC, there are other attack potentials in the implementation of V2V
These were investigated by Crash Avoidance Metrics Partnership (CAMP), which is a group of several auto manufacturers working to conduct different safety-related studies
  These took place in December 2010
CAMP performed an attack analysis on V2V systems through its Vehicle Safety Consortium (VSC3).
The analysis focused primarily on the core DSRC/WAVE protocol and attempted to simulate an attacker’s objectives with potential attacks

## Slide 103: Results of Crash Avoidance Metrics Partnership (CAMP) Tests
<number>
Shows some goals a malicious actor may have when attacking V2V systems, and perhaps some of the attacks they would launch
Top columns define an attacker’s possible objectives and areas they may focus on

## Slide 104: Results of CAMP Tests
<number>

## Slide 105
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 6.4
Attacking Connected/automated vehicles: Potential attacks on automated vehicles
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 106: Automated Vehicles
<number>
These vehicles help to improve the safety of passengers and increase the efficiency of transportation by interacting with the external world through V2X and V2V communications.
By sharing data like speed, position, and heading angle help to predict the succeeding location of the vehicle.
Using Sensor technologies, maneuvering of roads and terrains becoming easier and with the help of predetermined knowledge

## Slide 107: Why are autonomous vehicles more vulnerable to attacks?
<number>
Compared to conventional vehicle autonomous vehicle has to communicate with other vehicles and infrastructure which are external networks and may become a channel for attack and an opportunity for hackers.
For autonomous vehicles, vast information has to be processed particularly deep learning algorithms are used in processing image related data which are prone to adversarial attacks and the probability of false positives increases with increase in the amount of data to be processed.

## Slide 108: Why are autonomous vehicles more vulnerable to attacks? (2)
<number>
As the technology is in the nascent stage in both hardware and software and not yet rigorously tested because of which it is difficult to make it reliable in all conditions and also autonomous vehicles are prone to bugs and vulnerabilities also which can be exploited by the attackers.

## Slide 109: Attacks exploiting the vulnerabilities in various sensors of vehicle
<number>
Global Positioning System (GPS)
Inertial Measurement Unit (IMU)
Light Detection and Ranging (Lidar)
Monoscopic and Stereoscopic Cameras

## Slide 110: Global Positioning System (GPS)
<number>
provision of free access to the data with transparent architecture helping the hackers to mislead or manipulate the data to provide the wrong directions or to control the routing of the vehicle.
This lead to the security and safety issues of the passengers.
Misleading of the GPS signals is known as GPS spoofing and jamming where hackers transmit the unrealistic signal/data.

## Slide 111: Inertial Measurement Unit (IMU)
<number>
IMU is the combination of the Gyroscope and Accelerometers which provides the data of velocity, acceleration, and orientation of the vehicle. They also monitor the change in the environmental dynamics like the gradient.
The data provided by the sensors can be modified or not to recognize the gradient of the road. It causes the vehicle to moves slow on the gradient roads which intern slow down the following vehicles.

## Slide 112: Light Detection and Ranging (Lidar)
<number>
Light Detection and Ranging (LiDAR) is used to localize the environment, obstacle detection, and avoidance. It based on the technology, time taken by the light to travel to and fro to the vehicle determine’s the distance at which the object is located.
If the hacker sends a signal of the same frequency to the scanner and to assume the object is detected. It makes the Autonomous vehicle to move slowly or stop.

## Slide 113: Monoscopic and Stereoscopic Cameras
<number>
Cameras are used to detect lane detection, traffic sign recognition, headlight detection, obstacle detection, etc.
Functioning of cameras can be partially disabled by using high beam torches or headlights of the opposite vehicles. It may introduce the safety concerns like false detection or not detection of the objects.

## Slide 114: Vehicular Adhoc Network (VANET) attacks
<number>
Attacks on Internal Networks
  Passcode and Key attacks: passcode and keys are one of the safety features of the connected cars. Multiple attempts may crack the password or keys which works on the IR based technologies can be easily hacked.
Attacks on External Networks
  V2X Network Attacks: It can connect to a smartphone,cloud and other devices and communicate which is described as the V2X communication. Connecting to a smartphone is always a risk for a vehicle as it is interacting with an external unfamiliar device.

## Slide 115: Vehicular Adhoc Network (VANET) attacks (2)
<number>
Distributed Denial Of Services (DDOS)
  Denial of service is one of the most vulnerable threats that connected cars may experience. Service of the system denied by the several attacking mechanisms which results in disruption of the traffic flow and damages to the infrastructure. It may cause the collision of the vehicles, a life threat for the passengers.

## Slide 116: Hardware attacks and exploits
<number>
OBD port based attack:
  OBD stands for onboard diagnostics and OBD port is present in almost all the vehicles manufactured from 2008. OBD port is used for collecting the diagnostics data of the vehicle. It gives the data about the vehicle faults and performance. once connected PC can send and receive the data to and from the vehicle ECU’s and with a possible exploitation can also manipulate the data packets and inject malicious packets into the vehicle network.

## Slide 117: Hardware attacks and exploits (2)
<number>
ECU Firmware tampering attack:
  ECU code is propitiatory making it safe and secure but attackers started targeting recent attacks by re flashing the ECU with custom firmware altering its state and inducing malicious and unintended actions.

## Slide 118: Hardware attacks and exploits (3)
<number>
Rogue updates:
  Firmware updates in the connected cars are one of the sources for the Rogue updates. These updates are not from the manufacturer and lack of proper updates with safety and security. they are prone to the severe cyber attacks which leak private data of the vehicle. It allows hackers to provide enough security weakness to introduce malware and control the firmware of the connected cars.

## Slide 119: Adversarial Attacks on Autonomous vehicles
<number>
Deep Learning is based on the probabilistic estimation for the classification tasks predicting the data belonging to a particular class with a certain level of probability and when the probability is higher then we say that class has higher confidence.

## Slide 120: Adversarial Attacks on Autonomous vehicles (2)
<number>
Deep learning algorithms like Deep Neural Networks (DNN’s) are start of the art techniques that are used in the autonomous vehicles for perception and sensing.

## Slide 121: Adversarial Attacks on Autonomous vehicles (2)
<number>
Deep learning algorithms like Deep Neural Networks (DNN’s) are start of the art techniques that are used in the autonomous vehicles for perception and sensing.

## Slide 122: Adversarial Attacks on Autonomous vehicles (3)
<number>
But DNN’s are prone to certain adversarial attacks making the autonomous vehicles vulnerable to such attacks.Adversarial attack is a form of attack in which the small noise or perturbations are added to the original data misleading and deceiving the DNN’s decision making which may create dangerous consequences.

## Slide 123: Miscellaneous Attacks
<number>
Numerous attacks were getting implemented by many researchers and hackers. Gaining access to key less entry system by spoofing, Malware attacks and applications that installed in the infotainment and navigation systems.
New types of attacks like attacking the electric vehicle by exploiting the electric charger which is connecting and logging the data.

## Slide 124
<number>
Thank You
References:
C. Smith, "In-Vehicle Infotainment Systems," in THE CAR HACKER’S HANDBOOK A Guide for the Penetration Tester, William Pollock, 2016.
C. Smith, "Vehicle-to-Vehicle Communication," in THE CAR HACKER’S HANDBOOK A Guide for the Penetration Tester, William Pollock, 2016.
A. D. Kumar, K. N. R. Chebrolu, R. Vinayakumar, and S. K. P, “A brief survey on autonomous vehicle possible attacks, exploits and vulnerabilities,” CoRR, vol. abs/1810.04144, 2018. [Online]. Available: http://arxiv.org/abs/1810.04144