## Slide 1
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 3.1
Automotive electronics and ECUs: Introduction to ECUs, software, and firmware
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 2: Intro. to ECUs
The knowledge about ECUs and their software and firmware are very important for learning about potential attacks on vehicles.
ECUs are covered in the following CAAT course. In this topic, a summary of important topics about ECUs are provided. For more details, the following course can be used:
- Automated, Connected, and Intelligent Vehicles
<number>

## Slide 3: What is an ECU?
A vehicle typically has as many as a dozen or more electronic controllers, many of which are networked to communicate with each other.
These computerized devices go by many different names, including electronic control unit or engine control unit (ECU), transmission control unit (TCU), or transmission control module (TCM).
<number>

## Slide 4: What is an ECU? (2)
Brake Control Module (BCM or EBCM), Central Control Module (CCM), Central Timing Module (CTM), General Electronic Module (GEM), Body Control Module (BCM), Suspension Control Module (SCM), control unit, or control module.
<number>

## Slide 5: Example-Engine control module
It is a type of electronic control unit that controls a series of actuators on an internal combustion engine to ensure optimal engine performance.
It does this by reading values from a multitude of sensors within the engine bay, interpreting the data using multidimensional performance maps (called lookup tables), and adjusting the engine actuators.
<number>

## Slide 6: Example-Electronic engine management system
If the ECU has control over the fuel lines, then it is referred to as an electronic engine management system (EEMS).
The fuel injection system has the major role to control the engine's fuel supply. The whole mechanism of the EEMS is controlled by a stack of sensors and actuators.
<number>

## Slide 7: ECU software
The ECU software can be roughly subdivided into two sections:
The application contains the desired functionality
the infrastructure software handles basic functions.
<number>

## Slide 8: Infrastructure software
Usually the infrastructure software includes the operating system and software components for communication and underlying I/O and memory services.
<number>

## Slide 9: Programmability
A special category of ECUs are those which are programmable; these units can be reprogrammed by the user.
When modifying an engine to include aftermarket or upgrade components, stock ECUs may or may not be able to provide the correct type of control for the application(s) in which the engine may be used
<number>

## Slide 10: Programmability (2)
To accommodate for engine modifications, a programmable ECU can be used in place of the factory-shipped ECU.
Typical modifications that may require an ECU upgrade can include turbocharging, supercharging, or both, a naturally aspirated engine; fuel injection or spark plug upgrades, exhaust system modifications or upgrades, transmission upgrades, and so on.
<number>

## Slide 11: Programmability (3)
Programming an ECU typically requires interfacing the unit with a desktop or laptop computer; this interfacing is required so the programming computer can send complete engine tunings to the engine control unit as well as monitor the conditions of the engine in realtime. Connection typically used in this interface are either USB or serial.
<number>

## Slide 12
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 3.2
Attacking vehicles: ECU Hacking
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 13: Outline: Attacking ECUs
The ECU is a common target of reverse engineering, sometimes referred to as chip tuning.
The most popular ECU hack is modifying the fuel map to alter the balance of fuel efficiency and performance in order to give you a higher-performance vehicle.
<number>

## Slide 14: ECU HACKING
Electronic control unit
A vehicle typically has as many as a dozen or more electronic controllers, many of which are networked to communicate with each other
Let's attempt to look inside
<number>

## Slide 15: Gaining Entrance
Front Door Attacks
  Commandeering the access mechanism of the original equipment manufacturer (OEM)
Back Door Attacks
  Applying more traditional hardware-hacking approaches
Exploits
  Applying more traditional hardware-hacking approaches
It’s worth remembering that while the goal for ECU and other control module hacking is often the same to gain access in order to reprogram and change behavior it’s unlikely there’ll be a “master key” for all controllers.
<number>

## Slide 16: Reversing Automotive Firmware
At this point, you probably have anywhere from 4KB to 4MB of raw machine-ready code, with a mixture of various parameters and actual code that forms the program the processor will run.
First, you must know which chip this binary is for. There are several free decompilers for different chips out on the Internet.
Otherwise you can drop some cash and buy IDA Pro, which supports a large variety of chips.
<number>

## Slide 17: Reversing Automotive Firmware (2)
The next stage is to figure out what exactly you are looking at. When you’re starting to analyze raw data, a high-level understanding of the function of the devices you’re reverse engineering will be key to knowing what to look for.
When you’re starting to analyze raw data, a high-level understanding of the function of the devices you’re reverse engineering will be key to knowing what to look for. You can follow a number of breadcrumbs, or clues, for starters; these breadcrumbs are almost guaranteed to lead you to interesting and useful material.
<number>

## Slide 18: Automotive controller functions
Every engine controller has some type of self-diagnostic system that typically monitors most critical engine functions, and analyzing this is an excellent route to understanding firmware.
Self-Diagnostic System
Library Procedures
Finding Known Tables
<number>

## Slide 19: Self-Diagnostic System
Every engine controller has some type of self-diagnostic system that typically monitors most critical engine functions, and analyzing this is an excellent route to understanding firmware
first step in investigative disassembly is to identify the location of these procedures.
For example, knowing that code 10 refers to a failed intake air temperature sensor means you can find the piece of code that sets error code 10 to help you identify the internal variables associated with the air temperature sensor.
<number>

## Slide 20: Library Procedures
Being able to change the behavior of a control unit is often one of the primary goals of reverse engineering ECU firmware, and identifying data used by a controller is an important step in the process.
Most ECUs have a set of library functions used for routine tasks throughout the code.
Library functions used for table lookups are worth identifying early on in the reverse engineering process, as these can lead straight to the parameters you’re interested in
<number>

## Slide 21: Library Procedures (2)
Usually each type of data stored within the ECU—one-dimensional array of bytes; two-dimensional array of words; three-dimensional array of unsigned, signed, and float shorts; and so on.
Often, table lookup routines can be reused to pass information about the structure of the table, such as how many rows and columns are present.
A secondary characteristic of these lookup routines is that they tend to have lots of interpolation math.
<number>

## Slide 22: Finding Known Tables
One way to identify tables is to leverage the specific physical and electrical characteristics of vehicle sensors, which will display identifiable characteristics within ECU firmware.
For example, an ECU with a MAF sensor will have a table that translates raw readings of voltage or frequency from the MAF into airflow into the engine, providing an internal representation.
the signal output from an MAF is determined by physics—that is, King’s Law—so the curve will always have a characteristic shape, though it’ll be slightly different for each sensor.
<number>

## Slide 23: Finding Known Tables (2)
show similarly shaped Ford and Nissan sensor curves; the similarity they illustrate extends to multiple manufacturers.
<number>

## Slide 24: Finding Known Tables (3)
five different views of the same data.
<number>

## Slide 25: Parameter identification
Generally, data representation formats are dictated by the hardware present. Knowing the size of registers on the MCU running the show can be a big help for identifying parameters.
Comparing Bytes to Identify Parameters
Identifying ROM Data with WinOLS
<number>

## Slide 26: Comparing Bytes to Identify Parameters
It’s often possible to get multiple bins that’ll run on the same physical ECU. The more the better! Doing a simple compare in a hex editor will show which bytes differ between the files.
If less than 5 percent of the files differ, it’s generally safe to assume that the differences are parameters. If you know what’s been changed functionally between the two bins and you know which bytes have changed, you have further clues to help correlate changes in the ROM with changes in parameters.
<number>

## Slide 27: Comparing Bytes to Identify Parameters (2)
compare a 1996 V8 Mustang and a 1997 V6 Thunderbird, showing 6,667 differences out of 114,688 bytes.
<number>

## Slide 28: Identifying ROM Data with WinOLS
If the ROM type is known, it has many templates that automatically identify configuration parameters.
Most of the known built-in ROM types are geared toward Bosch Motronic ECUs. Templates and configurations can be saved, shared, and sold to enable users to make modifications to specific files with greater ease. WinOLS is arguably the most common software used for identifying interesting data within a ROM that doesn’t involve code analysis. It’s designed to facilitate rapid tuning changes to a controller.
<number>

## Slide 29: Code Analysis
Code analysis can be a long, complicated task.
When analyzing a new target, first identify the architecture you’re working with. Knowing what processor executed the blob of binary will help you choose an appropriate software tool to further assist. If you can’t identify a processor based on the markings on the chip itself, search online for data sheets to identify it.
To analyze code, you might need to find a disassembler. A quick Google search reveals that there are lots of them out there.
Bust out the disassembly tools and start trying to make sense of the mess, but this might take hundreds of hours.
<number>

## Slide 30: Code Analysis (2)
OEMs love to patent stuff. If you can find the patents relevant to your system, you may end up with a guided tour of the code being disassembled.
Look at any available software for manipulating the ECU at hand for insight into the structure and purpose of code segments.
Otherwise, start with a wiring diagram for the vehicle, and trace connections back through ECU circuitry to particular pins on the MCU.
<number>

## Slide 31: A Plain Disassembler at Work
(a plain disassembly of a 1990 Nissan 300ZX Twin Turbo ROM.)
This ECU has a 28-pin external 27C256 EPROM, so it’s relatively easy to obtain its contents. This particular platform uses a HD6303 MCU, a derivative of the Motorola 6800 8-bit MCU that appears to be supported by the free disassembler DASMx (see http://www.16paws.com/ECU/DASMxx/DASMx.htm).
<number>

## Slide 32: A Plain Disassembler at Work (2)
(a plain disassembly of a 1990 Nissan 300ZX Twin Turbo ROM.)
<number>

## Slide 33: Interactive Disassemblers
As of this writing, IDA Pro is the most popular interactive disassembler available.
One of the advantages of IDA Pro is that it’s programmable to allow additional opcodes for customizing automotive processors and plugins for further processing disassembled code
IDA Pro supports more embedded platforms out of the box than just about any other disassembler currently available.
You don’t necessarily need these functions to successfully analyze code, but they make things substantially easier.
<number>

## Slide 34: Interactive Disassemblers (2)
(screenshots from real code analysis with IDA Pro)
<number>

## Slide 35: ECU test bench
An ECU test bench, like the one shown in Figure 7-1, consists of:
  an ECU
  a power supply
  an optional power switch
  an OBD-II connector
<number>

## Slide 36: ECU test bench (2)
<number>

## Slide 37: ECU test bench (3)
<number>
You can also add an IC or other CAN-related systems for testing, but just building a basic ECU test bench is a great way to learn the CAN bus and how to create custom tools.

## Slide 38: The Basic ECU Test Bench
<number>
To make it easier to turn the device on and off, you can add a switch to the power supply.
An OBD port allows for specialized mechanics tools to communicate with the vehicle’s network.
In order for that OBD port to fully function, we need to expose the vehicle’s network wires from the ECU to the OBD port.

## Slide 39: Finding an ECU
<number>
One place to find an ECU is, of course, at the junkyard.
You’ll typically find the ECU behind a car’s radio in the center console or behind the glove box.
If you’re having trouble finding it, try using the massive wiring harness to trace back to the ECU.

## Slide 40: Finding an ECU (2)
<number>
You can use a reference website such as http://www.auterraweb.com/aboutcan.html to help you identify a target vehicle.
Also, make sure you leave at least a pigtail’s worth of wiring when you remove the ECU; this will make it easier to wire up later.

## Slide 41: Finding an ECU (3)
<number>
Instead of harvesting or buying a used ECU, you could also use a prebuilt simulator, like the ECUsim 2000 by ScanTool (Next page)

## Slide 42: Finding an ECU (4)
<number>

## Slide 43: Dissecting the ECU Wiring
<number>
Once you have all of the parts, you’ll need to find the ECU’s wiring diagram to determine which wires you need to connect in order to get it to work.
Visit a website such as ALLDATA (http://www.alldata.com/) or Mitchell 1 (http://mitchell1.com/main/) to get a complete wiring diagram.

## Slide 44: Dissecting the ECU Wiring (2)
<number>
Wiring diagrams aren’t always easy to read, mainly because some combine numerous small components.
Try to mentally break down each component to get a better idea of which wires to focus on.

## Slide 45: Dissecting the ECU Wiring (3)
<number>

## Slide 46: Pinouts
<number>
You can get pinouts for the ECUs on several different vehicles from http://www.innovatemotorsports.com/resources/ecu_pinout.php and from commercial resources like ALLDATA and Mitchell 1. Books like the Chilton auto repair manuals include block diagrams, but you’ll find that they typically cover only the most common repair components, not the entire ECU.

## Slide 47: Block Diagrams
<number>
Block diagrams are often easier to read than wiring diagrams that show all components on the same sheet.
show the wiring for only one component and offer a higher-level overview of the main components, whereas schematics show all the circuitry details.

## Slide 48: Block Diagrams (2)
<number>
Some block diagrams also include a legend showing which connector block the diagram refers to and the connectors on that module; you’ll typically find these in the corner of the block diagram

## Slide 49: Block Diagrams (3)
<number>
The legend should give the connector number, its number pin count, and the color.
  For instance, the line C1 = 68 WH in Table 7-1 means that the C1 connector has 68 pins and is white. L-GY probably means light gray, and so on.

## Slide 50: Wiring Things Up
<number>
Wire the CAN to the proper ports on the connector
When you provide power—a power supply from an old PC should suffice—and add a CAN sniffer, you should see packets.
You can use just a simple OBD-II scan tool that you can pick up at any automotive store.
If you have everything wired correctly, the scan tool should be able to identify the vehicle, assuming that your test bench includes the main ECU.

## Slide 51: Wiring Things Up (2)
<number>
If you’ve wired everything but you still don’t see packets on your CAN bus, you may be missing termination.
To address this problem, start by adding a 120-ohm resistor, as a CAN bus has 120-ohm resistors at each end of the bus. If that doesn’t work, add a second resistor.
The maximum missing resistance should be 240 ohms.
If the bus still isn’t working, then recheck your wires and try again.

## Slide 52: Building a More Advanced Test Bench
<number>
This unit combines an ECU with a BCM because it also has the original keys to start the vehicle.
Notice that the optional IC has two 1 kilohm potentiometers, or variable resistors, on the lower left side, both of which are tied to the engine temperature and fuel lines.
This particular test bench also includes a small MCU that allows you to simulate sending crankshaft and camshaft signals to the ECU.

## Slide 53: Building a More Advanced Test Bench (2)
<number>

## Slide 54: Simulating Sensor Signals
<number>
you can use the potentiometers in this setup to simulate various vehicle sensors, including the following:
  Coolant temperature sensor
  Fuel sensor
  Oxygen sensors, which detect post-combustion oxygen in the exhaust
  Throttle position, which is probably already a potentiometer in the actual vehicle
  Pressure sensors

## Slide 55: Hall Effect Sensors
<number>
Hall effect sensors are often used to sense engine speed and crankshaft position (CKP) and to generate digital signals.
In the following Image Hall effect sensor uses a shutter wheel, or a wheel with gaps in it, to measure the rotation speed.

## Slide 56: Hall Effect Sensors (1)
<number>

## Slide 57: Hall Effect Sensors (2)
<number>

## Slide 58: Hall Effect Sensors (3)
<number>
You can also use the camshaft timing sprocket to measure speed. When you look at the camshaft timing sprocket, the magnet is on the side of the wheel.

## Slide 59: Hall Effect Sensors (4)
<number>
(Image)

## Slide 60: Hall Effect Sensors (5)
<number>
Using a scope on the signal wire shows that the Hall effect sensor produces a square wave.
Typically, there are three wires on the camshaft sensor:
  power,
  ground,
  sensor.

## Slide 61: Hall Effect Sensors (6)
<number>
Power is usually 12V, but the signal wire typically operates at 5V back to the ECM.
Camshaft sensors also come as optical sensors, which work in a similar fashion except an LED is on one side and a photocell is on the other.

## Slide 62: Hall Effect Sensors (7)
<number>
You can gauge full rotation timing with a missing tooth called a trigger wheel or with a timing mark.
It’s important to know when the camshaft has made a full rotation. An inductive camshaft sensor produces a sine wave and will often have a missing tooth to detect full rotation.

## Slide 63: Hall Effect Sensors (8)
<number>
You can gauge full rotation timing with a missing tooth called a trigger wheel or with a timing mark.
It’s important to know when the camshaft has made a full rotation. An inductive camshaft sensor produces a sine wave and will often have a missing tooth to detect full rotation.

## Slide 64: Hall Effect Sensors (9)
<number>
shows the camshaft sensor repeating approximately every 2 milliseconds:

## Slide 65: Hall Effect Sensors (10)
<number>
The jump or a gap you see in the wave at around the 40-millisecond mark occurs when the missing tooth is reached.
The location of that gap marks the point at which the camshaft has completed a full rotation.
In order to fake these camshaft signals into the ECU test bench, you’d need to write a small sketch for your microcontroller.

## Slide 66: Hall Effect Sensors (11)
<number>
When writing microcontroller code to mimic these sensors, it’s important to know what type of sensor your vehicle uses so that you’ll know whether to use a digital or analog output when faking the teeth.

## Slide 67: Simulating Vehicle Speed
<number>
We’ll use this test bench together with the IC shown in Figure 7-4 in “The Car Hacker’s Handbook” to pull a vehicle’s VIN via the OBD-II connector.

## Slide 68: Simulating Vehicle Speed (2)
<number>
This will give us the exact year, make, model, and engine type of the vehicle. (We looked at how to do this manually in “Unified Diagnostic Services”

## Slide 69: Simulating Vehicle Speed (3)
<number>
Once we know a vehicle’s year of manufacture and engine type, we can fetch the wiring diagram to determine which of the ECU wires control the engine speed
Then, we can send simulated speed data to the ECU in order to measure effects.
Using wiring diagrams to simulate real engine behavior can make it easy to identify target signals on the CAN bus.

## Slide 70: Simulating Vehicle Speed (4)
<number>

## Slide 71: Simulating Vehicle Speed (5)
<number>
Figure shows how you can trace the wire from the CKP sensor so that connector C2, pin 27 receives the engine speed from the crankshaft sensor.
Having identified this pin in the wiring diagram, we locate the corresponding wire on the ECU. We can connect this wire to any digital IO pin on an Arduino. In this example, we’ll use pin 2 and then add a potentiometer to A0 to control the speed of the CKP sensor’s “teeth” going to the ECM. Pin 2 will send output to C2, pin 27.

## Slide 72: Simulating Vehicle Speed (6)
<number>
In order to simulate engine speed sent from the CKP sensor, we code up an Arduino sketch to send high and low pulses with a delay interval mapped to the potentiometer position(Next Page)

## Slide 73: Simulating Vehicle Speed (7)
<number>

## Slide 74: Simulating Vehicle Speed (8)
<number>
Now, we upload this sketch to the Arduino, power up the test bench, and when we turn the knob on the potentiometer, the RPM dial moves on the IC.

## Slide 75: Simulating Vehicle Speed (9)
<number>
In the figure on the previous slide, the second line of the cansniffer traffic shows bytes 2 and 3—0x0B and 0x89—changing as we rotate the potentiometer knob for Arbitration ID 0x110 (the column labeled ID).

## Slide 76: Simulating Vehicle Speed (10)
<number>
When this screenshot was taken, the needle was idling a bit below the 1 on the RPM gauge, so that’s probably the same algorithm.
To verify that arbitration ID 0x110 with bytes 2 and 3 controls the RPM, we’ll send our own custom packet. By flooding the bus with a loop that sends the following, we’ll peg the needle at max RPMs.

## Slide 77: Simulating Vehicle Speed (11)
<number>
While this method works and, once connected, takes only a few seconds to identify the CAN packet responsible for RPMs, there are still some visible issues:
  Every so often a CAN signal shows up that resets the values to 00 00 and stops the speedometer from moving. So while the ECM is fairly certain the crankshaft is spinning, it’s detecting a problem and attempting to reset.

## Slide 78: Simulating Vehicle Speed (12)
<number>
In two different terminals, we can check whether there was a diagnostic code:

## Slide 79: Simulating Vehicle Speed (13)
<number>
You should see this output in the first terminal:

## Slide 80: Simulating Vehicle Speed (14)
<number>
Looks like we have a DTC set. Querying PID 0x03 returned a 4-byte DTC (0x0068C107).
he first two bytes make up the standard DTC (0x00 0x68).
This converts to P0068, which the Chilton manual refers to as “throttle body airflow performance.”

## Slide 81: Simulating Vehicle Speed (15)
<number>
If we wanted to spoof that data as well, we’d need to spoof three additional sensors:
  the MAF sensor
  the throttle position
  the manifold air pressure
(These are other ways to trick the signals you want out of the PCM without having to be immune to triggering DTC faults.

## Slide 82
<number>
Thank You
Reference:
C. Smith, "ECU Hacking," in THE CAR HACKER’S HANDBOOK A Guide for the Penetration Tester, William Pollock, 2016.
C. Smith, "Vehicle Communication with SocketCAN," in THE CAR HACKER’S HANDBOOK A Guide for the Penetration Tester, William Pollock, 2016.