## Slide 1
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 1
Understanding Threat Models:
Identify areas with the highest risk components
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 2: Attack Surfaces (AS)
Attack surface refers to all the possible ways to attack a target, from vulnerabilities in individual components to those that affect the entire vehicle
Especially, we’re concerned with the entry points into a target
<number>

## Slide 3: Attack Surfaces (ASs): Analogy
Analogy: attack surface like the surface area versus the volume of an object
Two objects can have the same volume but radically different surface areas.
The greater the surface area, the higher the exposure to risk.
If an object’s volume its value, our goal in hardening security is to create a low ratio of risk to value
<number>

## Slide 4: Identifying Attack Surfaces
To find weaknesses in the vehicle’s security, evaluate the vehicle’s perimeter, and document the vehicle’s environment
Particularly, consider all the ways that data can get into a vehicle: vehicle communication channels with the outside world
<number>

## Slide 5: Ways Data Enter Vehicles
<number>
https://www.radiojitter.com/threat-modelling-for-automotive-part-2/

## Slide 6: Vehicle Examination
During the evaluation, you may ask yourself questions like:
What signals are received? Radio waves? Key fobs? Distance sensors? physical keypad access? touch or motion sensors?
• What are the audio input options: CD? USB? Bluetooth? diagnostic ports?
dashboard capabilities? GPS? Bluetooth? Internet? If electric, how does it charge?
<number>

## Slide 7
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 1.1
Understanding Threat Models:
Threat Modeling
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 8: Threat Modeling is Essential
Threat modeling is essential with all these ways data can enter the vehicle, even worse If data is malformed or intentionally malicious
The following slides give you a quick tour on building threat models
<number>

## Slide 9: Developing Threat Models (1)
For threat modeling, you collect information about the architecture of your target and create a diagram to illustrate how parts of the car communicate.
Maps are used to identify higher-risk inputs and to keep a checklist of things to audit; this will help you prioritize entry points that could yield the most return.
<number>

## Slide 10: Developing Threat Models (2)
Threat models are typically made during the product development and design process.
Company creates threat model when product development begins and continuously updates the model through development.
Threat models are living documents, updated as target changes and/or learning more about target
<number>

## Slide 11: Threat Levels
Threat models can consist of different levels;
If a process in model is complicated, you should consider breaking it down further by adding more levels to your diagrams.
Various potential levels will be discussed in the following slides.
<number>

## Slide 12: Level 0: Bird’s-Eye View (1)
At this level, we use the checklist of attack surfaces.
Depending on how data enter vehicle, draw vehicle in the center and label external/internal spaces.
It’s okay if you don’t recognize all acronyms yet; you will soon.
<number>
Level 0’s inputs
E.g. Tire Pressure Monitor Sensor (TPMS)

## Slide 13: Level 0: Bird’s-Eye View (2)
Boxes are inputs, and the circle in the center represents the entire vehicle.
Inputs cross two dotted lines, which represent external and internal threats.
The vehicle represent a complex process—that is, a series of tasks that could be broken down further.
<number>
Level 0’s inputs

## Slide 14: Level 0: Bird’s-Eye View (3)
Processes are numbered, this one is number 1.0. If more than one complex piece, you would label a second process 2.0; a third, 3.0; and so on.
As you learn about your vehicle’s features, you update the diagram.
<number>
Level 0’s inputs

## Slide 15: Level 1: Receivers (1)
<number>
Level 1 map of inputs and vehicle connections
For Level 1 diagram, a process is picked to explore.
For example, let’s dig in to the vehicle process and focus on what each input talks to.
Difference of Level 1 with Level 0: we specify vehicle connections that receive the Level 0 input.

## Slide 16: Level 1: Receivers (2)
<number>
Level 1 map of inputs and vehicle connections
We won’t look at the receivers in depth just yet;
we’re looking only at the basic device or area that the input talks to.
Each receiver is numbered. The first digit represents the process label from the Level 0; 2nd digit is receiver’s number.
Notes: <number>

## Slide 17: Level 1: Receivers (3)
<number>
Level 1 map of inputs and vehicle connections
E.g. infotainment unit is both a complex process and an input, it’s given a process circle.
Three other processes: immobilizer, ECU, and TPMS Receiver.

## Slide 18: Level 1: Receivers (4)
<number>
Level 1 map of inputs and vehicle connections
The dotted lines represent divisions between trust boundaries,
Least trusted from top to most trusted at the bottom.
The more trust boundaries that a communication channel crosses, the more risky that channel becomes.

## Slide 19: Level 2: Receiver Breakdown (1)
Level 2 focuses on communication inside vehicle.
Diagram focuses on a Linux-based infotainment console, receiver 1.1.
This is a complicated receiver that is often directly connected to vehicle’s internal network.
<number>
Level 2 map of the infotainment console

## Slide 20: Level 2: Receiver Breakdown (2)
Communications channels are grouped into boxes, dashed lines represent trust boundaries.
Kernel space: new trust boundary inside the infotainment console.
<number>
Level 2 map of the infotainment console

## Slide 21: Level 2: Receiver Breakdown (3)
Systems that talk directly to the kernel hold higher risk than those that talk to applications because they may bypass any access control mechanisms.
E.g. cellular is higher risk than Wi-Fi; it crosses a trust boundary
Wi-Fi communicates in user space.
<number>
Level 2 map of the infotainment console

## Slide 22: Level 2: Receiver Breakdown (4)
Kernel space includes kernel modules udev, HSI, and Kvaser, which receive input from our threat model.
The udev module loads USB devices, HSI is a serial driver that handles cellular communication, and Kvaser is vehicle’s network driver.
<number>
Level 2 map of the infotainment console

## Slide 23: Adding More Levels
Continue to drill down into as many complex processes as possible.
Discuss methods and libraries of applications; incorporate them into threat diagrams.
Mark methods with higher privileges or more sensitive information through trust boundaries at the application level between application and kernel, application and libraries, and among applications.
<number>

## Slide 24
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 1.2
Understanding Threat Models:
Threat Identification
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 25: Threat Identification
let’s list all potential threats with our threat models since we’ve gone two levels deep into our threat modeling maps.
Start at Level 0, considering potential high-level problems with inputs, receivers, and threat boundaries.
Threat identification is often more fun to do with a group and a whiteboard, but you can do it on your own as a thought exercise.
<number>

## Slide 26: Level 0 Threat Identification
Brainstorm all risks of processes and inputs, try to stay high level, and include all possible threats, even if already been addressed.
High-level threats at Level 0:
Remotely take over a vehicle
Shut down a vehicle
Spy on vehicle occupants
Unlock a vehicle
Steal a vehicle
Track a vehicle
Thwart safety systems
Install malware
<number>

## Slide 27: Level 1 Threat Identification
Level 1 focuses more on connections of each piece rather than connections that might be made directly to an input.
Vulnerabilities that affect what connects to the devices in a vehicle.
Including, cellular, Wi-Fi, key fob (KES), tire pressure monitor sensor (TPMS), infotainment console, USB, Bluetooth, and controller area network (CAN) bus connections.
<number>

## Slide 28: Level 1: Cellular Threat Identification (1)
Access internal vehicle network
Exploit infotainment’s application for incoming calls
Access the subscriber identity module (SIM) through infotainment
Use a cellular network to connect to the remote diagnostic system (OnStar)
<number>

## Slide 29: Level 1: Cellular Threat Identification (2)
Eavesdrop on cellular communications
Jam distress calls
Track the vehicle’s movements
Set up a fake Global System for Mobile Communications (GSM) base station
<number>

## Slide 30: Level 1: Wi-Fi Threat Identification (1)
Exploit Wi-Fi connection to:
Access the vehicle network from up to 300 yards away or more
Find an exploit for the software that handles incoming connections
Install malicious code on the infotainment unit
<number>

## Slide 31: Level 1: Wi-Fi Threat Identification (2)
Break the Wi-Fi password
Set up a fake dealer access point to trick the vehicle into thinking it’s being serviced
Intercept communications passing through the Wi-Fi network
Track the vehicle
<number>

## Slide 32: Level 1: Key Fob Threat Identification (1)
Exploit the key fob connection to:
Send malformed key fob requests that put the vehicle’s immobilizer in an unknown state
Actively probe an immobilizer to drain the car battery
Lock out a key
<number>

## Slide 33: Level 1: Key Fob Threat Identification (2)
Capture cryptographic information leaked from the immobilizer during the handshake process
Brute-force the key fob algorithm
Clone the key fob
Jam the key fob signal
Drain the power from the key fob
<number>

## Slide 34: Level 1: TPMS Threat Identification (1)
Exploit the Tire Pressure Monitor Sensor (TPMS) connection to:
Send an impossible condition to the engine control unit (ECU), causing a fault that could then be exploited
Trick the ECU into overcorrecting for spoofed road conditions
<number>

## Slide 35: Level 1: TPMS Threat Identification (2)
Put the TPMS receiver or the ECU into an unrecoverable state that might cause a driver to pull over to check for a reported flat or that might even shut down the vehicle
Track a vehicle based on the TPMS unique IDs
Spoof the TPMS signal to set off internal alarms
<number>

## Slide 36: Level 1: Infotainment Threat Identification (1)
Exploit the infotainment console connection to:
Put the console into debug mode
Alter diagnostic settings
Find an input bug that causes unexpected results
Install malware to the console
<number>

## Slide 37: Level 1: Infotainment Threat Identification (2)
Use a malicious application to access the internal CAN bus network
Use a malicious application to eavesdrop on actions taken by vehicle occupants
Use a malicious application to spoof data displayed to the user, such as the vehicle location
<number>

## Slide 38: Level 1: USB Threat Identification
Install malware on the infotainment unit
Exploit a flaw in the USB stack of the infotainment unit
Attach a malicious USB device with specially crafted files designed to break importers on the infotainment unit, E.g. MP3 decoders
Install modified update software on vehicle
Short the USB port, thus damaging the infotainment system
<number>

## Slide 39: Level 1: Bluetooth Threat Identification
Execute code on the infotainment unit
Exploit a flaw in the Bluetooth stack of the infotainment unit
Upload malformed info, E.g. a corrupted address book designed to execute code
Access the vehicle from close ranges (less than 300 feet)
Jam the Bluetooth device
<number>

## Slide 40: Level 1: CAN Threat Identification
Exploit Controller Area Network (CAN) bus to:
Install a malicious diagnostic device to send packets to CAN bus, or track vehicle
Plug directly into CAN bus to attempt to start a vehicle without a key
Plug directly into CAN bus to upload malware
Install a malicious diagnostic device to enable remote communications directly to CAN, making a internal attack to an external threat
<number>

## Slide 41: Level 2: Receiver Breakdown Threat Identification
Level 2: focuses on identifying specific threats.
By looking at exactly which application handles which connection, we can start to perform validation based on possible threats.
Five groups of threats : 1) Bluez (Bluetooth daemon) 2) wpa_supplicant (the Wi-Fi daemon) 3) HSI (high-speed synchronous interface cellular kernel module) 4) udev (kernel device manager) 5) and Kvaser driver (CAN transceiver driver).
<number>

## Slide 42: Level 2: Bluez Threat Identification
Older/unpatched versions of the Bluez daemon:
May be exploitable
May be unable to handle corrupt address books
May not be configured to ensure proper encryption
May not be configured to handle secure handshaking
May use default passkeys
<number>

## Slide 43: Level 2: wpa_supplicant Threat Identification
Older versions may be exploitable
May not enforce proper WPA2 style wireless encryption
May connect to malicious access points
May leak information on the driver via BSSID (network interface)
<number>

## Slide 44: Level 2: HSI Threat Identification
High-speed synchronous interface cellular kernel module (HSI)
Older versions may be exploitable
May be susceptible to injectable serial communication (man-in-the-middle attacks in which the attacker inserts serial commands into the data stream)
<number>

## Slide 45: Level 2: udev Threat Identification
Older kernel device manager, unpatched versions may be susceptible to attack
May not have a maintained whitelist of trusted devices, allowing an attacker to load additional drivers or USB devices that were not tested or intended for use
May allow an attacker to load foreign devices, such as a keyboard to access the infotainment system
<number>

## Slide 46: Level 2: Kvaser Threat Identification
Older, unpatched versions may be exploitable
May allow an attacker to upload malicious firmware to the Kvaser device
<number>

## Slide 47: Adding Potential Level 3
You may add a Level 3 map. Similarly, need to identify the lists of potential vulnerabilities through a brainstorming session.
E.g. adding a Level 3 map of potential threats to vehicle:
Pick one process, like HSI, and start to look at its kernel source to identify sensitive methods and dependencies that might be vulnerable to attack.
<number>

## Slide 48
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 1.3
Understanding Threat Models:
Threat Rating Systems
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 49: Threat Rating Systems (1)
We can rate potential threats with a risk level.
Common rating systems include DREAD, ASIL, and MIL-STD-882E.
DREAD is commonly used in web testing
Automotive industry and government use ISO 26262 ASIL and MIL-STD-882E.
<number>

## Slide 50: Threat Rating Systems (2)
ISO 26262 ASIL and MIL-STD-882E are on safety failures and are not adequate to handle malicious threats.
More details on these standards can be found at http://opengarages.org/index.php/Policies_and_Guidelines
<number>
Automobile Safety Issue types. Image credit: Mentor

## Slide 51: The DREAD Rating System
DREAD stands for the following:
Damage potential How great is the damage?
Reproducibility How easy is it to reproduce?
Exploitability How easy is it to attack?
Affected users How many users are affected?
Discoverability How easy is it to find the vulnerability?
<number>

## Slide 52: DREAD Risk Levels
<number>

## Slide 53: Applying DREAD
Apply each DREAD category to an identified threat from earlier in the chapter and score the threat from low to high (1–3).
For instance, if we take the Level 2 HSI threats discussed in “Level 2: Receiver Breakdown” on page 10 of textbook, we can come up with threat ratings like the ones shown in Table 1-2 of textbook.
Identify the overall rating by using the values in the Total column, as shown in Table 1-3.
In the case of the HSI threats, the risk to each of the threats is shown in Table 1-4.
<number>

## Slide 54: HSI Level 2 Threats (DREAD)
<number>

## Slide 55: Risk Assessment (DREAD) (1)
By looking at the results in Table 1-4, both risks are marked as high,
However, the older version of the HSI model poses a slightly higher risk than do the injectable serial attacks.
We can make it a priority to address this risk first.
<number>

## Slide 56: Risk Assessment (DREAD) (2)
In addition, the results also show that the reason why the injectable serial communication risk is lower is that the damage is less severe and the exploit is harder to reproduce than that of an old version of HSI.
<number>

## Slide 57: Summary of This Topic (1)
We learned:
Importance of using threat models to identify and document your security posture, and to brainstorm possible scenarios.
To drill down into these scenarios to identify all potential risks.
<number>

## Slide 58: Summary of This Topic (2)
We learned:
To use a scoring system,
ranking and categorizing each potential risk
defining product security posture, any countermeasure currently in place
and a task list of high-priority items that still need to be addressed.
<number>

## Slide 59
<number>
Thank You
Reference:
C. Smith, "Understanding Threat Models," in THE CAR HACKER’S HANDBOOK A Guide for the Penetration Tester, William Pollock, 2016.