## Slide 1
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 2.1
Bus Protocols & Vehicle Communication: CAN bus and diagnostic link connector (DLC)
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 2: The CAN Bus (1)
Simple communication protocol used in manufacturing and the automotive field
Used for communication between embedded systems and the ECU
  Used for communication between embedded systems and the ECU
  Became mandatory in 2008
<number>

## Slide 3: The CAN Bus (2)
CAN is a 2 wire system
  CAN High (CANH)
    3.5V
  CAN Low (CANL)
    1.5V
  Both CANH and CANL have a resting voltage of 2.5V
Three communication speeds
  Standard High Speed (HS-CAN)
  Mid Speed (MS-CAN)
  Low Speed (LS-CAN)
<number>

## Slide 4: The CAN Bus (3)
Uses Differential Signaling
  When a signal comes in, CAN increases the voltage on one line, and drops it on the other
  Makes the system relatively fault tolerant to noise
<number>

## Slide 5: Differential Signaling
When data is sent on the CAN Bus, both CANH and CANL go 1V higher/lower
If the ECU does not see both signals, it rejects the data as noise
<number>
CANH
CANL

## Slide 6: CAN Connector (1)
OBD-II Port
  16 pin connector also called the Data Link Connector (DLC)
<number>
https://www.nissanhelp.com/diy/maxima/projects/images/2005_nissan_maxima_obd_connector.jpg

## Slide 7: CAN Connector (2)
OBD-II Port Layout
<number>

## Slide 8: OBD-II Connector Pinout Maps (1)
<number>
Actual pins are manufacturer specific. These are just guidelines

## Slide 9: OBD-II Connector Pinout Maps (2)
<number>
Often you will use a DB9-to-OBD-II cable for connecting a PC to a vehicle
This is the plug view
This is the layout that is common in the United Kingdom and parts of Europe

## Slide 10: OBD-III
<number>
OBD-II was originally designed to be emissions testing compliant
  Now, with the advent of modern computation, the PCM can tell if the vehicle is emissions compliant, there is no need to get the car tested in a facility
OBD-III allows for the PCM to remotely transmit statuses without the owner having to take the vehicle in for testing
  Accomplished by cellular or satellite communication
OBD-III is not a standard and is manufacturer specific at best
Many third party technologies accomplish what OBD-III is designed to do
  OnStar is an example of this

## Slide 11
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 2.2
Bus Protocols & Vehicle Communication: CAN Bus Packet Layout
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 12: CAN Bus Packet Layout
Two types of packets
  Standard and Extended
Standard Packets
  Broken into four elements
    Arbitration ID
      Used to identify the broadcasting device
    Identifier Extension (IDE)
      Always “0” for Standard CAN
    Data Length Code (DLC)
      Size of incoming data, range of 0-8 bytes
    Data
      Max size of 8 bytes
<number>

## Slide 13: CAN Bus Packet Layout (2)
Standard
<number>

## Slide 14: CAN Bus Packet Layout (3)
Extended Packets
  Similar to standard
  Chained together “standard” packets to create longer IDs
  Designed to fit in standard packet size to allow for general compatibility
    If a device on the bus does not support extended packets it will not “break”
  The have a 18 bit identifier
In industry
  Many companies use the extended format for their own proprietary communication styles
<number>

## Slide 15: SAE J1850 Protocol
Older, slower, and cheaper version of CAN
  Originally adopted in 1994
  Still used by GM and Chrysler
Two versions of J1850
  Pulse width modulation (PWM) and variable pulse width (VPW)
Speed of the protocol is grouped into three classes
  Class A
    10.4 Kbps, Marketed towards non-automotive applications
  Class B
    100 Kbps, Marketed for anything, More Expensive
  Class C
    1 Mbps, Marketed in real-time critical systems and media networks, MOST expensive
<number>

## Slide 16: SAE J1850 Protocol - PWM
PWM Implementation on the OBD-II connector
Uses differential signalling on pins 2 + 10
High voltage is 5V
Operates at 41.6 Kbps
Other specifics of this protocol are identical to VPW
Mainly used by Ford
<number>

## Slide 17: SAE J1850 Protocol - VPW
Single-wire bus system
Uses ONLY pin 2
  High voltage of 7V, Low is near ground, Resting is 3V
  Operates at 10.4 Kbps
Uses time dependent signaling
  High/low voltage on the bus does not necessarily equal a 1/0
    Has to stay high/low for a set amount of time to be interpreted as a 1/0
<number>

## Slide 18
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 2.3
Bus Protocols & Vehicle Communication: Media Oriented Systems Transport (MOST)
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 19: MOST Protocol (1)
<number>
Media Oriented Systems Transport protocol (aka MOST)
  Designed for multimedia devices
  Laid out in a ring topology or virtual star
  Supports a max of 64 MOST devices
  One MOST device acts as the timing master
    Continuously sends frames into the ring
    Assigns addresses to all other devices in ring
  Runs at ~23 Mbaud
  Supports 15 uncompressed CD quality audio or MPEG1 audio/video channels
  Has a separate control channel at runs at 768 Kbaud
    Sends configuration messages to MOST devices on the ring
  Routes packets through seperate Input/Output ports

## Slide 20: MOST Protocol (2)
<number>
MOST has three speeds:
  MOST25
    Runs on plastic optical fiber (POF)
    Transmission is done using red wavelength light (650 nm) by LED
  MOST50
    Double the bandwidth of MOST25 (1025 Bits)
    Transmission done by UTP on cables instead of POF
  MOST150
    Implements ethernet
    Increased frame rate (3072 bits or 150 Mbps)

## Slide 21: MOST Network Layers
<number>
MOST is divided up amongst seven layers of Open Systems Interconnections (OSI) model that standardizes communication over the networks

## Slide 22: MOST Control Blocks
<number>
MOST25 blocks consist of 16 frames
One frame is 512 bits

## Slide 23: MOST Control Blocks (2)
<number>
Synchronous data contains 6 to 15 quadlets
  A quadlet is 4 bytes
Asynchronous data contains 0 to 9 quadlets
Control Data is 32 bytes
  2 bytes per control frame (x16 frames)

## Slide 24: MOST Control Blocks (3)
<number>
Data area contains:
  FblockID
  InstID
  FktID
  OP Type
  Tel ID
  Tel Len
  12 Bytes of Data
MOST50
  Exactly like MOST25 but with a larger data section
MOST150
  Provides two additional channels: Ethernet and Isochronous

## Slide 25: Hacking MOST
<number>
MOST main vulnerability is the devices that are connected to the ring
  Infotainment system is an example
  Any device that can be connected to the ring that support MOST
The most4linux driver project provides kernel support for linux based systems
  Allows for MOST communication in the user-space
  Links the Advanced Linux Sound Architecture (ALSA) to read and write audio data

## Slide 26: FlexRay Bus (1)
<number>
High-speed communication interface
  Communicates at speeds up to 10 Mbps
  Designed more for time sensitive communication
    Drive/steer/brake-by-wire
  Significantly more expensive to implement than CAN
FlexRay Hardware
  Data is transmitted across a twisted pair of wires
  Supports dual-channel setups
    Think differential signalling
  Generally, setup to mirrors CAN bus setups

## Slide 27: FlexRay Cycles
<number>
The cycle can be viewed as a packet
  Static segment contains reserved slots for data
  Dynamic segment contains slots for varying representations
  Symbol Window used by the network for signaling
  Idle segment is used for synchronization

## Slide 28: FlexRay Packet Layout
<number>

## Slide 29: FlexRay Packet Layout - Breakdown
<number>
Frame ID
  This IDs the slot the packet should be transmitted in
  If the packet is destined for a dynamic slot this shows the packets priority
    1 - 2047
    If two packets are transmitted at the same time, priority determines what is sent when
Payload Length
  The number of words (2 bytes) in the data
  Max of 127 (245 bytes)
Header CRC
  Info pertaining to the transmitter/receiver
Cycle Count
  Communication counter that increments each time the communication cycle starts

## Slide 30: Sniffing the FlexRay Network (1)
<number>
Currently, there is no official direct linux support for FlexRay
  Unofficial corporate driven drivers are out there
  This means that if you want to have some tool to do this, it will be extremely expensive
To do this “by hand” you will need…
  To know the baud rate of the data transmissions
  Cycle length (in milliseconds)
  Size of the cluster partitioning (static vs dynamic ratio)
  Ability to identify parameters in the packets
    “Automatic Parameter Identification in FlexRay based Automotive Communication Networks” (IEEE, 2006) by Eric Armengaud, Andreas Steininger, and Martin Horauer

## Slide 31: Automotive Ethernet
<number>
Becoming normal due to the high costs of MOST and FlexRay
Basically the same technologically as computer network style ethernet communication
Typically CAN packets are wrapped in UDP and transmitted across the network
  Allows for implementation alongside CAN
  Audio is transported as voice over IP or VoIP
Automotive Ethernet has transmit speeds up to 10 Gbps
Currently there is no common standard for Automotive Ethernet
  Though, manufacturers are starting to use the IEEE 802.1AS as common practice

## Slide 32
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 2.4
Bus Protocols & Vehicle Communication: SocketCAN interface
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 33: CAN Tools (1)
you may well find it to be a hodgepodge of different drivers and software utilities.
The ideal would be to unify the CAN tools and their different interfaces into a common interface so we could easily share information between tools.
If you have Linux or install Linux on a virtual machine (VM), you already have this interface
<number>

## Slide 34: CAN Tools (2)
The interface, called SocketCAN, was created on the Open Source development site BerliOS in 2006.
Today, the term SocketCAN is used to refer to the implementation of CAN drivers as network devices, like Ethernet cards, and to describe application access to the CAN bus via the network socket–programming interface.
<number>

## Slide 35: Goals
set up SocketCAN so that we’re more easily able to communicate with the vehicle.
  Volkswagen Group Research contributed the original SocketCAN implementation, which supports built-in CAN chips and card drivers, external USB and serial CAN devices, and virtual CAN devices.
  The can-utils package provides several applications and tools to interact with the CAN network devices, CAN-specific protocols, and the ability to set up a virtual CAN environment.
<number>

## Slide 36: Goals (2)
installing a recent version in a Linux VM on your system.
SocketCAN ties into the Linux networking stack, which makes it very easy to create tools to support CAN.
  SocketCAN applications can use standard C socket calls with a custom network protocol family, PF_CAN.
  This functionality allows the kernel to handle CAN device drivers and to interface with existing networking hardware to provide a common interface and user-space utilities.
<number>

## Slide 37: Goals - outline
<number>

## Slide 38: Setting Up can-utils to Connect to CAN Devices (1)
<number>
In order to install can-utils, you must be running a Linux distribution from 2008 or later or one running the 2.6.25 Linux kernel or higher.
First we’ll install can-utils, then cover how to configure it for your particular setup.

## Slide 39: Installing can-utils
<number>
You should be able to use your package manager to install can-utils. Here’s a Debian/Ubuntu example:

## Slide 40: Installing can-utils (2)
<number>
If you don’t have can-utils in your package manager, install it from source with the git command:

## Slide 41: Installing can-utils (3)
<number>
If you don’t have can-utils in your package manager, install it from source with the git command
(As of this writing, can-utils has configure, make, and make install files, but in older versions, you’d just enter make to install from source.)

## Slide 42: Configuring Built-In Chipsets
<number>
The next step depends on your hardware. If you’re looking for a CAN sniffer, you should check the list of supported Linux drivers to ensure your device is compatible. As of this writing, the Linux built-in CAN drivers support the following chipsets:
Atmel AT91SAM SoCs
Bosch CC770
ESD CAN-PCI/331 cards
Freescale FlexCAN
Freescale MPC52xx SoCs (MSCAN)
Intel AN82527
Microchip MCP251x
NXP (Philips) SJA1000
TI’s SoCs

## Slide 43: Configuring Built-In Chipsets (2)
<number>
CAN controllers, like the SJA1000, are usually built into ISA, PCI, and PCMCIA cards or other embedded hardware.
  For example, the EMS PCMCIA card driver implements access to its SJA1000 chip.

## Slide 44: Configuring Built-In Chipsets (3)
<number>
When you insert the EMS PCMCIA card into a laptop, the ems_pcmcia module loads into the kernel, which then requires the sja1000 module and the can_dev module to be loaded.
The can_dev module provides standard configuration interfaces—for example, for setting bit rates for the CAN controllers.

## Slide 45: Configuring Built-In Chipsets (4)
<number>
The Linux kernel’s modular concept also applies to CAN hardware drivers that attach CAN controllers via bus hardware, such as the kvaser_pci, peak_pci, and so on.
When you plug in a supported device, these modules should automatically load, and you should see them when you enter the lsmod command.

## Slide 46: Configuring Built-In Chipsets (5)
<number>
USB drivers, like usb8dev, usually implement a proprietary USB communication protocol and, therefore, do not load a CAN controller driver.

## Slide 47: Configuring Built-In Chipsets (6)
<number>
For example, when you plug in a PEAK-System PCAN-USB adapter, the can_dev module loads and the peak_usb module finalizes its initialization. Using the display message command dmesg, you should see output similar to this:

## Slide 48: Configuring Built-In Chipsets (7)
<number>
You can verify the interface loaded properly with ifconfig and ensure a can0 interface is now present:

## Slide 49: Configuring Built-In Chipsets (8)
<number>
Now set the CAN bus speed.
The key component you need to set is the bit rate.
This is the speed of the bus.
A typical value for high-speed CAN (HS-CAN) is 500Kbps.
Values of 250Kbps or 125Kbps are typical for lower-speed CAN buses.

## Slide 50: Configuring Built-In Chipsets (10)
<number>

## Slide 51: Configuring Built-In Chipsets (11)
<number>
Once you bring up the can0 device, you should be able to use the tools from can-utils on this interface. Linux uses netlink to communicate between the kernel and user-space tools. You can access netlink with the ip link command. To see all the netlink options, enter the following:

## Slide 52: Configuring Built-In Chipsets (12)
<number>
If you begin to see odd behavior, such as a lack of packet captures and packet errors, the interface may have stopped. If you’re working with an external device, just unplug or reset. If the device is internal, run these commands to reset it:

## Slide 53: Configuring Serial CAN Devices
<number>
External CAN devices usually communicate via serial. In fact, even USB devices on a vehicle often communicate through a serial interface—typically an FTDI chip from Future Technology Devices International, Ltd.

## Slide 54: Configuring Serial CAN Devices (2)
<number>
The following devices are known to work with SocketCAN:
Any device that supports the LAWICEL protocol
CAN232/CANUSB serial adapters (http://www.can232.com/
VSCOM USB-to-serial adapter (http://www.vscom.de/usb-to-can.htm)
CANtact (http://cantact.io)

## Slide 55: Configuring Serial CAN Devices (3)
<number>
In order to use one of the USB-to-serial adapters, you must first initialize both the serial hardware and the baud rate on the CAN bus:

## Slide 56: Configuring Serial CAN Devices (4)
<number>
The slcand daemon provides the interface needed to translate serial communication to the network driver, slcan0. The following options can be passed to slcand:
-o Opens the device
-s6 Sets the CAN bus baud rate and speed (see Table 3-1)
-t hw Specifies the serial flow control, either HW (hardware) or SW (software)
-S 3000000 Sets the serial baud, or bit rate, speed
/dev/ttyUSB0 Your USB FTDI device

## Slide 57: Configuring Serial CAN Devices (5)
<number>
Table 3-1 lists the numbers passed to -s and the corresponding baud rates.

## Slide 58: Configuring Serial CAN Devices (6)
<number>
As you can see, entering -s6 prepares the device to communicate with a 500Kbps CAN bus network. With these options set, you should now have an slcan0 device. To confirm, enter the following:

## Slide 59: Setting Up a Virtual CAN Network
<number>
If you don’t have CAN hardware to play with, fear not. You can set up a virtual CAN network for testing. To do so, simply load the vcan module:

## Slide 60: Setting Up a Virtual CAN Network (2)
<number>
If you check dmesg, you shouldn’t see much more than a message like this:

## Slide 61: Setting Up a Virtual CAN Network (3)
<number>
Now you just set up the interface as discussed in “Configuring Built-In Chipsets” on page 37 but without specifying a baud rate for the virtual interface.

## Slide 62: Setting Up a Virtual CAN Network (4)
<number>
To verify your setup, enter the following:

## Slide 63: The CAN Utilities Suite
<number>
With our CAN device up and running, let’s take a high-level look at the can-utils.
They’re listed and described briefly here; we’ll use them throughout the book, and we’ll explore them in greater detail as we use them.
(see next page)

## Slide 64: The CAN Utilities Suite (2)
<number>

## Slide 65: The CAN Utilities Suite (3)
<number>

## Slide 66: The CAN Utilities Suite (4)
<number>
You can specify as many interfaces as you like and have canbusload display a bar graph of the worst bandwidth offenders.
can-calc-bit-timing This command calculates the bit rate and the appropriate register values for each CAN chipset supported by the kernel.

## Slide 67: The CAN Utilities Suite (5)
<number>
candump This utility dumps CAN packets. It can also take filters and log packets.
canfdtest This tool performs send and receive tests over two CAN buses.
cangen This command generates CAN packets and can transmit them at set intervals. It can also generate random packets.

## Slide 68: The CAN Utilities Suite (6)
<number>
cangw This tool manages gateways between different CAN buses and can also filter and modify packets before forwarding them on to the next bus.
canlogserver This utility listens on port 28700 (by default) for CAN packets and logs them in standard format to stdout.

## Slide 69: The CAN Utilities Suite (7)
<number>
canplayer This command replays packets saved in the standard SocketCAN “compact” format.
cansend This tool sends a single CAN frame to the network.
cansniffer This interactive sniffer groups packets by ID and highlights changed bytes.

## Slide 70: The CAN Utilities Suite (8)
<number>
isotpdump This tool dumps ISO-TP CAN packets, which are explained in “Sending Data with ISO-TP and CAN” on page 55.
isotprecv This utility receives ISO-TP CAN packets and outputs to stdout.
isotpsend This command sends ISO-TP CAN packets that are piped in from stdin.

## Slide 71: The CAN Utilities Suite (9)
<number>
isotpserver This tool implements TCP/IP bridging to ISO-TP and accepts data packets in the format 1122334455667788.
isotpsniffer This interactive sniffer is like cansniffer but designed for ISO-TP packets.
isotptun This utility creates a network tunnel over the CAN network.

## Slide 72: The CAN Utilities Suite (10)
<number>
log2asc This tool converts from standard compact format to the following ASCII format:

## Slide 73: The CAN Utilities Suite (11)
<number>
log2long This command converts from standard compact format to a user readable format.
slcan_attach This is a command line tool for serial-line CAN devices.
slcand This daemon handles serial-line CAN devices.
slcanpty This tool creates a Linux psuedoterminal interface (PTY) to communicate with a serial-based CAN interface.

## Slide 74: Installing Additional Kernel Modules
<number>
Some of the more advanced and experimental commands, such as the ISO-TP–based ones, require you to install additional kernel modules, such as can-isotp, before they can be used.
As of this writing, these additional modules haven’t been included with the standard Linux kernels, and you’ll likely have to compile them separately.

## Slide 75: Installing Additional Kernel Modules (2)
<number>
You can grab the additional CAN kernel modules like this:

## Slide 76: Installing Additional Kernel Modules (3)
<number>
You can grab the additional CAN kernel modules like this:

## Slide 77: Installing Additional Kernel Modules (4)
<number>
If you run make in the root folder of the repository, it’ll try to compile some out-of-sync modules, so it’s best to compile only the module that you need in the current directory.

## Slide 78: Installing Additional Kernel Modules (5)
<number>
o load the newly compiled can-isotp.ko module, run insmod:

## Slide 79: Installing Additional Kernel Modules (6)
<number>
dmesg should show that it loaded properly:

## Slide 80: The can-isotp.ko Module
<number>
The can-isotp.ko module is a CAN protocol implementation inside the Linux network layer that requires the system to load the can.ko core module.
The can.ko module provides the network layer infrastructure for all in-kernel CAN protocol implementations, like can_raw.ko, can_bcm.ko, and can-gw.ko.

## Slide 81: The can-isotp.ko Module (2)
<number>
If it’s working correctly, you should see this output in response to the following command:

## Slide 82: The can-isotp.ko Module (2)
<number>
If you’ve forgotten to attach your CAN device or load the CAN kernel module, this is the strange error message you’ll see.
If you were to enter dmesg for more information, you’d see a series of missing symbols referenced in the error messages.

## Slide 83: Coding SocketCAN Applications
<number>
While can-utils is very robust, you’ll find that you want to write custom tools to perform specific actions.

## Slide 84: Connecting to the CAN Socket
<number>
In order to write your own utilities, you first need to connect to the CAN socket.
Connecting to a CAN socket on Linux is the same as connecting to any networking socket that you might know from TCP/IP network programming.
The following shows C code that’s specific to CAN as well as the minimum required code to connect to a CAN socket.

## Slide 85: Connecting to the CAN Socket (2)
<number>
This code snippet will bind to can0 as a raw CAN socket.

## Slide 86: Connecting to the CAN Socket (3)
<number>
This code snippet will bind to can0 as a raw CAN socket.

## Slide 87: Connecting to the CAN Socket (4)
<number>
This line specifies the protocol family, PF_CAN, and defines the socket as CAN_RAW.
You can also use CAN_BCM if you plan on making a broadcast manager (BCM) service.
A BCM service is a more complex structure that can monitor for byte changes and the queue of cyclic CAN packet transmissions.

## Slide 88: Connecting to the CAN Socket (5)
<number>
These two lines name the interface:

## Slide 89: Connecting to the CAN Socket (6)
<number>
These lines set up the CAN family for sockaddr and then bind to the socket, allowing you to read packets off the network:

## Slide 90: Setting Up the CAN Frame
<number>
Next we want to setup the CAN frame and read the bytes off the CAN network into our newly defined structure:

## Slide 91: The Procfs Interface
<number>
The SocketCAN network-layer modules implement a procfs interface as well.
Having access to information in proc can make bash scripting easier and also provide a quick way to see what the kernel is doing.

## Slide 92: The Procfs Interface (2)
<number>
You’ll find the provided network-layer information in /proc/net/can/ and /proc/net/can-bcm/. You can see a list of hooks into the CAN receiver by searching the rcvlist_all file with cat:

## Slide 93: The Procfs Interface (3)
<number>
Some other useful procfs files include the following:
  stats CAN network-layer stats
  reset_stats Resets the stats (for example, for measurements)
  version SocketCAN version

## Slide 94: The Procfs Interface (4)
<number>
You can limit the maximum length of transmitted packets in proc:
Set this value to whatever you feel will be the maximum packet length for your application. You typically won’t need to change this value, but if you find that you’re having throttling issues, you may want to fiddle with it.

## Slide 95: The Socketcand Daemon (1)
<number>
provides a network interface into a CAN network.
Although it doesn’t include can-utils, it can still be very useful, especially when developing an application in a programming language like Go that can’t set the CAN low-level socket options

## Slide 96: The Socketcand Daemon (2)
<number>
Socketcand includes a full protocol to control its interaction with the CAN bus. For example, you can send the following line to socketcand to open a loopback interface:

## Slide 97: The Socketcand Daemon (3)
<number>
The protocol for socketcand is essentially the same as that of Jan-Niklas Meier’s BCM server mentioned earlier; it’s actually a fork of the BCM server. (Socketcand, however, is a bit more robust than the BCM server.)

## Slide 98
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 2.5
Bus Protocols & Vehicle Communication: Diagnostics/Logging, CAN Security, ISO-TP protocol
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 99: Kayak (1)
<number>
a Java-based GUI for CAN diagnostics and monitoring is one of the best tools for use with socketcand.
Kayak links with OpenStreetMaps for mapping and can handle CAN definitions.
As a Java-based application, it’s platform independent, so it leans on socketcand to handle communication to the CAN transceivers.

## Slide 100: Kayak (2)
<number>

## Slide 101: Kayak (3)
<number>
You can download a binary package for Kayak or compile from source:

## Slide 102: Kayak (3)
<number>
You can download a binary package for Kayak or compile from source:

## Slide 103: Kayak (4)
<number>
Before you launch Kayak, start socketcand:

## Slide 104: Kayak (5)
<number>
Next, start Kayak and take the following steps:
  Create a new project with CTRL-N and give it a name.
  Right-click the project and choose Newbus; then, give your bus a name (see Figure 3-3).

## Slide 105: Kayak (6)
<number>
Next, start Kayak and take the following steps:
  Click the Connections tab at the right; your socketcand should show up under Auto Discovery (see Figure 3-4).

## Slide 106: Kayak (7)
<number>
Next, start Kayak and take the following steps:
  Drag the socketcand connection to the bus connection.
  To see the bus, you may have to expand it by clicking the drop-down arrow next to the bus name, as shown in Figure 3-5.

## Slide 107: Kayak (8)
<number>
Next, start Kayak and take the following steps:
  Right-click the bus and choose Open RAW view.
  Press the play button (circled in Figure 3-6); you should start to see packets from the CAN bus

## Slide 108: Kayak (9)
<number>
Next, start Kayak and take the following steps:
  Choose Colorize from the toolbar to make it easier to see and read the changing packets.
Kayak can easily record and play back packet capture sessions, and it supports CAN definitions (stored in an open KDC format). As of this writing, the GUI doesn’t support creating definitions, but I’ll show how to create definitions later.

## Slide 109: ISO-TP (1)
ISO 15765-2 (aka ISO-TP)
  Standard for sending packets over the CAN bus that extends the 8 byte data limit to 4095 bytes
  Most common use for ISO-TP is for diagnostics and KWP messages
    KWP is another communication protocol similar to CAN
  Can flood the data bus, be careful sending large amounts of data
CANopen Protocol
  Breaks the 11 bit identification code into two parts
    4-bit function code and 7-bit node ID
      This is called communication object identifier or COB-ID
  Mainly used in the industrial field
<number>

## Slide 110: ISO-TP (2)
GMLAN Bus
  CAN Bus implementation created by General Motors
  Based on ISO-TP
  Consists of a single-wire low speed and dual-wire high speed bus
    Low-speed bus operates at 33.33 Kbps with a max of 16 nodes
      Used to transmit non-critical data for things like the infotainment system, door locks, HVAC control, etc
    High speed bus operates at 500 Kbps with a max of 16 nodes
  (Nodes in this protocol are the sensors on the bus)
<number>

## Slide 111
<number>
Automotive Cybersecurity for Automotive Technicians
Topic 2.6
Bus Protocols & Vehicle Communication: SAE J1698 Standard
Craig Hoff and Mehrdad H. Zadeh
Kettering University
Notes: <number>

## Slide 112: SAE J1850 Protocol - VPW
<number>

## Slide 113: Keyword Protocol and ISO 9141-2
ISO 14230 or Keyword Protocol 2000 (aka KWP2000)
  Messaging protocol that uses pin 7
  Max message size 255 bytes
  Common in US vehicles after 2003
  Two core variations
    ISO 14230-4 KWP (5-baud init, 10.4 Kbaud)
    ISO 14230-4 KWP (fast init, 10.4 Kbaud)
ISO 9121-2 or K-Line
  Variation of KWP2000
  Often seen in European vehicles
  Mainly uses pin 7, optionally pin 15
  Is a UART protocol similar to serial
<number>

## Slide 114: Keyword Protocol and ISO 9141-2 (2)
<number>

## Slide 115: Keyword Protocol and ISO 9141-2 (3)
<number>
K-Line packets contain a source and destination address

## Slide 116: Local Interconnect Network Protocol
<number>
Local Interconnect Network or LIN
  Cheapest vehicle protocol
  Originally designed to complement CAN
  Has NO arbitration or priority codes
  A single Master node does ALL of the transmission
  Supports up to 16 slave nodes
    Slaves primarily just listen to the master, do not initialize communication
  The LIN master usually is the only one attached to the CAN bus
Functionality:
  Operates at max speed of 20 Kbps, 12V
  Single-wire bus

## Slide 117: Local Interconnect Network Protocol (2)
<number>
Message construction:
  Header only sent by Master
  Response is sent by either Master or Slave

## Slide 118
<number>
Thank You
Reference:
C. Smith, "Bus Protocols," in THE CAR HACKER’S HANDBOOK A Guide for the Penetration Tester, William Pollock, 2016.
C. Smith, "Vehicle Communication with SocketCAN," in THE CAR HACKER’S HANDBOOK A Guide for the Penetration Tester, William Pollock, 2016.