## Slide 1: Introduction to Transducers
Introduction to Transducers Learning Module
Macro-sized Incandescent light bulb
Micro-sized light emitting diode
Notes: In this presentation you will learn about transducers, what they are, what they can do, and various applications. To learn more about transducers, be sure to read the Introduction to Transducers lesson. An understanding of this information is important to microelectromechanical (MEMS) or microsystems technology.

## Slide 2: Unit Overview
The following topics are discussed:
What are Transducers?
Types of Transducers in both the macro and micro-scales
Notes: In this lesson we will answer the Questions – What are Transducers? And What are several type of transducers found in both the macro and micro-scales? Due to our need for things to get “smaller”, many macro-sized transducers are now being manufactured at much smaller scales, for less costs and more efficient results. We’ll talk about some of these transducers in this presentation.

## Slide 3: Introduction
A transducer converts one form of energy into another
A microphone converts sound into electrical impulses
An incandescent light bulb coverts electrical energy into light
An electric motor converts electrical energy into motion.
Three transducers: light bulb, microphone, and electric motors
Notes: So what is a transducer? A transducer is a device that converts one form of energy to another form of energy. Examples of transducers include the light bulb, microphone and motor that you see in this slide.
The incandescent light bulb converts current flowing through a filament into light.
The microphone converts sounds waves into electrical impulses or electrical energy.
The motor converts electrical energy or more specifically, electromagnetic energy into motion or mechanical energy
Can you think of other types of transducers? (Allow about a minute for students to think about the question)
How about a loudspeaker? It converts electrical impulses into sound waves or sound.
A solar cell converts light into electricity, and a thermocouple converts thermal energy into electrical energy.

## Slide 4: Actuators
An actuator is a device that actuates or moves something.
It is a specific type of a transducer.
Question
  Which of the previously mentioned transducers is an actuator?
Notes: Some actuators are transducers. What is an actuator? An actuator is a device that moves something or creates motion, such as levers, gears or hydraulic cylinders. So why are they also considered transducers? Because in some cases, they are converting one form of energy to another.
Which of the transducers from the previous slide is an actuator as well – the light bulb, microphone or motor?
Obviously it’s the motor because the motor converts electrical energy into movement or motion. The output motion of a motor can be used turn gears, raise levers and move pistons up and down. Therefore, a motor is both a transducer (it converts electrical energy to mechanical energy) and an actuator – It moves something!

## Slide 5: Sensors
A sensor is a device that receives and responds to a signal.
  The signal is some type of energy; for example, heat, light, motion, or chemical.
  A sensor detects a signal and converts it into a readable output signal.
Question:
What are some sensors that you are familiar with?
Thermometers
Notes: Transducers and sensors usually work hand-in-hand. Many sensors consist of a transducer and the electronics needed to evaluate the transducer’s input and output. Therefore, a sensor can be defined as a device that receives and responds to a signal. This signal is produced by some type of energy, such as heat, light, motion, or chemical reaction which, in many cases, is the output from a transducer. Once a sensor detects one or more of these signals, it converts it into a readable output. The output could be a readable scale, such as the scale on a mercury thermometer, or an analog or digital readout.
Let’s take the example of a thermometer. Here are the images of both a mercury thermometer and a digital thermometer. The mercury thermometer contains a small reservoir of mercury in the tip. As the temperature of the mercury increase, the mercury expands and moves up the tube to a marking that represents the temperature. In place of the mercury, the digital thermometer uses a thermocouple (which converts heat to voltage). The voltage output of the thermocouple is used to indicate an increase or decrease in temperature.
Based on this explanation of a sensor, you should realize that sensors are used in all aspects of life to detect and/or measure many different conditions. What are some sensors that you are familiar with? (allow a minute for the participant to think about it.)

## Slide 6: Basic Concepts of Transducers
A transducer is defined as a substance or a device that converts (or transfers) an input energy into a different output energy.
Variables - speed, pressures, temperatures and sound.
Transducers measure variables.
The incandescent light bulb
Notes: Now that you know what a transducers, sensors, and actuators are, let’s break the transducer down even further and talk about its basic concepts.
We’ll start with variables. There are many variables which affect our everyday lives. Some that you all should be familiar with include the speed of a car, heater levels, oven temperatures and light levels. The devices that convert one type of input to another type of output are transducers. For example, going back to the incandescent light bulb, the more current that flows (the input) through the tungsten filament (the transducer), the brighter the bulb (the output). The tungsten filament is converting electrical energy to light!
So once again, a transducer is a simple device (such as the tungsten filament) or substance (the mercury in the thermometer) that converts an input energy into a different output energy (current to light, temperature to motion).
Transducers come in many varieties, converting many different types of energy. So let’s talk about the different types of transducers.

## Slide 7: Electrochemical Transducers
pH probe
Molecular electric transducers (MET)
Fuel cell
Battery
Converting a Chemical Reaction to Electrical Energy (Fuel Cell)
pH meter
[Courtesy of Ildar Sagdejev through Creative Commons License]
Notes: Electrochemical transducers convert energy from a chemical reaction or chemical “change” to electrical energy. Some common electrochemical transducers are the pH probe, molecular electric transducer, fuel cell, and battery.
The pH probe measures pH as the activity of the hydrogen cations (or positive ions) surrounding the glass bulb at the tip of the probe by converting the hydrogen cation activity to voltage. For the amount of cation activity that indicates one pH unit, approximately 0.06 volts is produced by the probe or pH transducer.
Molecular electric transducers, or METs, are a class of inertial sensors (such as accelerometers, gyroscopes and seismometers) or a special type of electrolytic cell. METs use the motion in a liquid electrolyte to increase or decrease ion current flowing between two electrodes. The motion of the liquid is created by the motion of the device to which the MET is attached.
Another electrochemical transducers is the fuel cell. A fuel cell converts the chemical energy from a fuel into electricity through a chemical reaction with oxygen or another oxidizing agent. Hydrogen is the most common fuel used in fuel cells. Fuel cells are different from batteries in that they require a constant source of fuel and oxygen to run, but they can produce electricity continually for as long as the fuel is supplied.
We all are familiar with batteries. Batteries are transducers that convert chemical energy into electrical energy. Let’s take a closer look at the battery.
Don’t’ read – More on the MET
A MET consists of two electrodes (an anode and a cathode) immersed in an electrolytic solution or electrolyte. Movement of the MET creates a movement or convection of the liquid electrolyte. This movement alters the amount of ions flowing between the electrodes which in turn affects the output current. In effect, the liquid electrolyte is the inertial mass of the inertial sensor. If you aren’t familiar with accelerometers or gyroscopes, many of these devices use a solid mass that is referred to as the proof mass. The proof mass moves when affected by an external force, such as the sudden acceleration or deceleration of a car or the tilting of a computer. This movement is converted to a change in capacitance, voltage or current in many cases. Such devices are used to trigger the airbags in automobiles and rotate the screen on an iPad when it tilts. More about these devices later on in the learning module.

## Slide 8: Electrochemical Transducer - Battery
Consists of anode, cathode and salt bridge partially immersed in an electrolyte solution.
Ions flowing through the salt bridge creating a voltage (potential difference) between the electrodes.
Converting a Chemical Reaction to Electrical Energy (Battery)
Notes: A battery converts chemical energy directly into electrical energy. Referring to the graphic of a battery, a cathode and an anode of two dissimilar metals are immersed in an electrolyte solution containing salts of their respective metals. A medium (the salt bridge) separates the two electrodes, but allows ions to flow through the bridge from one solution to the other. Due to the flow of ions between the two solutions a potential difference (or voltage) is created. If a wire is placed connecting the two pieces of metals or the electrodes, current flows. The amount of voltage developed across the cathode and the anode depends on the materials that make up the battery.

## Slide 9: Micro-Electrochemical Transducers
Micro-sized components require micro-sized batteries
Microelectromechanical systems exists on the ocean floors, in roadways and bridges, and in medical devices such as pacemakers and insulin pumps.
Battery Pack for Artificial Retina system
[Courtesy of Sandia National Laboratories]
Notes: The fabrication of micro-sized batteries is a challenge but a challenge that needs to be met. Micro-sized sensors require micro-sized batteries in order to operate, especially when those sensors are placed in remote areas such as the ocean floor, embedded into bridges and roads, or in internal (or in vivo) devices such as pacemakers. This is an illustration of a battery that is being developed by Sandia National Laboratories that may be used in vivo to power an artificial retinal prosthesis.
So how do you get a long-lasting battery from a device that is smaller than the diameter of a strand of hair? “Traditional batteries have a two-dimensional array of positive and negative electrodes stacked on top of one another like sheets of paper. Increasing battery power means adding more electrode layers, more weight and more size.”1 One solution to creating smaller batteries is to fabricate a 3-dimensional microelectrode array consisting of high aspect ratio carbon posts (carbon posts that are much taller than they are wide). These posts (between 100 nm to 1 nm in diameter) serve as the electrodes for carbon MEMS batteries.3

## Slide 10: Electroacoustic, Electromagnetic, & Electrostatic Transducers
Electroacoustic
  Loudspeaker
  Microphone
  Hydrophone
Electromagnetic
  Magnetic cartridge
  Generator
Electrostatic
  Electrometer
  Van de Graaf generator
Van de Graaf Generator:
Converting Static into High Voltage
Notes: Other types of transducers include electroacoustic, electromagnetic and electrostatic.
Electroacoustic transducers work with sound energy and electrical energy.
Common electroacoustic transducers include Loudspeakers that convert an electrical signal into sound,
microphones that convert sound waves in air into an electrical signal, and
hydrophones that convert sound waves in water into an electrical signal. MEMS hydrophones are currently being used to detect various sounds within our oceans. Anchored to the bottom of the ocean or dragged behind a ship, micro-sized hydrophones detect the sounds generated by ships, submarines, ocean waves and marine animals.
Common electromagnetic transducers include Magnetic cartridges and generators which convert motion in a magnetic field into an electrical energy.
An electromagnetically driven and sensed MEMS gyroscope is currently on the market. This gyroscope uses a permanent magnet and a resonating “ring” to detect rotation or motion. The detected motion creates a capacitive charge within the device.
Common electrostatic transducers include the electrometer which converts static or energy from a vibrating reed into electricity, and the Van de Graaf generator. The images in the slide are of a Van de Graaf generator. This generator converts a build up of static charge into high voltage.
MEMS electrostatic transducers are found in MEMS resonators, On/Off valves for fuel injection, and drop ejectors that use an electrostaticly driven piston. A common electrostatic microtransducer is the comb drive. Refer to the Introduction to Transducers lesson to learn how a MEMS comb drive works.

## Slide 11: Electromechanical Transducers
Generators
Galvanometer
Motor
Strain gauge
Motors - Convert electrical energy to mechanical energy
Strain Gauge – converts strain or a change in material length and width to a change in resistance and thus a change in electrical energy through the material.
Notes: Electromechanical transducers are transducers that either convert electrical to mechanical energy or motion, or convert mechanical movement such as deformation or stress into electrical energy.
Electromechanical Transducers, some of which are also called actuators, include generators, which convert mechanical energy (or motion) into electrical energy, Galvanometer which convert the electric current of a coil in a magnetic field into movement, and motors which converts electrical energy into mechanical energy or motion.
Strain gauges are electromechanical transducers found in many MEMS components. A strain gauge converts the deformation, stress or strain of a material into a change in the material’s electrical resistance and thus a change in current flowing through the material. Referring to the strain gauge in the graphic, each leg of the gauge has a resistance, determined primarily by the material itself. As the gauge “stretches” or is strained, the legs getting longer, increasing the resistance in each leg and thus the overall resistance of the gauge.

## Slide 12: Strain Gauges
Transducers commonly incorporated into MEMS devices.
Use the piezoelectric properties of materials
A strain gauge used to measure an increase in cantilever mass.
Notes: Here is an example of a strain gauge at work. Strain gauges are commonly incorporated into MEMS devices such as pressure sensors and micro-cantilevers. MEMS strain gauges use the piezoelectric properties of metals and other materials to change the resistance of the material when the strain gauge is “stretched” due to mechanical movement, stress or strain.
This graphic illustrates a micro-cantilever with a strain gauge used to measure an increase in cantilever mass. As the analytes or particles being analyzed attach to the probe coating on the cantilever, the mass of the cantilever increases, causing the cantilever to “bend” and the strain gauge to lengthen. This changes the resistance of the gauge and thus the amount of current flowing through it. This change in current is proportional to the change in cantilever’s mass.

## Slide 13: Other Types of Transducers
Photoelectric – light energy to electrical energy or vice versa.
Thermoelectric – heat energy to electrical energy or vice versa.
Converts Electrical Signals into Light Energy
(Cathode Ray Tube)
Notes: Two other types of transducers include photoelectric and thermoelectric. Photoelectric transducers convert light energy to electrical energy or vice versa.
Thermoelectric transducers convert heat energy to electrical energy or vice versa.
Types of photoelectric transducers include the cathode ray tube or CRT shown in the graphic, light bulbs, laser diodes and light-emitting diodes.
Thermoelectric Transducers include the thermocouple and thermister. As previously discussed, the thermocouple converts heat energy to electrical energy while the thermister is a component that experiences changes in resistance with changes in temperature. In other words, as the temperature of the thermister increases, so does its resistance.
Micro-sized transducers that use temperature, chemical reactions, and mechanical stress to produce changes in voltage, resistance, resonant frequency, or light are used throughout microsensors. Such transducers are used in MEMS pressure sensors, temperature sensors, chemical sensor arrays, and optical modulators.

## Slide 14: Question
What type of transducers are you familiar with?
Explain how these transducer affect your life on a daily basis.
Notes: Now that you’ve had a quick review of transducers, what they are and what they do, what type of transducer are you familiar with? Look around you, think about your home, your car. Are there any devices that are sensing something? How do transducer affect your every day life?

## Slide 15: Summary
A transducer is a device that converts one form of energy into another.
If the output energy is motion, the transducer is also an actuator.
Sensors make sense from a transducer’s output.
There are many, many different kinds of transducers.
Notes: For a short review - A transducer is a device which converts one form of energy into another. Transducers are used in all aspects of life to measure changes in the environment, to enhance everyday applications, and to learn more about the world around us. An actuator is a device that converts energy into motion. Therefore, an actuator can also be a transducer. When the output of the transducer is converted to a readable format, the device is called a sensor.
At this point, if you haven’t already read the Introduction to Transducers lesson, then you should do so now. To learn even more about specific types of transducers both in the macro and micro-scales, complete the activity “What are Transducers?”

## Slide 16: Acknowledgements
Made possible through grants from the National Science Foundation Department of Undergraduate Education #0830384, 0902411, and 1205138.
Any opinions, findings and conclusions or recommendations expressed in this material are those of the authors and creators, and do not necessarily reflect the views of the National Science Foundation.
Southwest Center for Microsystems Education (SCME) NSF ATE Center
© 2010 Regents of the University of New Mexico
Content is protected by the CC Attribution Non-Commercial Share Alike license.
Revised May 2017