## Slide 1: Introduction to Actuators
Introduction to Actuators Learning Module
Micro-sized polysilicon mirror with drive motors consisting of combdrives and gears.
[Courtesy of Sandia National Laboratories, SUMMiT(TM) Technologies, www.mems.sandia.gov]
Notes: In this presentation you will learn about actuators, what they are, what they can do, and various applications. Be sure to read the lesson Introduction to Actuators. The lesson that goes into more detail on some of the devices discussed in this presentation.

## Slide 2: Unit Overview
The following topics will be discussed:
What are actuators?
Types of actuators in both the macro and microscales.
Notes: In this presentation we will answer the question – what are actuators? We will also discuss several types of actuators in both the macro and microscales. The understanding of this information is important to microelectromechanical (MEMS) or microsystems technology.

## Slide 3: What are Actuators?
An actuator actuates or moves something.
An actuator uses some type of energy to provide motion or to apply a force.
Types of actuators: electric motor, gear train, screw jack
[Image of microgears courtesy of Sandia National Laboratories, SUMMiT(TM) Technologies, www.mems.sandia.gov]
Notes: An actuator is a device that actuates or moves something. An actuator uses some type of energy to provide motion or to apply a force. For example, an electric motor uses electrical energy to create a rotational movement or to turn on object, or to move an object. A gear train uses an input such as mechanical or electrical to move something in rotary or linear motion, and a screw jack uses manual or mechanical input to create linear motion. So in short, an actuator converts some type of energy into motion. Actuators consist of motors, gears, pumps, pistons, valves, and switches.

## Slide 4: Types of Actuators
Manual or mechanical
Hydraulic/Pneumatic
Thermal
Electric
Notes: The energy used on the input of an actuator determines its classification. For example, manual actuator require a manual or mechanical input, such as levers and jacks. Hydraulic or pneumatic actuators use pressurized liquid or air to move something. Such devices include pistons and valves. Thermal actuators use hot and cold temperatures. A type of thermal actuator that we will discuss is the bimetallic switch. Electric actuators use electricity as the input energy. Such actuators include motors and resonators.

## Slide 5: Thermal Actuators
Converts thermal energy into motion
Utilizes an effect called thermal expansion.
If the joined metals are heated, in what direction will they bend – up or down?
Notes: Let’s start with a discussion of thermal actuators. Thermal actuators are actuators that convert thermal energy into movement. One type of thermal actuator is a bimetallic strip, a strip made from two different metals such as steel and copper. The two metals have different temperature coefficients which means, when heated, they expand at two different rates. The graphic illustrates this. When these two metals are heated, metal 2 expands more than metal 1; therefore, metal 2 has a higher temperature coefficient than metal 1.
Now let’s join these two strips together.
Since they are joined, and each metal is expanding, but expanding at different rates, the strip bends. In this case, in which direction does the strip bend?
If you said “upward”, you are correct! This bending is due to thermal expansion.
Thermal expansion is the manifestation of a change in thermal energy in a material. When a material is heated, the average distance between atoms (or molecules) increases. The amount of distance differs for different types of material. This microscopic increase in distance is unperceivable to the human eye. However, because of the huge numbers of atoms (or molecules) in a piece of material, the material expands considerably and, at times, is noticeable to the human eye.
The opposite reaction occurs with a decrease in temperature, when most materials contract. When exposed to the elements, a material constantly expands and contracts with ambient temperature changes. This is why expansion joints are built into roadways and bridges.

## Slide 6: Bimetallic Switch
Vertical Thermal Actuators
[Images courtesy of Southwest Research Institute. Copyright SwRI.]
Notes: A bimetallic strip takes advantage of the thermal expansion effect to generate motion. Two dissimilar strips of metal are joined together along their entire lengths. When heat is applied, the bimetallic strip bends in the direction of the metal with the smaller coefficient of thermal expansion. Bimetallic strips have many uses. One common use is in thermostats used to control the temperature in homes and offices. The diagram shows how a bimetallic is strip used in a thermostat. At temperature T1, the metals of the switch are the same length and the switch is open. As the temperature increases, the metal starts to bend. At temperature T2, the switch makes makes contact with the electrical contact and current flows through the switch. If the switch controls an air conditioner, the air conditioner will come on at the higher temperature of T2.
The thermal switches in the scanning electron microscope image on the right were developed by engineers at the Southwest Research Institute. These micro-sized vertical thermal actuators operate by a differential expansion between two layers of dissimilar materials in each arm of the switch. To obtain the initial upward curvature seen in the picture, the engineers took advantage of residual stresses in the film layers used to build the switch.
At the microscale, bimetallic actuators are made using both metallic and non-metallic materials. A variety of thin films with different thermal expansion characteristics are used to fabricate switches, electrodes, valves, strain gauges, and diaphragms.

## Slide 7: Electric Actuators
An electric motor is a transducer AND an actuator because it converts an electric current into a large magnetic field which then turns a shaft (mechanical energy).
Schematics of an Electric Motor
V
Shaft
Rotor
Coils
Notes: Electric actuators use electricity or electrical energy to create motion. An electric motor is a type of an electric actuator. Most direct current (DC) motors operate by current flowing through a coil of wire (the rotor) and creating a magnetic field around the coil. The coil is wrapped around the motor's shaft and is positioned between the poles of a large permanent magnet or electromagnet. The interaction of the two magnetic fields causes the coil to rotate on its axis, rotating the motor's shaft (see figure above). Reverse the direction of the current flowing through the rotor and the rotor will rotate in the opposite direction. Thus, an electric motor is a transducer AND an actuator because it converts electrical energy to magnetic energy to mechanical energy or motion.

## Slide 8: Mechanical Actuators
Anything that requires a mechanical input and causes motion
A Screw Jack is one example
A screw jack converts rotational energy into linear motion
Notes: Mechanical actuators convert a mechanical or manual input into linear or rotary motion. A common example of a mechanical actuator is a screw jack. The figure shows a screw jack in operation. Rotation of the screw causes the legs of the jack to move apart or move together. Inspecting the motion of the top point of the jack, this mechanical rotational input is clearly converted into linear mechanical motion.
Mechanical actuators can produce a rotational output with the proper gearing mechanism.

## Slide 9: MEMS Actuators
Electrostatic Comb drive
Uses in resonators, microengines, gyroscopes
SEM of a typical comb-drive resonator
[Courtesy of Sandia National Laboratories]
Notes: An example of a microactuator (or MEMS) is the electrostatic combdrive. Combdrives are used in many MEMS applications such as resonators, microengines, and gyroscopes. The force generated is low, usually less than 50µN. However, these devices are predictable and reliable making them usable for a variety of micro-applications.
The image above is an example of a MEMS electrostatic combdrive resonator which is a common MEMS actuator. A resonator is a device which naturally oscillates at its resonance frequency. The oscillations in a resonator can either be electrostatic or mechanical. As an actuator, this combdrive resonator can move another object at the rate of the combdrive’s oscillations. In the Introduction to Actuator’s unit, you will study a microelectromechanical system that uses combdrives to move an optical mirror.

## Slide 10: Questions
When was the last time that you “actuated” something?
What did you do?
What was the actuator?
What was moved?
Notes: Here’s some food for thought. Think about the answers to these questions.

## Slide 11: Summary
An actuator is a device that converts energy into motion.
Actuators can be thermal, electric, manual, or hydraulic/pneumatic.
Actuators are found in both the macro and micro-scales.
Notes: In summary, an actuator is a device that converts energy into motion…
If you haven’t already read the Introduction to Actuators lesson, you should do so at this time. It goes into further detail on many of the micro-actuators covered in this presentation. Once you have read the lesson, complete the activity – What are actuators?

## Slide 12: Acknowledgements
Made possible through grants from the National Science Foundation Department of Undergraduate Education #0830384, 0902411, and 1205138.
Any opinions, findings and conclusions or recommendations expressed in this material are those of the authors and creators, and do not necessarily reflect the views of the National Science Foundation.
Southwest Center for Microsystems Education (SCME) NSF ATE Center
© 2010 Regents of the University of New Mexico
Content is protected by the CC Attribution Non-Commercial Share Alike license.
Website: www.scme-nm.org
Revised May 2017