## Slide 1: MEMS for environmental and bioterrorism
MEMS for Environmental and Bioterrorism Learning Module
Cybernetic Insect

## Slide 2: Unit Overview
This unit introduces you to MEMS (MicroElectroMechanical Systems) applications for environmental and bioterrorism sensing.
You will identify several reasons that such sensing devices are needed, as well as the types of MEMS that are currently used or being tested for such applications.

## Slide 3: Objectives
Discuss at least three ways that MEMS are currently being applied to environmental or bioterrorism sensing.
Develop at least two ideas for possible MEMS applications in environmental or bioterrorism sensing.

## Slide 4: Introduction
December 26, 2004, a earthquake of magnitude 9.0 struck the coastal area off northern Sumatra in Indonesia (see graphic). A number of aftershocks occurred, some of magnitude 7.1.
These earthquakes triggered a series of tsunamis in the Indian Ocean affecting Indonesia and neighboring countries in Asia and the east coasts of Africa. All countries suffered serious damage to the coastal areas and small islands.

## Slide 5: Tsunami’s Effect
While the final death toll will never be known, an estimated 250,000 people in eleven countries perished.
The question that has been asked a thousand times since the tsunamis hit is
"Why weren’t people warned?"

## Slide 6: Lack of Indian Ocean Warning System
The tsunamis were detected by geophysicists at the Pacific Tsunami Warning Centre (PTWC) in Honolulu, Hawaii.
The PTWC did inform several agencies in countries on the Indian Ocean.
However, because there was no detection system in the Indian Ocean, nor was there a communication system in place for people living along the coasts, this warning never reached the people.
As a result, many lives were lost.

## Slide 7: MEMS Sensors
MEMS sensors have proven to be part of the answer to an effective warning system.
MEMS accelerometers (like the ones in airbag deployment units and the one above), MEMS pressure sensors, and MEMS hydrophones are being integrated into various warning systems.
MEMS Accelerometer - The inertial mass is deflected from its nominal position as a result of acceleration. This deflection of the mass is converted to an electrical signal as the sensor's output.
[Photo courtesy of Khalil Najafi, University of Michigan]

## Slide 8: MEMS Sensing
MEMS sensors help protect and preserve life on earth by doing the following:
Monitor weather and other environmental conditions, including agriculture and ecological concerns.
Monitor energy, fluid, machinery, and other systems in factories, facilities, buildings and homes as well as the structures themselves.
Sense transportation vehicles and related transportation infrastructure including roads, bridges, and equipment.
Sense potential security and safety problems in buildings, factories, airports, and war zones (to name a few).

## Slide 9: In This Unit…
Several examples of how MEMS technology can be and is being applied are presented here.
Their uses and applications on land, in air, or in water or a combination of the three are discussed.

## Slide 10: Marine Environment
Parameters commonly measured in the marine environment are
temperature,
pressure,
light,
tidal and current velocity,
plant pigmentation (chlorophyll in plankton),
pH,
pesticide concentration, and
seabed characteristics such as seismic signals.
MEMS sensor technology is used to sense and monitor many of these parameters.

## Slide 11: Tsunami Warning System
The objective of a warning system is to continuously monitor the state of the sea surface in near-real time. This allows for a fast and efficient warning to be issued through the correct channels.
A warning system consists of three components:
  scientific instrumentation
  communication system
  warning system

## Slide 12: Tsunami Warning System
The scientific instrumentation is an assortment of sensors designed to detect various ocean activity. Some sensors target the tsunami wave over different ocean depths by measuring wave height.
Additional sensors detect other environmental factors affecting the sea level (tides, atmospheric pressure, wind). These factors must be understood and monitored in order to separate their signals from the tsunami wave and other ocean waves.
The graphic illustrates the DART system with a total of 39 sensors in the Pacific, Atlantic, and Mediterranean Oceans.
Graphic source: National Oceanic and Atmospheric Administration

## Slide 13: How It All Ties Together
Once the data from the sensors, Global Navigation Satellite Systems, and tide gauges have been collected, a fast transmission of the data is sent to a processing center. Radio transmission are sent from a buoy to a land station. A distance greater than about 50 km between antennas require a satellite link.
Processing centers analyze the incoming data and detect potential sources of tsunamis and if a warning is required.

## Slide 14: Current Tsunami Warning Systems
Deep-ocean Assessment and Reporting of Tsunamis (DART) system of the National Oceanic and Atmospheric Administration (NOAA). As of 2008, 39 sensors/buoys have been placed in the Pacific, Atlantic and Mediterranean Oceans. (See the previous graphic of the Dart II System)
German and Indonesian Tsunami Early Warning System (GITEWS) - The GITEWS is focused on the Indian ocean in response to the Indian Ocean tsunamis. This system was put into operation in November, 2008.

## Slide 15: Other MEMS Ocean Sensors
Temperature Sensors
Monitoring the ocean's temperature is important because an increase in temperature decreases oxygen concentration. It also decreases solubility of some minerals and salts. This is extremely important for aquatic life.
Light Sensors
Decreased light penetration affects algal and marine plant growth. It also indicates the presence of silt and other light absorbing or reflecting compounds in the water.

## Slide 16: Attachment Devices for Ocean Sensors
MEM devices in the water can be attached to a variety of objects:
ships
floating devices (buoys)
fixed objects such as rigs
anchors on the bottom of the ocean or river
AUVs (automated underwater vehicles)

## Slide 17: AUVs and Lab-on-a-chip (LOC)
AUVs are unmanned underwater vehicles for real time monitoring in the oceans. AUVs can be equipped with "Lab on a Chip (LOC)", a set of sensors developed on a single chip, using MEMS technology. "Lab on a Chip" devices sense a large number of chemical pollutants simultaneously.
This first generation of miniaturized sensors that will measure the marine environment has been built to withstand conditions in the open ocean. (Image credit: National Oceanography Centre, Southampton)
ScienceDaily.

## Slide 18: Water and Land Environments
Clean Up
MEMS devices (e.g., pressure sensors) can be used to detect oil leakage from pipelines.
In the case of unfortunate oil spills, they sense information about the ocean currents to predict how far the oil slick can travel. This information helps in the clean up planning process.

## Slide 19: Water and Land Environments
Locating Oil and Gas Reserves
MEMS geophones and accelerometers can sense the vibrations sent up from the earth’s belly.
An array of MEMS geophones are planted over a wide area on the seabed.
Vibrations are intentionally produced on the ground surface.
MEMS devices measure the reflection of vibrations from different layers in the earth’s belly.
Readings are used to create a geological map, which indicates the size and location of the oil/gas reservoir.

## Slide 20: Hydrophones
Just as microphones collect sounds in air, hydrophones detect sounds in water.
A hydrophone could be anchored to the ocean bottom or dragged behind a ship. It "hears" the sounds in the water, sounds generated by ships, submarines, ocean waves or marine animals.
A hydrophone can "hear" tertiary waves created by earthquakes or any movements within the earth's crust.
Hydrophone Ocean Sensors

## Slide 21: Animal Tags
Tags are tiny devices attached to animals like whales and deer. They provide vital data about the surroundings and about the animal.
These tags contain MEMS devices that monitor a pressure, temperature, or sound. They also work as a camera or radio transmitter for data collection at remote locations.

## Slide 22: Smart Dust
Smart Dust is a network of micro-sized wireless MEMS sensors that communicate with each other through tiny transmitters.
These wireless sensor networks are being developed to detect and monitor an endless number of parameters like light, temperature, vibrations, and movement.
Smart dust can be incorporated into roads and bridges or suspended in the atmosphere to evaluate the make of air.

## Slide 23: Smart Dust
Each sensor in the network is called a mote and is the size of a dust particle.
A network contains several sensors, computing circuits, bidirectional wireless communications technology and a power supply.
Motes gather data, run computations and communicate, using two-way band radio, with other motes at distances approaching 1,000 feet.
When clustered together, motes automatically create highly flexible, low power networks.
Smart Dust mote conceptual diagram
Project through Berkeley,
DARPA and
National Science Foundation
Brett Warneke, Mike Scott, and Brian Leibowitz

## Slide 24: Applications of Smart Dust
What do you think are some possible applications of smart dust?

## Slide 25: Air Environment – the ENose
One Enose (electronic nose) senses a several gases, compound or combination of compounds at one time.
An ENose is being used by NASA on spacecraft to alert the crew to dangerous leaks such as ammonia and to evaluate the quality of the air.
The Enose has numerous medical, industrial and commercial applications such as environmental monitoring, quality control, food processing and medical diagnosis.

## Slide 26: ENose
The picture is the ENose developed by NASA and tested on the International Space Station in 2008. Since then its size has shrunk and its applications, expanded.
The ENose developed by NASA's Advanced Environmental Monitoring and Control division
[Graphic source: NASA]

## Slide 27: How the ENose Works
The ENose uses a collection of 16 different polymer films on a set of electrodes. The graphic (a) illustrates six films/electrodes. These films are specially designed to conduct electricity based on its resistance. A baseline resistance reading is established (a) with no odors (ambient air).
Six (6) films or electrodes in reference state (no odors)
[Graphics: NASA's Advanced Environmental Monitoring and Control division]

## Slide 28: How the ENose Works
When a substance -- such as the stray molecules from an ammonia leak -- is absorbed into these films, the films expand slightly (b), changing their resistivity. The change in resistivity then causes a change in electrode current.
Films reacting to the presence of a odor or gas
[Graphics: NASA's Advanced Environmental Monitoring and Control division]

## Slide 29: How the ENose Works
Because each film is made of a different polymer, each reacts to a chemical compound in a slightly different way. While the changes in resistivity in a single polymer film would not be enough to identify a compound, the varied changes in 16 films produce a distinctive, identifiable pattern for a specific compound. Graphics (b) and (c) shows two different compounds being sensed.

## Slide 30: Cybernetic Insects
Research is taking place for the development of
cybernetic insects and
genetically modified insects that mature around an implanted sensor.
Such insects can be used for surveillance and reconnaissance micro-air vehicles (MAVs), evaluating air quality, and collecting and evaluating environmental particles.
Cybernetic Insect

## Slide 31: Food for Thought
What are some other applications for seismic MEMS sensors?
What are some applications for the ENose that were not discussed?
Name some applications of MEMS sensors that could benefit military personnel.

## Slide 32: Summary
MEMS technology is used for environmental and bioterrorism sensing based on perceived risk and need.
The most common sensors are pressure (including flow rate and acoustical), temperature, radiation, chemical, and biological.
Sensors can be coupled together and transmit data via wireless networks to sites where the data is analyzed.

## Slide 33: Disclaimer
The information contained herein is considered to be true and accurate; however the Southwest Center for Microsystems Education (SCME) makes no guarantees concerning the authenticity of any statement. SCME accepts no liability for the content of this unit, or for the consequences of any actions taken on the basis of the information provided.

## Slide 34: Acknowledgements
Made possible through grants from the National Science Foundation Department of Undergraduate Education #0830384, 0902411, and 1205138.
Any opinions, findings and conclusions or recommendations expressed in this material are those of the authors and creators, and do not necessarily reflect the views of the National Science Foundation.
Southwest Center for Microsystems Education (SCME) NSF ATE Center
© 2009 Regents of the University of New Mexico
Content is protected by the CC Attribution Non-Commercial Share Alike license.
Website: www.scme-nm.org
Revised August 2017