## Slide 1: Retinal Prosthesis
Southwest Center for Microsystems Education
scme-nm.org
Notes: In February of 2013 the US Food and Drug Administration approved The Argus II retinal prosthesis for patients with advanced retinitis pigmentosa, an inherited, degenerative eye disease in which the photo receptors of the retina do not work like they are suppose to. This same system was approved in Europe two years prior.

## Slide 2: Overview
The FDA approval was based on data that included a clinical trial of 30 people that had received the Argus II. Results showed that most participants were able to performed basic functions better with the device than without it.
[FDA News Release, February 14, 2013, U.S. Department of Health and Human Services]
See letters
Notes: This approval was based on a clinical trial in which almost all of the 30 participants were able to perform basic tasks better with the prosthesis than without it. Some patients were able to recognize large letters and words, be able to step off a street curb, and match black, gray and white socks. Imagine not being able to do even that!

## Slide 3: Artificial Retinal Prosthesis
Prototype of a Retina Implant
[Photo by Randy Montoya. Courtesy of Sandia National Laboratories]
Argus Retinal Stimulation System
Glass with video camera
Video processor
Notes: The Argus™ Retinal Stimulation System consists of both in vivo (internal parts) and in vitro (external parts). The in vivo parts are the artificial retina that you see in the picture. This retina consists of and array of micro-size electrotrodes. Also in vivo is a receiver/ transmitter. The in vitro parts are a video camera built into the eyeglasses of the patient, a video processor and cable.

## Slide 4: The Human Eye
Normal vision - light enters the eye through the cornea then the lens.
The lens focuses the light on the retina.
The retina contains photoreceptors cells which convert the light to electric impulses.
Impulses travel into the optic nerve to the brain where the information is processed.
The Human Eye
[Public Domain: National Eye Institute]
Notes: Before we talk about how the retinal prosthesis works, let's take a quick look at how the human eye works. Normal vision occurs when light enters the eye through the cornea then the lens. The lens focuses the light on the retina, the inner-most lining of the eyeball. The retina contains photoreceptors cells which convert the light to electric impulses. These impulses travel into the optic nerve then to the brain where the information is processed.
In retinal diseases, such as age-related macular degeneration and retinitis pigmentosa, the photoreceptor cells in the retina do not work for one reason or another. That’s were the artificial retina comes into play. An artificial retina is designed to bypass these cells and interface with some of the retina’s viable cells which transmit signals directly to the optic nerve.

## Slide 5: Restoring Sight
Notes: The Artificial Retina system consists of a video camera, video processor, antenna/receiver, and the artificial retina (electrode array). A miniature video camera housed in the patient’s glasses where it is able to capture an image or scene. The video is sent to a small patient-worn computer or the video processing unit where it is processed and transformed into instructions that are sent back to the glasses via an external cable. These instructions are transmitted wirelessly to an antenna. The signals are then sent to the artificial retina or electrode array.

## Slide 6: MEMS Artificial Retina
Bypasses photoreceptor cells and transmits signals to the optic nerve.
Light hitting the array is converted to electric impulses.
These electric impulses travel into the optic nerve then to the brain.
MEMS Artificial Retinal Implant
Notes: This artificial retina is an electrode studded array placed on or beneath the surface of the retina. Each electrode is less than 100 micrometers in diameter which is the diameter of a human hair and smaller. Light from the receiver hits the electrodes in the array and is converted to electric impulses. These impulses bypass the damaged photoreceptors and stimulate the retina’s remaining cells, which transmit the visual information along the optic nerve to the brain, which perceives patterns of light and dark spots corresponding to the electrodes stimulated. With practice patients learn to interpret these visual patterns.

## Slide 7: What Does a Patient See?
[Images generated by the DOE-funded Artificial Retinal Implant Vision Simulator devised and developed by Dr. Wolfgang Fink and Mark Tarbell at the Visual and Autonomous Exploration Systems Research Laboratory, California Institute of Technology. Printed with permission.]
Argus I
16 pixels
Argus II
60 pixels
Argus III
200+ pixels
Argus IV
1000+ pixels
Notes: These images were generated by a vision stimulator to give us an idea of what a patient with artificial retinal devices could see. Increasing the number of electrodes in the retina array results in more visual perceptions and higher resolution vision. In Argus I there were 16 electrodes or 16 pixels, it took patients about 15 seconds to recognize objects using the retinal implant. In Argus II with 60 pixels that processing time was down to 2-3 seconds. Argus II had enough resolution for patients to see the edges of doors, or the shape of a building. Argus III is being designed with more than 200 pixels and Argus IV is anticipated to have at least 1000 pixels if not more. The hope is, that with 1000 pixels, one might actually have facial recognition. Wouldn’t that be marvelous!

## Slide 8: Goals and Challenges
Increasing resolution.
Designing the implant to be more flexible and compatible with the curvature of the eye.
Making ALL components internal.
Creating biocompatible, batteries for long lasting use in vivo.
Notes: These are some of the challenges and goals for future retinal prosthesis. We want increased resolution for that facial recognition. The implanted retina needs to be smaller, have more electrodes and be more compatible with the curvature of the eye.
There has been talk about eventually making all of the components in vivo or inside of the eye. To be able to do this, all components will need to be biocompatible and the batteries will need to be able to last a very, very long time.
We’ll get there.

## Slide 9: Acknowledgements
Made possible through grants from the National Science Foundation Department of Undergraduate Education #0830384, 0902411, and 1205138.
This Learning Module was developed in conjunction with Bio-Link, a National Science Foundation Advanced Technological Education (ATE) Center for Biotechnology @ www.bio-link.org.
Any opinions, findings and conclusions or recommendations expressed in this material are those of the authors and creators, and do not necessarily reflect the views of the National Science Foundation.
Southwest Center for Microsystems Education (SCME) NSF ATE Center
© 2010 Regents of the University of New Mexico
Content is protected by the CC Attribution Non-Commercial Share Alike license.
Website: www.scme-nm.org
For more information on BioMEMS therapeutic devices, download the
BioMEMS Therapeutic Learning Module
from scme-nm.org – educational materials. – bioMEMS.
Notes: For more information about the retinal prosthesis and other therapeutic devices, download the BioMEMS Therapeutic Learning Module form the SCME website. Thank you for viewing this presentation.