## Slide 1: Mems applications overview
MEMS Applications Overview Learning Module
3-D accelerometer (inertia sensor) – x & y axes upper left, z axis center
[Image courtesy of ChipWorks]

## Slide 2: Unit Overview
Microelectromechanical systems (MEMS) are very small devices or groups of devices that can integrate both mechanical and electrical components.
This unit provides a brief summary of MEMS devices already on the market, the various fields in which MEMS are used, and the possibilities for MEMS in these fields.

## Slide 3: What are MEMS?
Micro-Electro-Mechanical-System
Electronic and mechanical components constructed on one chip or device.
Milli, micro and nano-size components
Example – Digital Mirror Devices used for digital light processing.
Notes: A DMD is an array of micromirrors (left figure). Each micromirror (between 5um and 20um square) is designed to tilt into (ON) or away from (OFF) the light source. Each mirror sits on top of a hinge that tilts when a digital signal energizes an electrode beneath the hinge. Torsion springs return the mirror (hinge) to home position when the signal is removed.
One mirror can be turned OFF and ON as many as 30,000 times per second. There are thousands of mirrors in an array with less than 1 μm spacing between them. The DLP (digital light processing) 1080p technology delivers more than 2 million pixels for true 1920x1080p resolution.

## Slide 4: What do MEMS do?
Sense
Think
Communicate
Act
Movement
Vibration
Pressure
Light
Temperature
Mass
Collect information
Analyze data
Interpret data
Make decisions
React to change
Send information
Provide outputs
Transmit data
Provide warnings
Respond to changes
Move devices
Transmit light and fluids
Transport particles

## Slide 5: Types of MEMS Devices
  Pressure sensors
  Accelerometers (inertial sensors)
  Micromirrors
  Gear Trains
  Miniature robots
  Fluid pumps
  Microdroplet generators
  Optical scanners
  Probes (neural, surface)
  Analyzers
  Imagers
Notes: Examples of MEMS devices include pressure sensors, transducers, accelerometers (inertial sensors), micromirrors, miniature robots, flow sensors, fluid pumps, microdroplet generators, and optical scanners. The automotive industry was one of the first industries to commercially embrace MEMS devices in the '90's with the accelerometer – a MEMS device used to sense a sudden change in velocity causing the activation of a crash (or air) bag.
Other automotive applications currently in use or coming soon include sensors for monitoring tire pressure and fuel pressure, "smart" sensors for collision avoidance and skid detection, "smart" suspension for sport utility vehicles to reduce rollover risk, automatic seatbelt restraints and door locking, vehicle security, headlight leveling, and navigation.

## Slide 6: Applications of MEMS
Applications are developed where miniaturization is beneficial:
  Consumer products
  Aerospace
  Automotive
  Biomedical
  Chemical
  Optical displays
  Wireless and optical communications
  Fluidics

## Slide 7: Specific Applications of MEMS
  MEMS nozzles and pumps for inkjet printers
  RF devices – Switches, phase shifter resonators, filters and variable antennas
  Fuel delivery systems that can control propellant motion
  Coating sensors that compensate for coating problems (adhesion, surface tension)
MEMS-based InkJet Printhead
Piezoelectric or bubble jet based injection methods meeting the demand for higher and better resolution printing (smaller droplets). The graphic below illustrates a piezoelectric printhead. When a voltage is applied across the piezoelectric crystal, a minute amount of ink is released into the nozzle.
Notes: Below are a few more applications for MEMS:
RF devices – Small variable devices such as switches, tunable capacitors, phase shifters resonators, inductors, filters and variable antennas.
Fuel delivery systems – Sensors within systems for aircraft and spacecraft that can control propellant motion (or slosh)
Coating applications – Devices that compensate for coating problems such as adhesion and surface tension.
MEMS nozzles and pumps for inkjet printers (microfluidics) – Piezoelectrics or bubble jet based injection methods meeting the demand for higher and better resolution printing (smaller droplets). The graphic below illustrates a piezoelectric print head. When a voltage is applied across the piezoelectric crystal, a minute amount of ink is released into the nozzle.

## Slide 8: Retinal Prosthesis
Medical MEMS – aka BioMEMS - can consist of in vivo (internal) components and in vitro (external) components such as this retinal prosthesis
A microarray or retinal implant is implanted in vivo on the retina.
An external camera and processor are mounted in a pair of glasses.
Watch this video to see how it works.
https://youtu.be/Bi_HpbFKnSw
Notes: The component shown in the picture is a micro-electrode array used for a retina implant. It is placed within the eye on the retina or just below the surface of the retina.
A camera mounted in a pair of glasses captures the image and sends it to a microprocessor, also in the glasses.
The microprocessor translates the image into an electrical signal.
A transmitter sends the electrical signal to the retina implant (microarray) via a receiver and interface module.
The electrical signal stimulates the electrodes on the microarray.
This causes the array to emit pulses that enter to optic nerve and travel to the brain.
The brain translates these pulses into a version of the image seen by the camera. (The more electrodes in the array, the better the image.)

## Slide 9: Retinal Prosthesis: What the patient sees
These images show what a patient with a MEMS retinal prosthesis should see. Increasing the number of electrodes in the retina array results in more visual perceptions and higher resolution vision.
Images generated by the DOE-funded Artificial Retinal Implant Vision Simulator devised and developed by Dr. Wolfgang Fink and Mark Tarbell at the Visual and Autonomous Exploration Systems Research Laboratory, California Institute of Technology.
[Printed with permission.]
Notes: In 2007 six patients were successfully implanted with the first prototype Model 1 device or Argus I™. Argus I™ contained 16 electrodes (16 pixels - left picture). The Argus II™ (256 pixels-middle picture) is currently being tested in phase two of clinical trials. The third model (1000+ pixels – right picture) is under development.
UPDATE: In February 2011 the FDA granted market approval of the Argus II™

## Slide 10: MEMS Sensors
Sensors are a major application for MEMS devices.
Three primary MEMS sensors
  pressure sensors
  chemical sensors
  inertial sensors (accelerometers, gyroscopes)
MEMS sensors can be used in combinations with other sensors for multisensing applications. For example, a MEMS can be designed with sensors to measure the flow rate of a liquid sample and at the same time identify any contaminates within the sample.

## Slide 11: Smartphones and MEMS
Smartphones can do much of what they do because of the various MEMS sensors built into them.
  Inertial
  Pressure
  RGB
  Geomagnetic
  Temperature
  Humidity
  Proximity
  To name a few

## Slide 12: Smartphones, Tablets, Laptops, Cameras
Droid Card
Courtesy of ifixit.com
http://www.ifixit.com/Teardown/Motorola-Droid-Bionic-Teardown/6449/1
They all have MEMS inertial sensors (gyroscopes and accelerometers) as well as PS, transmitters/receivers.

## Slide 13: MEMS Scale – Pressure Sensors (PS)
[Macro PS photos courtesy of Bob Willis
MEMS diaphragm courtesy of UNM/MTTC]
A pressure sensor is a device consisting of a mechanical component (diaphragm) and electronic components. These pictures compare a macro-size pressure sensor (70mm in diameter) to a MEMS pressure sensor
Notes: An equivalent of a MEMS device at the macro scale is the diaphragm gauge used to measure pressures and pressure changes. Such a gauge consists of a mechanical component (the diaphragm) and electrical components that supply an input and output voltage(s). As the diaphragm moves due to changes in pressure, an output voltage proportional to the change in pressure is generated. Reduce the size of the diaphragm and the related electrical components, place them all on the same microchip, and you have a microelectromechanical system or MEMS. The above photographs compare the macro pressure sensor to the MEMS sensor (left picture) and the diaphragms (right pictures).

## Slide 14: MEMS Pressure Sensor
MEMS pressure sensors use a flexible diaphragm as the sensing device.
One side of the diaphragm is exposed to a sealed, reference pressure and the other side is open to external pressure.
The diaphragm moves with a change in the external pressure.
MEMS Pressure Sensor
[Courtesy of the MTTC, University of New Mexico]
What are some possible applications for this type of sensor?
Notes: MEMS pressure sensors are designed to measure absolute or differential pressures. They typically use a flexible diaphragm as the sensing device as seen in the picture to the right. One side of the diaphragm is exposed to a sealed, reference pressure and the other side is open to an external pressure. The diaphragm moves with a change in the external pressure. MEMS pressure sensors are specified to work in a variety of ranges, depending on the design and application. There are MEMS pressure sensors that can measure pressures near 0 ATM or as high as 10 ATM or ~150 psi.
A couple of challenges that have been met in the design of MEMS pressure sensors are signal conversion and the use of MEMS in diverse environments. MEMS can convert physical quantities such as air flow and liquid levels into pressure values that are measured by an electronic system. This design quality has enhanced the versatility of MEMS sensors.

## Slide 15: MEMS in the Automotive Industry
MEMS pressure sensors sense, monitor and transmit
  Tire pressure
  Fuel pressure
  Oil pressure
  Air flow
  Absolute air pressure within the intake manifold of the engine
Notes: The characteristic of MEMS that incorporates several devices on one chip allows them to be used in a variety of environments. MEMS pressure sensors are used in conjunction with other sensors such as temperature sensors and accelerometers for multisensing applications or other components. For example, a MEMS pressure sensor mounted inside a tire includes a special filter supplies only dry air to the sensor's diaphragm.
In the automotive industry, MEMS pressure sensors monitor the absolute air pressure within the intake manifold of the engine. MEMS are also being designed to sense tire pressure, fuel pressure, and air flow.

## Slide 16: Pressure Sensors in BioMedical Applications
  Blood PS
  Intracranial PS
  PS in endoscopes
  Sensors for infusion pumps
RF (radio frequency) elements incorporated into the MEMS device allow the sensor to transmit its measurements to an external receiver.
Notes: In the biomedical field, current and developing applications for MEMS pressure sensors include blood pressure sensors (see photo), single and multipoint catheters, intracranial pressure sensors, cerebrospinal fluid pressure sensors, intraocular pressure (IOP) monitors, and other implanted coronary pressure measurements. The picture shows three blood pressure sensors on the head of a pin. These sensors were developed by Lucas NovaSensor to measure blood pressure and provide an electrical output representative of the pressure. RF elements are incorporated into the MEMS device allowing the sensor to transmit its measurements to an external receiver.
MEMS Blood Pressure Sensors on the head of a pin. [Photo courtesy of Lucas NovaSensor, Fremont, CA]
MEMS pressure sensors are also incorporated into endoscopes for measuring pressure in the stomach and other organs, infusion pumps for monitoring blockage, and noninvasive blood pressure monitors. Applications of MEMS pressure sensors within the biomedical field are numerous.

## Slide 17: MEMS Inertial Sensors
Newton's First Law of Motion
"An object at rest tends to stay at rest and an object in motion tends to stay in motion with the same speed and in the same direction unless acted upon by an unbalanced force.”
MEMS inertial sensors are designed to sense a change in an object's inertia, and then convert, or transduce inertial force into a measurable signal
Notes: MEMS inertial sensors are designed to sense a change in an object's inertia, and then convert, or transduce inertial force into a measurable signal. They measure changes in acceleration, vibration, orientation and inclination. This is done through the use of micro-sized devices called accelerometers and gyroscopes.
MEMS inertial sensors can be found in navigation devices, anti-shake systems for high-magnification video cameras, airbag deployment systems, the Apple iPhone, pacemakers, and stabilization systems.
MEMS inertial sensors are one of the fastest growing segments of the MEMS market. "Driven by accelerometer applications like the Apple iPhone and the Nintendo Wii, and by the coming legislation requiring stability-control systems in all vehicles, these devices have moved out of industrial segments and into consumer ubiquity."

## Slide 18: MEMS Accelerometers
The simplest MEMS accelerometer sensor is an inertial mass suspended by springs. The mass is deflected from its nominal position as a result of acceleration. This deflection of the mass is converted to an electrical signal as the sensor's output.
MEMS out-of-plane Accelerometer
[Photo courtesy of Khalil Najafi, University of Michigan]
MEMS In-plane accelerometer
Notes: Like pressure sensors, MEMS accelerometers are devices that can be used in a variety of sensing applications due to their simplicity and versatility.
The simplest MEMS accelerometer sensor consists of an inertial mass suspended by springs (see SEM image above). Forces affect this mass as a result in an acceleration (change in velocity – speed and/or direction). The forces cause the mass to be deflected from its nominal position. As with the movement of the pressure sensor's diaphragm, the deflection of the mass is converted to an electrical signal as the sensor's output.

## Slide 19: MEMS Gyroscopes
A gyroscope is generally a spinning wheel or disk with a free axis allowing it to take any orientation (below left). Some MEMS gyroscopes use a vibrating structure rather than the traditional rotating disk to determine orientation (see bottom right).
MEMS Vibrating Ring Gyroscope
[(Photo courtesy of Sandia National Laboratories]
Notes: A gyroscope is generally a spinning wheel or disk with a free axis allowing it to take any orientation (below left). Some MEMS gyroscopes use a vibrating structure rather than the traditional rotating disk to determine orientation (see bottom right). This is possible based on the physical principle that a vibrating object tends to keep vibrating in the same plane as its support rotates. As the plane of oscillation rotates, the vibrating gyroscope or transducer is affected due to the Coriolis effect (the tendency for any moving body on or above the earth's surface, (e.g., an ocean current or an artillery round), to drift sideways from its course because of the earth's rotation.10)

## Slide 20: MEMS Inertial Sensors in Automobiles
  Airbag deployment
  "Smart" sensors for collision avoidance and skid detection
  Active suspension
  Automobile navigation
  Antitheft system
  Headlight leveling and positioning
  Rollover detectors
3-axis High-Performance Micromachined Accelerometer
(Each accelerometer senses movement in one direction. The top 2 “in-plane” accelerometers sense x & y directions. The “out-of-plane” accelerometer on the bottom sense movement in the z direction.)
[Image courtesy of Chipworks]
Polysilicon Connectors
Notes: Improvements in the area of shock or crash sensors include the ability of the sensor to detect where a person is sitting and to use the physical characteristics of that person to determine how the airbag will be deployed (the amount of force is required based on the size and position of the occupant).
One of the most traditional applications of MEMS devices is the use of inertial sensors in automotive airbag deployment. The type of inertial sensor used in air-bags is an accelerometer or shock sensor. The airbag deployment MEMS 3-axis accelerometer contains three accelerometers – one for each direction (x, y, z) – and the circuitry for each direction.
The accelerometers used in the original airbags were relatively large and bulky with the electronics mounted near the airbag. The cost of these earlier airbag sensors was over $50.11 Today's MEMS integrate the accelerometer and the electronics on a single chip (about the dimensions of a sugar cube), at a cost between $5 to $10.9 These sensors provide a quicker response to rapid deceleration and more reliable functionality
Below are several other applications of MEMS inertial sensors in the automotive industry:
"Smart" sensors for collision avoidance and skid detection2
"Smart" suspension for sport utility vehicles to reduce rollover risk2
Automobile diagnostics
Automobile navigation
Antitheft system
Headlight leveling and positioning
Rollover detectors
Active suspension

## Slide 21: Other Applications of MEMS Inertial Sensors
  Motion and shock detection
  Vibration detection and measurement
  Measurement of tilt and inclination
  Anti-theft devices
  Home security devices
  Computer screen scrolling and zooming devices
  Gaming devices for portables and PC's (e.g. Wii and Playstation)
  Image stabilizer cameras and phones
Comparison of 3-axis accelerometers – new technology (top), old technology (bottom)]
Notes: Other applications for MEMS inertial sensors:
Motion and shock detection - MEMS "shock sensors" are placed inside packages designated for shipping. They are used to monitor any type of damage that occurs while the package is in transit. When integrated with another MEMS device, they also monitor the time it takes to ship the package to the customer. When an RF MEMS is incorporated into the shock sensor, the collected data can be transmitted to external tracking systems.5
Vibration detection and measurement – Example: Devices that measure frequency and amplitude, and create a vibration signature
Measurement of tilt and inclination – Example: Compasses that can be read in any position or inclination
Anti-theft devices mounted in cars, computers, briefcases and other mobile devices
Home security devices mounted in windows, doors, ceilings and other places as deemed necessary by the homeowner
Computer screen scrolling and zooming devices (when interfaced with the appropriate software)
Gaming devices for portables and PC's - Example: The motion of the hand is sensed, eliminating the need for a mouse (e.g. Wii controllers)
Image stabilizer for video cameras, digital cameras and mobile phones
Remote monitoring of the physical movements and out-of-building mobility of people in assisted living or living at home.12
What are some other applcications for MEMS inertial sensors?

## Slide 22: Other Types of MEMS
In addition to sensors, MEMS consist of pumping devices, gear trains, moveable mirrors, miniature robots, tweezers, tools, lens, and lasers.
These devices have found numerous applications with various fields such as biomedical, optical, wireless networks, aerospace, and consumer products.
Notes: Several of these applications are discussed in the following sections.

## Slide 23: Pill Cam for Diagnostic Applications
Notes: In the biomedical field, current and developing applications for MEMS pressure sensors include blood pressure sensors (see photo), single and multipoint catheters, intracranial pressure sensors, cerebrospinal fluid pressure sensors, intraocular pressure (IOP) monitors, and other implanted coronary pressure measurements. The picture shows three blood pressure sensors on the head of a pin. These sensors were developed by Lucas NovaSensor to measure blood pressure and provide an electrical output representative of the pressure. RF elements are incorporated into the MEMS device allowing the sensor to transmit its measurements to an external receiver.
MEMS Blood Pressure Sensors on the head of a pin. [Photo courtesy of Lucas NovaSensor, Fremont, CA]
MEMS pressure sensors are also incorporated into endoscopes for measuring pressure in the stomach and other organs, infusion pumps for monitoring blockage, and noninvasive blood pressure monitors. Applications of MEMS pressure sensors within the biomedical field are numerous.

## Slide 24: MEMS in the Medical Field
  Drug delivery systems.
  Glucose monitors (chemical sensor)
  Clinical Lab Sample Analysis
MiniMed Paradigm[R] 522 insulin pump, with MiniLinkTM] transmitter and infusion set.
A chemical sensor (C) measures the blood glucose and a transmitter (D) that sends the measurement to the a computer in (A). (A) also contains a micropump that delivers a precise amount of insulin through the cannula (B) to the patient. This is a continuous bioMEMS monitoring and drug delivery system.
(Printed with permission from Medtronic Diabetes)
Notes: In addition to the medical pressure sensors already discussed, there are several applications for MEMS in the medical field. MEMS devices used in biological applications are called bioMEMS. These systems often require the use of biocompatible materials or biological molecules to avoid rejection by the host organism. Below is a partial listing of bioMEMS for medical applications:
The precise dispensing of small amounts of liquids (amounts as minute as a picoliter and flow rates of as low as a few microliters per minute) found in needleless injectors, nebulizers, insulin pumps, and drug delivery systems.
Sub-dermal glucose monitors that not only monitor one's glucose levels, but also deliver the necessary amount of insulin. The picture to the right of the MiniMed Paradigm 522 shows a diabetic patient wearing a chemical sensor (C) that measures the blood glucose and a transmitter (D) that sends the measurement to the a computer in (A). (A) also contains a micropump that delivers a precise amount of insulin through the cannula (B) to the patient. This is a continuous bioMEMS monitoring and drug delivery system that has eliminated the traditional finger pricks for blood samples that diabetics have to do daily.
MEMS tweezers or miniature robot arms that move, rotate, cut and place molecules, sort cells and proteins, and manipulate organelles and DNA inside a living cell.5
Miniature surgical tools that incorporate sensing and measuring devices.
Medical diagnostics (glucose monitoring, blood analysis, cells counts and numerous others).
MiniMed Paradigm[R] 522 insulin pump, with MiniLinkTM] transmitter and infusion set. (Printed with permission from Medtronic Diabetes)
Biosensing devices used to measure biomolecular information (cells, antibodies, DNA, RNA enzymes) Medical stents inserted into previously blocked arteries to open and maintain a clear channel for blood flow. There devices are coated with a nanocoating of a drug that is slowly released into the bloodstream over time. This prevents a re-narrowing of the artery and future procedures.
DNA microarrays are used to test for genetic diseases, medicine interaction, gene mutations, and other biological markers. They also compare the genes of two or more specimens, identify the activity of genes and show how genes are affected by external stimuli.
DNA duplication devices such as the Polymerase Chain Reaction (PCR) system that takes a miniscule bit of DNA, amplifies it and produces an exact duplication.

## Slide 25: Clinical Laboratory Testing
A lab-on-a-chip (LOC) takes the laboratory testing of biomolecular samples (e.g. blood, urine, sweat, sputum) out of the clinical lab and places it in the field or point-of-care (POC).
LOCs use microfluidics and chemical sensors to simultaneously identify multiples analytes (substances being analyzed).
Lab-on-a-chip (LOC)
Printed with permission. From Blazej,R.G.,Kumaresan,P. and Mathies, R.A. PNAS 103,7240-7245 (2006).
Notes: An example of a home LOC is the home pregnancy test. This bioMEMS uses a reactive coating that identifies a specific protein found in the urine of pregnant women. One can also test for HIV and hepatitis B and C at home using a LOC.
Astronauts currently use a LOC to do daily blood tests for complete blood counts and any biomarkers that could identify health problems.

## Slide 26: DNA Microarrays
  Genetic testing
  and comparison
Notes: An example of a home LOC is the home pregnancy test. This bioMEMS uses a reactive coating that identifies a specific protein found in the urine of pregnant women. One can also test for HIV and hepatitis B and C at home using a LOC.
Astronauts currently use a LOC to do daily blood tests for complete blood counts and any biomarkers that could identify health problems.

## Slide 27: Optical MEMS – The Digital Mirror Device (DMD)
[Images Courtesy of Texas Instruments]
Notes: A DMD is an array of micromirrors (left figure). Each micromirror (between 5um and 20um square) is designed to tilt into (ON) or away from (OFF) the light source. The mirror tilts when a digital signal energizes an electrode beneath the mirror. One mirror can be turned OFF and ON as many as 30,000 times per second. There are thousands of mirrors in an array with less than 1 μm spacing between them. The DLP 1080p technology delivers more than 2 million pixels for true 1920x1080p resolution. The diagram on the right illustrates how the DLP system works
Levels of a DMD Array (left) and How a DLP system works (right).
[Images Courtesy of Texas Instruments]
Texas Instrument's Digital Mirror Devices (DMD) have been used for several years in a variety of projection systems including video projection and digital cinema. The technology is called digital light processing or DLPTM, a trademark owned by Texas Instruments, Inc. A DMD is an array of micromirrors (see figure of DMD array below and left). Each micromirror (between 5um and 20um per side) is designed to tilt into (ON) or away from (OFF) a light source. The mirror tilts when a digital signal energizes an electrode beneath the mirror. The applied actuator voltage causes the mirror corner to be attracted to the actuator pad resulting in the tilt of the mirror. When the digital signal is removed, the mirror returns to the "home" position. In the ON position, the mirror reflects light towards the output lens. In the OFF position, the light is reflected away from the output optics to a light absorber within the projection system housing. . One mirror can be turned OFF and ON over 30,000 times per second.

## Slide 28: Optical MEMS - Grating Light Valve (GLV)
Silicon nitride ribbons coated with aluminum. A set of four ribbons (two fixed and two moveable) produce a 20 μm square pixel.
Moveable ribbons are "moved" up and down electrostatically.
GLVs are used in high definition TVs and are being investigated for use in maskless photolithography.
Grating Light Valve (GLV) – top view and side view showing actuated state and unactuated state
Notes: Grating Light Valve – Top view and side view showing actuated and unactuated states
The GLV (Grating Light Valve) device (shown above) developed by Silicon Light Machines, is another micro optical based system. This microdevice consists of an array of silicon nitride ribbons coated with aluminum. A set of four ribbons (two fixed and two moveable) produce a 20 μm square pixel. The ribbons are held "up" by the tensile strength of the material (silicon nitride and aluminum). The moveable ribbons are "moved" up and down electrostatically. Variable voltages applied to the electrodes pull the ribbons down variable distances. For projection devices, red, green, and blue laser light is passed across the array as the ribbons move up and down. The position of each ribbon determines how much light is diffracted or reflected to a lens. When no voltage is applied, the tensile strength of the ribbon will allow it to snap back.
Both of these systems (DLP and GLV) are considered types of spatial light modulators (SLMs) which modulate (redirect) light to create high definition imaging from digital signals.

## Slide 29: Other Optical Applications of MEMS
  Optical Communication Networks
  Display screens on cell phones and PDAs
  Optical Spectrometers
  Bar code readers
  Micromirrors
  Atomic Force Microscopes
MEMS Pop-up mirror for optical applications. Notice the hinge allowing for the different angles needed to direct light in different directions. Also notice the track that assists in positioning the mirror at the correct angle.
[Image Courtesy of Sandia National Laboratories
SUMMITTM Technologies, www.mems.sandia.gov]
Notes: MEMS micromirror arrays are often the key components used in spatial light modulators or SLM’s. These devices are used in high definition display systems as well as optical switching networks. Optical micromirror arrays transmit optical information without going through the timely and costly signal conversion process of optical to electronic and back to optical. The micromirrors can act as switches that direct light from a fiber optic to another fiber optic or to a specific output port by moving up and down, left to right or swiveling to a desired position. This requires the individual mirrors to be actuated, supported on a movable mount or stage, and integrated into a digital network.
The scanning electron microscope image to the right shows a popped-up micromirror. Notice the hinge allowing for the different angles needed to direct light in different directions. Also notice the track that assists in positioning the mirror at the correct angle.
Other optical applications of MEMS:
Projection displays (GLV's and DLP's)
Tunable lasers and filters
Spatial Light Modulators (SLMs)
Variable optical attenuators
Optical Spectrometers
Bar code readers
Maskless lithography

## Slide 30: More MEMS
Zyvex Microgrippers
[Printed with permission © 2002 Zyvex]
In vivo battery to power artificial retina arrays
[Courtesy of Sandia National Laboratories]
Cyborgs and
Drones
Notes: Microgrippers – Grippers or tweezers used in a variety of fields to clasp, pick up, and move micron to nanosize components. The microgrippers (50 microns thick), developed by Zyvex Corporation, pick and place other microdevices in an automated microassembly process. The gripper on the left opens to 100 microns. The gripper on the right opens to 125 microns.
Microgrippers are also used in MIS or minimally invasive surgery systems as the “hands” of the surgeon.

## Slide 31: Summary
The automotive industry was one of the first industries to embrace the use of MEMS. Since then, MEMS have found applications in wireless communications, biomedical, aerospace, and consumer products (to name a few).
The potential uses for MEMS are endless.

## Slide 32: Acknowledgements
Made possible through grants from the National Science Foundation Department of Undergraduate Education #0830384, 0902411, and 1205138.
Any opinions, findings and conclusions or recommendations expressed in this material are those of the authors and creators, and do not necessarily reflect the views of the National Science Foundation.
Southwest Center for Microsystems Education (SCME) NSF ATE Center
© 2009 Regents of the University of New Mexico
Content is protected by the CC Attribution Non-Commercial Share Alike license.
Website: www.scme-nm.org
Revised August 2016