## Slide 1: Introduction to Sensors
Introduction to Sensors Learning Module
Micro-Pressure Sensor

## Slide 2: Unit Overview
The following topics will be discussed:
What are Sensors?
Types of Sensors
Type of micro-sensors

## Slide 3: Introduction
A sensor is a device that receives and responds to a signal.
  The signal could be heat, light, motion, or chemical.
  A sensor converts the signal into an analog or digital representation of the input signal.
  Sensors detect and/or measure many different conditions.
What are some sensors that you have used?
Notes: A sensor is a device that receives and responds to a signal. This signal must be produced by some type of energy, such as heat, light, motion, or chemical reaction. Once a sensor detects one or more of these signals (an input), it converts it into an analog or digital representation of the input signal. Based on this explanation of a sensor, you should see that sensors are used in all aspects of life to detect and/or measure many different conditions. What are some sensors that you are familiar with or use daily?

## Slide 4: Introduction
Humans are equipped with 5 different types of sensors.
Human Sensors
Notes: Human beings are equipped with 5 different sensors.
Eyes detect light energy, ears detect acoustic energy, a tongue and a nose detect certain chemicals, and skin detects pressures and temperatures. The eyes, ears, tongue, nose, and skin receive these signals then send messages to the brain which outputs a response. For example, when you touch a hot plate, it is your brain that tells you it is hot, not your skin.
This unit describes the basic concepts of sensors and introduces the different types in both the macro and micro scales.

## Slide 5: Basic Concepts of Sensors
Detect the presence of energy
Detect changes in or the transfer of energy
Detect by receiving a signal then responding to that signal
Convert a signal into a readable output
350° F
278° F
Setpoint
Thermocouple
Sensor electronics
Actual
Temperature
Heater element
Notes: Sensors detect the presence of energies as well as changes in or the transfer of energies. Sensors detect by receiving a signal from a device such as a transducer, then responding to that signal by converting it into an output that can easily be read and understood. Typically sensors convert a recognized signal into an electrical – analog or digital – output that is readable. In other words, the sensor takes the output of the transducer and converts it to a readable format. In many sensors, the sensor compares the input and output signals to the transducer or sensor, quantifies the change, and responds with an appropriate output.
Let’s take a look at an oven’s temperature sensor. This diagram show how such a sensor works. The oven is initially programmed with a setpoint, in this case – 350 degrees which turns on the heating element. As the oven heats, the oven’s thermocouple converts the temperature of the oven to a voltage. This voltage is read by the sensor’s electronic circuitry. The sensor compares the setpoint with the thermocouple output. If the thermocouple output is less than the setpoint, the sensor provides an output that keeps the heating elements on and that displays the actual temperature. Once the setpoint and the actual temperature (as sensed by the thermocouple) match, then the heating element is turned off.

## Slide 6: Thermal Sensors
Thermometer
Thermocouple gauge
Resistance Temperature Detectors (RTDs)
Infrared ear thermometer
[Image courtesy of NASA Jet Propulsion Laboratory]
Notes: Just like there are different types of transducers, there are many different types of sensors. Thermal sensors are devices that measure hot and cold. Thermal sensors use some type of transducer that converts temperature or heat to another form of energy.
For example, a thermometer, like the one you use to take your body temperature, measures absolute temperatures (temperatures relative to absolute zero). The thermometer in the picture is an infrared thermometer than can sense body temperature without contact with the body. These thermometers work using a phenomenon called black body radiation. Any object at a temperature above absolute zero has molecules inside moving around. The higher the temperature, the faster the molecules move. As they move, the molecules emit infrared radiation--a type of electromagnetic radiation below the visible spectrum of light. As the object gets hotter, it emits more infrared radiation. An infrared thermometer measures the amount of radiation, converts it to temperature, and provides a readout.
Other thermal sensors include thermocouple gauges which use thermocouples to measure temperature, and RTDs or resistance temperature detectors. RTDs are a coiled wire that exhibits a change in resistance when the temperature of the wire changes. RTD sensors monitor the resistance change and outputs a reading of the effective temperature.
Read more: How Do Infrared Thermometers Work? | eHow.com http://www.ehow.com/how-does_4965130_infrared-thermometers-work.html#ixzz1qvPoUxRM

## Slide 7: Mechanical Sensors
Pressure sensor
Barometer
Altimeter
Liquid flow sensor
Gas flow
Accelerometer
Aneroid Barometer
Diagram of Aneroid Barometer
Notes: Another type of sensor is the Mechanical sensor. Mechanical sensors use movement of some type to sense a specific parameter such as pressure, the flow rate of a fluid, or acceleration. An example is the Aneroid Barometer shown in the graphic. An aneroid barometer senses changes in atmospheric pressure by the expansion or compression of an aneroid capsule (a thin, disk-shaped capsule, usually metallic, and partially evacuated of gas). An external spring is connected to the capsule and a needle is mechanically linked to the spring. As the pressure on the outside of the capsule increases, the capsule compresses causing the spring to move the needle indicating an increase in barometric pressure. As the pressure drops, the capsule expands, and the spring moves in the opposite direction, moving the needle to show a decrease in barometric pressure.
Other types of mechanical sensors include the Pressure sensor which measures pressure, Barometers which measures atmospheric pressure, and
Altimeters which measures the altitude of an object above a fixed level.
The we have
Liquid flow sensors, which measure flow rates of liquids, gas flow sensors which measure velocity, direction, and the flow rate of a gas, and accelerometers which measure acceleration and deceleration.

## Slide 8: Electrical Sensors
Ohmmeter
Voltmeter
Galvanometer and ammeter
Watt-hour meter
Schematic and photograph of a Galvanometer
used for sensing electrical currents
Notes: Electrical sensors are sensors that measure changes in resistance, current voltage, or electrical energy.
Examples of electrical sensors are the
Ohmmeter which measures resistance,
The Voltmeter which measures voltage,
The Galvanometer and ammeter which measure current and the
Watt-hour meter which measures the amount of electrical energy supplied to and used by a residence or business.
The images show galvanometer, a special type of ammeter, which is used to sense and measure the amount of current flowing through a wire.
In a galvanometer, current flows through a coil, the red wire wound around a metal cylinder in the leftmost image. This current creats a magnetic field around the coil. Permanent magnets surround the coil. The interaction of these two magnetic fields causes the coil/cylinder combination to pivot around its central axis. The amount and direction of the pivot move the needle at the readout (the right image) left or right, indicating the level of current and its polarity (negative or positive, respectively). This device uses two energy conversions to sense and quantify an electric current: electrical to magnetic and magnetic to mechanical rotation.

## Slide 9: Chemical Sensors
Carbon dioxide detector
Oxygen sensor
Schematic and Photo of a Carbon Dioxide Sensor
Notes: Chemical sensors detect the presence of certain chemicals or classes of chemicals and quantify the amount and/or type of chemical detected.
For example, an oxygen sensor measures the percentage of oxygen in a gas or liquid being analyzed.
A carbon dioxide sensor detects the presence of CO2 . There are chemical sensors that detect a specific gas such as CO2, arsenic, or ammonia. However, microtechnology has enabled the ability to fabricate micro-sized sensors that can detect several different gases simultaneously.
Chemical sensing has really taken off with microtechnology. Just like the macro-sized components, MEMS chemical sensors can detect a wide variety of different gases but because of their size, they can go places that macro-sized sensors can’t really go. MEMS sensors can also be incorporated into objects for continuous sensing of a gas or selection of gases.
MEMS chemical sensors have numerous medical, industrial, and commercial applications such as biohazard detection, quality control in food processing, and medical diagnosis. Such devices are sometimes referred to an ENose or electronic nose.5

## Slide 10: Optical Sensors
Photodetectors
Proximity Detectors
Infra-red sensor
Solar cell and the solar cells
on the International Space Station
[Public Domain]
Notes: Optical sensors detect light of a specific wavelength or light within a range of wavelengths. The manner in which the light is detected depends upon the type of optical sensor. For example, the photocells seen in the pictures, use photovoltaic cells to convert light energy directly into electricity. The photocells on the international space cells are double sided in order to maximum the amount of light detected. The electricity generated supplies the electricity for all operations aboard the station.
Photodetectors range from simple resistive photocells to photodiodes and transistors. The detector must be part of a switching or amplification circuit; by themselves, they can carry only small amounts of current. They're used to control elevator-door closers, assembly-line part counters and safety systems. Light-sensitive semiconductor materials have been used in a variety of electronic components.
Miniature proximity detectors use light to sense when objects are nearby. They contain an LED source and a detector to measure reflected light. Measuring a few millimeters on a side, they're small enough to be used in small electronic appliances and cell phones. They have a range of a few inches, useful for determining the alignment of paper in a copier, for example, the presence of your hand, or if a laptop case is open or closed.
Infrared sensors are used in situations where visible light would be inconvenient or counterproductive. They can be used to tell if someone's in a room, by the heat given off by a person's body. As we saw previously, infrared sensors are being used to measure body temperature by measuring the amount of black body radiation. Read more: Types of Optical Sensors | eHow.com http://www.ehow.com/about_5454698_types-optical-sensors.html#ixzz1qvmq2slx
Read more: Types of Optical Sensors | eHow.com http://www.ehow.com/about_5454698_types-optical-sensors.html#ixzz1qvlXfdwI
Light sensors (photodetectors) – detects light and electromagnetic energy
Photocells (photoresistor) – a variable resistor affected by intensity changes in ambient light.
Infra-red sensor – detects infra-red radiation

## Slide 11: Other Types of Sensors
Acoustic wave sensors
Seismometers
Motion sensors
Speedometers
Geiger counters
Biological sensors
Geiger Counter: Detects
Atomic Radiation
Notes: Other types of sensors include Acoustic sensor such as the Acoustic wave sensors which measure the wave velocity in an environment to detect the chemical species present and Seismometers which measure seismic waves.
  There are also motion sensors such as accelerometers and gyroscopes with detects motion, acceleration, rotation, and vibration;
  Speedometers which measure speed, Geiger counters which detect atomic radiation and biological sensors which can sense and measure specific biological molecules in the human body.

## Slide 12: Macro vs. Micro Sensors
Example of a Diaphragm MicroPressure Sensor [University of New Mexico, MTTC]
Notes: Transducers and sensors can be found in both the macro and microscales. For most macro sensors there is an equivalent micro-sensor that can perform the same function or functions more efficiently and in many cases, for lower production costs. The images seen here show a macro-sized pressure sensor on the left and its equivalent on the right. The pressure sensor on the left is a capacitor manometer. Underneath the electronics board that you can see is a diaphragm and reference chamber that are used to measure changes in pressure. The right image shows the micro-pressure diaphragm and electronics sensing circuit. Both components perform the same function; however, their size difference is dramatic. You can see this in the left image. The green circle is around a MEMS pressure sensor, which you can see is extremely small in comparison.
Other such comparisons can be found with pumps, inertial sensors, chemical sensors, photosensors, and many, many more.

## Slide 13: Question
Is it possible for a device to be defined as both a sensor and a transducer?
Describe an example.

## Slide 14: Summary
A sensor is a device that receives and responds to a signal.
This signal must be produced by some type of energy, such as heat, light, motion, or chemical.
Notes: As we’ve said many times before, a transducer is a device which converts one form of energy into another. When the output of the transducer is quantified and converted to a readable format, the transducer is called a sensor.
Therefore, a sensor is a device that receives and responds to a signal. This signal usually comes from a transducer as some type of energy, such as heat, light, motion, or chemical.

## Slide 15: Acknowledgements
Made possible through grants from the National Science Foundation Department of Undergraduate Education #0830384, 0902411, and 1205138.
Any opinions, findings and conclusions or recommendations expressed in this material are those of the authors and creators, and do not necessarily reflect the views of the National Science Foundation.
Southwest Center for Microsystems Education (SCME) NSF ATE Center
© 2010 Regents of the University of New Mexico
Content is protected by the CC Attribution Non-Commercial Share Alike license.
Website: www.scme-nm.org
Revised May 2017