## Slide 1
ACADs (08-006) Covered
Keywords
Exposure, gamma ray constant, time, distance, shielding, shield placement, dose rate, sky shine, stay time, inverse square, line source, parallel source, Bremsstrahlung, attenuation, buildup, energy absorption, rule of thumb, 10th value.
Description
Supporting Material
1.1.8.3.2 | 3.3.3.9 | 3.3.3.11.1 | 3.3.3.11.2 | 3.3.3.11.3 | 3.3.3.12 | 3.3.3.13 | 3.3.8.4
3.3.8.11 | 3.3.8.18 | 3.3.8.22 | 3.3.8.29 | 3.3.8.32 | 4.11.7 | 4.11.9.1 | 4.11.9.2
4.11.9.3 | 4.11.10 | 4.11.11 | 4.12.2 | 4.15.1 |  |  | 
Notes: <number>

## Slide 2: External Radiation Exposure Control
HPT-001.017
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 3: Enabling Objectives - 1
Identify 3 Exposure Control Methods
Describe Dose and Dose Rate
Use ‘Stay Time’ Equation
Use Inverse Square Law & Line Source Equation
Use DR = 6CE Equation
Define & Use Specific Gamma Ray Constant
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 4: Enabling Objectives - 2
Define “Bremsstrahlung”
Describe Neutron Shielding Materials
List 3 Factors Influencing Attenuation of Photons
Describe: “Linear Attenuation Coefficient” “Mass Attenuation Coefficient” “Energy Absorption Coefficient”
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 5: Enabling Objectives - 3
Use Shielding Equations to Calculate: 1. Exposure Levels 2. Shield Thicknesses
Define Radiation “Buildup”
Define: 1. Half-Value Layer 2. Tenth-Value Layer
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 6: Enabling Objectives - 4
List Rule of Thumb TVLs for: 1. Lead 2. Steel 3. Concrete 4. Water
Define “Skyshine” & Describe its Impact
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 7: Radiation Exposure Control Methods
Limit Time of Exposure
Increase Distance
Provide Shielding
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 8: Dose & Dose Rate
Dose – Radiation Absorbed
Dose Rate – Time Over Which the Radiation is Absorbed
Dose = Time * Dose Rate, or
Time = Dose/Dose Rate
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 9: Dose Example
Need to Calibrate an Instrument in a 50 mrem/hr Field.
Estimated Time = 2 hours
What will be the Total Dose?
Solution: Dose = 2 hours * 50 mrem/hr = 100 mrem
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 10: Stay Time
Stay Time – Time Allowed in an Area Before Exceeding a Limit.
Example: 1. Need to Replace a Filter Where Dose Rate is 100 mrem/hr. 2. Cannot Exceed 300 mrem/week 3. Time = 8 hours
How Long can each person work?
How many people must work?
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 11: Stay Time - Solution
Time = Dose/Dose Rate.
Time = 300 mrem/100 mrem/hr.
Time = 3 hours.
# of People =8 Hr/Job ÷ 3 Hr/Person
# of People = 2.66, or 3 People
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 12: Types of Radiation Sources
Point Source – Small Valve
Line Source – Length of Pipe
Plane Source – Tank or Pool of Water
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 13: Inverse Square Law
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 14: Inverse Square Law Calculations
Distance From Intensity
Source, cm Photons/cm2-sec.
0 1,000,000
10 (x) 796
20 (2x) 199 (1/4 * 796)
30 (3x) 88 (1/9 * 796)
40 (4x) 50 (1/16 * 796)
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 15: Inverse Square Law Equation
As Distance Increases by a Factor of 2, Intensity Decreases by the Square of the Distance. Therefore:
I1/I2 = d22/d12, or I1d12 = I2d22 Rearranging:
I2 = (I1 * d12)/d22
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 16: Problem # 1
A Ra-226 Source Produces a Dose Rate of 10,000 µR/hr at 1 foot. What will be the Dose Rate at 10 ft?; 20 ft?; 25 ft?; 30 ft?; and 40 ft?
Solution: I2 = (I1 * d12)/d22 = [10,000 µR/hr * (1 ft)2]/(10 ft)2, or I2 = 100 µR/hr at 10 feet
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 17: Problem # 1, Cont’d
Solving for the Other Distances: d2, ft I2, µR/hr 10 (x) 100 20 (2x) 25 (1/4) 25 16 30 (3x) 11 (1/9) 40 (4x) 6.25 (1/16)
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 18: Problem # 2
A Source Reads 125 rem/hr at 1 Foot. At What Distance Would the Reading be Reduced to 1 rem/hr?
I1d12 = I2d22 d22 = I1d12/I2,= (125 mrem/hr*1 ft2)/1 rem/hr d22 = 125 ft2, or d2 = 11.2 ft
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 19: Approximation of Exposure For Gamma Emitters
DR = 6CEn, Where, DR = Dose Rate, R/hr at 1 Foot C = Activity, Curies En = Total Effective Gamma Energy (MeV) per Disintegration
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 20: Limitations of Equation
Useful to Within ± 20%
Only Used for Gamma and X-Rays
Good for Energy Levels 0.07 – 2 MeV
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 21: Problem # 3
Determine the Exposure Rate From a Point Source With 10 Ci of Cs-137.
DR = 6CEn (En for Cs-137 = 0.662 MeV)
DR = (6)(10 Ci)(0.662 MeV)
DR = 39.6 R/hr at 1 Foot
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 22: Problem # 4
Determine the Exposure Rate 12 ft From a Point Source With 50 Ci of Co-60. (Co-60 has 2 Gamma Photons, Both of Which are Emitted with Every Disintegration. Therefore, the Effective Gamma Energy for Co-60 is: En = 1.17 MeV + 1.33 MeV = 2.50 MeV
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 23: Problem # 4 Solution
DR = 6CEn
DR = (6)(50 Ci)(2.50 MeV)
DR = 750 R/hr at 1 Foot
I2 = (I1 * d12)/d22, = (750 R/hr*1 ft2)/(12 ft)2
I2 = (750/144) R/hr = 5.2 R/hr at 12 Feet
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 24: Problem # 5
Determine the Exposure Rate From a Point Source With 2.5 Ci of Fe-59. From Handout # 02 we see that Fe-59 has 4 Gamma Photons: 0.143 MeV Emitted 1.0% of the time 0.192 MeV Emitted 3.1% of the time 1.099 MeV Emitted 56% of the time 1.292 MeV Emitted 43% of the time
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 25: Problem # 5 Solution
En for Fe-59 is Determined by: En = (0.143*0.01) + (0.192*0.03) + (1.099*0.56) + (1.292*0.43), or En = 1.18 MeV
DR = 6CEn = (6)(2.5 R/hr)(1.18 MeV) = 17.7 R/hr at 1 Foot
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 26: Specific Gamma Ray Constant
The Gamma Exposure Rate in R/hr 1 cm From a 1 mCi Source.
Γ = R-cm2/hr-mCi, or
Γ/10 = R/hr at 1 meter for each Curie of Activity
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 27: Specific Gamma Ray Constant, Example
Γ for Ra-226 = 8.25 R-cm2/hr-mCi, or
Γ/10 = 0.825 R/hr at 1 Meter for Each Curie Therefore, the Dose Rate 1 Meter From a 1 Ci Ra-226 Source = 0.825 R/hr.
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 28: Problem # 6
Determine the Exposure Rate 5 Meters From a 2 Ci Ra-226 Source.
Γ/10 = 0.825 R/hr at 1 Meter for Each Curie Therefore, for 2 Ci, the Exposure Rate is DR = 1.65 R/hr at 1 Meter
I2 = (I1 * d12)/d22, = (1.65 R/hr*1m2)/(5 m)2
I2 = 0.066 R/hr, or 66 mR/hr at 5 Meters
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 29: Problem # 7
Determine the Exposure Rate 6 Meters From 3 Ci Co-60. Γ /10 = 1.32 R/hr at 1 Meter for each Ci Therefore, for 3 Ci, DR = 3.96 R/hr I2 = (I1 * d12)/d22, = (3.96 R/hr*1m2)/(6m)2 I2= (3.96 R-m2/hr)/36m2 = 0.11 R/hr at 6 m
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 30: Line or Parallel Source
Dose Rate Decreases Linearly As the Distance Increases, so that: I1d1 = I2d2, or I2 = I1d1/d2
Applicable When d1 & d2 are ≤ One-Half the Length of the Line Source (L/2). The Inverse Square Law Applies from the Point where the Distance Exceeds L/2.
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 31: Problem # 8
100 mR/hr 2 Feet From a 20-Foot Section of Pipe. What is the Dose Rate 4 Feet From the Pipe? d1 & d2 < L/2 (10 Feet), Therefore, I2 = I1d1/d2 = (100 mR/hr*2ft)/4 ft I2 = 50 mR/hr
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 32: Problem # 9
2 R/hr on Contact With a Pipe. How Far Away Should Workers Stay to Avoid a Dose Rate of 200 mR/hr? (Assume Contact Reading at 1 inch From the Pipe). d2 = I1d1/I2 = (2 R/hr*1 in)/0.2 R/hr d2 = 10 in
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 33: Problem # 10
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program
Dose Rate 15 rem/hr at 1ft.
What will be the Dose Rate at 20 ft?

## Slide 34: Problem # 10 Solution
1. Use Linear Equation to Determine Dose Rate at Distance L/2. I2 = I1d1/d2 = (15 rem/hr*1 ft)/3 ft I2 = 5 rem/hr at 3 ft.
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 35: Problem # 10 Solution
2. Use Inverse Square Law to Determine Dose Rate at 20 ft. I2 = (I1 * d12)/d22 I2 = (5 rem/hr)(3ft)2/(20 ft)2 I2 = 0.1125 rem/hr or 112.5 mrem/hr
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 36: Shielding
Radiation Shielding: 1. Alpha Air, Paper 2. Beta Aluminum, Plastic 3. Gamma Lead, Steel, Concrete (High Z) 4. Neutron Water, Polyethylene (Low Z)
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 37: Bremsstrahlung
Braking Radiation, Produced by the Deflection of a Charged Particle (Beta Particle) So That it Slows Down and Releases Excess Energy as a Photon.
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 38: Bremsstrahlung
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program
Beta Particle
Photon

## Slide 39: Bremsstrahlung & Shielding
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 40: Attenuation
The Lessoning of the Amount, Force, Magnitude, or Value of…
Weaken
The Reduction in the Severity, Vitality, or Intensity of…
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 41: Factors Affecting Attenuation of Photons
The Energy of the Photon
The Type of Material (High or Low Z)
The Thickness of the Material
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 42: Attenuation Model
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 43: Linear Attenuation Coefficient
Constant Fractional Decrease in Intensity per Unit Thickness of a Substance.
Symbol: µ
Units: cm-1
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 44: Shielding Equation
The Intensity (I) of the Portion of a Beam That Penetrates a Shield is Given By: I = I0e-µx, Where: I0 = Original Intensity I = Exit Intensity e = Base of Natural Logarithms µ = Linear Attenuation Coefficient x = Shield Thickness
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 45: Problem # 11
The Exposure Rate From a 1 MeV Gamma Source is 500 mR/hr. You Package the Source in a Container with 2 inches of Lead Around the Source. What is the Dose Rate Outside the Package?
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 46: Problem # 11 Solution
x = 2 in or 5.08 cm
From Handout # 03: µ = 0.804 cm-1 I = I0e-µx = (500 mR/hr)(e-(0.804)(5.08)) I = (500 mR/hr)(e-4.084) = (500)(0.0168) I = 8.42 mR/hr
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 47: Problem # 12
What Thickness of Water is Needed to Reduce a 1 MeV Gamma Dose Rate From 100 mR/hr to 10 mR/hr? From Handout # 3, µ = 0.0707 cm-1
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 48: Problem # 12 Solution
I = I0e-µx, Rearrange to Solve for x: I/I0 = e-µx, and ln(I/I0) = ln(e-µx), or ln(I/I0) = -µx, and x = ln(I/I0)/-µ x = [ln(10/100)]/-0.0707 = ln(0.1)(-0.0707) x = (-2.303)/(-0.0707) = 32.57 CM
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 49: Total Linear Attenuation
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 50: Mass Attenuation Coefficient
Removes the Density (ρ) Dependence From the Attenuation Coefficient.
Symbol: µm
Units: cm-1/cm2/g so That: µm*ρ = µ, and
I = I0e-(µm)(ρ)x
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 51: Mass Attenuation Coefficient Graph
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 52: Problem # 13
A Source is to be Shipped in a Wooden Box. The Gamma Reading at the Surface of the Box is 1 R/hr. What Thickness of Lead Lining is Required to Reduce the Exposure Rate at the Surface of the Box to 2 mR/hr if the Energy Level is 0.66 MeV? Use the Mass Attenuation Coefficient (µm) From Handout # 4 and the Density (ρ) From Handout # 3.
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 53: Problem # 13 Solution
Rearranging the Equation I = I0e-(µm)(ρ)x to Solve for x Gives: x = [ln(I/I0)]/-(µm)(ρ) From Handouts # 3 & 4, µm = 0.105 cm2/g ρ = 11.35 g/cm3 x = ln(2/1000)/-1.192 = 5.21 cm
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 54: Buildup Factor
The Increase in Intensity of the Exiting Beam Resulting From the Scattered Radiation in a Shield Medium.
Equation: I = BI0e-µx , Where, B = the Buildup Factor
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 55: Buildup Factor Figure
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program
PHOTON INTENSITY VERSUS LENGTH OF TRAVEL

## Slide 56: Energy Absorption Coefficient
A Measure of the Attenuation Caused by Absorption of Energy That Results From its Passage Through a Medium.
Symbol = µe
Units = cm-1
The Sum of the Absorption Coefficient and the Scattering Coefficient is the Attenuation Coefficient.
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 57: Energy Absorption Coefficient Equation
I = I0e-µex, Where: I0 = Original Intensity I = Exit Intensity e = Base of Natural Logarithms µe = Energy Absorption Coefficient x = Shield Thickness
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 58: Problem # 14
Given a Box Containing a Non-Point Parallel Source of Ra-226 With an Exposure Rate of 0.75 R/hr and a 0.8 MeV Gamma. Determine the Amount of Lead Required to Reduce the Box Surface Reading to 2 mR/hr.
µe = 0.5727 cm-1
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 59: Problem # 14 Solution
Rearranging the Equation to Solve for x: x = [ln(2 mr/hr ÷ 750 mR/hr)]/0.5727 cm-1 x = ln(0.00267)/ 0.5727 cm-1 x = 10.35 cm
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 60: Quick Shielding Estimates
Half-Value Layer (Thickness) - HVL The Thickness of Material Required to Reduce the Photon Intensity to One-Half of the Initial Intensity.
Tenth Value Layer (Thickness)-TVL The Thickness of Material Required to Reduce the Photon Intensity to One-Tenth of the Initial Intensity.
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 61: TVL & HVL For 1 MeV Photons
  TVL, in HVL, in
Lead 1.15 0.33
Concrete 6.5 1.9
Water 13.5 4.0
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 62: Rule of Thumb – TVL Nuclear Plant Environment
Material TVL, in Lead 2 Steel/Iron 4 Concrete 12 Water 24
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 63: Number of Tenth-Value Thicknesses
# of TVLs Material, Inches Water Concrete Steel Lead ¼ 6 3 1 ½ ½ 12 6 2 1 1 24 12 4 2 2 48 24 8 4 3 72 48 12 6
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 64: Problem # 15
The Dose Rate From a Valve is 1200 R/hr. If 4 Inches of Lead is Used to Shield the Valve, What Will be the Shielded Dose Rate?
4 Inches of Lead = 2 TVL Shielding Dose Rate None 1200 mR/hr 1 TVL 120 mR/hr 2 TVL 12 mR/hr
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 65: Problem # 16
A Source With a Contact Dose Rate of 200 mR/hr is Laying Under 24 Inches of Water. What is the Dose Rate at the Surface of the Water?
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 66: Problem # 16 Solution
24 Inches of Water = 1 TVL Shielding, TVLs Dose Rate, mR/hr None 200 1 TVL 20 The Dose Rate at the Surface of the Water is 20 mR/hr.
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 67: Problem # 17
The Dose Rate From a Component is 10 R/hr. If 3 Half-Value Layers of Shielding is Placed Around the Component, What Would be the Shielded Dose Rate?
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 68: Problem # 17 Solution
Shielding, TVLs Dose Rate, mR/hr None 10 1 HVL 5 2 HVL 2.5 3 HVL 1.25 Dose Rate at 3 HVL Shielding = 1.25 R/hr
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 69: TVL/HVL Equations
TVL: D = D0(1/10)N
HVL: D = D0(1/2)M Where: D = Final Dose D0 = Initial Dose N = Number of Tenth-Thicknesses M = Number of Half-Thicknesses
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 70: Problem # 18
A Source Reading 900 R/hr is Shielded by 7 TVLs of Iron. What is the Shielded Dose Rate? D = D0(1/10)N D = 900 R/hr(0.1)7 = 900 R/hr(1 E-7) D = 9 E-5 R/hr or 0.09 mR/hr
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 71: Problem # 19
A Source With a Dose Rate of 400 R/hr is Shielded by 5 Half-Layers of Lead. What is the Shielded Dose Rate? D = D0(1/2)M D = 400 R/hr(0.5)5 = 400 R/hr(0.03125) D = 12.5 R/hr
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 72: Calculate Number of TVLS
Rearrange Equation D = D0(1/10)N to Solve For N. D/D0 = (0.1)N , or log(D/D0) = log(0.1)N From Log Rules, log(M)N = N*log(M), and log(0.1) = -1,Then log(D/D0) = N*log(0.1) = -1*N log(D/D0) = -N, or N = -log(D/D0)
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 73: Problem # 20
How Many Tenth-Value Layers Are Required to Decrease a Dose Rate From 300 rem/hr to 2 mrem/hr? N = -log(D/D0) N = -log(2 mrem/hr ÷ 300,000 mrem/hr) N = 5.18 Tenth Value Layers
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 74: Problem # 21
Assume That the Radiation Level From a Pump is 30 mR/hr One Foot From the Pump. If a Shield of Lead 2 Inches Thick is Placed so That the Outside Edge of the Lead is One Foot From the Pump, Calculate the Readings at a Distance of 10 Feet From the Pump.
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 75: Problem # 21 Solution
A. Calculate The Dose Rate at the Shield. 2 Inches of Lead is 1 TVL, so the Dose Rate is 3 mR/hr Through the Shield.
B. Calculate the Dose Rate 10 Feet From the Shield. I2 = (I1 * d12)/d22, = 3 mR/hr*(1 ft)2/(10 ft)2 I2 = 3 mR- ft2/hr ÷ 100 ft2 = 0.03 mR/hr
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 76: Shield Placement
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 77: Skyshine
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 78: Summary -1
Radiation Protection 1. Time 2. Distance 3. Shielding
Radiation Types/Shielding 1. Alpha – Air, Paper 2. Beta – Wood, Aluminum 3. Neutron – Water, Polyethylene (High Z) 4. Gamma – Pb, Steel, Concrete (Low Z)
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 79: Summary -2
Mathematical Principles & Equations 1. Least Square Law 2. Line or Parallel Source Equation 3. DR = 6CE 4. Attenuation Equations (Attenuation = Absorption + Scattering) 5. Half-Value Layer 6. Tenth-Value Layer
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 80: Summary -3
Additional Considerations: 1. Bremsstrahlung 2. Buildup 3. Skyshine
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program

## Slide 81: REMEMBER!
Follow Procedures
STAR S top T hink A ct R eview
Have a Questioning Attitude Qualify Validate Verify
TP-<number>
TVAN Technical Training
Health Physics (RADCON) Initial Training Program