## Slide 1: Coding with Arduino III: Ultrasonic Sensor
2016-2018 Shamsi Moussavi, Giuseppe Sena, Susanne Steiger-Escobar and Marina Bograd.
This material is based upon work supported by the National Science Foundation under grant no. DUE-1501451

## Slide 2: Electronic Components controlled by the Arduino:

## Slide 3: Ultrasonic Sensor

## Slide 4: What is a Sensor?
A device that receives a stimulus and respond with an electrical signal.
A special type of transducer (device that converts one type of energy into another.

## Slide 5: Common Sensors
Mechanical
  Accelerometers
  Gyroscopes
Optical
  Photodetectors
  Infrared
Semiconductor
  Gas
  Temperature
  Magnetic

## Slide 6: The Ultrasonic Sensor
This sensor has 4 pins but we’ll use it as a 3 pin sensor.
Data:
  The echo pin - listens for the returned pulse
  The trig pin - gets triggered to start the detection
5 v
ground

## Slide 7: How the Ultrasonic Sensor works
The ultrasonic range finder detects the distance of objects in front of the sensor for distances between 3 cm (1.8 in)to up to 4 meters (13.12 ft).
It works by sending out a burst of ultrasound to trigger the detection, and then listens for the echo when it bounces off an object.
The Arduino sends a short pulse to the Trig pin to trigger the detection.
It then listens on the Echo pin for a pulse.
The duration of the echo pulse is equal to the time taken by the ultrasound to travel to the object and back to the sensor.

## Slide 8: Using ultrasonic sensors (cont.)
You can use the speed of sound to convert the duration to a distance.
The speed of sound is 340 meters per second, which is 29 microseconds per centimeter.
The signal travels to the object and back, so the object is actually only half the distance.
The formula for the distance of the round trip is:
distance to the object = (duration / 29) / 2

## Slide 9: Understanding the Code:
const int pingPin = 7; // This is the pin number for sensor
void setup() {
Serial.begin(9600); // initialize serial communication
}
void loop() {
// establish variables for duration, and distance in in & cm
long duration, inches, cm;
// The PING))) is triggered by a HIGH pulse of 2 or more ms.
// Give a short LOW pulse beforehand to ensure a clean HIGH
pinMode(pingPin, OUTPUT);
digitalWrite(pingPin, LOW);
delayMicroseconds(2);
digitalWrite(pingPin, HIGH);
delayMicroseconds(5);
digitalWrite(pingPin, LOW);
// The same pin is used to read the signal from the PING))): a HIGH
// pulse whose duration is the time (in ms) from the sending
// of the ping to the reception of its echo off of an object.
pinMode(pingPin, INPUT);
duration = pulseIn(pingPin, HIGH);
// use a function to convert the time into a distance
inches = microsecondsToInches(duration);
cm = microsecondsToCentimeters(duration);
Serial.print(inches);
Serial.print("in, ");
Serial.print(cm);
Serial.print("cm");
Serial.println();
delay(100);
}

## Slide 10: Converting signal duration to inches or centimeters
long microsecondsToInches(long microseconds) { // this is a function
// According to Parallax's datasheet for the PING))), there are
// 73.746 microseconds per inch (i.e. sound travels at 1130
// feet per second). This gives the distance travelled by the // ping, outbound and return, so we divide by 2 to get the
//distance of the obstacle.
return microseconds / 74 / 2;
}
long microsecondsToCentimeters(long microseconds) { // this is a function
// The speed of sound is 340 m/s or 29 microseconds per centimeter.
// The ping travels out and back, so to find the distance of the
// object we take half of the distance travelled.
return microseconds / 29 / 2;
}

## Slide 11
Any questions?

## Slide 12
2016-2018 -- Shamsi Moussavi, Giuseppe Sena,
Susanne Steiger-Escobar, Marina Bograd
Boston College - Lynch School of Education
MentorNet - iCREAT MentorNet Community
This material is based upon work supported by the National Science Foundation under grant no. DUE-1501451