## Slide 1: iCREAT I - List of Components
2016-2018 Shamsi Moussavi, Giuseppe Sena, Susanne Steiger-Escobar and Marina Bograd.
This material is based upon work supported by the National Science Foundation under grant no. DUE-1501451

## Slide 2: List of Components
Ultrasonic Sensor
Motor Shield
LDR/Photoresistor
Arduino
Potentiometer
USB Cable
Buzzer/Speaker
9V Battery
9V Battery Clip
3V Coin Battery
Coin Battery Holder
Breadboard
Mini Breadboard
Resistors
LED
Cables:
Male-Female
Male-Male
Female-Female
Y-Cable
Micro Servo Motor

## Slide 4
-4 pin sensor
-Outer pins for power and ground
- releases an ultrasonic sound then triggers when the sound returns, giving distance.
-Used to easily control up to 4 DC motors
-Can control up to 2 servo motors as well.
-Plugs directly into the top of the Arduino
-Inner pins to send and receive a ping
-Used to read distances from the sensor
-Used with the breadboard
-Outputs a value for how much light it's receiving
(SEE NEXT SLIDE FOR CLOSEUP)

## Slide 5
Light dependent Resistor
- Is a resistor that is photosensitive
- Will let voltage flow based on the light level it is receiving.

## Slide 6: -Micro controller will run a single program on loop. -Can read and write information to the different pins.
- Is used to power and
Write code to the Arduino
- 3 pin resistor on a Knob
- the center is constant while the two sides are opposite scaling values
- Plays a tone at a specified frequency
- Is sensitive to which side is +-

## Slide 7
-Used as a power source for the Arduino
-Plugs into the 9V Battery
-Small coin battery
-Can be put inside the coin battery holder
-Holds the 3V Battery
-Has positive and negative pins on the back to plug into
-Rechargeable 9V battery
-Plugs into the 9V Battery Clip to supply power

## Slide 8
Male – Female cable
- Is used to either extend other cables, or directly connect a component to the Arduino
Male – Male cable
- is standard cable, used for connecting Arduino to breadboard as well as components to breadboard.
Female – Female cable
- Generally used as extension cable.

## Slide 9
-Used to connect the two middle pins (ECHO and TRIG) of the ultrasonic sensor to one analog pin on the Arduino
3 pin connector for servo motor
Brown – ground/gnd/-
Red – Power/5V/+ constant 5V supply needed
Orange - Serial/data, connect this to the pin to control the
servo

## Slide 10
A circuit board with long vertical strips located at the end of the board labeled '-' and '+' are connected by long, conductive metal strips.
The shorter middle horizontal strips – known as the terminal strips - located in the middle are connected by a shorter horizontal conductive metal strip.
Used to dampen voltage for example, an LED needs a resistor so it does not burn out
Light Emitting Diode
- Emits light based on voltage
- Positive leg "anode" is the longer leg
- Negative leg "cathode" is the shorter leg

## Slide 11
More information on the ultrasonic sensor pins, the data pin will correspond with a digital pin on the Arduino, the ground pin will attach to the ground pin on the Arduino and the 5V will attach to the 5V on the Arduino

## Slide 12
Ultrasonic sensor mount,
This mount enables the sensor to be attached to both the robot structure and to the servo motor(shown on next slide)

## Slide 13
Micro Servo and Holder mount

## Slide 14
The servo motor attaches to the bottom of the sensor mount

## Slide 15
Assembly of Ultrasonic Sensor, Servo and Holders on the Chassis

## Slide 16
Motor Shield and Arduino Assembly

## Slide 18
Chassis base will come assembled, you will attach the sensor/motor mount, battery, your 3D design, breadboard and Arduino to this

## Slide 19
Any questions?

## Slide 20
2016-2018 -- Shamsi Moussavi, Giuseppe Sena,
Susanne Steiger-Escobar, Marina Bograd
Boston College - Lynch School of Education
MentorNet - iCREAT MentorNet Community
This material is based upon work supported by the National Science Foundation under grant no. DUE-1501451