## Slide 1: Coding with Arduino VI: Basic Strategies for Collision Avoidance
2016-2018 Shamsi Moussavi, Giuseppe Sena, Susanne Steiger-Escobar and Marina Bograd.
This material is based upon work supported by the National Science Foundation under grant no. DUE-1501451

## Slide 2: OUTLINE
Micromouse Competition
Final Project: Telepresence Base (Micromouse)
Generating Random Numbers with an Arduino
Basic Strategies for Collision Avoidance

## Slide 3: Electronic Components used to control the Arduino:

## Slide 4: Micromouse Competition

## Slide 5: Micromouse Competition: Overview
A Micromouse is a small robot vehicle that is able to navigate its way through an unknown maze.
It is autonomous, battery-operated and self-contained, encompassing computer technology, electronics, robotics and artificial intelligence.

## Slide 6: Micromouse Competition: Overview (cont.)
Main challenge: incorporate adaptive intelligence which enables exploration of different maze configurations, and to work out the optimum route with the shortest run time from start to destination and back.
Reliably navigate the maze at a very high speed without crashing into the maze walls.
See Micromouse competition in progress...

## Slide 7: Rules for the Micromouse Competition
A Micromouse shall be self-contained (no remote controls).
A Micromouse shall not leave any part of its body behind while negotiating the maze.
A Micromouse shall not jump over, fly over, climb, scratch, cut, burn, mark, damage, or destroy the walls of the maze.
A Micromouse shall not be larger either in length or in width, than 25 centimeters. The dimensions of a Micromouse that changes its geometry during a run shall not be greater than 25cm x 25cm. There are no restrictions on the height of a Micromouse.
Any violation of these rules will constitute immediate disqualification.
See link for IEEE 2015 Micromouse Competition Rules.

## Slide 8: Rules for the Maze
Maze is composed of multiples of an 18cm x 18cm unit square. The maze comprises 16 x 16 unit squares. The outside wall encloses the entire maze.
The sides of the maze walls are white, the tops of the walls are red, and the floor is black. The maze is made of wood, finished with non-gloss paint.
The start of the maze is located at one of the four corners. The start square is bounded on three sides by walls. The start line is located between the first and second squares. The destination square has only one entrance.
Small square zones (posts), each 1.2cm x 1.2cm, at the four corners of each unit square are called lattice points.
Multiple paths to the destination square are allowed and are to be expected.
See link for IEEE 2015 Micromouse Competition Rules.

## Slide 9: Maze to Tree
Maze is transformed to a tree and back again.
Dead ends become the leaves of the tree.

## Slide 10: Micromouse: Maze Solver - Theory
Maze Solving Algorithms
P Control
Stepper Motor Theory

## Slide 11: iCREAT I - Final Project: Telepresence Base (Micromouse)

## Slide 12: Requirements and Design Considerations
What are design considerations?
What should requirements be?
What else should Simone have considered?

## Slide 13: iCREAT I - Final Project Overview
Students in iCREAT I will work on the:
Requirements
Design
Programming
Development
of a small and autonomous moving 2-wheels robotic base, that will be the platform used for a full telepresence solution to be developed on iCREAT II

## Slide 14: iCREAT I - Final Project Description (Micromouse)
Design an autonomous (no user interaction allowed) robot based on a typical device used in Micromouse events.
The robot’s (Micromouse) job is to navigate an obstacle course without collision.
The robot should be built using existing materials including:
A 2-wheels robotic chassis
An Arduino microcontroller with a ”motor shield“
Motors, sensors, and other electronic components as necessary (provided).
The robot will include at least one unique supportive or decorative structure that fits well within the design of the system. The structure must be designed using SolidWorks software.

## Slide 15: Main Goals
Avoid collisions with any object in your path
Develop an efficient and fast algorithm
Build a durable and well functioning device with components easily reached for repair and update

## Slide 16: Important Arduino Functions

## Slide 17: Generating Random Numbers with Arduino
We can use these function:
  random(): generates pseudo-random numbers.
  randomSeed(seed): initializes the pseudo-random number generator, causing it to start at an arbitrary point in its random sequence.

## Slide 18: Arduino random() Function
Description
The random function generates pseudo-random numbers.
Syntax
random(max)
random(min, max)
0 <= random(max) <= max-1
min <= random(min, max) <= max-1
Parameters
min - lower bound of the random value, inclusive (optional)
max - upper bound of the random value, exclusive
Returns
a random number between min and max-1 (long)a

## Slide 19: Arduino random() Function Examples
Based on https://www.arduino.cc/reference/en/language/functions/random-numbers/random/

## Slide 20: Arduino randomSeed(seed) Function
Description
Initializes the pseudo-random number generator.
This sequence, while very long, and random, is always the same.
Syntax
randomSeed(seed)
Parameters
long, int - pass a number to generate the seed.
Returns
no returns

## Slide 21: Arduino randomSeed(seed) Function
Use randomSeed() to initialize the random number generator with a fairly random input, such as analogRead() on an unconnected pin.
Conversely, it can occasionally be useful to use pseudo-random sequences that repeat exactly. This can be accomplished by calling randomSeed() with a fixed number, before starting the random sequence.

## Slide 22: Arduino randomSeed(seed) Function Example
https://www.arduino.cc/reference/en/language/functions/random-numbers/randomseed/

## Slide 23: Basic Strategies for Collision Avoidance

## Slide 24: Simple Maze Algorithms
A very unintelligent robot or perhaps a mouse arrives at a junction. What to do?
make a random decision about the next direction to follow or
always keep the wall to your right.
Although such methods would eventually find the right solution, these algorithm can be extremely slow.

## Slide 25
Any questions?

## Slide 26
2016-2018 -- Shamsi Moussavi, Giuseppe Sena,
Susanne Steiger-Escobar, Marina Bograd
Boston College - Lynch School of Education
MentorNet - iCREAT MentorNet Community
This material is based upon work supported by the National Science Foundation under grant no. DUE-1501451