## Slide 1: Coding with Arduino II: if/else blocks, and Analog & Digital input
2016-2018 Shamsi Moussavi, Giuseppe Sena, Susanne Steiger-Escobar and Marina Bograd.
This material is based upon work supported by the National Science Foundation under grant no. DUE-1501451

## Slide 2
Analog Input: Reading Sensors and a Potentiometer
Connect a light sensor or a potentiometer to an Analog Pin and check the data being received!
They will send a value between 0 and 1023.
Display or test the Analog pin!
Analog Input will only work with the analog pins on the Arduino. Use an If/Else block to test the data received.

## Slide 3
Displaying the Data Read
We know the sensor and the potentiometer are sending data through the pin. It would be nice to see the data. Right?
Let’s ask the Arduino to print it on the screen so we can see it.
Print to the Serial Monitor

## Slide 4
Using the Analog Input with Sensors - the LDR
Simulate first!
In TinkerCAD connect a light sensor to an Analog Pin. Code to display the data read on the serial monitor. It will be a value between 0 and 1023. Make sure to use a resistor!

## Slide 5
Ask a question. This is the test statement
If the answer is TRUE, then run code here
If the answer is FALSE, then run code here
Use an IF/ELSE block to make decisions
Use Comparison Operator blocks to test values in the question
Less than
Less or equal
Equal
Not equal
Greater than
Greater or equal

## Slide 6: How to use the monitor and LDR in a sketch
You must initialize the serial communication if you plan to display to the monitor.
Use Serial.print() to display to the monitor.
Read the sensor values by using the analogRead function with the pin number being used by the sensor.

## Slide 7
Open Serial Monitor and Check the data
Open Serial Monitor

## Slide 8
Challenges:
Make an LED turn on when the light sensor reads low levels.
Play a tone on the buzzer based on the light hitting the sensor
Control intensity of LEDs using a potentiometer
Control how many LEDs to turn on using a potentiometer
Control LED blinking speeds with a potentiometer

## Slide 9
Any questions?

## Slide 10
2016-2018 -- Shamsi Moussavi, Giuseppe Sena,
Susanne Steiger-Escobar, Marina Bograd
Boston College - Lynch School of Education
MentorNet - iCREAT MentorNet Community
This material is based upon work supported by the National Science Foundation under grant no. DUE-1501451