## Slide 1
Resistors!!!!!!!
How do we read them???
2016-2018 Shamsi Moussavi, Giuseppe Sena, Susanne Steiger-Escobar and Marina Bograd.
This material is based upon work supported by the National Science Foundation under grant no. DUE-1501451

## Slide 2
When you look at a resistor you'll notice 4-5 bands located at the center these indicate the value of the resistor. The bands are read from left to right. The side of the resistor with a band closest to the edge is the left, or start, of the bands.
You'll also notice the colors – we'll go into what those mean over the next few slides

## Slide 3
I mentioned that resistors typically have 4-5 bands.
In the case of 4 bands, the first two bands indicate the digits resistance value (in this case a 2-digit value) and the third indicates the multiplier.
Otherwise, in the case of 5 bands, the first three bands indicate a 3 digit resistance value. The 4th digit, in turn, represents the multiplier.
For both 4 and 5 band resistors, the final band represents its tolerance – also known as its percentage of error

## Slide 4
The second to last band on the resistor represents the multiplier, but this could also be referred to as a metric prefix. In this case black represents the base unit, brown deka, red hecto and so on... A chart with the prefixes and values is located on the following slide.
https://neurophysics.ucsd.edu/courses/physics_120/resistorcharts.pdf

## Slide 5
http://newhopestreamwood.com/wp-content/uploads/2017/09/metric-prefixes-chart-prefixes-png.png

## Slide 6
At the top and bottom of the chart, sample resistors are given. The way this is calculate is such:
10*100± =1000(1000=kilo or k)Ω±5% =1.0KΩ±5%
254*1±1%=254Ω±1%
But how do I calculate it??
1
0
100
±
5%
5%
2
5
4
*
*
1
±
1%
https://neurophysics.ucsd.edu/courses/physics_120/resistorcharts.pdf

## Slide 7
This is the start of the resistor
This is the end of the resistor
Now try an example from our own kit!!!
Write down the value of this resistor
33
0
*
1
±
1%
=330Ω±1%

## Slide 8
Any questions?

## Slide 9: Credits
2016-2018 -- Shamsi Moussavi, Giuseppe Sena,
Susanne Steiger-Escobar, Marina Bograd
Boston College - Lynch School of Education
MentorNet - iCREAT MentorNet Community
This material is based upon work supported by the National Science Foundation under grant no. DUE-1501451