## Slide 1: Coding with Arduino I: Arduino, Arduino IDE, and TinkerCAD
2016-2018 Shamsi Moussavi, Giuseppe Sena, Susanne Steiger-Escobar and Marina Bograd.
This material is based upon work supported by the National Science Foundation under grant no. DUE-1501451

## Slide 2: Programming the Arduino
To program the Arduino board we will use the Arduino Integrated Development Environment (IDE)
We will also use TinkerCAD, a simulation tool, to design our circuits and initially use its blocks programming language to help us code
Find TinkerCAD - Circuits at
Start the Arduino IDE by clicking Arduino IDE icon
on your desktop

## Slide 3: Components we will control with the Arduino:
Buzzer
Push button
Resistor
Other components we will need:

## Slide 4: Important Pins in the Arduino Microcontroller
Internal LED on Pin 13. Use it to test components!
Use these digital pins for your LEDs and push button. You can send or read a HIGH or LOW value only. DIGITAL!
Use these analog pins for your LDR or temperature sensors, potentiometer. You will read values between 0 and 1023. ANALOG!
Make sure your circuits are closed! Do not forget to connect components to GROUND!
PWM is a common technique for supplying variable power levels to slow electrical devices. The Arduino has 6 PWM pins. These are the digital I/O pins with a ~ (3, 5, 6, 9, 10 and 11).
Use PWM pins with servo motors.

## Slide 5: Terminology

## Slide 6: Using TINKERCAD
Go to https://www.tinkercad.com/ , and sign in
Select Circuits
Create new circuit

## Slide 7
Making an LED Blink (Review)
Turn pin 13 ON.
Stop program for 1 second.
Turn pin 13 OFF.
Stop program for 1 second.

## Slide 8: Using Variables to Simplify your Code
Use the blocks to get started and switch to text as soon as possible!
To use several LEDs, you must use multiple pins.
Your sketch will become long and repetitive.
Use variables!
A variable is a way of naming and storing a value for later use by our program. It has a name, a value, and a type.
Define good variable names for the pins you’ll use.
Changing pin numbers or adding new ones will be much easier.

## Slide 9: Example of code with variables
Variable ledA is used for pin 9.
Since the pins are whole numbers, we use the type int.
If you decide to use pin 5 instead of pin 9, you only need to change the value of ledA.
If you decide to use 3 LEDs, you will need to define one additional pin variable and cut and paste the rest to specify what to do with the new pin.

## Slide 10: Understanding Sound

## Slide 11: The Tone Procedure
For more info watch: Using the Arduino tone() function with a piezo speaker

## Slide 12
Notes and Frequencies

## Slide 13
Any questions?

## Slide 14
2016-2018 -- Shamsi Moussavi, Giuseppe Sena,
Susanne Steiger-Escobar, Marina Bograd
Boston College - Lynch School of Education
MentorNet - iCREAT MentorNet Community
This material is based upon work supported by the National Science Foundation under grant no. DUE-1501451