## Slide 1: INTRODUCTION TO ENGINEERING DESIGN & 3D MODELING
2016-2018 Shamsi Moussavi, Giuseppe Sena, Susanne Steiger-Escobar and Marina Bograd.
This material is based upon work supported by the National Science Foundation under grant no. DUE-1501451

## Slide 2: REQUIREMENTS: DEFINITION
A requirement is an expression of desired appearance and behaviour
Requirements focus on the user’s needs, not on the
  solution OR
  implementation
    designate what behaviour, without saying how that behaviour will be realized

## Slide 3: TYPES OF REQUIREMENTS
Functionality
Physical
Data
Usability
Reliability
Performance
Supportability

## Slide 4: ENGINEERING DESIGN PROCESS
We solve problems by designing solutions
There is a common cycle to the design process
The cycle is iterative and is repeated as we test and redesign until the most optimal solution is found
Watch the following videos for more information on the Engineering Design Process
http://www.youtube.com/watch?v=jUks3N3KliA
http://www.youtube.com/watch?v=0vOw41iYwMs
1.ASK
-Identify the problem
2.IMAGINE
-brainstorm solutions and ideas
3.PLAN
-Choose couple of the best ideas
4.CREAT
-Build a working prototype
5.TEST
-Evaluate the solution
6.IMPROVE
-Make improvements
-Repeat steps 1-6

## Slide 5: REQUIREMENT CONSIDERATIONS
Other:
Cost
User requirements
Aesthetics (How it looks)
Size and Shape (Geometry)
Environmental
Manufacturability
Regulatory
Ease of repair
Reliability
Lifespan
Disposability
Physical:
Weight
Material
Color
Transparency
Reflectance
Surface texture (polished, rough)
Elasticity
Hardness
Magnetic properties
Electrical properties
Performance:
Accuracy
Strength
Reproducibility, repeatability (Does it always do the same thing given the same input?)
Speed
Permeability (Do things leak through it?)
Flammability (ability to set on fire)
Insulation value
http://www.sciencebuddies.org/engineering-design-process/design-requirements-examples.shtml

## Slide 6: DISCUSSION
Based on the project description, what are the physical requirements?
Notes: Spend 5 -10 minutes getting students to think about:
What are the physical requirements?
What are the functional requirements?
After student discussion, explain that what they are compiling is a list of functional and physical requirements for a system. Next slide.
But we can’t ask them to tell us the physical and functional requirements before we have told about these are.
I think this slide should be moved to after we have talked about requirements

## Slide 7: PARTS - > FASTENERS -> ASSEMBLIES
Notes: Spend 5 -10 minutes getting students to think about:
What are the physical requirements?
What are the functional requirements?
After student discussion, explain that what they are compiling is a list of functional and physical requirements for a system. Next slide.
But we can’t ask them to tell us the physical and functional requirements before we have told about these are.
I think this slide should be moved to after we have talked about requirements

## Slide 8: iCREAT I - FINAL PROJECT DESCRIPTION (TELEPRESENCE BASE)
Design an autonomous (no user interaction allowed) robot based on a typical device used in Micromouse events.
The robot’s (Micromouse) job is to navigate an obstacle course without collision.
The robot should be built using existing materials including:
  A 2-wheels robotic chassis
  An Arduino microcontroller with a ”motor shield“
  Motors, sensors, and other electronic components as necessary (provided).
The robot will include at least one unique supportive or decorative structure that fits well within the design of the system. The structure must be designed using SolidWorks software.

## Slide 9: Project Grading Requirements
Teams must split the coding and design work very clearly for grading purposes. Each team will only use one chassis. Please make sure your project meets the following specifications.
Your robot must use:
Functional or decorative 3D printed components (each member of the team designs one part)
An ultrasonic sensor to avoid obstacles (Ex. team member 1 responsible)
A servo motor to sweep or other functionality (Ex. team member 1 responsible)
2 DC motors for the wheels and a motor shield (Ex. team member 2 responsible)
Integrate any of the following components (at least one component per each members of the team)
  At least 2 LEDs
  A buzzer.
  An LDR.

## Slide 10
For Example:
Team member #1: will code the servo motor, the ultrasonic sensor and LEDs and will design a functional or decorative component
Team member #2: will code the DC motors and the buzzer and will design a functional or decorative component
Team member #3: will code an additional servo motor, an additional ultrasonic sensor and an LDR and will design a functional or decorative component

## Slide 11: IDEA - PROTOTYPE
Functional Prototype
https://easybikerider.wordpress.com/tag/dmy/
CAD Model
http://blogs.solidworks.com/solidworksblog/wp-content/uploads/sites/2/6a00d83451706569e20191023f69f0970c.jpg
Idea Sketch
http://www.jefftk.com/p/sketches-of-bicycles

## Slide 12: ORTHOGRAPHIC PROJECTION
A way to represent a three dimensional object in two dimensions. Used in technical drawing to accurately describe an object in three views.
Note: when creating orthographic projection sketches, position of each view on the paper is very important. Each view is located in a specific place on the paper.
In the United States we use Third Angle Projection
Watch this interractive video to learn more: https://www.wisc-online.com/GammaPlus/Apps/ViewLearningApp/336
By en:User:Iseeaboar, derivative work by BAxelrod, vectorized by User:Biezl [CC BY-SA 3.0 (https://creativecommons.org/licenses/by-sa/3.0) or GFDL (http://www.gnu.org/copyleft/fdl.html)], from Wikimedia Commons
By Fvasconcellos (talk · contribs), original drawing by Christophe Dang Ngoc Chan [GFDL (http://www.gnu.org/copyleft/fdl.html) or CC-BY-SA-3.0 (http://creativecommons.org/licenses/by-sa/3.0/)], via Wikimedia Commons

## Slide 13: MEASURE
Measure existing parts to ensure your design will fit
By Joaquim Alves Gaspar, modified by ed g2s [GFDL (http://www.gnu.org/copyleft/fdl.html), CC-BY-SA-3.0 (http://creativecommons.org/licenses/by-sa/3.0/) or CC BY 2.5 (https://creativecommons.org/licenses/by/2.5)], from Wikimedia Commons
https://commons.wikimedia.org/wiki/File:Vernier_caliper.svg
Legend:
Outside jaws: used to measure external length
Inside jaws: used to measure internal length
Depth probe: used to measure depth
Main scale (cm)
Main scale (inch)
Vernier (cm)
Vernier (inch)
Retainer: used to block/release movable part
Watch this video to learn more about using the Vernier Calliper

## Slide 14: DIMENSIONS
Dimension Lines
Notations
Extension Lines
Leaders
Symbols
https://ocw.mit.edu/courses/mechanical-engineering/2-007-design-and-manufacturing-i-spring-2009/related-resources/drawing_and_sketching/

## Slide 15: ORTHOGRAPHIC PROJECTION PRACTICE
Follow orthographic projection and dimensioning rules to sketch the following model:

## Slide 16: ORTHOGRAPHIC PROJECTION PRACTICE SOLUTION
Check your sketch

## Slide 17
Modeling Parts and Assemblies in 3D
Refer to SolidWorks Vocabulary(W9 SolidWorks Vocabulary) for definition of commonly used terms
Watch this SolidWorks First Look Video to learn about SolidWorks capabilities
https://www.youtube.com/watch?v=fc2B3fkW1uA

## Slide 18: AFTER COMPLETING THIS LESSON YOU CAN NOW WORK ON
Orthographic Projection Drawing(Module 8 Final Project Part Engineering Drawing Assignment) of your final project part
Practice using SolidWorks - 2 Lessons (Part and Assembly)
  Open SolidWorks and click on Tutorials link
  Follow instructions in Lessons 1 and 2
  For video instruction go to http://www.solidworks.com/sw/resources/getting-started-3d-parts-design.htm

## Slide 19
3. Model your final project part in SolidWorks(read: iCREAT I-Module 9-Final Project SolidWorks Model Assignment).

## Slide 20
Any questions?

## Slide 21
2016-2018 -- Shamsi Moussavi, Giuseppe Sena,
Susanne Steiger-Escobar, Marina Bograd
Boston College - Lynch School of Education
MentorNet - iCREAT MentorNet Community
This material is based upon work supported by the National Science Foundation under grant no. DUE-1501451